## Slide 1: 225Ac in Belgium: Sample purity and 225Ra / 225Ac collection efficiencies
Jake Johnson
MEDICIS collaboration board July 2024

## Slide 2: 225Ac interest
100%
225Ra
14.90d
Kratochwil, C. et al.J. Nucl. Medicine 57, 1941–1944 (2016).
10 MBq patient doses.
7000 patient doses only produced WORLDWIDE via 229Th generators[1]
New production methods needed
Notes: Get on average cancer around 4 times a day.
Almost universally dealt with by our immune system
Reason we get cancer when older?

## Slide 3: natTh (p , X / X’) 225Ac / 225Ra production route (1)
127.7 − 11267 GBq production of 225Ac per month[1]
Robertson, Andrew KH, et al. Instruments 3.1 (2019): 18.
[1]Robertson, Andrew KH, et al. Curr. Radiopharm. 11.3 (2018): 156-172.
[2] https://www.isotopes.gov/information/actinium-225.
40.77 GBq of 225Ac in five years from tri lab effort[2]
Robertson, Andrew KH, et al. Inorgan. Chem. 59.17 (2020): 12156-12165.
Production
Separation
44-98% efficient…

## Slide 4: natTh (p , X / X’) 225Ac / 225Ra: The problem
227Ac (t1/2 = 21.8 y) co-produced ~equal cross section
> ~0.1 % of 225Ac activity
Mass separation enhances 225Ac/227Ac activity ratio with competitive efficiency to radiochemistry?
Measured in samples:
[1] 0.15%
[2] 0.142%
[1] Tollefson, A. D. et al. Appl. Radiat. Isot. 172,109693 (2021)
[2] Robertson, A. K. et al. Inorg. Chem. 59, 12156–12165(2020).
3 samples collected to analyse purity
Collection efficiency analysis performed

## Slide 5: Purity

## Slide 6: 3 samples collected from 3 “sources”
Source | A | B | C
Preparation method | [227Ac/225Ac]Ac(NO3)3 solution deposition + evaporate + dry | Direct irr. | Direct irr.
Collection time | Dec 2022 | Nov 2021 | May 2023
Target material | 15.08 g ThO2 | 14.65 g ThO2 fibre felt | 98.9 g ThCx pellets
s.o.c (227Ac) (MBq) | 100(5) | 4.7(2) | 1.64(2)
s.o.c (225Ac) (MBq) | 10.8 (6) | 2.37(7) | 1.03(3)
Source | A | B | C
Preparation method | [227Ac/225Ac]Ac(NO3)3 solution deposition + evaporate + dry | Direct irr. | Direct irr.
Collection time | Dec 2022 | Nov 2021 | May 2023
Target material | 15.08 g ThO2 | 14.65 g ThO2 fibre felt | 98.9 g ThCx pellets
 |  |  | 1.64(2)
 | 10.8 (6) | 2.37(7) | 

## Slide 7: 225Ac / 225Ra activity through nuc. decay spec.
-singles
coincidence
-singles

## Slide 8: E.O.C activities: 225Ac and 225Ra
*
sA:
sB+C:
*
Sample | A | B | C
(225Ac) (kBq) | 52.9(12) | 79.0(10) | 91.2(21)
(225Ra) (kBq) | - | 11.3(12) | 0*
Sample | A | B | C
 | 52.9(12) | 79.0(10) | 91.2(21)
 | - | 11.3(12) | 0*

## Slide 9: 227Ac activity measured using -recoil spectroscopy
Frantellizzi, Viviana, et al. Cancer biother. radiopharm. 35.6 (2020): 437-445.

## Slide 10: -decay recoil spectra
225Ac chain
227Ac chain
219Rn
215Po
217At
213Po
Notes: Emphasis: Exciting method as it allows the 227 Activity to be evaluated much quicker than just waiting.

## Slide 11: Direct alpha decay spectrometry validation
297 days
276 days
t since E.O.C:
Recoil method
Direct spec
3.70 (25) Bq
0.248 (17) Bq
3.90 (13) Bq
0.244 (33) Bq

## Slide 12: 227Ac / 225Ac activity ratio result
Mass separation enhances the 225Ac / 227Ac by a factor of ~500 – 1000.
Isotopic purity ~O(10) > than reasonable limit.

## Slide 13: Other contaminants?
206Po18O+
1% of 225Ac activity at e.o.c
Not seen in all samples
Implies even more (#) 209Po in collected sample.
208Po, 210Po seen in alpha spec…
Also…
214Po and 218Po seen in alpha spec… 226Ra daughters…

## Slide 14: Collection efficiency

## Slide 15: ThCx targets irradiated in 2023
Fluka simulations for in-target activity performed by C. Duchemin
Proton charge (Ah) | 42 | 40.7 | 159 | 95
 | 42 | 40.7 | 159 | 95
In target 225Ac (MBq) | 1030 | 997 | 611 | 2400
In target 225Ra (MBq) | 149 | 144 | 100 | 348
May
Jun
Aug
Sep
Notes: 100s of patient doses produced per 1 day irradiations…

## Slide 16: Collections in 2023
225Ra release:
T > 1600
225Ac release T > 2240C

## Slide 17: Preliminary collection efficiency estimate from beam current
Jun
May
225Ra: 55 MBq  37% coll. eff. (Prelim)
225Ac: 2.2 MBq  0.2% coll. eff. (Prelim)
225Ra: 25.9 MBq  18% coll. eff. (Prelim)
225Ac: 2.1 MBq  0.2% coll. eff. (Prelim)
Assign beam current to 225Ra and 225Ac regions
Integrate + convert to activity (accounting for feeding 225Ra  225Ac)
Normalise to -spec activity

## Slide 18: All 225Ac / 225Ra collection efficiencies (2023)
May
Jun
Aug
Sep

## Slide 19: Conclusions:
225Ac and 225Ra has been produced at MEDICIS
The isotopic purity of the collected 225Ac samples has 227Ac content below a reasonable limit for medical use
Most 225Ac can be produced from 225Ra implantation and decay
Target reuse is possible, but efficiency is reduced if target is ‘punished’
Outlook:
Possible “Best” 225Ac production:
Irradiate 232Th metal target
Radiochemistry to separate Ra and Ac fractions
Use the Ra fraction as 225Ac generator
Perform mass separation on the Ac fraction
More research:
Ionize Ra using Raman laser at MEDICIS
Re-use of target at lower temperature, collecting 225Ra/224Ra only, not 225Ac
…

## Slide 20: Thanks to wonderful colleagues
Mia Au2, Cyril Bernerd1,2, Frank Bruchertseiffer3, Thomas E. Cocolios1, Marie Deseyn1, Charlotte Duchemin2, Michael Heines1, Max Keppens1, Laura Lambert2, Nathan Meurrens1, Ralf E. Rossel2, Thierry Stora2, Viktor Van den Bergh1, Wiktoria Wojtaczka1
MEDICIS collaboration, CERN SY-STI group…
[1] KU Leuven
[2] CERN
[3] JRC Karlrushe
20
SY-STI coffee hour 21/10/2022

## Slide 21: Backup slides…

## Slide 22: How to get Ac-227 activity from recoil spectrum (1)
~Same for same generation daughters in 227Ac and 225Ac chains

## Slide 23: How to get Ac-227 activity from recoil spectrum (2)

## Slide 24: Geometric corrections due to recoil + ping pong

## Slide 25: Alpha decay activities of Fr, At, Po with and without ping pong

## Slide 27: Gamma spectroscopy curves

## Slide 28: Gamma-gamma spectroscopy curve

## Slide 29: Ra-226 contamination
Activities:
A | B | C
4.7 (4) Bq | 0.6 (6) Bq | 4.1 (7) Bq

## Slide 31: Production
Activity prod. Rate 225Ac (MBq /Ah / g) | p+ Beam energy (MeV) | Facility
0.55[3]* | 800 | LANL
0.026[4] | 438 | TRIUMF
0.25* | 1400 | MEDICIS
 | p+ Beam energy (MeV) | Facility
0.55[3]* | 800 | LANL
0.026[4] | 438 | TRIUMF
0.25* | 1400 | MEDICIS

## Slide 33: ThCx target reuse: effect on collection efficiency
From implanted ion current from fresh target:
225Ra activity = 50.1 MBq  34% efficiency
225Ac activity = 1.7 MBq  0.17% efficiency
For re-used target:
225Ra activity = 25.6 MBq  18% efficiency
225Ac activity = 2.1 MBq  0.21% efficiency
Irradiation conditions 2nd time round almost identical.
Notes: Overlay the two plots of ion current vs time on top of each other, along with target temperature. Show the decrease in Ra release, but the overall increase of Ac efficiency. Talk about the laser test done on mass 227 showing that Ac-227 was present even at low temperature.

## Slide 34: Influence of ion source temperature on Ra and Ac beam
Laser ionization efficiency improves with temperature
Surface ionization efficiency improves with temperature
Several x improvement in efficiency possible
Higher temperature  Better ion confinement  higher surface / laser ionization efficiency
.
and normalization constant only free parameters.

## Slide 35: Influence of target temperature on Ac beam
Increase temperature: Good for collecting quicker, bad for collecting more efficiently!
Temperature systematics well described by Arrhenius-law for diffusion…

## Slide 36: How easy is it to get α-emitters?
Medical alpha emitters production
Only few choices
Often high-Z
“Difficult” target material or beams
Notes: Ra-226 target for producting Ra-223 and Ac-225 and Th-227.
Natural neodymium, praseodymium targets for Tb-149 wih carbon beam
Natural bismuth or enriched bismuth targets with alpha beam.

## Slide 37: Collections as they happened
What do we implant on our foils?
Exp1: integrated ion current consistent with measured 10% collection efficiency
Exp2: Integrated ion current overestimates implanted 225Ac activity, Kromek gets it right!
Exp3: Integrated ion current: wtf? Kromek gets it (mostly) right, but misses implanted 225Ra
[1] Bernerd C., et al. "Production of innovative radionuclides for medical applications at the CERN-MEDICIS facility." NIM B [in progress] (2023): 541 .
Notes: 10.0 % vs 10.1 % so in very very good agreement with each other for ex 1
in ex2: relative overestimation of 30% compared with offline spectroscopy measurement, while kromek has a relative overestimation of less than 10% and agrees with the measured result to within 1-sigma.
In ex3, the relative overestimation by simply counting ions is plain wrong. The kromek on the other hand is roughly in agreement with the 200kBq measured offline.
This begged the question – what on earth have we collected?

## Slide 38: A wolf in Sheep’s clothing: The beam at mass 225
Intense ion beams of masses have significant mass tailing, in all experiments so far with varying degrees…
Major contributor to ion beam current at mass 225
Precludes identification with resonance laser ionization enhancement
Notes: Talk about the mass tailing effect coming from the Lanthanide region.
Beam scatter of extremely intense beams. 3 orders of magnitude less than the peak of an intense beam, it still contributes significantly at these higher masses.
Reason for lower collection efficiencies is the need to go to very high target temperatures for a very modest beam of Ac225
While doing that all other beams that can be produced, are, which builds up background ions on our mass of interest. The background makes it much more difficult to identify Ac225. Our tactic now is to thoroughly outgas the target before beginning collection. In online collection we just collect radium at first.

## Slide 39: Most mass scans ever taken…

## Slide 40: Laser enhancement

## Slide 41: Ra-225 ID during beamtime