Muon Cooling for a Neutrino Factory and Muon Collider
Demonstrator Magnetic Lattice
C. T. Rogers
Rutherford Appleton Laboratory

---
Lattice design process
- Understand basic parameter dependencies
  - Solenoid optics
  - RF/longitudinal optics
  - Dipole field/dispersion
- Lattice design
  - Choose working point based on parameter dependencies
  - By-hand optimisation based on reasoned arguments
- Final optimisation
  - Throw into some optimiser
I am here

---
Last time...
- Last time
  - Found some good working magnet parameters
  - Started looking at RF
  - Started looking at dispersion control
- This time
  - Settle on cooling cell parameters
  - Look at performance indicators

---
Schematic – one (half) cell
Coil
Coil
Coil
Coil
Wedge
thickness
Wedge
angle
RF window
thickness
RF cavity
length
Iris
radius
Coil radial
thickness
Coil
length
Coil
Z centre
position
Coil
inner
radius
Dipole z
centre
position
Dipole
length
Cell Length

---
Closed Orbit: ++++
+
+
+
+

---
Closed orbit: +--+
Note
absorber
flip
-
-
+
+

---
Schematic – one (half) cell

---
Dispersion
By = 0.1 T; ++++
By = 0.2 T; ++++
By = 0.1 T; +--+
By = 0.2 T; +--+

---
DA – no dipole

---
DA – 0.1 T +--+

---
DA – 0.2 T +--+

---
DA – 200 MeV/c +--+

---
Introducing Wedge/cooling

---
Introducing Wedge/cooling
Note
Initial
mismatch

---
Transmission
Blue – transmitted particles
Orange – scraped particles

---
Acceptance
Fraction that scrape
in each bin
Initial distribution

---
Iris factor
Baseline
Iris radius
- Iris factor – ratio of RF aperture to ideal cavity radius
  - Nominal radius @ 704 MHz is 163.1 mm
  - Choose baseline 0.5 (81.6 mm)

---
Window thickness

---
RF phase

---
Absorber material
No absorber
windows

---
Absorber material

---
Dipole
- Understand basic parameter dependencies
  - Solenoid optics
  - RF/longitudinal optics
  - Dipole field/dispersion
  - Introduce wedge (maybe cooling without stochastics?)
- Lattice design
  - Choose working point based on parameter dependencies
  - By-hand optimisation based on reasoned arguments
- Final optimisation
  - Throw into some optimiser
- Tagged as 2024-05-23_prerelease on github
Work in progress
Work in progress