## Slide 1
Matteo Solfaroli
13th Large Hadron Collider Physics Conference
May 05th, 2025
Status of the LHC

## Slide 2: Outline
2024 run highlights
2025 configuration and key aspects
Beam intensity limitations and plans
2025 schedule and projections
  + considerations on IONS run

## Slide 3: LHC in 2024
First injection: 8th March (3 days early)
First Stable Beams @6.8 TeV 5th April (3 days early)
LHCb VELO closed for the 1st time
1200 bunches on 14th April (10 days early)
Reverse Polarity optics
commissioned (~ +1 week)
β* limited to 36 cm 17th April
Bunch length control/target
Limit RF module heating risk
VdM & Calibration
Runs, 16th – 20th May
BCMS beams
May
β* back to 30 cm 17th June
Beyond 110 fb-1
IONS run
(YETS started on 25th November)
pp reference run 28th Oct – 2nd Nov
90% availability
Q1
Q4
March
April
May
June
July
September
October
pp run
August
IONS run
November
ref run
Stable Lumi
Production
Summer period
1.9 nb-1 in IP1/2/5
(same as 2023 in 50% of the time)

## Slide 4: 2024 production
124 fb-1 in ATLAS/CMS
11 fb-1 in LHCb
67.5 pb-1 in ALICE
Highest production rate ever
Single most productive year in LHC history so far!
2024 AVG rate = 0.83 fb-1/24h
2024 highest rate = 1.5 fb-1/24h
(midnight to midnight)
LS1
LS2
IP1/2/5: Almost same luminosity as 2023, in about half the time, achieving the (ambitious) target of 1.9 nb-1
IP8: About double the 2023 luminosity in about half the time
~30% higher intensity with performance beyond HL-LHC projection
~2h of levelling at 6.4x1027 cm-2 s-1
IONS

## Slide 5: Outline
2024 run highlights
2025 configuration and key aspects
Beam intensity limitations and plans
2025 schedule and projections
  + considerations on IONS run

## Slide 6: Triplet radiation – the problem
Radiation dose on inner triplet magnets located next to the high-luminosity interaction points, is approaching levels close to the estimated damage thresholds
  though they carry significant uncertainties
A failure of one of these magnets could lead to substantial downtime for the LHC or even compromise the results of the nearby physics experiments
To address this risk a taskforce was established in 2022 to study the impact of radiation on equipment lifetime in the inner triplet regions and to propose possible mitigations
Limiting quadrupole in Interaction Region (IR) 5

## Slide 7: Triplet radiation – the solution
The dose can be spread over different azimuths by:
  Inverting quadrupole polarities (Reversed Polarity optics)
  Change crossing angles sign and/or plane
There are in principle 8 configurations, however only 4 are possible, due to stability requirements
  Alternate H-V or V-H crossing angle plane in IR1 and IR5
2024: RP optics in Interaction Region (IR)1
  Significant reduction of radiation dose on IR1 magnets
  Increased background for Forward physics detectors
2025: RP optics in IR5 & restored “nominal” optics in IR1 + crossing plane inversion
  Significant reduction of radiation dose on IR5 magnets
  Situation restored for Forward physics detectors
ex. of 2024 change in IR1
Longitudinal distribution of radiation

## Slide 8: Triplet radiation – consequence
The Inner Triplet beam screen shape is asymmetric, arranged for larger aperture in the “standard” crossing plane (beam size in IT quadrupoles is  1/):
With inversion of planes, the aperture in the crossing angle plane is significantly reduced
  Less aperture in the rotated crossing plane: minimum β* increases from 30 cm (2024 value) to 60 cm
  More aperture in the rotated separation plane: minimum β* decreases from 30 cm to 18 cm
Flat optics: luminosity ~equivalent

## Slide 9: Levelling in physics – why?
The LHC can operate at more than twice its nominal peak luminosity of 1x1034 cm-2 s-1
However, the instantaneous luminosity needs to be kept under control, due to:
  heat load to the cryogenic system of the superconducting magnets close to the interaction points
  event pile-up in the experiments
For this reason, the instantaneous luminosity during a physics fill is limited to ~2.1x1034 cm-2 s-1, until the point of natural decay is reached

## Slide 10: Levelling in physics
2024 and 2025
Combined (b* + offset) levelling
  6-7 hours constant luminosity
  Well balanced luminosity between CMS and ATLAS
LHCb levelled through the entire fill
Luminosity control ~1.5% (5% is Run3 request)
Fast increase to levelling start point (few % gain)
There are different ways to control instantaneous luminosity:
Beams separation offset
Crossing angle
Beam dimension at interaction point (b*)

## Slide 11: Outline
2024 run highlights
2025 configuration and key aspects
Beam intensity limitations and plans
2025 schedule and projections
  + considerations on IONS run

## Slide 12: Intensity limitation – warm vacuum modules
IMPACT in 2023
~5 days lost
Bunch intensity limited to 1.6x1011 protons per bunch (ppb)
IMPACT in 2024
Bunch intensity limited to 1.6x1011 ppb, while maximizing the bunch length through the cycle
  Difficult to identify intensity limitation (strong dependence on contact quality)
Consolidation: 71 modules replaced
Improved control of bunch length provides safety factor in power deposition
NO more intensity limitations in 2025
This operational improvement, together with the completion of the warm vacuum modules consolidation can open a window for higher intensity tests/operation, with very low risk of impact on availability
Bunch length during the energy ramp

## Slide 13: Intensity limitation – heat load
Heat load (HL) deposited by the beams can become a limitation when cryo capacity is not enough
  Electron cloud generated
  Presently well beyond the Design Report value
Degradation observed when sectors are vented to air
Heat load is not homogeneously distributed
  Sector 78 is the highest sector in Run3
Geographical HL distribution

## Slide 14: Intensity limitation – heat load
HL brings limitations on total number of bunches and bunch intensity
Gradual conditioning helps to increase beam intensity
  Dedicated sessions (so-called scrubbing) are regularly carried out
  Conditioning by operation over 2024 allowed to gain ~5-10% margin
conditioning by operation
Scrubbing

## Slide 15: 2025 proton-proton operation
In Run3 LHC has been so far operated with train of 1.6×1011 proton per bunch (ppb):
  Run3 target (1.8×1011 ppb) was not (yet) achieved
The injector chain achieved target parameters for LHC Injectors Upgrade (LIU) project
  4x72 bunches @2.3×1011 ppb at SPS flat top
Different scenarios for 2025 run
  No risk pp production - NOT more knowledge at end of 2025 than today!
  Early, distributed, late intensity steps towards 1.8x1011 ppb
Agreed scenario
Stable run at 1.6x1011 ppb until september THEN increase bunch intensity until 1.8x1011 ppb, before ION run

## Slide 16: Towards HL-LHC intensity
End of Run 3: last window to probe HL-LHC beam intensities
Critical investment into the success of HL-LHC!
Increasing intensity can reveal “unexpected limitations”
  BSRT mirror, (old) TDIs, vacuum modules, roman pots
Once operation at 1.8x1011 ppb (Run3 goal) demonstrated, test to explore intensity range up to 2.3x1011 ppb
  Beam dynamics tests: compatible with intensity limits (lower number of bunches)
    Started: RF capture, electron cloud, beam in(stability), beam-beam…
  Heating test ( 2000 bunches)
    Heating power will exceed the peak values achievable in operation with 1.8×1011 ppb
    Potential risk to components and to machine availability from “unexpected limitations”
Heating test proposed for 2026:
Advance the ion run by 2 weeks
No risk to physics program in case of equipment failures
Q1-Q2 2026

## Slide 17: Outline
2024 run highlights
2025 configuration and key aspects
Beam intensity limitations and plans
2025 schedule and projections
  + considerations on IONS run

## Slide 18: 2025 schedule
First stable beams at 6.8 TeV on May 5th
Intensity ramp up (number of bunches) at 1.6×1011 ppb  full machine around mid-May, followed by long production period
Oxygen run during 1st week of July
Q1-Q2
Q3-Q4

## Slide 19: Availability
Availability is THE key factor for accelerator performance
Availability factor is ~constant through Run2 and Run3 for small (<24h) faults
NOTE: the availability of the proton run is calculated on the effective time from the retrospetctively calculated schedule (long faults are not included)
Minor differences in numbers are due to slightly different choices in term of dates (including or not scrubbing run, TS recovery etc)
2024 pp run

## Slide 20: pp run performance estimate
LHCb prediction (driven by hours in stable beams and levelling target)
~11 fb-1
Performance estimate depends on many operational parameters, but above all availability!
Assuming conditions 2024-like:
  ATLAS/CMS: ~120 fb-1
  LHCb: ~11 fb-1
  ALICE: ~65 pb-1
ATLAS/CMS prediction
~120 fb-1
2024 AVG production rate
0.83 fb-1/24h

## Slide 21: Oxygen run
Luminosity targets in nb-1
Injection
Ramp to 6.8 Z TeV, β*=1m/
1.5m
Squeeze β*=0.5m 1m
Physics
Injection
Physics
Ramp to 5.36 Z TeV, β*=1m/
1.5m
p-O
O-O
Preferred by experiments
Injection
Ramp to 6.8 Z TeV, β*=1m/
1.5m
Pb-Pb
Squeeze β*=0.5m 1m
Physics
8 days allocated for Oxygen - setup and physics
Requests from the experiments require 3 distinct machine configurations (LHCf β*  1m, OO at 5.36 TeV)
Estimates indicate that some targets are difficult to reach. Time estimates range between 7 days (perfect availability) and 9 days
Short runs are very sensitive to availability

## Slide 22: LS3 planning
LS3 start delayed to 29th June 2026
LS3 goal: 47 months beam to beam
  Still ~1.5 month to optimize, promising options being discussed, expected to converge by June 2025
Early June 2030: beam back in the LHC
  Experiments caverns closure mid-May ‘30
  Beam vacuum valves opening end-May ‘30

## Slide 23: Conclusions
2025 run has started and the LHC is ready for 2025 goals
  Stable operation with 1.6x1011 ppb until the end of summer
  Increase bunch intensity to reach 1.8x1011 ppb before the ION run
  ~120 fb-1, ~11 fb-1, ~65 pb-1 can be in reach in 2025, assuming 2024-like availability
Pushing bunch intensity during Run3 is key to unveil potential limitations before LS3 and prepare the road to High Luminosity LHC
It looks easy, but the fact that we can operate the LHC at such a high level is a tremendous achievement and a true reflection of the incredible dedication of everyone involved!

## Slide 24: SPARE

## Slide 25: 2026 draft schedule

## Slide 26: Heat-load – the problem
BASE
(2 K loops, thermal shields, DFB, SAM, RF, etc.)
Beam screen*
170 W/hc
LHC
Today
HL-LHC
(without BST)
BASE
(2 K loops, thermal shields, DFB, SAM, RF, etc.)
Beam screen*
285 W/hc
HL-LHC
(with BST)
BASE
(2 K loops, thermal shields, DFB, SAM, RF, etc.)
Beam screen*
160 W/hc
NB: The graphics are not scaled, they are only illustrative
Cryogenic operation margin
for daily operation
(handle transients during
injection and magnet ramping)
+ facing disturbances
Operational margin
Operational margin

BASE
(2 K loops, thermal shields, DFB, SAM, RF, etc.)
Operational margin
Beam screen
84 W/h
LHC
Design Report
*Beam screen values are given as example, as e-cloud varies along the machine
Inner Triplet
Inner Triplet
1 cryoplant capacity
~18 kW @4.5 K

## Slide 27: HL-LHC operation
Recent update: IONS operation in 2031-2041