## Slide 1: Alignment analysis of the RFD prototype during cold test at CERN
Vivien RUDE
2024-10-09
14th HL-LHC Collaboration Meeting, Genoa (Italy), 7-10 October 2024
On behalf :
Mateusz SOSIN
Praneeth Sarvade,
Daniel Szarata
Clara Cala Franco
Julia Calmels

## Slide 2: Outline
Alignment objectives (3 objectives)
Internal monitoring configuration and challenges
Alignment RFD Prototype results
Conclusion and perspectives
Spare : FSI following during Cavity 2 repair

## Slide 3: Internal monitoring for “special” components
Vacuum vessel
Cold mass
Crab cavities
Cryomodule
Nominal axis
Vacuum vessel
Axis of the Cold mass
At cold
Axis of the Crab cavities
At Cold
Cryomodule
Q1, Q2a, Q2b, Q3
Crab-Cavities

## Slide 4
Alignment Objective n°1 : Fiducialisation
Bare Cavity
Cavity radio frequency axis  Approximated to mechanical axis of the capacitive plate
Dressed Cavity
8 Alignment targets :
FSI targets
Alignment requirement
Position : 50 μm (1)
Roll : 100 μrad (1)
Axis of the
capacitive plate
Axis of the
capacitive plate

## Slide 5
Alignment Objective n°2 : Internal monitoring
Cavities RF
Cryomodule
Alignment requirement
Position : < 100 μm (1)
Roll : < 400 μrad (1)

## Slide 6
Alignment Objective n°3 : External monitoring
Alignment requirement
Align all the components per IP side : < 100 μm (1)
Align all the components (Left and Right) : Vertical < 170 μm (1)
Align all the components (Left and Right) : Radial < 330 μm (1)
Roll : < 150 μrad (1)
R = 0.33 mm
Left
Right
Q5
Q4
CC2
CC1
D2
TCLX
TCTPH
TCTPV
TAXN
D1
CP
Q3
Q2b
Q2a
Q1
EXP.
UPS gallery
P1
P2
P3
P4
P5
P6
Q1
Q2a
Q2b
Q3
CP
D1
TAXN
TCTPV
TVTPH
TCLX
D2
CC1
CC2
Q4
Q5
Alignment between Q1 and Q5 :
Limits :  (1 sigma) < 0.1 mm
Alignment between Q5-left and Q5-right :
Vertical Limits :  (1 sigma) < 0.17 mm
Radial Limits :  (1 sigma) < 0.33 mm
R = 0.1 mm
R = 0.1 mm
Inner
Tracker

## Slide 7: Internal monitoring
Alignment requirement
Position : < 100 μm (1)
Roll : < 400 μrad (1)

## Slide 8: Internal monitoring : Configuration
  FSI : Frequency Scanning interferometry
   Absolute distance measuring interferometric technique
Largest standard uncertainties | Uncertainty (1)
Position of the FSI Sensor in the framework of the cryomodule | 40 µm
Position of the FSI target in the framework of the crab-cavity | <15 µm
FSI target
on the flange of Helium TANK of the cavities
reflection
Reflecting
glass sphere
(FSI target)
Flange of Helium Tank of RF Crab-cavities
Support
FSI target
FSI Head (sensor)
on the Cryomodule
Optical fibre
FSI Acquisition system
Feedthrough
(FSI Head)
Fiber ferrule tip
8 FSI meas.
8 FSI meas.
Total : 16 observations
(3D distances)

## Slide 9: Internal monitoring : Challenges and prerequisites
Beam
All adjustments should be carried out at ambient pressure.
Ambient pressure
Measurement + Adjustment
The position of two cavities should be determined at cold at less than 0.1 mm (1sigma)
The position of two cavities at cold should be aligned at less than 0.1 mm (1sigma)
Two inner components
Non compensable misalignment
on the external envelope
No possibility to adjust
ANTICIPATION : The position of the cavities should be at their nominal position at warm with an accuracy of less than 40 microns.
The position of the FSI sensors w.r.t. cryomodule must be measured with an accuracy of less than 40 microns.
Cooling down
Anticipation
Anticipation of the Deformation of the outer envelope with an accuracy of less than 40 microns
(deformation up to 0.1 mm)
Anticipation of the Movement of the cavities :
(Complex movement up to 1.2 mm
7 DOF)
Anticipation of the Deformation of the outer envelope with an accuracy of less than 40 microns
(deformation up to 1.2 mm)
Anticipation of the Movement of the cavities :
(Complex movement up to 0.4 mm
6 DOF)
Under vacuum
Anticipation
Cryomodule
FSI Sensor
RF cavity
RF cavity

## Slide 10
Alignment analysis of the RFD prototype during cold test at CERN

## Slide 11
Ambient pressure
Under vacuum
Shape Repeatability
For 3 cycles :
Maximum dispersion : 67 μm
Average dispersion : 18 μm
Shape Repeatability
For 3 cycles :
Maximum dispersion : 57 μm
Average dispersion : 16 μm
Max deformation :
1.20 mm
Deformations of the cryomodule (due to pumping and cooling down)
No deformation was observed on the edge of the top plate during pumping.
Shape of the cryomodule under vacuum
Repeatable at +/- 0.040 mm (RMS)
Shape of the cryomodule at ambient pressure
Repeatable at +/- 0.040 mm (RMS)
Cold
Shape Repeatability
For 3 cycles :
Maximum dispersion : 68 μm
Average dispersion : 17 μm
Max deformation :
0.12 mm
During cooldown, the top plate observed a thermal contraction due to thermal convection between the thermal screen and the top plate --> not expected but repeatable--> Can be anticipated
Shape of the cryomodule at cold
Repeatable at +/- 0.040 mm (RMS)

## Slide 12
A priori sigma : 0.04 mm | Parameter | Accuracy expected (simulation)
Cav1 | Tx (mm) radial | 0.16
 | Ty (mm) longitudinal | 0.08
 | Tz (mm) vertical | 0.08
 | Rx (mrad) pitch | 0.08
 | Ry (mrad) roll | 0.41
 | Rz (mrad) yaw | 0.41
Cav2 | Tx (mm) radial | 0.04
 | Ty (mm) longitudinal | 0.10
 | Tz (mm) vertical | 0.02
 | Rx (mrad) pitch | 0.04
 | Ry (mrad) roll | 0.36
 | Rz (mrad) yaw | 0.10
SCALE (mm/m) |  | 0.11
Bad geometry
for cavity 1
Uncertainty of position of cavities inside the cryomodule
Jumper
Alignment requirement
Position : < 100 μm (1)
Roll : < 400 μrad (1)

## Slide 13
Uncertainty of position of cavities inside the cryomodule
Issue with FSI Target Holder:
FSI targets are not making proper contact with the holder.
Different thermal contraction of glass and metal causes spring permanent deformation
 Upgrade to spring frictionless fixation
 | Parameter | Current accuracy (reality)
Cav1 | Tx (mm) radial | 0.20
 | Ty (mm) longitudinal | 0.20
 | Tz (mm) vertical | 0.15
 | Rx (mrad) pitch | 0.15
 | Ry (mrad) roll | 0.70
 | Rz (mrad) yaw | 0.50
Cav2 | Tx (mm) radial | 0.08
 | Ty (mm) longitudinal | 0.10
 | Tz (mm) vertical | 0.05
 | Rx (mrad) pitch | 0.05
 | Ry (mrad) roll | 0.40
 | Rz (mrad) yaw | 0.10
SCALE (mm/m) |  | 0.20
Maximum
Residual
[mm]
Pumping
Cooling down
Objective : RMS residual < 0.04 mm
The current uncertainties for cavity 2 stay within
the objective
Alignment requirement
Position : < 100 μm (1)
Roll : < 400 μrad (1)

## Slide 14
Motions of the cavities during the three states
Objective at cold
Objective at cold

## Slide 15
Pumping
Cooling down
Objective : 0 mm +/- 0.1 mm
IN (cav 2)
OUT (cav 2)

## Slide 16
Chart: Radial position (mm)
| 0 | 3000
Objective at cold | 0 | 0
Cav 2 : ambient pressure | -0.724 | -0.429
Cav 2 : Cold | -0.014 | 0.007
Cav 1 : ambient | -0.701 | -0.371
Cav 1 : cold | 0.112 | 0.25
obkectif min | -0.083333 | -0.083333
objectif max | 0.083333 | 0.083333
Chart: Vertical position (mm)
| 0 | 3000
Objective at cold | 0 | 0
Cav 2 : ambient pressure | -0.729 | -0.757
Cav 2 : Cold | 0.126 | 0.024
Cav 1 : ambient | -0.708 | -0.773
Cav 1 : cold | 0.132 | -0.191
obkectif min | -0.083333 | -0.083333
objectif max | 0.083333 | 0.083333
Current positions at cold (Sept 2024)
Warm position
Cold position
Radial
Vertical
Cavity 1
Cavity 2
Cavity 1
Cavity 2
Objective
at cold

## Slide 17
Chart: Relative vertical motion (mm)
| 0 | 3000
Objective at cold | 0 | 0
Cav 2 : ambient pressure | -0.855 | -0.781
Cav 2 : under vacuum | -1.262 | -1.122
Cav 2 : Cold | 0 | 0
IN
OUT
875 mm
Step 3 : Cavity with
cryomodule at cold
Step 1 :
Cavity with cryomodule
at ambient pressure
Step 2 : Cavity with
cryomodule under vacuum
Chart: Relative Radial motion (mm)
| 0 | 3000
Objective at cold | 0 | 0
Cav 2 : ambient pressure | -0.71 | -0.436
Cav 2 : under vacuum | -0.336 | -0.062
Cav 2 : Cold | 0 | 0
Step 3 : Cavity with
cryomodule at cold
Step 1 :
Cavity with cryomodule
at ambient pressure
Step 2 : Cavity with
cryomodule under vacuum
Relative Motions of the cavities
due to vacuum and cooling down (cycle 3)

## Slide 18
Repeatability on the motions
 | Cavity 2 | 
Impact of cold | Cycle 2 | Cycle 3
Tx [mm] (radial translation) | 0.60 | 0.57
 | +/-0.10 | +/-0.08
Ty [mm] (longi translation) | 0.15 | 0.27
 | +/-0.15 | +/-0.10
Tz [mm] (vertical translation) | 0.76 | 0.81
 | +/-0.05 | +/-0.05
Rx [mrad] (Pitch angle) | 0.05 | -0.08
 | +/-0.05 | +/-0.05
Ry [mrad] (Roll angle) | -0.74 | -0.41
 | +/-0.40 | +/-0.40
Rz [mrad] (Yaw angle) | 0.45 | 0.31
 | +/-0.15 | +/-0.10
Scale [mm/m] | -2.22 | -2.14
 | +/-0.20 | +/-0.20
Cycle 2 : 15/16 FSI observations are operational
Cycle 3 : 16/16 FSI observations are operational
Radial : 30 μm
Uncertainty : 100 μm
Difference between motion of cavity 2 on cycle 2 and cycle 3
Longitudinal : 120 μm
Uncertainty : 150 μm
Vertical : 50 μm
Uncertainty : 50 μm
Pitch : 130 μrad
Uncertainty : 50 μrad
Roll : 320 μrad
Uncertainty : 400 μrad
Yaw : 140 μrad
Uncertainty : 150 μrad
Repeatable
Repeatable
Close to be
repeatable
Repeatable
Repeatable
Repeatable
Chart: Vertical position (mm)
| 0 | 3000
Objective at cold | 0 | 0
Cav 2 : ambient pressure | -0.729 | -0.757
Cav 2 : Cold | 0.126 | 0.024
obkectif min | -0.083333 | -0.083333
objectif max | 0.083333 | 0.083333
Warm position
(before cycle 3)
Cold position
(after cycle 3)
Experience from cycle 2

## Slide 19
Conclusion
Cryomodule
The shape of the cryomodule must be repeatable at ambient pressure with an uncertainty of less than 40 μm.
The shape of the cryomodule must be repeatable under vacuum with an uncertainty of less than 40 μm.
The shape of the cryomodule must be repeatable under vacuum with an uncertainty of less than 40 μm.
Crab-cavities
The movement of the two cavities between warm (ambient pressure) and cold should be repeatable with an uncertainty of less than 40 μm
 50 μm for cavity 2 (Translations)
 150 μm for cavity 1 (difficult to confirm due to lack of accuracy for cavity 1
The accuracy of each FSI measurement must be validated within 40 μm
 FSI targets holders to be improved

## Slide 20
Next steps
RFD prototype : SPS installation
The installation of the cryomodule in the SPS is scheduled for the technical stop (TS) in 2024-2025
The impact of transport of the cryomodule will be tested to ensure that it does not affect the alignment
A new alignment of the cavities will be carried out in the SPS during this period (with experience results of cycle 3)
The position of the radio-frequency axis will be analysed using the beam, confirming the alignment and validating the assumption that the radio-frequency axis can be approximated to the mechanical axis of the capacitive plates.
Series
FSI targets holders will be improved

## Slide 21
Conclusion
The RFD prototype is ready to go into the SPS accelerator !
Many thanks to STFC team :
Nik
Ed
Luke
Ryan
Carlos
Andy
…
Many thanks to CERN team :
Teddy
Simon
Marco
Nuria
Katarzyna
Kurt
Rama
Raphael
Luca
Ofelia
Julien
…
Thank you for your attention

## Slide 22
FSI following
Cavity 2 repair

## Slide 23
  Doors removed & installation of tooling
  Check of position and torques
  Removal of cavity supporting plate
  Access to leak zone (FPC copper body)
Hands gymnastics to access this zone
  Live monitoring (survey) of cavity and FPC during all activities
  Leak repair
Survey measurement on load charge transfer of TANK2

## Slide 24
Situation before installation of tooling support of cavity 2
8 March 2024
EDMS : 3065222

## Slide 25
Situation after installation of tooling support of cavity 2
13 March 2024 : 9h12
Impact on cavity
Impact on
FPC flange
Impact of installation tooling system : < 0.1 mm
EDMS : 3065222

## Slide 26
Movie during the load charge transfer
Impact on
FPC flange
Impact on cavity
Impact of load transfer : 0.35 mm in vertical
EDMS : 3065222

## Slide 27
Spare

## Slide 28
Repeatability on the motions
 | Cavity 1 |  |  | Cavity 2 |  | 
Impact of cold | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 1 | Cycle 2 | Cycle 3
Tx [mm] (radial translation) | 0.69 | 0.87 | 0.72 | 0.37 | 0.60 | 0.57
 | +/-0.30 | +/-0.20 | +/-0.20 | +/-0.20 | +/-0.10 | +/-0.08
Ty [mm] (longi translation) | 0.32 | 0.35 | 0.39 | 0.39 | 0.15 | 0.27
 | +/-0.30 | +/-0.20 | +/-0.20 | +/-0.20 | +/-0.15 | +/-0.10
Tz [mm] (vertical translation) | 0.75 | 0.62 | 0.71 | 0.76 | 0.76 | 0.81
 | +/-0.20 | +/-0.15 | +/-0.15 | +/-0.10 | +/-0.05 | +/-0.05
Rx [mrad] (Pitch angle) | -0.36 | -0.40 | -0.30 | -0.11 | 0.05 | -0.08
 | +/-0.20 | +/-0.15 | +/-0.15 | +/-0.10 | +/-0.05 | +/-0.05
Ry [mrad] (Roll angle) | -0.23 | -0.74 | -0.20 | -1.65 | -0.74 | -0.41
 | +/-1.00 | +/-0.70 | +/-0.70 | +/-1.00 | +/-0.40 | +/-0.40
Rz [mrad] (Yaw angle) | 0.08 | 0.41 | 0.21 | 0.12 | 0.45 | 0.31
 | +/-0.35 | +/-0.20 | +/-0.50 | +/-0.20 | +/-0.15 | +/-0.10
Scale [mm/m] | -2.06 | -2.22 | -2.14 | -2.06 | -2.22 | -2.14
 | +/-0.20 | +/-0.20 | +/-0.20 | +/-0.20 | +/-0.20 | +/-0.20
Cycle 1 : 12/16 FSI observations are operational
Cycle 2 : 15/16 FSI observations are operational
Cycle 3 : 16/16 FSI observations are operational

## Slide 29
Pumping
Cooling down
IN (cav 2)
OUT (cav 2)
Objective : 0 mm +/- 0.1 mm

## Slide 30
IN (cav 1)
OUT (cav 1)
Pumping
Objective : 0 mm +/- 0.1 mm

## Slide 31
Objective : 0 mm +/- 0.1 mm
IN (cav 1)
OUT (cav 1)
Pumping