## Slide 1: Mechanical measurements, experience during transport and testing of cryomodules
EN/MME Mechanical Measurement Lab
M. Guinchard, D. Thuliez

## Slide 2: STFC Transport frame and Transport restraints
Z=Transverse
X= Longitudinal
Y= Vertical
*Installation of restraints was monitored with the mechanical instrumentation (optical fibres)

## Slide 3: Timeline
18th October 2023@ 9h30 : Loading
18th October 2023@ 11h20 : Departure
18th October 2023@ 11h20 : Departure
18th October 2023@ 19h30 :
Ashford customs
18th October 2023@ 21h00 :
Departure Ashford customs
18th October 2023@ 22h00 : Tunnel
19th October 2023@ 01h00 : Hotel
19th October 2023@ 10h00 : Departure
19th October 2023@ 12h00
19th October 2023@ 14h00
19th October 2023@ 17h00
19th October 2023@ 19h00 : Dole Hotel
20th October 2023@ 12h00 : CERN
Huge thanks to Pierre-Loic (driver), Christophe (driver) and David (instrumentation) for the efforts !

## Slide 4: Baseline Vibration and shock instrumentation
2 Shocklog® Systems with GPS and GSM connections worldwide: shocks, Temp, HR, Tilt :
- Cryomodule (3 directions)
- Transport frame (3 directions)
Z=Transverse
X= Longitudinal
Y= Vertical
Z=Vertical
X= Lateral
Y= Longitudinal

## Slide 5: CERN Instrumentation – Extra
Continuous vibration monitoring system based on :
- 3 ICP triaxial accelerometers PCB-356A14
- Spectrum Analyzer with real time FFT analysis MicroQuantus®
    Online visualization
    Storage in an SSD hard drive
    Fs : 1024 Hz
Z=Vertical
X= Lateral
Y= Longitudinal

## Slide 6: CERN Instrumentation – Cryomodule
Continuous strain measurements installed on blades and FPC tubes :
- Optical strain measurements based on FBG
- Online visualization with recording at 1000 Hz
Z=Vertical
X= Lateral
Y= Longitudinal
Baseline
Extra

## Slide 7: Results – Shocklog units

## Slide 8: Results – Shocklog units
Chart: Temperature = f(Times)
Chart: HR = f (Times)
Chart: TILT = f (Times)
Chart: ROLL = f(Times)

## Slide 9: Results – Vibration monitoring system
Z=Vertical
X= Lateral
Y= Longitudinal
Set of data from Warwick to Ashford Customs

## Slide 10: Results – Vibration monitoring system – Transfer function
Cut-off frequency  13 Hz

## Slide 11: Results – Vibration monitoring system
Chart: Transport STFC to CERN according to ASTMD4169
| 1 | 3 | 4 | 6 | 12 | 16 | 25 | 30 | 40 | 80 | 100 | 200
ASTMD4169 High level | 0.00072 | 0.03 | 0.03 | 0.0012 | 0.0012 | 0.006 | 0.006 | 0.0012 | 0.006 | 0.006 | 0.0006 | 3e-05
ASTMD4169 Medium level | 0.00072 | 0.018 | 0.018 | 0.00072 | 0.00072 | 0.0036 | 0.0036 | 0.00072 | 0.0036 | 0.0036 | 0.00036 | 1.8e-05
ASTMD4169 Low level | 0.0004 | 0.01 | 0.01 | 0.0004 | 0.0004 | 0.002 | 0.002 | 0.0004 | 0.002 | 0.002 | 0.0002 | 1e-05

## Slide 12: Results – Optical strain measurement system
Chart: Temperature = f(Times)
Stop Measurement during the night
Full transport data
Transport effects
Low frequency effects are related to temperature

## Slide 13: Results – Optical strain measurement system
Typical response of the blade instrumentation during transport event
Strain (m/m)

## Slide 14: Results – Optical strain measurement system
Chart: Temperature = f(Times)
Stop Measurement during the night
Full transport data

## Slide 15: Results – Optical strain measurement system
 | 18th August 2023 | 17th October 2023 | 23th October 2023 | variation due to transport
 | Strain (µm/m) | Strain (µm/m) | Strain (µm/m) | Strain (µm/m)
CAV1_FPC_Secondary_Line | 29.12 | -13.4 | -23.8 | -10.4
CAV1_FPC_Short_Side | -29.91 | -43.41 | -59.47 | -16.06
CAV1_FPC_Long_Side | 17.97 | -76.33 | -99.1 | -22.77
CAV1_FPC_Cavity_Line | 104.7 | -24.16 | -46.58 | -22.42
CAV1_RightBlade_Cavity_Long Side | 299.1 | 281.62 | 262.4 | -19.22
CAV1_RightBlade_Secondary_Long Side | 22.24 | -43.96 | -52.49 | -8.53
CAV1_RightBlade_Secondary_Short Side | -268.3 | -418.47 | -447.9 | -29.43
CAV1_RightBlade_Cavity_Short Side | -388.7 | -489.43 | -519.1 | -29.67
CAV1_LeftBlade_Secondary_Long Side | 90.7 | 59.36 | 26.7 | -32.66
CAV1_LeftBlade_Cavity_Long Side | 6.579 | -47.39 | -41.57 | 5.82
CAV1_LeftBlade_Cavity_Short Side | -147.3 | -242.3 | -267.74 | -25.44
CAV1_LeftBlade_Secondary_Short Side | -103.3 | -146.14 | -161.43 | -15.29
CAV2_FPC_Secondary_Line | -73.02 | -129.23 | -141.69 | -12.46
CAV2_FPC_Short_Side | 41.06 | -19.99 | -29.3 | -9.31
CAV2_FPC_Long_Side | 168.6 | 64.92 | 53.54 | -11.38
CAV2_FPC_Cavity_Line | 48.74 | -44.96 | -58.38 | -13.42
CAV2_LeftBlade_Secondary_Long Side | -182.9 | -139.04 | -170.8 | -31.76
CAV2_LeftBlade_Cavity_Long Side | -34.94 | -153.79 | -169.67 | -15.88
CAV2_LeftBlade_Cavity_Short Side | -360.1 | -411.13 | -387.81 | 23.32
CAV2_LefttBlade_Secondary_Short Side | 48.44 | -23.51 | -42.46 | -18.95
CAV2_RightBlade_Cavity_Short Side | -44.86 | -97.98 | -118.8 | -20.82
CAV2_RightBlade_Secondary_Short Side | -184.1 | -321.01 | -354.98 | -33.97
CAV2_RigthBlade_Secondary_Long Side | 150.6 | 98.07 | 64.25 | -33.82
CAV2_RightBlade_Cavity_Long Side | 26.02 | -5.79 | -31.13 | -25.34
Notes: Also validation of the restraint assembly method

## Slide 16: Results – Worst case event
Chart: Max Peak = f (Times)
Sample rate = 4096 Hz
Sample rate = 1024 Hz
Sample rate = 1024 Hz
Sample rate = 1024 Hz
Blue frame
Sample rate = 1000 Hz
18/10/23 11h30 19/10/23_10h00 20/10/23 8h30

## Slide 17: Results – Worst case event
Chart: Max Peak = f (Times)
Sample rate = 4096 Hz
Blue frame
Sample rate = 1000 Hz
18/10/23 11h30 19/10/23_10h00 20/10/23 8h30
0.2 g @ 2 Hz

## Slide 18: Use of the mechanical instrumentation during repair
Continuous optical strain monitoring : (https://mml.web.cern.ch/)

## Slide 19: Summary Transport
 |  | Min value | Max Value
Shocklog Data | Temperature | 14 °C | 20 °C
 | Humidity | 55 % | 100 %
 | Tilt | - 7 ° | +15 °
 | Roll | -10 ° | +5 °
 | Vertical RFD acceleration (@4096 Hz) | / | < 0.6 g
 | Longitudinal RFD acceleration (@4096 Hz) | / | < 0.6 g
 | Lateral RFD acceleration (@4096 Hz) | / | < 0.6 g
Monitoring system | Vertical RFD acceleration (@1024 Hz) | / | < 0.5 g
 | Longitudinal RFD acceleration (@1024 Hz) | / | < 0.5 g
 | Lateral RFD acceleration (@1024 Hz) | / | < 0.5 g
 | Strains on blade components | / | +/- 20 m/m
 | Strains on FPC components | / | +/- 20 m/m

## Slide 20: Summary Transport and Mechanical instrumentation
The transport of the SPS RFD cryomodule from STFC to CERN was a success.
Transport frame combined with transport restraints
No damage linked to transport was found
Two shock logs as baseline during transport
The extra instrumentation during the first DQW and RFD (from TRIUMF transport)
The strain measurements on the FPC pipe can/should be used more extensively during the assembly and recorded. Requires training + some preparation
FPC strain gauges > base line