## Slide 1: Studies for transport of crab cavities equipment
Teresa Guillén Hernández on behalf of WP4
14th HL-LHC Collaboration Meeting, Genoa (Italy), 7-10 October 2024

## Slide 2: Outline
Introduction
Risk analysis
Risk mitigation
HOMs transport calculations
Conclusions
Teresa Guillen, 14th HL-LHC Collaboration Meeting

## Slide 3: Introduction
Teresa Guillen, 14th HL-LHC Collaboration Meeting
M. Garlasche ¨Transport of RFD Equipment to UK¨ 11th HL-LHC Collaboration Meeting. 2021

## Slide 4: Risk analysis
    What issues can arise during transport
      Shock
      Vibration
      Contamination/humidity
      Untightening screws
      Misalignment
    What equipment is critical
      Manufacturing Cost/ delay
      Material properties
      Difficulty of risk detection
    Risk analysis on
      Components
      Assemblies
    Deep analyses of risks
      FEM
Teresa Guillen, 14th HL-LHC Collaboration Meeting
K. Artoos ¨Transport aspects¨ International review of the CRAB cavity system design and production plan for the HL-LHC. 2019
M. Garlasche ¨Transport of RFD Equipment to UK¨ 11th HL-LHC Collaboration Meeting. 2021

## Slide 5: Risk mitigation
    Some mitigations are applied on the design of the equipment
Teresa Guillen, 14th HL-LHC Collaboration Meeting
K. Artoos ¨Transport aspects¨ International review of the CRAB cavity system design and production plan for the HL-LHC. 2019
M. Garlasche ¨Transport of RFD Equipment to UK¨ 11th HL-LHC Collaboration Meeting. 2021
Eduardo Cano-Pleite

## Slide 6: Risk mitigation
Other risks are mitigated designing transport equipment
    Transport frame for the Dressed Cavity
Teresa Guillen, 14th HL-LHC Collaboration Meeting
M. Garlasche ¨Transport of RFD Equipment to UK¨ 11th HL-LHC Collaboration Meeting. 2021
    Rigid boxes with foam for transport of HOMs antennas and HOMS assembled. Courtesy of S. Barriere.
    Transport frame for STFC RFD cryomodule. Courtesy of T. Capelli

## Slide 7: HOMs transport calculations
  Verify the integrity of the HOMs during transport
  RFD AUP H-HOM
FEM analyses for transport
  Modal
  Shock
  Random vibration
  Fatigue
Teresa Guillen, 14th HL-LHC Collaboration Meeting
Calculations done on the components
without mitigation methods

## Slide 8: RFD AUP H-HOM transport calculations
1. Modal analysis
  It is a preliminary analysis needed before
    Response spectrum analysis
    Random vibration analysis
  Natural frequencies and modes
Teresa Guillen, 14th HL-LHC Collaboration Meeting
Mode | Frequency [Hz]
1 | 65.9
2 | 67.0
3 | 342.4
4 | 349.0
5 | 445.5
Mode 3
Mode 2
Mode 1

## Slide 9: RFD AUP H-HOM transport calculations
2. Shock analysis
  Dynamic and non-deterministic load in a very short time
  2 approaches
    Response spectrum analysis - 10 g and 20 ms in the frequency domain
    Transient analysis - 10 g and 20 ms in time domain
Teresa Guillen, 14th HL-LHC Collaboration Meeting
Experimental value
More critical than MIL-STD-810H

## Slide 10: RFD AUP H-HOM transport calculations
2. Shock analysis – Response spectrum
  Results – X direction (most critical)
    Response spectrum – Max stress = 75 MPa > 37 MPa =
Teresa Guillen, 14th HL-LHC Collaboration Meeting
Plasticization
Transient analysis needed

## Slide 11: RFD AUP H-HOM transport calculations
2. Shock analysis - Transient
  Results -X direction (most critical)
      Time-dependant simulation needed to analyse the effect of the high stresses on the permanent deformation
      Important simulations parameters:
        Total time = 0.7 s – it is enough to damp most of the oscillations
        Damping ratio = 2% (standard value)
Teresa Guillen, 14th HL-LHC Collaboration Meeting
Evolution of the maximum deformation
Plastic strain with a shock of 10g and 20ms in X direction
Peak deformation with a shock of 10g and 20ms in X direction
Permanent deformation
⩽
0.04mm
Peak instantaneous deformation = 1.23 mm
<
Space hook-cavity = 9mm

## Slide 12: RFD AUP H-HOM transport calculations
3. Random vibration analysis
  Dynamic, non-deterministic loads in a long time
  RV = Gaussian process: stationary and zero mean
  Also the stresses
Teresa Guillen, 14th HL-LHC Collaboration Meeting
[1] L.E. Ballesteros ¨Failure prediction of structures subjected to random vibrations¨ http://hdl.handle.net/10150/630147
Amplitud-time history [1]
Gaussian random process [1]
Standard deviation RMS | Probability
1σ | 68%
2σ | 95%
3σ | 99.7%
Limit considered

## Slide 13: RFD AUP H-HOM transport calculations
3. Random vibration analysis
  Power Spectral Density (PSD) function
    From time domain – to frequency domain
    Average Power or energy of the vibration as a function of the frequency
Teresa Guillen, 14th HL-LHC Collaboration Meeting
[2] “ASM D4169 -16 - Standard Practice for Performance Testing of Shipping Containers and Systems,” ASTM International,
West Conshohocken, PA, 2016.
PSD curve of truck transport [2]

## Slide 14: RFD AUP H-HOM transport calculations
Random vibration analysis
PSD curve of truck transport. From ASTM D-4169 [2] and CERN transport data from STFC to CERN in X direction [3]
[2] “ASM D4169 -16 - Standard Practice for Performance Testing of Shipping Containers and Systems,” ASTM International, West Conshohocken, PA, 2016.
[3] M. Guinchard, “Mechanical vibration and stress measurements on the RFD cryomodule during transport from UK” EDMS 2755675.
Teresa Guillen, 14th HL-LHC Collaboration Meeting
Natural frequency ≈ 67Hz

## Slide 15: RFD AUP H-HOM transport calculations
Random vibration analysis
  Results – X direction is the most critical
Teresa Guillen, 14th HL-LHC Collaboration Meeting
Probability of occurrence 4,28%
99.73% of probability to not exceed 5 MPa
Probability of occurrence 68.27%
68.25% of probability to not exceed 1.6 MPa
Probability of occurrence 27,18%
95.45% of probability to not exceed 3.4 MPa
No plasticization but Cyclic load.
Therefore, it could failure by:
– Fatigue (Assessed by the stress life method)

## Slide 16: RFD AUP H-HOM transport calculations
Fatigue analysis
  Cyclic random vibration load
  ANSYS Fatigue tool RV – stress life (Whoeler)
    S-N curve of Nb
      Linear or bi-linear
      R = / = -1 (default)
      Strain rate (frequency)
    Three sigma method + Damage (Miner’s rule):
Teresa Guillen, 14th HL-LHC Collaboration Meeting
RMS stress level | Occurrence Probability | Stress Amplitude [MPa]
1σ | 68.27% | 1.6
2σ | 27.18% | 3.4
3σ | 4.28% | 5
RMS stress level |  | Stress Amplitude [MPa]
1σ | 68.27% | 1.6
2σ | 27.18% | 3.4
3σ | 4.28% | 5
SN curve of Nb: f = 25 Hz and R = 0.1 (draft results, pending publication)
Courtesy of A. Galifa
Depends on the point considered
= RMS stress velocity
= RMS stress
Narrow band process assumption
(each zero up crossing = 1 cycle)

## Slide 17: RFD AUP H-HOM transport calculations
Fatigue analysis
  Results
Teresa Guillen, 14th HL-LHC Collaboration Meeting
Time of transport
2.5 days
No fatigue fracture

## Slide 18: Conclusions
Transport is a daily and challenging activity of the crab cavity project
To protect our components and assemblies during transport
  Risk analysis
  Risk mitigation
HOMs calculations: RFD AUP
  Shock
  Random vibration
  Fatigue
Results show no risk for the component 
Teresa Guillen, 14th HL-LHC Collaboration Meeting

## Slide 19: Studies for transport of crab cavities equipment
Teresa Guillén Hernández on behalf of WP4
14th HL-LHC Collaboration Meeting, Genoa (Italy), 7-10 October 2024

## Slide 20: RFD AUP H-HOM transport calculations
Random vibration analysis – max PSD of the norm ASTM D-4169
  Results – X direction is the most critical
Teresa Guillen, 14th HL-LHC Collaboration Meeting
Probability of occurrence 4,28%
99.73% of probability to not exceed 97 MPa
Probability of occurrence 68.27%
68.25% of probability to not exceed 32 MPa
Probability of occurrence 27,18%
95.45% of probability to not exceed 64 MPa
Plasticization

## Slide 21: RFD AUP H-HOM transport calculations
Linear elastic static structural analysis
Elasto-plastic static structural analysis
Teresa Guillen, 14th HL-LHC Collaboration Meeting
0.1% of plastic strain and cyclic load.
Therefore, there could be two possible failures:
– Fatigue (Cannot be assessed for the moment)
– Ratcheting (It doesn’t happen when we have a Random vibration because the stress cycling is symmetric)

## Slide 22: RFD AUP H-HOM transport calculations
Random vibration analysis
  Results – X direction is the most critical
Teresa Guillen, 14th HL-LHC Collaboration Meeting
0.05 mm << 9 mm (Space hook-cavity)
Probability of occurrence 4,28%
99.73% of probability to not exceed 0.05 mm