## Slide 1: LHC longitudinal impedance measurement through Schottky spectra
Christophe Lannoy, Kacper Lasocha, Diogo Alves, Nicolas Mounet
Acknowledgements: Tatiana Pieloni, Ivan Karpov, Theodoros Argyropoulos
14th HL-LHC Collaboration Meeting, Genoa, 10th October 2024

## Slide 2
Outline
Introduction
  Longitudinal Schottky spectrum
  Transverse Schottky spectrum
Experimental Schottky spectra from the LHC
  Longitudinal impedance effect
  Estimate of the LHC longitudinal impedance
  Transverse impedance effect
Conclusion

## Slide 3: Introduction: The Schottky Monitor
Details of the LHC Schottky system in
M. Betz et al., NIM, vol. 874, pp 113-126, 2017
The Schottky spectrum is based on the measurement of the beam fluctuations in the longitudinal and transverse planes.
The Schottky spectrum is the power spectral density of the beam current in the longitudinal plane and the dipole moment in the transverse planes.
Important non-invasive method for beam diagnostics (emittance, tune, chromaticity, bunch profile, …).
The Schottky monitor is one of the only instruments with the potential of measuring the LHC chromaticity in a non-invasive way.
However, impedance, non-linearities, and other collective effects can strongly affect the Schottky spectrum, preventing the extraction of beam and machine parameters.
   The distortion caused by impedance can also be used to estimate the impedance itself.

## Slide 4: Longitudinal Schottky Spectrum (synchronous particle)
Time domain:
Frequency domain:
Schottky Monitor
Summation
over harmonic

## Slide 5: Longitudinal Schottky Spectrum
Inserting the harmonic synchrotron motion in )
Writing the Fourier series of this periodic signal
Using the Jacobi Anger relation
 The intensity signal can be written in the following form:
: Time difference between particle and the synchronous particle
Amplitude
Summation
over harmonic
Summation over
Bessel satellites
Frequency
Frequency domain:
Time domain:
Schottky Monitor
Analytical expression for
Phase

## Slide 6: Longitudinal Schottky Spectrum
: Time difference between particle and the synchronous particle
Amplitude
Summation
over harmonic
Summation over
Bessel satellites
Frequency
Frequency domain:
Time domain:
Schottky Monitor
Phase

## Slide 7: Longitudinal Schottky Spectrum
Synchrotron oscillations:
к: Elliptic integral of the first kind
From the theory of the non-linear pendulum:
Spectrum for a bunch of particles
Spectrum for two particles with different synchrotron frequencies

## Slide 8
Amplitude
Phase
With
Frequency
Transverse Schottky spectrum
Lower transverse
side-band
Upper transverse
side-band
Longitudinal band

## Slide 9: Experimental LHC spectra: Longitudinal Impedance Effects
Longitudinal impedance significantly affects proton Schottky spectra.
Spectra of bunches of different intensities (0.5e11 to 2e11 ppb) acquired at injection during MD block 1.
Schottky spectra from MD 11723
Intensity dependent shift of the satellites.
Longitudinal impedance
Synchrotron tune shift
Shift of Schottky satellites

## Slide 10: Longitudinal Impedance Effects on LHC Schottky spectra
Impedance can be source of instabilities and can cause intensity limitation.
 Important to have a good knowledge of the machine impedance.
Current LHC longitudinal impedance model is a byproduct of the transverse impedance model. N. Mounet, PhD thesis, The LHC Transverse Coupled-Bunch Instability
Could be inaccurate. Main source of longitudinal impedance not necessarily the same as for transverse impedance.
Model re-evaluation is in progress (RF team, Michail Zampetakis, Ivan Karpov).
Can we extract information about the machine (longitudinal) impedance from the shift of the Schottky satellites?
Understand how impedance affects the dynamic of the particles (amplitude dependent tune shift).
How this new dynamic will be reflected in the Schottky spectrum.

## Slide 11: Longitudinal Impedance Effects on LHC Schottky spectra
к: Elliptic integral of the first kind.
Longitudinal equation of motion.
Where the coefficients account for the effect of impedance and are defined from the bunch spectrum and the impedance function
Longitudinal equation of motion including forces coming from impedance:
Without impedance
With impedance
 Impedance is responsible of an amplitude-dependent synchrotron tune shift.
With some approximations, a relation between synchrotron frequency and oscillation amplitude can be derived.
From the theory of the non-linear pendulum.
Nominal tune shift
Details in: C. Lannoy et al 2024, JINST 19 P03017

## Slide 12: Longitudinal Impedance Effects on LHC Schottky spectra
The new relation between synchrotron frequency and amplitude can be inserted in the original theoretical expression of the Schottky spectrum:
Synchrotron frequency with impedance
This last expression allows to extend theoretical frameworks such as the Monte Carlo approach or the matrix formalism (K. Lasocha and D. Alves).
Notes: Shunt resistance
Cut-off frequency
Quality factor

## Slide 13: Longitudinal Impedance Effects on LHC Schottky spectra
Benchmark of the theory against macro-particle simulation (PyHEADTAIL).
e
Simulation conducted with a first estimate of the (longitudinal) broad-band part of the LHC impedance:
Simulated Schottky spectra
equivalent to:

## Slide 14: Fitting of experimental LHC Schottky spectra
Fitting of Schottky spectrum is not trivial as it depends on many parameters:
All longitudinal parameters
Betatron tune
Chromaticity
Transverse profile
Transverse impedance
Lattice non-linearities
…
Transverse bands
 The longitudinal band is easier to fit as it depends on less parameters.
RF voltage
Long. bunch profile
Long. impedance
Intensity
Longitudinal band

## Slide 15: Fitting of experimental LHC Schottky spectra
Fitting of Schottky spectrum is not trivial as it depends on many parameters:
RF voltage
Long. bunch profile
Long. impedance
Intensity
Longitudinal band
Fitted once on low intensity bunch where impedance effect is low. Agree with measured RF voltage within 0.5%.
Measured with BCT.
Measured precisely with the WCM (if measurement available, else supposed Gaussian with length from BQM):
Bunch spectrum
(impedance calculation)
Analytical calculation
Synchr. amplitude distribution
(Schottky theory)
Fitted with a q-Gaussian
  Only variable left:
  Impedance - Modeled as a broadband resonator of parameters:
        : Scanned variable

## Slide 16: Fitting of experimental LHC Schottky spectra
Schottky spectra from MD 11723: Nominal Gaussian bunch, fit with
Notes: Bunch profile assumed Gaussian with length given by BQM. (Spectra from 13h45 – 14h05)

## Slide 17: Fitting of experimental LHC Schottky spectra
Schottky spectra from MD 11723: Nominal Gaussian bunch, fit with
Notes: 13h45 – 14h05

## Slide 18: Fitting of experimental LHC Schottky spectra
Schottky spectra from MD 11786: Short q-Gaussian bunch
Short q-Gaussian bunch:
ppb
Fitting less obvious  Neither the full LHC impedance model nor a BB resonator can reproduce closely the measurement.
Better agreement might be obtained by fitting both shunt impedance and cutoff frequency (study ongoing).
a

## Slide 19: Fitting of experimental LHC Schottky spectra
Overall, best fitting obtained with:
Increase of 70% compared with the current longitudinal impedance model:
Still preliminary result, impact of the cut-off frequency of the broadband model to be analysed.
N. Mounet, PhD thesis, The LHC Transverse Coupled-Bunch Instability
I. Karpov and L. Giacomel IWG talks, https://indico.cern.ch/event/1422663/

## Slide 20: Experimental LHC spectra: Transverse impedance effects
Schottky spectra from MD 11723
Central satellite
Transverse impedance
Betatron tune shift and tune spread
Shift and spreading of Schottky satellites
Transverse impedance significantly affects proton Schottky spectra.
Spectra of bunches of different intensities (0.1e11 to 2e11 ppb) acquired at injection during MD block 1.
Notes: 11h05 – 11h25

## Slide 21: Conclusion
  Summary of the talk:
  Longitudinal impedance.
    Shift of synchrotron satellites observed experimentally.
    Theory available allowing fitting of impedance.
    First measurements seem to indicate an increased impedance w.r.t. current model.
    Further studies needed to analyse the impact of cut-off frequency.
  Transverse impedance.
    Tune shift observed in experimental spectra.
    Theory available for quadrupolar impedance and still to be developed for dipolar impedance.