## Slide 1
Requirements for design studies
50% losses for injection in the DR (assumed) + 20% additional losses from target up to the end of the e+ linac (assumed)
20% additional losses from target up to the end of the e+ linac
  e+ linac simulations (including chicane) will provide more realistic estimation of the accepted yield
  Include the ESC in the linac start-to-end simulations
  Still a reasonable safety margin
50% losses for injection in the DR
  To be discussed/fixed with the WP4 (studies including ESC from 2023 => DR acceptance ~ 80% )
The complete filling for Z running => Requirement ~2.75 ⨯ 1010 e+/bunch (4.4 nC) at the linac end or 5.4 nC accepted in the DR
*A safety margin of 2.5 is currently applied for the whole studies (60% losses for transport, collimation and injection into the DR).
Ne-/bunch ⨯ ηe+Accepted ≥ 5.4 nC/bunch ⨯ 2.5

## Slide 2
Target & cryostat
Positron linac 2 GHz, 20 MV/m
200 Hz, 23 RF structures
Positron/Electron
Separation at 200 MeV
Energy collimator
and compressor
106 m
53 m
6 GeV electron beam
from common linac
Injection section
Damping ring
DR C = 242 – 271 m
E = 1.54 GeV
Qb = 5.4 nC
E = 1.54 GeV
Q = 13.5 nC (considering 60% losses for transport, collimation and injection into DR)
E = 6 GeV
Q = 1.9-2.1 nC
Capture linac 2 GHz, 20 MV/m
200 Hz, 5 RF structures
DC solenoid
DC solenoid
Electron/Photon? dumps
1846 – 1500 = 346 mm
105 mm
72 mm
240 mm
509.5 mm
3000 mm
200 mm
Capture system -version 1
Positron production: conventional scheme (e- beam size on target = 1 mm rms ). Target exit located at 40 mm w.r.t. peak field.
Matching Device is based on the SC solenoid (5 HTS coils, 72 mm bore including shielding)
Capture Linac is based on the L-band TW RF structures ( 2 GHz, 60 mm, 3-m long)
NC long solenoid B = 0.5 T (realistic conventional design based on the short coils B = 0.31 T) + short “tuning” solenoid B = 0.124 T before the 1st RF structure
Shielding made of W before the 1st RF structure (position tbc)
Positron source physics design (current baseline)
295 – 36 = 259 mm
HTS solenoid – based option
Does FLUKA model include short “tuning” solenoid?
346 - 259 – 72 = 15 mm available ?? Or it is installed upstream?