## Slide 1: ABP computing meeting: news from INC section

## Slide 2: Overview of INC computing activites
Tracking simulations for LHC & HL-LHC for protons and ions: beam-beam (weak-strong), noise effects (power supply ripple, CC noise, white noise). DA studies for beam and machine opitimizations, emittance evolution, losses and tail population.
Tracking simulations for the injectors with space charge for protons and ions: PSB specific functions, PS transition crossing, IBS & space charge in SPS..
IBS in Xsuite: several analytical formalisms, “simple kick” and kinetic theory now fully integrated in Xsuite, PIC IBS (similar to SIRE) currently under development.
Cooling in Xsuite: e-cooling, laser cooling
Luminosity model: leveling à la operation, crab cavities, impact from LHCb
Control room tools such as PyJAPCScout
Medical applications
Will start getting more involved with FCC-ee beam-beam studies following the lead of Xavier.
Notes: )

## Slide 3: Needs from the section- Xsuite related
Towards more systematic tracking of realistic distributions: A standarized tool to generate various matched distributions beyond Gaussian:
    q-Gaussian for studies with heavily tail populated transverse profiles
    “colored” distributions with weights for more information on the tails.
    GPU needs will increase in the upcoming months.
Emittance monitor: several requests for a standarized emittance monitor
  Several members have developed their own implementations and it would be important to converge to one.
  Flexibility to extract the full profile if needed would be useful.
Storing scan results (e.g. DA scans) and corresponding configurations to be able to retrieve results from the past. Difficult task as DA scans are systematically evolving.

## Slide 4: Needs from the section- Xsuite related
Beam-beam (strong-strong):
  At the moment, bunch-by-bunch weak-strong approximation for beam-beam bbb orbit effects for the LHC, in agreement with strong-strong.
  Useful to have a pytrain integration in Xsuite.
A method to study higher order derivative mapping (in particular for crabbing) in the twiss: to have a “complete” function y(z) we have to track several particles and extract it manually  an automatic calculation of (at least) second order derivatives
Space charge:
  PIC: 3d and 2p5d benchmarked , some issues with 2p5daveraged (small emittance discrepancy, not faster than 2p5d)
  Analytical: user cannot define how often to update and cannot use different longitudinal profiles.
  SPS ions: loss of symplecticity
Issue with synchrotron radiation damping times for LHC?

## Slide 5: Needs from the section- Other codes
Luminosity model:
  A very big code that is extensively used for performance projections and comparison of beam parameter evolutions with respect to our models and identify sources of discrepancy.
  Not a clean code, need to put effort into transforming it into a benchmarked, reliable and user friendly code.
There is the need of understanding which tools we should be using for simulating (low energy) electron beams (for e- lenses, e- cooling, e- guns, …).
PyJAPCScout based on PyJAPC, move to PyDA?