## Slide 1
Three-dimension hybrid simulation on plasma jet formation in Zirconium-Deuterium multi-component vacuum arc discharge
Wei Yang, Qiang Sun, Mengmeng Song, Qianhong Zhou
yangwei861212@126.com
Institute of Applied Physics and Computational Mathematics
2025.06
12th International Workshop on the Mechanisms of Vacuum Arcs (MeVArc 2025)

## Slide 2: Table of contents
Introduction: vacuum arcs of composite electrode
Insights from multi-component fluid simulation
Recent results of three-dimension hybrid simulation
I
III
IV
Insights from PIC-DSMC simulations
II
Conclusions
V

## Slide 3: Vacuum arcs of multi-component composite cathode
Vacuum arcs (VA) of multi-component composite cathode have been widely used in ion source, thin film deposition and other industrial fields, due to its ability to generate ion beams of different elements.
A. G. Nikolaev, IEEE TPS 47, 3590 (2019)
Liu H, et al. Appl Surf Sci, 501, 144025 (2020).

## Slide 4: Velocity distribution of two-component vacuum arcs
The directed velocity of light ions is slightly higher than that of heavy ions.
The directed velocity of ions of same element but with different charge states is usually very close to each other.
Frolova et al., 28th ISDEIV (2018).
A. G. Nikolaev, J Appl Phys 116, 213303 (2014)

## Slide 5: Angular distribution of two-component vacuum arcs
The angular distribution of light ions is rather unifrom, while that of heavy ions is more concentrated in the central axis.
Comparing the angular distribution of pure metal cathode and composite cathode, similar trend is observed for heavy ions but different for light ions.
A. G. Nikolaev, IEEE TPS 47, 3590 (2019).
A. G. Nikolaev, J Appl Phys 116, 213303 (2014)
Angular distributions of ions (ZrD)
comparisons: pure metal cathode and composite cathode

## Slide 6: Table of contents
Introduction: vacuum arcs of composite electrode
Insights from multi-component fluid simulation
Recent results of three-dimension hybrid simulation
I
III
IV
Insights from PIC-DSMC simulations
II
Conclusions
V

## Slide 7: The structure of VA plasma and their parameters
  The vaccum arc plasma is composed of sheath, cathode spot, plasma jet, arc column etc., in which physical parameters can vary orders-of-magnitude! Therefore, different numerical approaches are needed.
 | arc column | cathode spot
electric field | ~MV/m | >GV/m
current density | 107-108A/m2 | 108-1012A/m2
plasma density | 1021-1022m-3 | 1020-1027m-3
pressure | ~103Pa | 1Pa-107Pa
different zone of vacuum arc plasma
parameters of arc column and cathode spot
Langlois et al., J. Appl. Phys. 109, 113306 (2011)
Qiang Sun, Wei Yang, et al. 2020 Phys Plasmas 27: 053501

## Slide 8: The numerical approaches: kinetic, fluid and hybrid
  The numerical approaches are usually chosen according to reactor scale and mean free path (gas pressure), and categorized by the description of (full/partial) kinetic behavior of particle species.

## Slide 9: fully kinetic PIC-DSMC method is computationally heavy
In explicit ES-PIC simulations, the spatial step should resolve Debye length (to avoid numerical heating), and time step should resolve plasma oscillation frequency.
In standard DSMC simulations, the spatial step should resolve mean free path, time step should resolve collision frequency, and around 100 particles per cell (to avoid stochastic noise).
Although implict scheme can enlarge the temporal step, the Courant–Friedrichs–Lewy (CFL) condition should always be ensured (particles do not travel across spatial cell per step).
PPC (particles per cell) ~100

## Slide 10: Fully kinetic 2D modeling on short-gap vacuum breakdown
Wei Yang, Qianhong Zhou ... J. Appl. Phys. 126, 243303 (2019);Wei Yang, ... J. Appl. Phys. 128, 060905 (2020)
  Previously, a 2D r-z geometry electrostatic (ES) PIC-DSMC fully kinetic model is used to simulate micro-meters scale short-gap vacuum breakdown.
The computing cycle of PIC-DSMC simulation at each time step
Cu+ density distribution at different times during the short-gap vacuum breakdown

## Slide 11: 1D3V spherical PIC-DSMC method: time-saving technique
Time-saving technique：effective cross-section method for Coulomb collision
Song et al., High Power Laser and Particle Beams, 2021, 33: 034004; Computer Physics Communications. under review
Time-saving technique： 1D spherical momentum-conserving implicit PIC scheme
comparison with traditional TA and Nanbu method: accuracy and improved efficiency
Implicit scheme with larger spatial and time steps compared with explicit scheme: 1dr1dt

## Slide 12: 1D spherical PIC-DSMC simulation on plasma expansion
1D spherical PIC-DSMC method was used to study ion acceleration in vacuum spark and arcs, VA plasmas of composite cathode in longer gaps (~100 microns)
Song et al., Phys Plasmas. 32, 023506, 2025; J Phys D: Appl Phys, 57, 315207, 2024
Plasma Source Sci Technol, 33, 105009, 2024; Plasma Source Sci Technol, 32, 095002, 2023
Phase-space plot showing ion acceleration
plasma expansion in quasi-spherical geometry

## Slide 13: Insights from 1D3V PIC simulation
The directed velocity of light and heavy ions is quite close. However, light ions show higher thermal velocity. These effects make the expansion of D ions more isotropically in broad area (thermal energy->kinetic energy), but is not affordable in PIC simulation (mm-scale).
M Song, Q Sun, W Yang et al., Plasma Source Sci Technol 33, 075004, 2024
Ion velocity distribution
The directed velocity of ions (solid line) as well as potential distribution (red dash)

## Slide 14: Table of contents
Introduction: vacuum arcs of composite electrode
Insights from multi-component fluid simulation
Recent results of three-dimension hybrid simulation
I
III
IV
Insights from PIC-DSMC simulations
II
Conclusions
V

## Slide 15: Simulation domain, assumptions and BCs of fluid model
Q. Sun, W. Yang, Q. Zhou*, J. Phys. D: Appl. Phys. 53, 375201 (2020).
The system is assumed to be 2D axisymmetric and in steady state.
Each species (for example Ti, Ti+, Ti2+, Ti3+) has the same velocity and temperature.
The plasma is assumed to be quasi-neutral.
The electron inertia and viscosity can be neglected.
the Lorentz forces can be ignored compared to the pressure gradients.
The electrons and ions are regarded as ideal gases.

## Slide 16: Fluid model of multi-component plasma jet
schematic of fluid model
governing equations in steady state
28 reaction channels
Q. Sun, W. Yang, Q. Zhou*, J. Phys. D: Appl. Phys. 53, 375201 (2020).
To study the physical process of a cathode spot jet in VA with metal deuteride cathode (TiD), a two-dimensional hydrodynamic model based on three-fluid theory is established.
28 reaction channels with 8 plasma species are considered, including ionization and recombination processes.

## Slide 17: calculated plasma parameters and comparison with experiment
Plasma parameter | Simulation results | Experimental results
 | 2.03-2.33 | 2.0-2.3 [1]
 | 16320m/s | 15400m/s [2]
 | 4.43 | 4.3 [2]
Plasma parameter | Simulation results | Experimental results
 | 2.03-2.33 | 2.0-2.3 [1]
 | 16320m/s | 15400m/s [2]
 | 4.43 | 4.3 [2]
[1] Oks E M, Anders A, Brown I, Dickinson M and MacGill R 1996 IEEE TPS 24 1174
[2] Anders A and Yushkov G Y 2002 JAP 91 4824
calculated plasma parameters along the z axis
comparison with experimental results in literature
The charge states and directed velocity of metal ions agreed well with previous experiment.
However, the directed velocity of light and heavy ions is quite close in simulation.

## Slide 18: plasma jet mixing of multi-component VA plasma
schematic of jet mixing
Q. Sun, Q. Zhou* …, Plasma Sources Sci. and Technol. 31, 015014 (2022)
simulation domain with two CS
阴极斑1和2：轻重离子速度一致（Zr、D设为12000m/s），速度方向为75度角射流。由于二维轴对称结构，阴极斑1呈圆形，而2呈环状，代表阴极斑1周围的许多个单独的阴极斑点。
velocity separation in arc column
While directed velocity of light and heavy ions is close in plasma expansion of single cathode spot (CS), the plasma jet mixing of multiply CS is simulated in mm-scale.
Due to 2D r-z geometry, two CS is set in the inlet: the spot 1 has a circular shape but the spot 2 has a ring shape, representing a number of separate CS.

## Slide 19: velocity and flux separation of light and heavy ions
angular distribution of ion flux: experiment*
angular distribution of ion flux: simulation
angular distribution of ion velocity: simulation
angular distribution of ion density: simulation
* Nikolaev A G 2019 IEEE Trans. Plasma Sci. 47 3590

## Slide 20: The underline mechanism: collision between D-Zr ions
The ion flux angular distribution with and without Zr–D collisions
collision term v.s. pressure gradient
Q. Sun, Q. Zhou* …, Plasma Sources Sci. and Technol. 32 (2023) 085021
D ions
Zr ions
Zr–D ion collision force RZr-D is close to the pressure gradient of D, but far less than that of Zr. Therefore, RZr-D has little effect on Zr ions momentum, but significant effect on D ions.
Comparing the situation whether the Zr–D ion collision is considered in the model, the angular distribution of D ions differs substantially, but that of Zr ion is similar (in experiment, angular distribution of heavy ions is similar for pure metal cathode and composite cathode).

## Slide 21: The influencing factors: ion density, temperature and mass
The influence of ion density
The influence of ion mass
The influence of ion temperature
(via incident angle)
The separation of ions can be enhanced by increasing ion temperature, decreasing ion density and selecting electrode components with significant differences in elemental mass.

## Slide 22: Table of contents
Introduction: vacuum arcs of composite electrode
Insights from multi-component fluid simulation
Recent results of three-dimension hybrid simulation
I
III
IV
Insights from PIC-DSMC simulations
II
Conclusions
V

## Slide 23: Hybrid model of multi-component plasma jets
PIC module
(ions: velocity and position
fluid module
(electrons: density, velocity, and temperature)
assumption 1：quasi-neutrality
assumption 2：mass-less fluid
Electromagnetic field module
(electric field and magnetic field
Darwin approximation
Ions are treated as super-particles, and ion kinetics are tracked.
Electrons are treated as mass-less fluids, and electron kinetics is not resolved.

## Slide 24: Pros and cons of Darwin approximation in hybrid model
Maxwell equation
Darwin approximation
generalized Ohm’s law: different forms
Pros
self-consistent treatment of the electromagnetic field, allowing electromagnetic waves to propagate in vacuum or plasma
Fast calculation, low-frequency approximation, ignoring light waves, only need to deal with ion time scales
cons
In FDTD scheme, the time step size is strictly limited by the speed of light
the transmission of magnetic field in low density or vacuum region is greatly limited

## Slide 25: predictor-corrector method for high accuracy field solution
ion position and electric field are defined on integer time step
ion velocity, magnetic field and electron fluid variables (,, ) are defined on half integer time step.
field is updated by predictor-corrector method instead of 1st-order forward Euler
D. Winske, Homa Karimabadi, Ari Le, N. Omidi, Vadim Roytershteyn, Adam Stanier. 2022. Hybrid codes (massless electron fluid)

## Slide 26: methods for electron-ion and ion-ion collision
friction force is calculated according to the velocity of electrons and ions
for Zr:
for D:
ion-ion collision by Monte-Carlo method
Post-collision velocity is related to pre-collision velocity according to momentum and energy conservation
electron-ion collision by fluid method
In ion pushing, electron-ion friction force is treated
Based on scattering angle and azimuthal angle sampled in Monte-Carlo method, the relative velocity is calculated.

## Slide 27: constraint on spatial step in hybrid simulation with collision
the minimum of inertial length and mean free path of ions
ion inertial length
mean free path of ion-ion collision

## Slide 28: constraint on time step in hybrid simulation with collision
ion plasma frequency
ion collision frequency
CFL stability criterion for waves in the whistler limit
resistive term of magnetic
diffusion equation
M A. Belyaev …, Phys. Plasmas 31, 012902 (2024)

## Slide 29: plasma expansion of single CS: influence of spatial grid
Schematic of three-dimension hybrid simulation on plasma expansion of single CS
spatial grid 20 μm
10 μm
5 μm

## Slide 30: Ion distribution during plasma expansion of single CS
In the XOZ plane, the distribution of ion density does not differ substantially during plasma expansion of single CS.

## Slide 31: hybrid simulation on plasma jet mixing of multiply CS
The plasma jets originated from the separate CS mix together to form a common arc column after a certain distance from the cathode.

## Slide 32: Ion distribution during plasma jet mixing of multiply CS
In the XOZ plane, the distribution of ion density differs for light ion and heavy ion: heavy ions is more concentrated in the central axis, but light ions are distributed in a much broader area.

## Slide 33: angular distribution of ion density, velocity and flux
angular distribution of ion density (left), velocity (middle) and flux (right), at a distance 0.16 mm away from the CS
The angular distribution of light and heavy ions is confirmed by 3D hybrid simulation on plasma jet mixing of multiply CS.
In the center, the flux of D ions is much smaller than that of Zr; in the edge, the flux of D ions is three times higher than that of Zr.

## Slide 34: Table of contents
Introduction: vacuum arcs of composite electrode
Insights from multi-component fluid simulation
Recent results of three-dimension hybrid simulation
I
III
IV
Insights from PIC-DSMC simulations
II
Conclusions
V

## Slide 35
Regarding multi-component plasma of vacuum arc discharge with composite cathode, we have developed different numerical approaches including fully kinetic particle method, fluid method, and hybrid method.
During plasma jet mixing, the ion collision is an important factor leading to the separation of light and heavy ions, and three main factors are found: ion mass, ion density and ion temperature.
Conclusions

## Slide 36
Thank you for listening!
questions or comments?