## Slide 1: UQDS - IT– Reliability Analysis
12/07/2024

## Slide 2: Progress since last meeting
Analysis of the failure rate apportionment of the Digital Platform
Continuous demand
  Calculation of the failure rate
    Below 3kA (4oo8 QHDS) and above 3kA (7oo8 QHDS or 1 CLIQ)
    1 year and 3 years Inspection interval
  Sensitivity Analysis
    Determined for which inspection interval the reliability target can be met
No Continuous demand
  Determined a model, which can be used for simulations
  Started to do simulations for different demand rates and inspection intervals

## Slide 3: Reliability Block Diagram for a single quench in a magnet (e.g. Quench in Coil PA3)
x6

## Slide 4: Quench scenario

## Slide 5: Reliability Block Diagram for a single quench in a magnet (e.g. Quench in Coil PA3)
Pessimistic scenario

## Slide 6: Failure rates
System/Component | Failure rate/FITs
Voltage Tap | 13.38
UQDS | 
Channel | 70.29
PSU | 874.70
Midplane | 38.42
FPGA | 1183.00
Trigger Interface | 7.00
PDSU | 
PSU | 0
FPGA | 1183.00
Midplane | 46.16
QHDS/CLIQ Trigger Interface | 7.00

## Slide 7: Failure rates
System/Component | Failure rate/FITs
Voltage Tap | 13.38
UQDS | 
Channel | 70.29
PSU | 0
Midplane | 38.42
FPGA (Digital Platform) | 1183.00
Trigger Interface | 7.00
PDSU | 
PSU | 0
FPGA (Digital Platform) | 1183.00
Midplane | 46.16
QHDS/CLIQ Trigger Interface | 7.00
Chart: Total FITs in given category
| Capacitor | Transistor | Resistor | Switch | External | Diode | Connector | IC, Plastic Encapsulated | Optoelectronic Device | Inductor
Total FITs in given category | 369.0271 | 275.9201 | 176.9628 | 155.8474 | 84.63 | 59.0971 | 32.724 | 27.3067 | 1.1223 | 0.058614
Chart: 
| Capacitor | Transistor | Resistor | Switch | External | Diode | Connector | IC, Plastic Encapsulated | Optoelectronic Device | Inductor
FITS per component | 0.9867 | 14.5221 | 0.71936 | 51.9491 | 4.03 | 2.273 | 1.818 | 1.517 | 0.14029 | 0.0041867
PSU only influences the availability.

## Slide 8: Failure rates
System/Component | Failure rate/FITs
Voltage Tap | 13.38
UQDS | 
Channel | 70.29
PSU | 0
Midplane | 38.42
FPGA (Digital Platform) | 962.00
Trigger Interface | 7.00
PDSU | 
PSU | 0
FPGA (Digital Platform) | 1183.00
Midplane | 46.16
QHDS/CLIQ Trigger Interface | 7.00
Chart: Total FITs in given category
| Capacitor | Transistor | Resistor | Switch | External | Diode | Connector | IC, Plastic Encapsulated | Optoelectronic Device | Inductor
Total FITs in given category | 369.0271 | 275.9201 | 176.9628 | 155.8474 | 84.63 | 59.0971 | 32.724 | 27.3067 | 1.1223 | 0.058614
Chart: 
| Capacitor | Transistor | Resistor | Switch | External | Diode | Connector | IC, Plastic Encapsulated | Optoelectronic Device | Inductor
FITS per component | 0.9867 | 14.5221 | 0.71936 | 51.9491 | 4.03 | 2.273 | 1.818 | 1.517 | 0.14029 | 0.0041867
-221 FITs
Only the failure mode short of the Capacitors of the DSP card – FPGA power delivery can cause blind failures.
-> Is a protection against this failure mode possible?

## Slide 9: Failure rates
System/Component | Failure rate/FITs
Voltage Tap | 13.38
UQDS | 
Channel | 70.29
PSU | 0
Midplane | 38.42
FPGA (Digital Platform) | 962.00
Trigger Interface | 7.00
PDSU | 
PSU | 0
FPGA (Digital Platform) | 1183.00
Midplane | 46.16
QHDS/CLIQ Trigger Interface | 7.00
Can a safe failure fraction be defined (in particular for the Digital Platform)?
UQDS v3
When will the new version of the system be released?
By what Percentage will the number of which components increase?
PDSU
Can the same assumptions for the Digital Platform of the UQDS also be made for the PDSU?
  PSU only influences the availability
  Only the failure mode short must be considered for the capacitors of the DSP card – FPGA power delivery

## Slide 10: Calculations – Continuous Demand
Assumptions
Continuous Demand (if there is a failure of the system, there is always a quench)
Reliability Target of maximum 1 allowed failure in 1.000 years
  No magnet protection leads to a downtime of months, which leads to a target of max. 1 failure/100 years
  Multiplied by 10 because of other systems that can cause a similar downtime
  We don’t have 1 system but ~5000 QDS systems
 | below 3kA (4oo8 QHDS) |  | above 3kA (7oo8 QHDS or 1 CLIQ) | 
Inspection Interval | 1 year | 3 years | 1 year | 3 years
Failures per system in 1000 years | 0.3329 | 1.1916 | 0.3329 | 1.1916

## Slide 11: Sensitivity Analysis – Continuous Demand
Inspection Interval | above 3kA (7oo8 QHDS or 1 CLIQ)
1 year | 1664.4
1 month (30 days) | 167.56
1 week | 39.12
5 hours | 1.16
4 hours | 0.93
Failures per 1000 years, when considering the 5000 QDS systems:
The reliability target can be met for an Inspection Interval of ~ 4-5 hours

## Slide 12: Comparison with results from QPS Analysis in 2004
Inspection Interval | above 3kA (7oo8 QHDS or 1 CLIQ)
1 year | 0.0000
1 month | 0.0179
2004
Now
Probability of protecting LHC S.C. elements in all quenches (20 years) when considering 5000 QDS and a continuous demand.

## Slide 13: Conclusion
The reliability target can not be met with a continuous demand and an Inspection Interval above ~4-5 hours.
We have to check whether we can lower the failure rate of the boards by excluding certain components or failure modes which do not cause a blind failure.
We have to and and also started to check for
  different inspection intervals,
  for which demand rate
  the reliability target can be met.