## Slide 1
Network Connectivity
University of Oklahoma

## Slide 2
Connection Suite
Four Geographical Location
North Campus.
Main Campus.
South Campus.
Research Campus.
Functional Connections
Internet Connectivity
Campus Connectivity
Local Data Center (aka Legacy DC)
Data Center (aka S2 DC)
VoIP
Peering Connections
North
Campus
Main
Campus
South
Campus
Research
Campus
Legacy
Data
Center
Core
Shared
Services
Peers
VoIP
Internet
Services
Edge
Three Campus Location
Norman
Oklahoma City
Tulsa
Cameron University
Rogers State University
Notes: Our approach to the campus network can be divided into two categories:
  Geographical Location
  Functional Connectivity

## Slide 3
This document may contain information that is privileged, confidential and/or exempt from disclosure under applicable law. If you are not an Employee of the University of Oklahoma, you are hereby notified that any disclosure, copying, distribution or use of the information contained herein is STRICTLY PROHIBITED. If you received this information in error, please immediately contact the sender and destroy the material in its entirety, whether electronic or a hard copy format.
INFORMATION
TECHNOLOGY
DataCenter
(Tulsa)
Firewall
Appliance
DataCenter
(OKC)
Internet Service Provider
(OneNet)
Main Campus
North Campus
South Campus
Research Campus
Data Center
( ie. NOC, SRTC, 4PP )
NC
MDF
(Merrick)
Firewall Appliance
Main Campus
South Campus
Football Stadium
Research Campus
Legacy DC
Core
Campus Backbone
Access
Layer
1gig interfaces
2.5/5 gig
10gig interfaces
25gig interfaces
Architecture
Distribution
Layer
40gig interfaces
Buildings connections = 1/10 Gbps
Wireless Controllers = 40 Gbps
Campus Backbone = 40 Gbps
Core/Edge
4 x 10 Gbps
4 x 10 Gbps
10 Gbps
10 Gbps
10 Gbps
100 Gbps

## Slide 4
This document may contain information that is privileged, confidential and/or exempt from disclosure under applicable law. If you are not an Employee of the University of Oklahoma, you are hereby notified that any disclosure, copying, distribution or use of the information contained herein is STRICTLY PROHIBITED. If you received this information in error, please immediately contact the sender and destroy the material in its entirety, whether electronic or a hard copy format.
INFORMATION
TECHNOLOGY
Firewall
Appliance
Core/Edge
Main Campus
Firewall Appliance
Main Campus
Core
Campus Architecture
North & Main Campus
Geographic Locations
Leadership

## Slide 5
This document may contain information that is privileged, confidential and/or exempt from disclosure under applicable law. If you are not an Employee of the University of Oklahoma, you are hereby notified that any disclosure, copying, distribution or use of the information contained herein is STRICTLY PROHIBITED. If you received this information in error, please immediately contact the sender and destroy the material in its entirety, whether electronic or a hard copy format.
INFORMATION
TECHNOLOGY
Firewall
Appliance
Core/Edge
Firewall Appliance
South Campus
Core
Campus Architecture
South Campus
Geographic Locations
Museum of Natural History

## Slide 6
This document may contain information that is privileged, confidential and/or exempt from disclosure under applicable law. If you are not an Employee of the University of Oklahoma, you are hereby notified that any disclosure, copying, distribution or use of the information contained herein is STRICTLY PROHIBITED. If you received this information in error, please immediately contact the sender and destroy the material in its entirety, whether electronic or a hard copy format.
INFORMATION
TECHNOLOGY
Firewall
Appliance
Core/Edge
Research Campus
Firewall Appliance
Research Campus
Core
Campus Backbone
Research Campus
National Weather Center
Radar
Innovation Lab
Research Tenants
ESNET
Peering
Supercomputer
Networks
Services
* OU Research Disk (OUR Disk) is a ceph infrastructure. It provides a high performance disk resource that is available both on OU IT's supercomputer, servers in the data center and devices residing on campus.

## Slide 7
Solutions @ Work
Data Center Network Architecture

## Slide 8
Hypervisors
Baremetal
servers
Border Leaf Nodes
In place to support endpoints such as routers, firewalls, load balancers or uplinks to other network devices.
Responsible for providing layer 2 and layer 3 connectivity between the data center fabric and anything outside of the data center.
Compute Leaf Nodes
Responsible for providing connectivity to endpoints such servers, compute nodes and storage appliances.
Spine
Network Architecture
Leaf Nodes
Dual uplink, with an uplink to each spine.
Each uplink is connected at 100Gbps.

## Slide 9
Multi-pod Deployment
Region 1 - OKC
Region 2 - Norman
Region 3 - Tulsa
Ease of Administration: Single data center fabric and single management cluster.
Resiliency: Each pod runs its own instance of a control-plane. A pod failure does not impact another pod.

## Slide 10
Multi-pod Deployment
Region 1 - OKC
Region 2 - Norman
Region 3 - Tulsa
OKC-IPN1
OKC-IPN2
Norman-IPN1
Norman-IPN2
OU
DWDM
Tulsa-IPN2
Tulsa-IPN1
100 Gbps
An Inter-Pod Network (IPN) is deployed at each pod. This provides Pod-to-Pod communication (also known as east-west traffic).
The IPN represents an extension of the ACI fabric underlay infrastructure.
All inter-pod traffic is encapsulated with VXLAN
East / West Traffic

## Slide 11
Model | Topology Layer | Media | Port Speeds | Port Quantity Per Switch
N9K-C9364C-GX | Spine | QSFP+ | 100 Gigabit Ethernet | 64 x 100 Gigabit Ethernet
N9K-C93180YC-FX3 | Leaf | SFP+ | 10 Gigabit Ethernet 25 Gigabit Ethernet 100 Gigabit Ethernet | 48 x 10/25 Gigabit Ethernet 6 x 100 Gigabit Ethernet
Nexus 93108TC-EX | Leaf | Copper | 100 Megabit Ethernet 1 Gigabit Ethernet 10 Gigabit Ethernet 100 Gigabit Ethernet | 48 x 100 Mbp, 1,10 Gigabit Ethernet 6 x 100 Gigabit Ethernet
N9K-C93600CD-GX | IPN, Leaf | QSFP+ | 40/100 Gigabit Ethernet 400 Gigabit Ethernet | 28 x 100 Gigabit Ethernet 8 x 400 Gigabit Ethernet
Nexus 93108TC-EX
N9K-C93600CD-GX
N9K-C93180YC-FX3
N9K-C9364C-GX
Hardware

## Slide 12
Pod Deployment: 3 switches (1 x copper and 2 x SFP).
Pod supports up to three racks of servers.
Pod supports dual connectivity of servers.
Leaf Nor-2215
Baremetal Host
Leaf Nor-2213
Hosting Endpoints
Leaf Nor-2214
Leaf Nor-2213 (copper)
Leaf Nor-2214 (SFP)
Leaf Nor-2215 (SFP)
Rack 2
Rack 1
Rack 3
SAMPLE RACK
SAMPLE RACK
SAMPLE Pod

## Slide 13
Each leaf has the ability to host different endpoints.
Each port will be assigned to an Endpoint Groups (EPGs).
The EPG will be responsible for defining both forwarding policy and security segmentation simultaneously.
Leaf Nor-2201
( Border Leaf )
Leaf Nor-2214
Edge
Router/FW
DC
Baremetal
DC
Baremetal
Leaf Nor-2215
Hosting Endpoints
DC
Host

## Slide 14
Each leaf has the ability to host different endpoints.
Each port will be assigned to an Endpoint Groups (EPGs).
The EPG will be responsible for defining both forwarding policy and security segmentation simultaneously.
Leaf Nor-2201
( Border Leaf )
Leaf Nor-2209
Leaf Nor-2210
Hosting Endpoints
Enterprise
Edge
(Firewall)
DC
Host
DC
Baremetal
DC
Baremetal
DC
Host
Research Edge
Research
Baremetal
Research
Baremetal
Tenant
ISP
Tenant
Baremetal

## Slide 15
Hosting Endpoints
Sample Interface Policy
CEPH_Cloud_Trunk_PolicyGroup
CDP Policy: disabled
LLDP Policy: enable
Attached Entity Profile (VLANs allowed): VLAN 112,212,1062, trunk
Interface Polices
10G-auto
1G-auto
LLDP-off
LLDP-on
LACP-active
Interface polices define interface behavior and features to be configured on a specific interface. The goal is for objects to be reused.
LACP-active
CDP
enable
Interface
Policy Group
(template)
CDP
Policy (off)
LLDP Policy (enable)
Other
options
Other
options
Access Port
Port-Channel
vPC
Interface
Policy Group
(template)
Attatching Profile
VLANs used
Domain type
Baremetal_Trunk_PolicyGroup
CDP Policy: disabled
LLDP Policy: enable
Attached Entity Profile (VLANs allowed): VLANs 2-200, trunk
IDRAC_V251_PolicyGroup
CDP Policy: disabled
LLDP Policy: enable
Attached Entity Profile (VLANs allowed): VLANs 251, untagged

## Slide 16
Looking Ahead

## Slide 17
Edge Routers
Norman
Tulsa
OKC
Norman-Edge
Routers
Tulsa-Edge
Routers
Onenet
Internet
OKC-Edge
Routers
Tri-Campus WAN Connectivity
Internet Connectivity
Campus to Data Center Connectivity
Physical Connectivity: 100 Gbps
Campus
Backbone
Data Center
Fabric
Campus
Backbone
Data Center
Fabric
Campus
Backbone
Data Center
Fabric
100 Gbps
100 Gbps

## Slide 18
Model | Topology Layer | Media | Port Speeds | Port Quantity Per Switch
DCS-7280CR3K-32D4-F | - | - | 100 Gigabit Ethernet 400 Gigabit Ethernet | 32 x 100 Gigabit Ethernet and 4 x 400 Gigabit Ethernet
DCS-7280CR3K-32D4-F
Hardware

## Slide 19
Virtual Machine Managers Integration
Simplifying tasks by automating network functions.
Manage network policies in your virtual environment.
ACI Integrates with the following VMM
Microsoft
Vmware
Red Hat
OpenStack
ACI Integrates with the following Container Domain
Cloud Foundry
Kubernetes
OpenShift

## Slide 20
END