## Slide 1: Performance estimates for the new HL-LHC baseline & variants
R. De Maria, S. Kostoglou, R. Tomas
H. Bartosik, I. Efthymiopoulos, L. Mether, N. Mounet, G. Sterbini
WP2 02/07/2024

## Slide 2: Baseline
Run | Year | Efficiency | Bunch intensity (1e11 ppb) | βx* (cm) | βy* (cm) | CC | PUmax | Days Intensity ramp-up | Days Proton physics [1] | # colliding IP1/5 bunches [2] | # colliding IP8 bunches | Emit start of SB (μm) | IP1/5 crossing plane | IP1/5 φ/2 (μrad) | LHCb Lpeak (1e33 Hz/cm2) [3]
4 | 2029 | 0.5 | 1.8 | 30 | 30 | off | 101 | 20 | 6 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2030 | 0.5 | 2.2 | 25 | 25 | on | 132 | 15 | 136 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2031 | 0.5 | 2.2 | 20 | 20 | on | 132 | 10 | 154 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2032 | 0.5 | 2.2 | 20 | 20 | on | 132 | 10 | 152 | 2748 | 2574 | 2.5 | H/V | 250 | 2
5 | 2035 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 152 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2036 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 195 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2037 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2038 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198 | 2748 | 2574 | 2.5 | H/V | 250 | 2
6 | 2040 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 165 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2041 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 203 | 2748 | 2574 | 2.5 | H/V | 250 | 2
[1]: No ion operation beyond Run 4
[2]: 25ns_2760b_2748_2492_2574_288bpi_13inj_800ns_bs200ns
[3]: Not considering LHCb upgrade after LS4, up to 3% loss of integrated lumi for ATLAS/CMS.
Input from new proposed DMR

## Slide 4: Intensity ramp up
Run 4
Run 5
Based on Riccardo’s Chamonix 2024 talk

## Slide 5: Intensity ramp up
Run 4
Run 5
Based on Riccardo’s Chamonix 2024 talk

## Slide 6: Variations
Run | Year | Efficiency | Bunch intensity (1e11 ppb) | βx* (cm) | βy* (cm) | CC | PUmax | Days Intensity ramp-up | Days Proton physics [1] | # colliding IP1/5 bunches [2] | # colliding IP8 bunches | Emit start of SB (μm) | IP1/5 crossing plane | IP1/5 φ/2 (μrad) | LHCb Lpeak (1e33 Hz/cm2) [3]
4 | 2029 | 0.5 | 1.8 | 30 | 30 | off | 101 | 20 | 6 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
 | 2030 | 0.5 | 2.2 | 25 | 25 | on | 132 | 15 | 136 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
 | 2031 | 0.5 | 2.2 | 208 | 2018 | on | 132 | 10 | 154 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
 | 2032 | 0.5 | 2.2 | 208 | 2018 | on | 132 | 10 | 152 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
5 | 2035 | 0.5 | 2.2 | 158 | 1518 | on | 132 | 15 | 152 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
 | 2036 | 0.5 | 2.2 | 158 | 1518 | on | 132 | 10 | 195 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
 | 2037 | 0.5 | 2.2 | 158 | 1518 | on | 132 | 10 | 198 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
 | 2038 | 0.5 | 2.2 | 158 | 1518 | on | 132 | 10 | 198 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
6 | 2040 | 0.5 | 2.2 | 158 | 1518 | on | 132 | 15 | 165 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
 | 2041 | 0.5 | 2.2 | 158 | 1518 | on | 132 | 10 | 203 | 2748 | 2574 | 2.5 | H/VV/H | 250 | 2
”Flat 8/18 cm”

## Slide 7: Variations
Run | Year | Efficiency | Bunch intensity (1e11 ppb) | βx* (cm) | βy* (cm) | CC | PUmax | Days Intensity ramp-up | Days Proton physics [1] | # colliding IP1/5 bunches [2] | # colliding IP8 bunches | Emit start of SB (μm) | IP1/5 crossing plane | IP1/5 φ/2 (μrad) | LHCb Lpeak (1e33 Hz/cm2) [3]
4 | 2029 | 0.5 | 1.8 | 30 | 30 | off | 101 | 20 | 6 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
 | 2030 | 0.5 | 2.2 | 25 | 25 | on | 132 | 15 | 136 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
 | 2031 | 0.5 | 2.2 | 20 | 20 | on | 132 | 10 | 154 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
 | 2032 | 0.5 | 2.2 | 20 | 20 | on | 132 | 10 | 152 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
5 | 2035 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 152 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
 | 2036 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 195 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
 | 2037 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
 | 2038 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
6 | 2040 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 165 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
 | 2041 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 203 | 2748 2440 | 2574 2240 | 2.5 | H/V | 250 | 2
”Round hybrid”: 25ns_2452b_2440_1952_2240_248bpi_12inj_mixed

## Slide 8: Variations
Run | Year | Efficiency | Bunch intensity (1e11 ppb) | βx* (cm) | βy* (cm) | CC | PUmax | Days Intensity ramp-up | Days Proton physics [1] | # colliding IP1/5 bunches [2] | # colliding IP8 bunches | Emit start of SB (μm) | IP1/5 crossing plane | IP1/5 φ/2 (μrad) | LHCb Lpeak (1e33 Hz/cm2) [3]
4 | 2029 | 0.5 | 1.8 | 30 | 30 | off | 101 | 20 | 6 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
 | 2030 | 0.5 | 2.2 | 25 | 25 | on | 132 | 15 | 136 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
 | 2031 | 0.5 | 2.2 | 20 | 20 | on | 132 | 10 | 154 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
 | 2032 | 0.5 | 2.2 | 20 | 20 | on | 132 | 10 | 152 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
5 | 2035 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 152 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
 | 2036 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 195 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
 | 2037 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
 | 2038 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
6 | 2040 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 165 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
 | 2041 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 203 | 2748 2736 | 25742370 | 2.5 2.2 | H/V | 250 | 2
”Round BCMS”: 25ns_2744b_2736_2246_2370_240bpi_13inj_800ns_bs200ns_BCMS_5x48b

## Slide 9: BCMS performance in 2024
Emittance start of injection (μm) | B1H | B1V | B2H | B2V
Fills 9575-9663 | 1.57 | 1.59 | 1.5 | 1.5
Fills 9664-9694 | 1.19 | 1.27 | 1.13 | 1.16
% | -24.2 | -20.1 | -24.7 | -22.7
Emittance end of injection (μm) |  |  |  | 
Fills 9575-9663 | 1.77 | 1.71 | 1.63 | 1.62
Fills 9664-9700 | 1.49 | 1.44 | 1.32 | 1.31
% | -15.7 | -16 | -18.7 | -18.8
Emittance start of SB (μm) |  |  |  | 
Fills 9575-9663 | 1.84 | 1.66 | 2.25 | 2.3
Fills 9664-9694 | 1.57 | 1.53 | 1.99 | 2.04
% | -14.67 | -7.83 | -11.56 | -11.3
Bunch intensity (1e11 ppb) | B1 INJPHYS | B2 INJPHYS | B1 STABLE | B2 STABLE
Fills 9573-9663 | 1.59 | 1.59 | 1.56 | 1.55
Fills 9664-9694 | 1.62 | 1.62 | 1.59 | 1.57
% | +1.89 | +1.89 | +1.92 | +1.29

## Slide 10: BCMS performance in 2024: Leveling time
Leveling time
Emittance
Bunch intensity
PU target
Step in leveling time results from the combination of smaller emittances at start of SB and increased bunch intensity.
Notes: 9614, 9618, 9667, 9670

## Slide 11: BCMS performance in 2024: Performance gain
Fill 9614, Standard
Fill 9667, BCMS
Considering a turn-around time of 2.5h:
        From 1.22 fb-1/day with standard to 1.32 fb-1/day with BCMS: +8.2% integrated luminosity for fills that make it to the optimal fill length (>8h)

## Slide 12: BCMS performance in 2024: Performance gain
Fill 9614, Standard
Fill 9667, BCMS
Considering a turn-around time of 2.5h:
        From 1.22 fb-1/day with standard to 1.32 fb-1/day with BCMS: +8.2% integrated luminosity for fills that make it to the optimal fill length (>8h)
Based on BCMS experience of 2024, 10% smaller emittance at start of SB + 2% larger bunch intensity
 8% gain in integrated luminosity for LHC. Explore feasibility of BCMS scenario as baseline for HL-LHC?

## Slide 13: BCMS performance in 2024: Performance gain
Fill 9614, Standard
Fill 9667, BCMS
Considering a turn-around time of 2.5h:
        From 1.22 fb-1/day with standard to 1.32 fb-1/day with BCMS: +8.2% integrated luminosity for fills that make it to the optimal fill length (>8h)
Impact of tails in the LHC to be considered and studied (“BCMS with reduced tails” from the injectors F. Asvesta, M. Bozatzis).
MD on non-factorization of VdM beams E. Lamb, G. Sterbini

## Slide 14: Variations
Run | Year | Efficiency | Bunch intensity (1e11 ppb) | βx* (cm) | βy* (cm) | CC | PUmax | Days Intensity ramp-up | Days Proton physics [1] | # colliding IP1/5 bunches [2] | # colliding IP8 bunches | Emit start of SB (μm) | IP1/5 crossing plane | IP1/5 φ/2 (μrad) | LHCb Lpeak (1e33 Hz/cm2) [3]
4 | 2029 | 0.5 | 1.8 | 30 | 30 | off | 101 | 20 | 6 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2030 | 0.5 | 2.2 | 25 | 25 | on | 132 | 15 | 136 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2031 | 0.5 | 2.2 | 20 | 20 | on | 132 | 10 | 154 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2032 | 0.5 | 2.2 | 20 | 20 | on | 132 | 10 | 152 | 2748 | 2574 | 2.5 | H/V | 250 | 2
5 | 2035 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 152130 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2036 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 195172 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2037 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198175 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2038 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198175 | 2748 | 2574 | 2.5 | H/V | 250 | 2
6 | 2040 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 165141 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2041 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 203179 | 2748 | 2574 | 2.5 | H/V | 250 | 2
“Nominal ions”  “Extended ions”

## Slide 15: Scenarios
Scenario | Optics | Duration | Filling scheme
Baseline | Round Run4 20cm | Nominal ions | Standard
Round hybrid | Round Run4 20cm | Nominal ions | Hybrid
Round BCMS | Round Run4 20cm | Nominal ions | BCMS
Flat 8/18 cm | Flat 8/18 cm | Nominal ions | Standard
Vbaseline extended ions | Round Run4 20cm | Extended ions | Standard
Round hybrid extended ions | Round Run4 20cm | Extended ions | Hybrid
Round BCMS extended ions | Round Run4 20cm | Extended ions | BCMS
Flat extended ions | Flat | Extended ions | Standard

## Slide 16: Leveling time & optimal fill length
Run 6 | Baseline | Round hybrid | Round BCMS | Flat 8/18 cm
Run 6 leveling time (h) | 6.7 | 6.5 | 6.8 | 7.5
Run 6 optimal fill length (h) | 8.1 | 8 | 8.2 | 8.8
Yearly integrated lumi (fb-1) | 269.1 | 240.9 | 270.9 | 277
Baseline
Round hybrid
Round BCMS
Flat 8/18 cm
For Run 4, reaching 15 cm instead of 20 cm results in 3.44% increase of integrated lumi per year

## Slide 17: Yearly & total integrated luminosity
Run | Year | Baseline | Round hybrid | Round BCMS | Flat 8/18 cm | Vbaseline extended ions | Round hybrid extended ions | Round BCMS extended ions | Flat 8/18 cm extended ions
4 | 2029 | 9.6 | 9.1 | 10 | 9.6 | 9.6 | 9.1 | 10 | 9.6
 | 2030 | 208 | 186.1 | 210.7 | 208 | 208 | 186.1 | 210.7 | 208
 | 2031 | 238.8 | 213.4 | 241 | 254.1 | 238.8 | 213.4 | 241 | 254.1
 | 2032 | 235.7 | 210.7 | 237.9 | 250.8 | 235.7 | 210.7 | 237.9 | 250.8
5 | 2035 | 248.5 | 222.6 | 250.2 | 256 | 213.8 | 191.6 | 215.3 | 220.3
 | 2036 | 311.7 | 278.6 | 313.7 | 320.5 | 275.4 | 246.2 | 277.2 | 283.2
 | 2037 | 316.4 | 282.9 | 318.4 | 325.3 | 280.1 | 250.5 | 281.9 | 288.1
 | 2038 | 316.4 | 282.9 | 318.4 | 325.3 | 280.1 | 250.5 | 281.9 | 288.1
6 | 2040 | 269.1 | 240.9 | 270.9 | 277 | 213.2 | 207.1 | 232.8 | 238.1
 | 2041 | 324.3 | 289.9 | 326.4 | 333.4 | 286.5 | 256.1 | 288.3 | 294.6
Total (fb-1) |  | 2478.5 | 2217 | 2497.7 | 2560 | 2259.2 | 2021.2 | 2277.1 | 2334.9

## Slide 18: Realtive yearly & total integrated luminosity
Run | Year | Baseline (fb-1) | Round hybrid | Round BCMS | Flat 8/18 cm | Vbaseline extended ions | Round hybrid extended ions | Round BCMS extended ions | Flat 8/18 cm extended ions
4 | 2029 | 9.6 | -5.21% | 4.17% | 0% | 0% | -5.21% | 4.17% | 0%
 | 2030 | 208 | -10.53% | 1.30% | 0% | 0% | -10.53% | 1.30% | 0%
 | 2031 | 238.8 | -10.64% | 0.92% | 6.41% | 0% | -10.64% | 0.92% | 6.41%
 | 2032 | 235.7 | -10.61% | 0.93% | 6.41% | 0% | -10.61% | 0.93% | 6.41%
5 | 2035 | 248.5 | -10.42% | 0.68% | 3.02% | -13.96% | -22.90% | -13.36% | -11.34%
 | 2036 | 311.7 | -10.62% | 0.64% | 2.82% | -11.65% | -21.02% | -11.07% | -9.14%
 | 2037 | 316.4 | -10.58% | 0.63% | 2.81% | -11.48% | -20.83% | -10.90% | -8.94%
 | 2038 | 316.4 | -10.58% | 0.63% | 2.81% | -11.48% | -20.83% | -10.90% | -8.94%
6 | 2040 | 269.1 | -10.48% | 0.67% | 2.94% | -20.78% | -23.04% | -13.49% | -11.52%
 | 2041 | 324.3 | -10.60% | 0.65% | 2.81% | -11.66% | -21.03% | -11.10% | -9.15%
 |  | 2478.5 | -10.55% | 0.77% | 3.28% | -8.85% | -18.45% | -8.13% | -5.79%
Reaching 15 cm in Run 4 results in 3.44% increase of integrated lumi per year
Slight increase with BCMS (+1%) for HL-LHC
+3% gain with flat optics
-9% if ion runs beyond Run 4
-10% with hybrid, -19% if hybrid + ion runs beyond Run 4
Loss of performance due to ion runs beyond Run 4 can be partially mitigated with flat optics

## Slide 19: Summary

## Slide 20: Summary

## Slide 21: Backup slides

## Slide 22: Variations
Run | Year | Efficiency | Bunch intensity (1e11 ppb) | βx* (cm) | βy* (cm) | CC | PUmax | Days Intensity ramp-up | Days Proton physics [1] | # colliding IP1/5 bunches [2] | # colliding IP8 bunches | Emit start of SB (μm) | IP1/5 crossing plane | IP1/5 φ/2 (μrad) | LHCb Lpeak (1e33 Hz/cm2) [3]
4 | 2029 | 0.5 | 1.8 | 30 | 30 | off | 101 | 20 | 6 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2030 | 0.5 | 2.2 | 25 | 25 | on | 132 | 15 | 136 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2031 | 0.5 | 2.2 | 20 | 20 | on | 132 | 10 | 154 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2032 | 0.5 | 2.2 | 20 15 | 20  15 | on | 132 | 10 | 152 | 2748 | 2574 | 2.5 | H/V | 250 | 2
5 | 2035 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 152 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2036 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 195 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2037 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2038 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 198 | 2748 | 2574 | 2.5 | H/V | 250 | 2
6 | 2040 | 0.5 | 2.2 | 15 | 15 | on | 132 | 15 | 165 | 2748 | 2574 | 2.5 | H/V | 250 | 2
 | 2041 | 0.5 | 2.2 | 15 | 15 | on | 132 | 10 | 203 | 2748 | 2574 | 2.5 | H/V | 250 | 2
”Round Run4 20 cm” “Round Run4 15cm”