## Slide 1: Simplified layout of AWAKE Run2c beamlines
Alena Puckova
CSCP Meeting #1
04/07/2024

## Slide 2: Why there is a need for a layout?
Services needs functional specification:
Layout with integration of the main beam elements
Pressure requirements for laser, e-source, proton and electron lines
Special requirements if any (dust, gas compositions, pumpdown from atmospheric, etc.)
Gas sources (if any) – special instrumentation, etc.
Beam envelope along the lines, according to the optics (if several options the most pessimistic)
Inputs and outputs for vacuum control system (alarms, beam interlock system, etc.)
CP4
Each CP leader

## Slide 3: What a “simplified” layout should deliver?
All beamline elements placed in their correct location and using the correct element model (when available) with their:
name,
position along beamline,
approximate distance between flanges,
approximate height under element (support height).

## Slide 4: How are we going to implement it?
5 beamlines (UV+IR laser, p+, 2xe-) with magnets and BI where they exist
Only top view

## Slide 5: How to define PFs:
For Run2c, elements from four beamlines (e-x2, laser and p+) have the same longitudinal position -> need for different numbering for those “parallel” lines:
41: proton line (existing)
42: IR laser (existing)
43: keep spare (run 2ab e-line)
44: 1st electron line (new)
45: 2nd electron line (new)
46: UV laser (new)
+ horizontal position defined by the start of the sector
+ the name stays the same (could be changed in case of new or special equipment)

## Slide 6: Current status
3D model has the correct configuration for the p+ and 1st e-lines
Laser lines will be added during July
High energy e-line still under discussion
Fred is working on the layout and PFs – details in his presentation

## Slide 7: Thank you for your attention!