## Slide 1
ARM compute @ Glasgow
Status & Updates
Emanuele Simili GridPP52 Ambleside - 29 August 2024
+
Notes: PoW @ GridPP

## Slide 2
Outline
Update on Glasgow cluster (heterogeneous compute) - ScotGrid Glasgow cluster fully updated - ARM & x86 resources “transparently” available through CE endpoints - Physics Validation updates (June 2024)
Benchmarking and Power Measurement - updates on HEPscore/Watt & Frequency Scan - new IPMI validation campaign against external PDU - first step in testing RISC-V architecture for HEP
Upcoming conferences - Few contributions will be presented at HTCondor workshop (AMS, Sep. 2024) - A plenary and a few track talks accepted at CHEP 2024 (KRK, Oct. 2024)
Outlook …
Notes: outline

## Slide 3
2xAMD64ht: Dual Socket AMD EPYC 7513 32-Core Processor (DELL) CPU: 2 * x86 AMD EPYC 7513 (Milano), 32C/64HT @ 2.6GHz (TDP 200W) RAM: 512GB (16 x 32GB) DDR4 3200MT/s  4 GB/core HDD: 3.84TB SSD SATA Read Intensive
in-House (production)
~ 5k cores
2xAMD64ht: Dual Socket AMD EPYC 7452 32-Core Processor (DELL) CPU: 2 * x86 AMD EPYC 7452 (Roma), 32C/64HT @ 2.35GHz (TDP 200W) RAM: 512GB (16 x 32GB) DDR4 3200MT/s  4 GB/core HDD: 3.84TB SSD SATA Read Intensive
2xIntel40ht: Dual Socket Intel XEON 10-Core CPU E5-2630 v4 (HP) CPU: 2 * x86 Intel(R) Xeon(R) E5-2630 v4, 10C/20HT @ 2.2GHz (TDP 85W) RAM: 160GB (4 x 32GB + 4 x 8GB) DDR4 2400 MHz  4 GB/core HDD: 2TB disk SATA @ ‎7200 RPM
~ 7.5k cores
~ 1.5k cores
2*ARM80c: Dual Socket Ampere Altra Q80-30 80-Core Processor (Ampere) CPU: 2 * ARM Ampere Q80-30, 80C @ 3GHz (TDP 210W) RAM: 512GB (32 x 16GB or 16 x 32GB) DDR4 3200MT/s  3.2 GB/core HDD: 2 * 1TB NVMe
~ 2k cores
ARM128c: Single Socket Ampere Altra Max M128-30 128-Core Processor (SuperMicro) CPU: ARM Ampere M128-30, 128C @ 3GHz (TDP 250W) RAM: 512GB (8 x 64 GB) DDR4 3200MHz  4 GB/core HDD: 8TB NVMe
~ 2k cores
Notes: hardware currently in production at Glasgow Tier2 compute cluster

## Slide 4
Cluster Update
We have completed the update of our Tier2 cluster at Glasgow, due to the long-awaited End Of Life (in June 2024) of CentOS7, which we used for the past 4-5 years:
- all compute nodes and services updated to Alma 9 - all CEPH nodes updated to Alma 8 and CEPH v14 (Nautilus), next: Pacific - batch system updated to HTCondor 10.0, ARC-CE v6.20 (waiting for v7), no ARGUS - updated monitoring services: Prometheus 2.5, Loki 3, Grafana 11, …
- updated management stuff: Ansible v2.14, GitLab v17.3, … - installed perfSONAR 5.1 testpoint (rather than toolkit)
Notes: updates

## Slide 5
Heterogeneous Compute Cluster
Condor Manager
wn_x86
wn_ARM
UKI-SCOTGRID-GLASGOW_CEPH
wn_x86
wn_x86
wn_x86
wn_x86
wn_x86
wn_ARM
wn_ARM
wn_ARM
wn_ARM
wn_ARM
wn_ARM
wn_x86
wn_x86
wn_x86
ce01.gla.scotgrid.ac.uk
ce02.gla.scotgrid.ac.uk
ce03.gla.scotgrid.ac.uk
ce04.gla.scotgrid.ac.uk
jobs
x86 queue
ARM queue
~15k cores (ht)
~4k cores
ce-test.gla.scotgrid.ac.uk
We started providing ARM resources by creating a separate queue for ARM (former ce-test endpoint).
Then, after upgrading the whole HTCondor cluster to v10, we tried to join the queues …
This is the idealized view of our heterogeneous computing cluster:
The condor_requirements setting in the ARC-CE configuration modifies the ClassAd for the jobs that ARC submits to Condor by inserting an architecture request (*)
decommissioned
Notes: ce01.gla.scotgrid.ac.uk
ce02.gla.scotgrid.ac.uk
ce03.gla.scotgrid.ac.uk
ce04.gla.scotgrid.ac.uk
ce-test.gla.scotgrid.ac.uk

## Slide 6
Heterogeneous Compute Cluster Issues
Condor Manager
wn_x86
wn_ARM
UKI-SCOTGRID-GLASGOW_CEPH
wn_x86
wn_x86
wn_x86
wn_x86
wn_x86
wn_ARM
wn_ARM
wn_ARM
wn_ARM
wn_ARM
wn_ARM
wn_x86
wn_x86
wn_x86
ce01.gla.scotgrid.ac.uk
ce02.gla.scotgrid.ac.uk
ce03.gla.scotgrid.ac.uk
ce04.gla.scotgrid.ac.uk
jobs
x86 queue
ARM queue
~15k cores (ht)
~4k cores
ce-test.gla.scotgrid.ac.uk
In reality, we only enabled the dual queue on ce03, because not all VOs can deal with the architecture settings (e.g., BioMed), and we kept the ce-test entry point because it is still in use by some VOs, while the other ces are still single queue (x86).
So, this is the actual view of our heterogeneous compute cluster:
We are still in a transitioning state, but as more VOs adhere to the dual queue standard, we hope to make the dual queue submission mechanism more ideal …
… soon to be decommissioned
Notes: dual queue issues

## Slide 7
This also works for GPU queue (tested already !)
Heterogeneous Compute Cluster Config
[queue:condor]
comment = Condor queue
condor_requirements = (Arch == "X86_64" && (TARGET.GPUs IS UNDEFINED || TARGET.GPUs == 0))
[queue:condor_arm]
comment = Condor queue (ARM)
condor_requirements = (Arch == "aarch64" && (TARGET.GPUs IS UNDEFINED || TARGET.GPUs == 0))
[queue:condor_gpu]
comment = Condor queue (x86 + GPU)
condor_requirements = TARGET.GPUs > 0
(*) The condor_requirements setting in the ARC-CE configuration modifies the ClassAd for the jobs that ARC submits to Condor by inserting an architecture request.
Because … HTCondor doesn't have a concept of queues: it matches jobs to resources based on their ClassAd, which includes an architecture entry …
What VOs need to do is to ensure that their job submission mechanism specifies the appropriate ARC queue (i.e., what architecture they are targeting).
Note: the ARC default queue selection appeared buggy in earlier version of ARC v6, hopefully it will improve in v7.
Notes: dual queue config

## Slide 8
ARM Physics Validation
Most LHC experiments (ATLAS, CMS, ALICE) have done a first round of extensive Physics Validation campaigns against our ARM cluster @ Glasgow:
  ATLAS: Full simulation and Reconstruction are physics validated.
      ATLAS is ready for pledged ARM resources!
  CMS: Physics validation on ARM mostly successful, but not conclusive. CMS is not in a position to use ARM processors in production!
  ALICE: Extensive test of MC simulation jobs, no analysis workflows. Recommends ARM segregation or mixed queue with enable/disable!
  LHCb: Groundwork & test samples done, full physics validation not done. Production use of ARM unlikely before end of 2024!
Latest reports from GDB (June 2024 @ CERN): https://indico.cern.ch/event/1356135/
It’s time for VOs to start sending ARM jobs our way … we have over 4k ARM cores !




Notes: GDB (June 2024 @ CERN): https://indico.cern.ch/event/1356135/
ATLAS: https://indico.cern.ch/event/1356135/contributions/5971895/attachments/2875966/5036670/20240612%20ARM%20for%20ATLAS.pdf
(all ok, ready to pledge)
CMS: https://indico.cern.ch/event/1356135/contributions/5971888/attachments/2875790/5036232/GDB_WLCG_CMS_Adriano_12Jun24_Pub.pdf
(ok Monte Carlo simulations, significant differences for detector data, not ready to pledge)
ALICE: https://indico.cern.ch/event/1356135/contributions/5971898/attachments/2875360/5035311/ARM%20in%20ALICE.pdf
(ok MC simulation jobs, no analysis workflows)
LHCb: https://indico.cern.ch/event/1356135/contributions/5971887/attachments/2873979/5036103/20240612%20GDB%20-%20ARM%20status%20(1).pdf
(groundwork done, full physics validation not done, creation of test-samples demonstrated, production use of ARM unlikely before end of 2024)

## Slide 9
AMD96ht: Single AMD EPYC 7003 48-Core Processor (GIGABYTE) CPU: x86 AMD EPYC 7643, 48C/96HT @ 2.3GHz (TDP 225W) RAM: 256GB (16 x 16GB) DDR4 3200MHz  2.7 GB/core HDD: 3.84TB SSD SATA
Grace144c: Dual Socket* NVidia Grace 144-Core Processor (SuperMicro) CPU: NVidia Grace 144-Core 480GB DDR5 @ 3.4GHz (TDP 500W) RAM: 480GB (on chip) DDR5 4237MHz  3.3 GB/core HDD: 1TB NVMe + 4TB NVMe
ARM80c: Single socket Ampere Altra Q80-30 80-Core Processor (GIGABYTE) CPU: ARM Ampere Q80-30, 80C @ 3GHz (TDP 210W) RAM: 256GB (16 x 16GB) DDR4 3200MHz  3.2 GB/core HDD: 3.84TB SSD SATA
in-House Testing
2xAMD48ht+GPU: Dual Socket AMD EPYC 7443 24-Core Processor (DELL) CPU: 2* AMD EPYC 7443, 24C/48HT @ 2.3GHz (TDP 200W) GPU: 2* NVIDIA A100 PCIe 80GB (TDP 300W) RAM: 256GB (16 x 16GB) DDR4 3200MHz  2.7 GB/core HDD: 480GB SSD SATA + 5TB SSD SCSI
Notes: in-house

## Slide 10
Remote Testing
2*AMD256ht: Dual Socket AMD EPYC 9754 128-Core Processor (SuperMicro) CPU: 2 * x86 AMD EPYC 9754 (Bergamo), 128C/256HT @ 3.1GHz (TDP 360W) RAM: 1.536TB (24 x 64GB) DDR4 3200MHz  3 GB/core HDD: 512GB NVMe + 3.84TB SSD OS: Rocky 9.2
ARM128c: Single Socket Ampere Altra Max M128-28 128-Core Processor (XMA) CPU: ARM Ampere M128-28, 128C @ 2.8GHz (TDP 250W) RAM: 512GB (8 x 64GB) DDR4 3200MHz  4 GB/core HDD: 1TB NVMe Storage OS: Rocky 8.8
XMA
AMD128ht: Single Socket AMD EPYC 8534P 64-Core Processor (SuperMicro) CPU: AMD EPYC 8534P (Siena), 64C/128HT @ 3.1GHz (TDP 200W) RAM: 576GB (6 x 96GB) DDR5 3200MT/s  4.5 GB/core HDD: 1TB NVMe Storage OS: Rocky 8.8
Coming soon : AmpereOne (96 - 192 cores)
… we expect to get remote access to a test box next month!
SuperMicro
SuperMicro
SuperMicro
SuperMicro
Notes: AmpereOne: https://amperecomputing.com/briefs/ampereone-family-product-brief

## Slide 11
HEPscore/Watt
Using the new Figure of Merit (<75-95%> quantile average) as best proxy for Power, we estimate the Performance per Watt as HEP-Score/Power FoM. (Note: replaced Altra Max M128-28 with M128-30).
*
*
Notes: … but, this is not the whole story: each machine runs at its highest frequency (conservative governor), and frequency directly affects power usage.
See next slide (!)

## Slide 12
Frequency Scan (update)
HEP-Score/Watt vs. CPU Frequency gives a better picture of hardware potentials and shows optimal performances per watt at mid frequency range. Plots have been updated with the most recent Power F.o.M. and a scan of the whole Altra Max frequency range, thanks to the newly acquired M128-30 nodes.
x86
ARM
Notes: (!) see performance/watt of Max vs Grace …
NOTE: the x coordinate shows the “nominal” frequency, i.e., the frequency that has been set via ‘cpupower frequency-set’.
This does not always stay constant during the run, especially x86 have a “high frequency” turbo mode that is switched on/off depending on load.

## Slide 13
IPMI Validation
We acquired a metered PDU with remote readings and we are validating our IPMI power readings against the PDU. This is our current configuration:
AMD96ht: Single AMD EPYC 7003 48-Core
Grace144c: Dual Socket NVidia Grace 144-Core
ARM80c: Single socket Ampere Altra Q80-30 80-Core
Milk-V Pioneer : Single socket RISC-V 64-Core
Notes: PDU specs: APC Easy Rack PDU, Metered, 1U, 1 Phase, 3.7kW, 230V, 16A, 8 x C13 outlets, IEC60320 C20 inlet

## Slide 14
Validation Strategy
The PDU provides a single reading, so we measured the baseline with all machines off:
When off, the AMD, ARM and Grace test boxes each draw about 16 W for IPMI/OOB services, RISC-V next to nothing, as it’s a desktop PC with no BMC.
For testing, we turned on one machine at each time, and collected Power readings from:
IPMI (via ipmitool “Instantaneous Power”) ;
PDU (via ModBus “Active power”), with sampling interval 5 sec for both.
We ran 3 tests: stress (10 min.) , sleep (10 min.) , HEP-Score (3-6h) …
This strategy was motivated by minimizing the presence in the data center … we also tried a different approach, by connecting a single machine per time to the PDU and measuring power usage during stress and sleep. Results are still being interpreted.
Base consumption is extremely stable at 67 Watts
Notes: baseline

## Slide 15
Validation Results (preliminary)
Here a first comparison of 3 machines running stress and a sleep job, one after the other:
stress sleep
stress sleep
stress sleep
We’d expect difference (D=PDU-IPMI) to have small oscillation around the 67 Watts baseline … but it is not really the case.
Known issues:
- there seem to be a lot more oscillations in idle (sleep) than at full load (stress), probably due to lower efficiency of the PSUs at lower output levels, and variation in background load having a relatively larger impact;
- the export scripts tend to skip beats or introduces delays, making the two time-series asynchronous;
- PDU readings show a longer tail (?) …
67
Work in Progress
Notes: Key points:
* We believe we understand the difference between the IPMI and PDU readings: largely due to OOB services on the nodes which were offline during the tests (16 W from Eclipse / Grace).
* We can quantify the difference between IPMI and PDU readings for a single host (e.g. ~1% on Eclipse hosts under load, about 4.5% on Grace when idle), but this needs to be done for each type of hardware and at various load levels. IPMI accuracy / usefulness will vary from one type of host to another. There will likely not be a general rule, which we knew. These are preliminary results, and there is work to be done here.
* Our Eclipse test nodes exhibit significant variation when idle which makes characterisation tricky. Grace is much more consistent. This could be due to relative price point of the hardware, i.e. cheap PSUs in the Eclipse boxes?
Worthy of further consideration: powering a node down will reduce power dissipation, but can totally mess with your PF, presumably as PF correction in the PSUs is ineffective / inactive when only minimal power is supplied. Will have to correct elsewhere to keep utility suppliers happy.

## Slide 16
Milk-V Pioneer : Single socket RISC-V 64-Core Processor (Milk-V) CPU: SOPHON SG2042 (64 Core C920, RVV 0.71) riscv64 @ 2GHz (TDP 120W) RAM: 128GB (4 x 32GB) DDR4 3600 MT/s  2 GB/core HDD: 1TB PCIe 3.0 NVMe OS: Fedora 38
RISC-V testing
Progress: - We managed to compile and install ROOT, CVMFS and XRootD by building locally from source:
  ROOT: https://github.com/hahnjo/root.git (RISC-V ported version)
  CVMFS: https://github.com/cvmfs/cvmfs.git (original Git)
  XRootD: https://github.com/xrootd/xrootd (original Git)
- Tommaso (INFN) managed to compile and run Geant4, also by building from source:
  Geant4: https://gitlab.cern.ch/geant4/geant4 (original Git)
- Muzafar (CMS) made some progress in porting the CMSSW framework to RISC-V: most code can be ported, major issues are PyTorch & TensorFlow compatibility.
We have acquired a RISC-V desktop PC and started experimenting with it:
Main motivations:
- Open-source and royalty-free architecture,
- Extremely low power usage (140 Watts @ full load - 64 cores),
- Growing ecosystem and potential for fast innovation (e.g., EPI will build on RISC-V).
Notes: European Processor Initiative (EPI):
https://en.wikipedia.org/wiki/European_Processor_Initiative
https://www.european-processor-initiative.eu/
Here's a quick list of key motivations for adopting RISC-V architecture:
Open-source and royalty-free
Customizable and extensible
Lower power consumption
Reduced costs
Independence from proprietary architectures
Scalability across different applications
Growing ecosystem and community support
Potential for faster innovation
Alignment with European Processor Initiative (EPI)
Simplified licensing and compliance

## Slide 17
RISC Results (preliminary)
We could run ROOT tests, ROOT benchmarks, and DB12 on RISC and few other architectures.
Results are a bit tricky to compare, because not all machines can run all benchmarks …
So far, DB12 is the only benchmark that could run on all hardware !
Work in Progress
Notes: ROOT: https://github.com/hahnjo/root.git
CVMFS: https://github.com/cvmfs/cvmfs.git
XRootD: https://github.com/xrootd/xrootd
Geant4: https://gitlab.cern.ch/geant4/geant4
DB12: https://github.com/DIRACGrid/DB12 HEP-Score: https://gitlab.cern.ch/hep-benchmarks/hep-score
indeed … RISC-V does not seem that good when compared to other chips, but its main selling point is the low power usage!

## Slide 18
Upcoming Conferences
Talks accepted at CHEP (Krakow, October 2024)
Simulating the Carbon Cost of Grid Sites
Main Authors: David Britton; Steve Lloyd
Comparative efficiency of HEP codes across languages and architectures Main Author: Samuel Cadellin Skipsey
Heterogeneous Computing and Power Efficiency in HEP
Main Author: Emanuele Simili
Taking on RISC for Energy-Efficient Computing in HEP
Main Authors: Emanuele Simili; Tommaso Boccali; Shazad Muzafar
On-Grid GPU development via interactive HTCondor jobs and Analysis Facility style workflows
Main Author: Albert Gyorgy Borbely
Contributions at the HTCondor Workshop (NIKHEF, September 2024)
(titles to be defined)
Main Authors: Emanuele Simili & Albert Borbely
Notes: output

## Slide 19
Outlook
Improve on the methodology and develop an Analysis framework: - energy measurement is now integrated in HEP-Score - HEP-Score analysis package (HEPiX summer student is studying aggregation metrics, e.g., k-mean: https://indico.cern.ch/event/1433496/)
Follow up on RISC-V updates and integration: - Actively participate in the testing and benchmarking cycle - Look into new hardware solutions (RISC servers?)
Keep exploring new hardware: - benchmark GPU+CPU using Celeritas (Bruno) - test the newly released AmpereOne … - what’s next?
Notes: outlook

## Slide 20
end
Emanuele Simili GridPP52 Ambleside - 29 August 2024
Notes: end

## Slide 21
- Major work undertaken at your site since last GridPP meeting (April to July 24)​
- Added 2,304 Ampere Altra Max M128-30 cores​
- Migrated to EL9 and HTCondor 10​
- set-up a heterogeneous endpoint with dual queue (ARM & x86)
2 - Key problems faced and resolved during this time. ​
- dealing with a dual queue is tricky, and not all VOs can cope with it
​
3 - Pending issues and plans for resolving the existing issues. ​
- Upgrades to ARC 7 and latest version of HTCondor​
​
4 - Projection of resource availability for next year, will there be any change in the capacity and how much ​
- No significant change expected
Notes: Glasgow updates

## Slide 22
What Watt
New Figure of Merit (FoM), i.e., the best proxy of power usage for standard HEP workloads:
FoM should be easy to implement, we could fit this peak, but there are other ways of doing it.
Arrange the data in power order and perform an upper quaRtile average, but removing the top 5% of data
2*AMD64ht
<75-95%> Blue line sits nicely in the plateau
Modal power also sits in the plateau – but we found edge cases where this breaks (e.g., Grace has a very steady idle state)
*
75-95% quaNtile
average
Notes: Wordy explanation/motivation: Neither the Max nor the Average power is the best way of characterizing the performance. The Max can be exaggerated by significant 'spikes' that can momentarily be higher than the plateau; the average is suppressed by the low-power start-up phase that can extend to 20% of the run-time for the short jobs in the HEP-Score suite. Thus, using Max power will underestimate HEP-Score/Watt and using Average power will overestimate HEP-Score/Watt. Instead, we propose to use the average power calculated from the 75-95% quaNtile. The upper quartile eliminates most of the start-up phase that would be over-emphasized by short benchmarking jobs, while the cut of the highest 5% prevents power spikes to have any significant effect.
The result is relatively insensitive to the shape of the distribution and well fits the upper plateau in the power drain plots, while giving less importance to the start-up phase and to isolated spikes in power. It can be noted that the modal power itself (the mode of the power distribution, corresponding to the most common power-draw) is a good estimate for single workloads, but not for the combination of different workloads in the HEP-Score suite that can have different power draws.

## Slide 23
HEPscore/Watt (comparing old & new )
removed for consistency
Notes: … to better understand the HEP-Score/Watt graph: the ranking slightly changed with the new definition power F.o.M.
Also confirmed by the Frequency Scan: the HEP-Score shown here corresponds to the last data point in the frequency plot (i.e., the highest frequency set).

## Slide 24
ARM + x86 Farm @ Glasgow
Job submission chain @ ScotGrid Glasgow:
Condor10
~17000
~ 4000
Notes: Dwayne’s

## Slide 25
Results^ (preliminary)
We could run ROOT tests, ROOT benchmarks, and DB12 … results are a bit tricky to compare, because not all machines can run all benchmarks …
So far, DB12 is the only benchmark that can run on all hardware !
Notes: ROOT: https://github.com/hahnjo/root.git
CVMFS: https://github.com/cvmfs/cvmfs.git
XRootD: https://github.com/xrootd/xrootd
Geant4: https://gitlab.cern.ch/geant4/geant4
DB12: https://github.com/DIRACGrid/DB12 HEP-Score: https://gitlab.cern.ch/hep-benchmarks/hep-score

## Slide 26
Notes: …