## Slide 1: Progress on the EDIPO 2 test facility (Sat-Af-Or1-03)
X. Sarasola,
P. Bruzzone,
N. Bykovskiy,
J. Greenwood,
T. Nes, K. Sedlak
July 5th, 2025

## Slide 2: Motivation and design targets
 | SULTAN (SPC) | EDIPO (SPC) | FRESCA2 (CERN) | EDIPO 2 | Units
Bcenter aperture | 10.9 | 12.35 | 13 (14.6) | 15 | T
Aperture size | 94×144 | 90×141 | Ø100 | 144×144 | mm
Homogeneous field length (1%) | 320 | 680 | 650 | 900 | mm
Sample current | ≤100 | ≤100 | ≤ 32 (50) | >100 | kA
Sample operating temperature | 4.5 to 50 | 4.5 to 50 | 1.9 & 4.2 | 4.5 to 50 | K
SULTAN has been pivotal in qualifying forced-flow conductors in the last three decades.
Rising demand towards:
  High current conductors (beyond 100 kA)
  Conductors for high field magnets (partly driven by the development of HTS)
EDIPO 2 will enhance the background B field and the aperture size while keeping attractive features from SULTAN and EDIPO
Since January 2025, the ETH board (ERI dispatch) funds the construction of EDIPO 2 (as part of the Swiss Fusion Hub)

## Slide 3: Conceptual design of the EDIPO 2 magnet
Dipole based on two pairs of planar racetrack coils:
  Bath cooled (4.2 K), high jeng winding pack (as opposed to SULTAN and EDIPO1)
  Operating current ≤ 18 kA (limited by existing power supply)
    It requires a large cross-section of superconductor
  There is no 3D transition in the coil ends:
    No hardway bending → Presumably no performance limitation in the ends region
    Simplifies manufacturing
    Simplifies management of mechanical stress

## Slide 4: Cable design
Nb3Sn high-jc strand:
  jc,nc ≥ 2600 A/mm2 at 12 T and 4.2 K, 0.7 mm diam, Cu:nCu = 1.0
  Two procurements from Bruker:
    ~110 kg for the prototype cabling (delivered in Dec 2023)
    1.6 tons for the production of the magnet (expected delivery in Jan 2026)
Cable based on a flat two-stage design: 24×(6+1), 0.7 mm
  Cabling R&D activities (copper dummy):
    Two industrial partners + CERN were qualified in 2024 to produce this cable
  Nb3Sn prototype cable:
    Production of 150 m at WST (expected delivery in Q3 2025)
  Nb3Sn production cable:
    Call for tender to be launched in Q4 2025

## Slide 5: Magnetostatic 3D analysis
 | Iop = 0.85×Iss | Iop = Imax | 
Cable layout | 24×(6+1), 0.7 mm diam |  | 
Number of turns | Side coils: 2×6×16 Vertical coils: 2×4×46 |  | 
Total number of turns, ntotal | 560 |  | 
Total area of insulated conductor | 52886 |  | mm2
Operating current, Iop | 17.438 (85%×Iss) | 18.00 (87.7%×Iss) | kA
B field in the center of the aperture, B0 | 14.99 | 15.43 | T
Peak B field in the coils, Bpeak | 15.03 | 15.47 | T
Total ampere-turns, Itotal | 9.77 | 10.08 | MAt
Total magnet stored energy, Etotal | 20.8 | 22.1 | MJ
Magnet self-inductance, L | 136.5 |  | mH
Engineering current density, jeng | 184.6 | 190.6 | A/mm2
Copper current density, jCu | 523.3 | 540.1 | A/mm2
B field in the magnet
B field in the winding pack
Iop = 0.85×Iss
https://doi.org/10.1109/TASC.2025.3526109

## Slide 6: 3D quench analysis
[W/m3]
 56’000 nodes to evaluate heat propagation in 3-D (560 turns x 100 nodes per turn)
Protection scheme based exclusively on energy extraction:
  Assumed delay time: 100 ms
  Vmax = ±0.9 kV (assuming symmetric grounding)
  Tmax = 280 K for the operation at 18 kA and Vth = 0.1 V detection threshold
(Poster by T. Nes, Fri-Af-Po.02-04)
Hot spot temperature [K]
Time [s]
Coil terminal voltage [kV]
Time [s]

## Slide 7: Mechanical 3D analysis
Coils assembled in a steel casing
Lorentz forces reacted by the casing and a 30-mm-thick steel shell
Vertical coils are preloaded to maintain stress/strain within allowable limits
Side coils cannot be preloaded. During operation:
  They detach from the poles
  The test well is stress-free
Deformation during operation
Longitudinal cross-section
Transversal cross-section

## Slide 8: Mechanical 3D analysis
Vertical coils at B = 15 T
Side coils at B = 15 T
von Misses stress
von Misses stress
Longitudinal strain
Longitudinal strain
https://doi.org/10.1109/TASC.2025.3526109
    εL ranging from -0.04 and +0.08%.
    σeq ≤ 78 MPa
    σeq ≤ 136 MPa
    εL ranging from -0.2 and +0.16%.
(Poster by X. Sarasola, Sat-Mo-Po.03-03)

## Slide 9: Magnet R&D activities and manufacturing design
Goal: de-risk technologies associated with the EDIPO2 magnet design
Contract recently signed with ASG (completion by the end of 2026)
Cable and subscale coil tests planned in SULTAN in 2026:
  Nb3Sn cable and joints
  Subscale coil (pancake transitions and detachable poles)

## Slide 10: Cooling / Cryogenics
EDIPO 1 was based on a CICC design (cooled by a forced-flow of supercritical He)
The EDIPO 2 magnet will be bath-cooled at 4.2 K
  Volume: ~100 l
New helium vessel
https://doi.org/10.1016/j.cryogenics.2023.103648
Modified cryogenic circuit (preliminary)
(Poster by T. Nes, Thu-Af-Po.10-04)

## Slide 11: Conclusions and Outlook
EDIPO 2 will generate a background field of 15 T in a large aperture (144×144 mm2)
Use of a Nb3Sn two-stage cable design for high operating current
Dipole purely based on the use of planar racetrack coils:
  No hardway bending
  Simplification of the coil manufacturing
  The vertical coils are pre-loaded, but not the side coils
Outlook:
  Ongoing industrial contracts:
    High-jc Nb3Sn wire: procurement of 1.6 tons (delivery in Jan 2026)
    Cable:
      Production of 150 m of Nb3Sn prototype cable (delivery in Q3 2025)
      Call for tender for the magnet production cable to be launched in Q4 2025
    Magnet R&D activities (completion by the end of 2026):
      Including production of a subscale coil and test in SULTAN
    Magnet manufacturing design (completion by the end of 2026)
  Modify the EDIPO2 cryogenic circuit.

## Slide 12
Thanks for your attention!