## Slide 1: Exploring Hybrid Designs for a 14 T Common Coil Demonstrator Magnet (DAISY)
J.A. García-Matos, C. Martins, F. Toral (CIEMAT)
J.C. Pérez, E. Todesco (CERN)

## Slide 2
CIEMAT’s contribution to the HFM program.
14 T prototype magnet based on common coil topology.
It honors Margarita Salas [1].
Previous study (ASC24) [2]:
Several designs evaluated with a fixed iron geometry at 1.9 K (limited field quality).
Promising results using NbTi for the low field region (LHC main dipole inner layer strand).
[1] PUM! estudio, “Margarita Salas: The legacy of a lifetime devoted to science,” Fundación Margarita Salas. Accessed: Jul. 10, 2024. [Online]. Available: https://fundacionmargaritasalas.com/en/margarita-salas-en/
[2] J. Á. García-Matos, C. M. Jardim, F. Toral, J. C. Perez, and E. Todesco, “Magnetic Design of a 14 T Common Coil Demonstrator Magnet (DAISY),” IEEE Transactions on Applied Superconductivity, vol. 35, no. 5, Art. no. 4002605, Aug. 2025, doi: 10.1109/TASC.2025.3537069.
  Feasible!
  Better superconductor usage!

## Slide 3
The use of NbTi instead of Nb3Sn in a hybrid dipole:
Decrease superconductor material cost.
Reduce coil fabrication complexity: easier handling, no reaction, not so easy to degrade.
Potentially decrease of AC losses and magnetic instabilities.
Main goals:
Explore hybrid designs with accelerator-like features: Field quality, low multipole variation, efficiency.
Compare with pure Nb3Sn reference and accelerator-like designs to determine if they keep being cost-effective.
Strands | ERMC-1 | MBINL*
Material | NB3Sn | NbTi
Diameter [mm] | 1 | 1.2
Cu / Non Cu ratio | 0.9 | 1
Cu Area per strand [mm2] | 0.37 | 0.57
*NbTi strand hypothesis (Suppliers consults ongoing)
Hybrid common coil:
a cost-effective solution for FCC-hh
Parameter | Value | Units
Operational field target | 14 | T
Free aperture diameter | 50 | mm
b3 / a2 | <10 | units
Other multipoles | <1 | units
Multipole variation from injection | <30 | units
Intrabeam distance | 320 | Mm
Straight section length | 0.5 | M
Magnetic length | 0.8 | M
Physical length | ≈1 | m
Outer diameter | <800 | mm
Load (1.9 K) | 80 | %
Operating temperature | 1.9 | K
Non-Cu Jc (16 T, 4.22 K) | 1200 | A/mm2
Jo | 350-600 | A/mm2
Equivalent coil width | 50-55 | mm
Protection system | Dump resistor | mΩ
Protection time margin | 40 | ms
Max. voltage | 1000 | V

## Slide 4
Tailored Genetic Algorithm (GA) + RoxieApi:
More flexibility and control over the algorithm behavior.
Deeper insights during the solving process.
Inclusion of variables not computed by Roxie.
Interdependencies between input variables.
Methodology
Weighting the GA fitness function :
EQW
FQ
LOAD
QH
Optimal design
Equivalent width (EQW): Tends to adapt the coil shape for the better contribution of each strand to B1, decreasing turns and strands per cable.
Field quality (FQ): Tends to use a lot of superconductor and produce tall coils (less strands, more turns).
Quench performance (QH): Penalizing JCu avoid using fewer strands than necessary, controlling hot spot temperature.
Load requirement (LOAD): Usually tends to use more strands than necessary. It is the easier to manually tune later.

## Slide 5
REF1: Minimum amount of superconductor
REF1 will be our reference model:
No good field quality: solid coil blocks.
Large multipole variation with the current: iron close to aperture.
But… Maximum superconductor efficiency.
*All models for 320 mm of intrabeam distance and 14T in a 50 mm aperture

## Slide 6
*All models for 320 mm of intrabeam distance and 14T in a 50 mm aperture
REF2: Low multipole variation with the current
*All models for 320 mm of intrabeam distance and 14T in a 50 mm aperture
REF2 is an intermediate step:
Better field quality, but not good enough: 10 mm midplane gap at high field coil.
Sextupole variation is decreased by placing the iron further from the aperture.
55 mm coil equiv. width: 13% more Nb3Sn
Next step is to improve field quality.

## Slide 7
Midplane region → B1 and B3
B3 contribution ↓ 1/r3
Usual approach: placing ancillary coils in the highlighted areas.
Upper region discarded to avoid non-planar coils.
Maximum contribution (+)
Null contribution (0)
Minimum contribution (-)
Dealing with a large sextupole in a common coil magnet

## Slide 8
*All models for 320 mm of intrabeam distance and 14T in a 50 mm aperture
SN0: exploring the asymmetric field quality coil (I)
SN0 try to use asymmetric common coil design as proposed by PSI on SMACC1 [3]:
Sextupole and its variation are decreased.
63 mm coil equiv. width: 42% more Nb3Sn.
Inefficient for DAISY. Why?
[3] D. Araujo, B. Auchmann, A. Brem, T. Michlmayr, A. Haziot, and E. Ravaioli, “Electromechanical Design of Nb3Sn Stress Managed Asymmetric Common-Coils,” IEEE Trans. Appl. Supercond., vol. 35, no. 5, pp. 1–5, Aug. 2025, doi: 10.1109/TASC.2025.3532906.

## Slide 9
SN0: exploring the asymmetric field quality coil (II)
Mechanics!! This additional coil is pushed towards the aperture. Some gap for support is required.
Few strands hit the maximum B3 contribution region.
Fy
Fy
Low contribution to B1.
Wide cables get close to the vertical axis : high peak field/load low efficiency.
Fy
Sextupole can be compensated but the midplane gap is still large, losing efficiency.
A more efficient approach is required to decrease the sextupole in DAISY.

## Slide 10
Dealing with a large sextupole: What if…?
…we move the lower turns of the high field coil towards aperture?

## Slide 11
…we move the lower turns of the high field coil towards aperture?
Single or double layer additional “Field quality” coil.
More efficient sextupole compensation.
Better contribution to B1 (gap further from the aperture).
A casing could hold the electromagnetic forces + partial support from the other coils.
Dealing with a large sextupole: What if…?
SN1
SN2
Fy
Fy

## Slide 12
Comparing pure Nb3Sn models
*All models for 320 mm of intrabeam distance and 14T in a 50 mm aperture
Displacing the lower turns of high field coil is more efficient than the original asymmetric case (SN0) for DAISY.
59 mm coil equiv. width: 27% more Nb3Sn, instead of 42%.

## Slide 13
Comparing hybrid models with pure Nb3Sn ones
Accelerator-like features.
Less efficient in equiv. coil width but large Nb3Sn savings.
Temperature margin at NbTi is around 2K, more than current LHC main dipoles (1.4K).
NbTi
NbTi
*All models for 320 mm of intrabeam distance and 14T in a 50 mm aperture

## Slide 14
Conclusions
CIEMAT is actively contributing to the HFM Programme through the development of common coil magnet designs.
We have obtained promising results for hybrid magnets combining Nb₃Sn and NbTi coils.
Accelerator-like 14 T magnets appear feasible, using NbTi in the low-field region, pointing toward a viable path for cost-effective solutions.
While challenges remain, such as mechanical support or long magnet protection, the hybrid approach shows strong potential moving forward.
Our first demonstrator, DAISY, will focus on validating hybrid magnet mechanics in a common coil configuration, without targeting full accelerator-grade field quality in the initial phase.
In the next step, we aim to develop a hybrid common coil magnet that meets full accelerator field quality requirements, building on the foundation laid by DAISY.

## Slide 15
Extra slides

## Slide 16
[1] M. Bonora, ‘Interfacing with ROXIE: Scripting, Python, and Model Based Design’, presented at the ROXIE Users Workshop: ROXIE 23 Launch Event, Accessed: Jan. 23, 2024. [Online]. Available: https://indico.cern.ch/event/1318061/contributions/5574693/attachments/2711597/4708647/interfacing_roxie.pdf
[2] T. Salmi et al., ‘Quench protection analysis integrated in the design of dipoles for the Future Circular Collider’, Phys. Rev. Accel. Beams, vol. 20, no. 3, p. 032401, Mar. 2017, doi: 10.1103/PhysRevAccelBeams.20.032401.
Input data
Manual tuning of the model
Script #1
Roxie23 environment
model.output
model_induc.output
Compute quench and retrieve results
Coherent cable libraries
Quench computation [5]
Results
Script #2
Model
comparison
Stop
Roxie23
(RoxieAPI [4])
Genetic Algorithm
(in-house development)
Optimal design results & plots
Start
Tuning the GA fitness function
Equivalent width (EQW): Tends to adapt the coil shape for the better contribution of each strand to the main field, decreasing turns and strands per cable.
Field quality (FQ): Tends to use a lot of superconductor and makes the coils tall (less strands, more turns).
Quench performance (QH): Penalizing Jcu avoid using fewer strands than necessary, therefore, controlling hot spot temperature.
Load requirement (LOAD): Usually tends to use more strands than necessary. It is the easier to manually tune later.
EQW
FQ
LOAD
QH
Optimal design
[4] M. Bonora, ‘Interfacing with ROXIE: Scripting, Python, and Model Based Design’, presented at the ROXIE Users Workshop: ROXIE 23 Launch Event, Accessed: Jan. 23, 2024. [Online]. Available: https://indico.cern.ch/event/1318061/contributions/5574693/attachments/2711597/4708647/interfacing_roxie.pdf
[5] T. Salmi et al., ‘Quench protection analysis integrated in the design of dipoles for the Future Circular Collider’, Phys. Rev. Accel. Beams, vol. 20, no. 3, p. 032401, Mar. 2017, doi: 10.1103/PhysRevAccelBeams.20.032401.