## Slide 1
Upgrades and initial weathering test results of the liquefied natural gas testbed at NASA Kennedy Space Center
Adam Swanger1, Mai Harrison2, Andrew Kelly1, Julie Foroosh1, and Will Reaves3
  1NASA Kennedy Space Center, Cryogenics Test Laboratory, KSC, FL 32899 USA
  2Astrion LASSO2, Kennedy Space Center, Cryogenics Test laboratory, KSC, FL 32899 USA
  3Noetic Strategies LASSO2, Kennedy Space Center, Cryogenics Test laboratory, KSC, FL 32899 USA
Cryogenic Engineering Conference
Wednesday May 21st, 2025
C3Or4A-01

## Slide 2
INTRODUCTION
2
Historically, only liquid hydrogen (LH2) and kerosene (RP1) have been used as rocket fuels
Recently, Blue Origin, ULA, and SpaceX have all switched to liquefied natural gas (LNG) or “liquid methane”
Image: Blue Origin
Image: NASA
Image: NASA

## Slide 3
INTRODUCTION
3
Unlike LH2 and RP1, LNG is susceptible to “weathering”
  Weathering = preferential evaporation of lower boiling point constituents over time, leading to a change in the bulk liquid composition
Image: NASA
Typical operation of cryogenic storage tanks at launch pads is problematic
  Long delays between launches historically → propellants sit idle in storage tanks for long durations, with the boiloff vented to atmosphere
Image: NASA
Weathering of LNG could affect engine performance or cause a violation of launch commit criteria

## Slide 4
LNG Testbed — phase 1
4
In 2017, Cryogenics Test Lab at NASA Kennedy Space Center began building an LNG test capability to examine weathering and other storage-related topics
Image: NASA
Testbed Configuration
400 L dewar (repurposed)
New top plug assembly
Vertical probe with five sample tubes at 0%, 25,%, 50%,75%, and 100% fill levels
Five corresponding RTD temp sensors
MKS Precisive® 5 gas analyzer
Integrated coldhead
Images: NASA

## Slide 5
LNG Testbed — phase 1
5
A single LNG weathering test was conducted in 2019 on the original testbed setup
Image: NASA
Good results, but much room for improvement!
  Completely manual
  Course compositional data
  No boiloff data
  Finicky pressure control
System was mothballed after 2019

## Slide 6
LNG Testbed — phase 2
6
In 2022, NASA Rocket Propulsion Test (RPT) program funded effort to resurrect the system, make improvements, and conduct more testing
Image: NASA
Testbed Upgrades
100% automated sampling
Boiloff mass flow meter
Load cells
Additional vertical temperature sensors
Precise tank pressure control

## Slide 7
LNG Testbed — phase 2
7
Image: NASA
Chill-Down & Boiloff Vent Stacks
Mass Flow Meter & Back Pressure Regulator
Unclassified Electrical Equipment
4.6 m
Vertical Probe Assembly
RTDs
1.6 mm Diameter Sample Tubes
G-10
C-Channel
Top Plug Assembly
Images: NASA

## Slide 8
LNG Testbed — phase 2
8
Two more LNG weathering tests conducted in 2024-2025
LNG provided by Pivotal LNG out of
Jacksonville, Florida
Constituent | Tanker #1 | Tanker #2
Methane | 96.058% | 96.874%
Ethane | 3.772% | 2.723%
Propane | 0.170% | 0.176%
Isobutane | 0% | 0.030%
Nitrogen | 0% | 0.197%
Total | 100% | 100%
System outperformed expectations!
  Virtually flawless data collection
  100% automated sampling every 30 min
  Boths tests ran for roughly 46 days
Image: NASA

## Slide 9
LNG Testbed — phase 2 Results
9
Tank pressure control to ±1.45 kPa on average for both test runs
Minimal thermal stratification in the liquid
Image: NASA
Subcooled for first ~6 days due to prechilling tank with liquid nitrogen before LNG offload

## Slide 10
LNG Testbed — phase 2 Results
10
Weathering is nonlinear
Boiloff gas is ~100% methane for most of the test
  Not 100% for Run #1 due to gas analyzer calibration
  Re-zeroed for Run #2
Abrupt methane-to-ethane boiloff transition late in the process
Run #2 took ~6 days longer to completely boiloff
Image: NASA

## Slide 11
LNG Testbed — phase 2 Results
11
Run #2 boiloff reduction likely due to lower ambient temperature in the winter months
Average heat load on the system = 22.1 ± 2 W across all tests
Boiloff drops dramatically following methane-to-ethane boiloff transition, and then recovers
Image: NASA

## Slide 12
Current status & forward work
12
System currently in a stand-by configuration, awaiting further funding
Plans are being prepared for additional testing, with a focus on three primary goals:
  Zero boiloff (ZBO) testing using the cryocooler
  Weathering with LNG refills at partial fill levels
  Weathering with refills following LNG flows out of the tank.
Image: NASA

## Slide 13
13
THANK YOU FOR YOUR ATTENTION!
QUESTIONS?