## Slide 1: Lumped-Element Modeling of Density Wave Oscillations in Two-Phase Hydrogen Flows
C1Or4A-05
Trinity Templeton, Professor Konstantin Matveev, and Professor Jacob Leachman
Cryogenic Engineering Conference
Reno, Nevada
May 19th, 2025
Flow Boiling and Instabilities in Cryogenic Systems
Density Wave Oscillations
Modeling
Validation of the Stability Boundary for Freon-113 and Liquid Nitrogen
Liquid Hydrogen Results
Future Work and Conclusions

## Slide 2: Flow Boiling in Cryogenic Systems
Two-phase flow instabilities occur in cryogenic flow boiling systems.
Vapor generation causes instabilities due to density differences between liquid and vapor states
Can damage equipment
High heat input to a cryogenic system causes flow boiling.
Transfer line chill in
Cryogenic flow evaporators
Rocket engines
To scale up cryogenic systems two-phase flow instabilities must be prevented and understood.
Component design
Fueling stations
Flow evaporators

## Slide 3: Two-Phase Flow Instabilities
Two-phase flow
Heat
Liquid
flow
Inlet flow
Boiling boundary
Z
0
d
Density wave oscillations.
Dynamic instability
Studied heavily for boiling water reactors
Limited data for cryogenic applications
Typical system for density wave oscillation analysis found in literature.
Inlet mass flux, boiling boundary, and exit quality fluctuate in time.

## Slide 4: Density Wave Oscillation Mechanism
2
3
2  3
Inlet mass flux passes maximum and begins decreasing
Boiling boundary and pressure continue increasing
Inertia of single-phase causes continued rise in inlet mass flux and pressure
State 3:
Maximum boiling boundary
Maximum pressure
Inlet mass flux is decreasing
1
State 2:
Inlet mass flux, boiling boundary, and pressure increasing coming closer to the maximum value
1  2
Increase in mass flux causes boiling boundary to move upwards
Shift in boiling boundary increases pressure by compressing two-phase flow
State 1:
Minimum boiling boundary
Minimum pressure
Inlet mass flux is increasing
1
2
3

## Slide 5: Partial Differential Equations
Assumptions:
One-dimensional homogeneous flow
Overall system pressure drop is constant
Fixed fluid properties at the inlet
Sub-cooled boiling neglected
Constant wall heat input
[1] Papini D, Cammi A, Colombo M, and Ricotti M E 2012 Chemical engineering science 81 118-39
Mass
Energy
Momentum
Z
0
Q
G
Mass Flux

## Slide 6: Reduced Order Model
Ordinary differential equations:
Functions of boiling boundary (), exit quality (), and inlet mass flux ()
and are modeling constants
Partial differential equations integrated in the spatial domain to become functions of time.
Model implementation:
MATLAB
Explicit temporal finite differencing of , , and
Z
0
= Constant
Q
[1] Papini D, Cammi A, Colombo M, and Ricotti M E 2012 Chemical engineering science 81 118-39

## Slide 7: Pressure Drop Terms
Accelerative pressure drop:
Only considered in the two-phase region
Due to the pressure associated with the inertia of the multi-phase region
Gravitational pressure drop:
Considered in the single-phase and two-phase regions
Pressure drop caused by gravitational forces on the fluid
Frictional pressure drop:
Considered in the single-phase and two-phase regions
Pressure drop associated with the friction between the pipe and fluid as well as the friction between the vapor and liquid phases
is the two-phase friction factor
Z
0
= Constant
Q
[1] Papini D, Cammi A, Colombo M, and Ricotti M E 2012 Chemical engineering science 81 118-39

## Slide 8: Validation of Stability Boundary for Freon-113
Approximate agreement between experimental and modeling data.
Experimental and modeling data for Freon-113.
Investigates multiple two-phase friction factors.
Characteristic L shape is present.
Lockhart-Martinell friction factor was selected due to lowest margin of error (~25%)
is influenced by inlet enthalpy which is dictated by inlet temperature.
is influenced by the ratio between heat input and inlet mass flux.
[2] Saha P 1974 Thermally induced two-phase flow instabilities, including the effect of thermal non-equilibrium between the phases
PhD Thesis Georgia Institute of Technology
[3] Friedel L 1979 European Two-Phase Flow Group Meeting
[4] Lockhart W R 1949 Chemical engineering progress 45(1) 39-48
[5] Martinelli R T and Nelson D B 1948 Transactions of the American Society of Mechanical Engineers 70(6) 695-702
[6] Todreas N E and Kazimi M S 2011 Nuclear Systems I: Thermal Hydraulic Fundamentals (Boca Raton: Taylor & Francis)
* sub = subcooling
* pch = phase change

## Slide 9: Validation of Stability Boundary for Liquid Nitrogen
Z
0
= Constant
Q
 | Case 1: | Case 2: | Case 3: | Case 4: ,
Experimental q |  |  |  | 
Model q |  |  |  | 
% deviation |  |  |  | 
Experimental q |  |  |  | 
Model q |  |  |  | 
% deviation |  |  |  | 
Experimental and modeling data using the Lockhart-Martinelli friction factor for liquid nitrogen.
Model underpredicts experimental results by ~25%.
Cases with larger inlet resistance coefficient have a larger % deviation.
Approximate agreement between the experimental and modeling data.
[7] Ozawa M, Asao Y, and Takenaka N 1993 Instabilities in Multiphase Flows (Boston: Springer)

## Slide 10: Transient Response: Limit Cycle Oscillations
Fluid | Mean pressure () | Mean velocity () | Tube length (L) | Diameter (d) | Inlet resistance coefficient () | Outlet resistance coefficient () | Heat input (Q)
Liquid hydrogen | 3 [bar] | 1 [m/s] | 1 [m] | 1 [cm] | 1 | 1 | Variable
Fluid |  |  | Tube length (L) | Diameter (d) |  |  | Heat input (Q)
Liquid hydrogen | 3 [bar] | 1 [m/s] | 1 [m] | 1 [cm] | 1 | 1 | Variable
Z
0
= Constant
Q

## Slide 11: Transient Response: Limit Cycle Oscillations
Provide a small perturbation of the system pressure to induce fluctuations.
Limit cycle oscillations neither grow nor decay in time.
Single-phase and two-phase pressure drop are out of phase.
Limit cycle oscillations are present from 585 W – 639 W.
Amplitude of the limit cycle oscillations for several parameters increases with heat input.
Q = 590 W
Q = 590 W

## Slide 12: Liquid Hydrogen Stability Boundary Study
Stable
Unstable
is influenced by inlet enthalpy which is dictated by inlet temperature.
is influenced by the ratio between heat input and inlet mass flux.
Unstable
Stable
* sub = subcooling
* pch = phase change

## Slide 13: Liquid Hydrogen Stability Boundary Study
Increasing and mean pressure stabilizes the system.
Increasing and decreasing mean velocity destabilizes the system.
Increasing mean pressure allows for more heat input, discrepancy is caused by the influence of the specific volume of vapor in the term.
Default Case: |  |  |  | 
 | 3 bar | 1 m/s | 1 | 1
Default Case: |  |  |  | 
 | 3 bar | 1 m/s | 1 | 1
Stable
Unstable
Unstable
Stable

## Slide 14: Conclusions and Future Work
Conclusions:
Understanding density wave oscillations is critical for liquid hydrogen systems
Reduced order modeling can provide insights into density wave oscillation behavior
Stabilize a system by increasing and mean pressure while decreasing and mean velocity
Future work:
Higher fidelity modeling
Modeling of higher complexity systems
Exploration of different modeling correlations
Exploring the influence of additional two-phase flow instabilities
Experimental work

## Slide 15: Thank You!
Trinity Templeton
trinity.templeton@wsu.edu
+1 541 480 3679