## Slide 1
General Information
FCC-ee Optics Design Meeting #188 & 57th FCCIS WP2.2 meeting, 10 July 2024
1
Frank Zimmermann

## Slide 2
MTR recommendations on FCC-ee machine
well-defined baseline layout for entire FCC-ee, including optimised e+e- injector, especially the linac
clarify order of the energy stages, with motivation for running order linked explicitly to the physics case
consolidate design of the RF system to allow efficient energy-staging, as well as to reduce complexity, risk, and cost; study options to avoid the 1-cell/2-cell RF cavity reconfiguration between Z and ZH/WW running
alternative beam optics, to improve the dynamic aperture with relaxed mechanical alignment tolerances
develop survey and alignment techniques, procedures and instrumentation, to guarantee the alignment of magnets [on the girder] to 50 mm at 1 s; develop and apply, in simulations, the whole set of beam-based correction techniques
identify residual risks to achieving the design luminosity, with lessons to be learnt from other facilities like SuperKEKB, and specify required further critical-path R&D
from FCC SAC, FCC CRP, CERN SPC, and CERN FC

## Slide 3: FCC-ee baseline RF configuration so far
1-cell Nb/Cu
1-cell Nb/Cu
2-cell Nb/Cu
addt’l 5- or 6-cell bulk Nb cavities
O. Brunner
Z
W, H
ttbar,
booster
low R/Q, HOM damping, powered by 1 MW RF coupler and high efficiency klystron
moderate gradient and HOM damping requirements; 500 kW / cavity, allowing reuse of klystrons already installed for Z
high RF voltage and limited footprint thanks to multicell cavities and higher RF frequency; 200 kW/ cavity
  1-cell
  400 MHz,
  Nb/Cu
  2-cell
  400 MHz,
  Nb/Cu
  5-cell
  800 MHz,
  bulk Nb
F. Peauger,
O. Brunner

## Slide 4
Input RF power for optimum detuning
Need for adjustable/variable fundamental power coupler with wide range of coupling (2 orders of magnitude)
Presence of 0-mode requires additional longitudinal feedback Transverse feedback needed
40%-increase of HOM power / cryomodule → “2-coax concept”
I. Karpov, R. Calaga, E. Montesinos, S. Zadeh, F. Peauger, O. Brunner
A 2-cell 400 MHz SRF cavity for all energies ?

## Slide 5: Solution for FCC-ee simplified RF system !
2-cell for all energies
Reverse phase operation (RPO)  higher RF cavity voltage (Y. Morita et al., SRF, 2009)
Experimentally verified with high beam loading in KEKB (Y. Morita et al., IPAC, 2010)
Baseline solution for EIC ESR (e.g., J. Guo et al., IPAC, 2022)
T. Abe et al., PTEP, 2013
KEKB HER synchrotron tune measured for several SC cavity configurations. RPO “(7 - 1)” case with1.56 MV/cavity yielded about the same fs as for 8 in-phase cavities with 1.18 MV/cavity [T. Abe et al., 2013]
 RPO potentially allows same optimal quality factor for Z, W, and H modes
Advantages:
Rationalize RF resources during the development process (3 → 2 cavity types)
Simplify, shorten the installation sequence (no cryo-module removal)
Great flexibility in physics running modes
Potential savings (cost, manpower, and time)
I. Karpov

## Slide 6
Summary of SuperKEKB spring run from Belle II
For analyses that
do not involve
TDCPV, can add
an extra 100 fb-1
N.B. machine
studies were the
priority during this
running period.
T. Browder

## Slide 7
Summary of SuperKEKB spring run from Belle II -2
T. Browder

## Slide 8
Summary of SuperKEKB spring run from Belle II -3
T. Browder

## Slide 9
Progress with understanding e- blow up in BT line
V. Dispersion発生
Bump=0
QAD4EでDY: +12mm
N. Iida, T. Yoshimoto, Y. Funakoshi, K. Oide

## Slide 10
Emittance measurement at MSE.10
QAD4EでDY: +12mm
no Bump
Tailあり
Tail補正
PY_A1_M
PY_13_5
でMSE.10での
Tailがなくなるように
調整(今井氏)
QAD4EでDY: +11mm
QAD4EでDY: +6mm, QAD6EでDY: +4mm
2nC
Measurement: T. Yoshimoto
N. Iida, T. Yoshimoto, Y. Funakoshi, K. Oide

## Slide 11
Today’s agenda