## Slide 1: Highly Sensitive Optical Quantum Sensors
Young Jin Kim
Leanne Duffy, Igor Savukov
Los Alamos National Laboratory (LANL), USA
January 22, 2025
International Conference on Quantum Technologies for High-Energy Physics
CERN

## Slide 2
Based on lasers (pumping and probing) and alkali-metal (Cs, Rb, K) vapor cells
Manipulate electron spins for magnetic sensing
Optical Quantum Sensor (OQS)
Manipulate one valence electron
Typical implementation of OQS:
Cryogen-free sensor!

## Slide 3
Optical Quantum Sensor (OQS)
Pumping:
Polarize atomic spins

## Slide 4
Optical Quantum Sensor (OQS)
Spin tilt:
Spin tilt proportional to field strength

## Slide 5
Optical Quantum Sensor (OQS)
Probing:
Detect magnetic field with probe beam
1 pT
1 fT
= light polarization rotation

## Slide 6
OQS Noise Limit
Fundamental quantum noise limit:
Spin noise
Light shift noise
Photon shot noise
 = gyromagnetic ratio of alkali-metal atoms
n = density of alkali-metal atoms
V = active measurement vapor cell volume
T2 = coherence time of electron spins
 = photodiode quantum efficiency in probe beam readout
Rpr = absorption rate of probe beam photons
OD = optical depth of the probe beam
Fundamental quantum limit | 10 aT/Hz1/2 in the cell volume of 200 at > kHz
Current best OQS sensitivity | 240 aT/Hz1/2 at 423 kHz in the cell volume of 96 Romalis, Sauer, Savukov, Seltzer, Lee, U.S. Patent# 7521928B2 (2007)
Fundamental quantum limit | 
Current best OQS sensitivity | 

## Slide 7
Axion wave
ADMX
Application: Ultralight Axion Dark Matter Search
Resonant Cavity experiment
Resonant inductor-capacitor (LC) circuit experiment
LANL axion search: New detection concept based on optical quantum sensor
Axion wave
Cavity size >> 1 m
(e.g., 1 km for 10-9 eV)
Cavity size ~ 1 m for ~10-6 eV

## Slide 8
LANL Axion Search: Target Signal
Axion dark matter is “wave-like”: an oscillating field at a frequency of the axion mass (ma) that permeates all of space

## Slide 9
LANL Axion Search: Target Signal
Axion dark matter is “wave-like”: an oscillating field that permeates
all of space and interacts with the electromagnetic field
Axion-photon coupling

## Slide 10
LANL Axion Search: Target Signal
Axion dark matter is “wave-like”: an oscillating field that permeates
all of space and interacts with the electromagnetic field
Axion-photon coupling

## Slide 11
LANL Axion Search: Target Signal
Axion dark matter is “wave-like”: an oscillating field that permeates
all of space and interacts with the electromagnetic field

## Slide 12
LANL Axion Search: Target Signal
Axion dark matter is “wave-like”: an oscillating field that permeates
all of space and interacts with the electromagnetic field
Resonant circuit

## Slide 13
LANL Axion Search: Target Signal
Resonant circuit
Axion dark matter is “wave-like”: an oscillating field that permeates
all of space and interacts with the electromagnetic field

## Slide 14
LANL Axion Search: Target Signal
Resonant circuit
Axion dark matter is “wave-like”: an oscillating field that permeates
all of space and interacts with the electromagnetic field

## Slide 15
LANL Experiment Layout
  Low temperature resonant LC circuit + quantum limited (10 aT/Hz1/2) OQS

## Slide 16
Publication

## Slide 17
Intrinsic Noise of Optimized Axion Detector
Intrinsic noise of LANL LC circuit-OQS axion detector:
Target range
At MHz target frequency (i.e., neV mass range), axion detector sensitivity is determined by optical quantum sensor noise
OQS noise reduction = key to success of the project!

## Slide 18
Projected Sensitivity of LANL Axion Search
Unprecedented sensitivity 7 orders of magnitude beyond the current limit
Will probe a completely unexplored axion mass range near 10 neV

## Slide 19
Spin Squeezing Method
To reduce spin noise
The Heisenberg’s uncertainty principle:

## Slide 20
Spin Squeezing Method
Probe pulsing for spin squeezing:
The first pulse squeezes spins
Subsequent pulses readout spin states when the uncertainty is minimal

## Slide 21
OQS Setup
Magnetic shield
Potassium vapor cell
(outside the shield for illustration purpose)
Opening for probe Laser beam
Pump Laser beam
  Built an OQS module based on a potassium vapor cell and stable lasers with measured OQS field noise at 10-15 T level
Magnetic shield with vapor cell
Probe laser
Pump laser
Photo-detectors

## Slide 22
Photon shot noise
Spin noise
Spin Noise Measurement
  Measured the spin noise term (resonant bump) with continuous probe (i.e., without spin squeezing)
Probe laser noise
Noise ( V/Hz1/2 )
Frequency ( kHz )
4
6
8

## Slide 23
Spin Squeezing with Acousto-optic Modulator (AOM)
Magnetic shield with vapor cell
Probe laser
Pump laser
AOM
  We added an AOM between the probe beam and the vapor cell for probe pulsing.

## Slide 24
Protocol for Spin Squeezing
  During the delay time, the spin state is un-squeezed.
  Spin noise in measurement state depends on the delay time.

## Slide 25
Preliminary Spin Squeezing Verification
Spin noise increases at longer delay time (preliminary Verification of spin squeezing effect!)
Data fluctuation due to ambient magnetic noise
Time delay (ms)
OQS spin noise (a.u.)

## Slide 26
Research Team
Key investigators at Los Alamos National Laboratory:
Young Jin Kim
Igor Savukov
Leanne Duffy
Thank you!
Axion search using OQS recently selected for a QuantISED 2.0 award (Quantum Information Science Enabled Discoveries in High Energy Physics)!