## Slide 1: wakis: 3D Electromagnetic Time- Domain Wake and Impedance Solver
ABP-CEI Meeting, 25th April 2024
Elena de la Fuente, Lorenzo Giacomel, Giovanni Iadarola, Carlo Zannini, Manuel Cotelo (UPM)
 Special thanks to: Chiara Antuono, Giovanni Rumolo, Benoit Salvant, Leonardo Sito, Jean Luc Vay (Berkeley Lab) and yet again to Lorenzo Giacomel

## Slide 2: Outline
1. Introduction to Beam-Coupling Impedance simulations & Motivation
3. Conclusions, Challenges & Future work
Slides 4 - 11
Slides 13 - 38
Slides 40 - 42
2. The Finite Integration Technique (FIT) step-by-step:
2.1. Numerical Algorithm in free-space
2.2. Geometry definition: STL importer
2.3. Adding material tensors: and
2.4. Particle beam injection & Absorbing boundaries
2.5. Adding conductivity
2.6. Low- simulations

## Slide 3: Outline
2. The Finite Integration Technique (FIT) step-by-step:
2.1. Numerical Algorithm in free-space
2.2. Geometry definition: STL importer
2.3. Adding material tensors: and
2.4. Particle beam injection & Absorbing boundaries
2.5. Adding conductivity
2.6. Low- simulations
1. Introduction to Beam-Coupling Impedance simulations & Motivation
3. Conclusions, Challenges & Future work
Slides 4 - 11
Slides 13 - 38
Slides 40 - 42

## Slide 4: Beam Coupling Impedance
Wakefields are generated as the particle beam traverses the different accelerator devices and ‘perceives’ discontinuities:
in the geometry
or the electromagnetic properties (…)
These wakefields will affect the trailing particles/bunches. The beam-coupling impedance is the frequency-dependent property of each accelerator device, used to quantify the wakefields’ effects.
Fig: 3D Time domain simulation of a smooth pipe with obstacle with a passing proton beam (1-4) with CST®

## Slide 5: Beam Coupling Impedance (II)
The impedance of all relevant accelerator components is gathered in each accelerator's impedance model
And used in beam-dynamics codes (pyHeadTail, Xsuite) to predict beam behaviour
[1] SPS Transverse vertical impedance model.
C. Zannini
[2] PyHEADTAIL concept schematic.
K. Li & G. Rumolo
Or assess beam-induced heating of individual accelerator components and propose mitigation solutions
[3] Simulated Head-Tail
mode-zero instability
[5] Warm Vacuum modules Power lost map (2023)
[4] SPS BWS mitigation solution (2023)

## Slide 6: How to obtain ?
From the time domain (TD)
Directly in frequency domain (FD)
Eigenmode solver (CST®):
Resistive wall impedance: (IW2D)
Wakefield solver (CST®):
[1] N. Mounet. The LHC Transverse Coupled-Bunch Instability, PhD thesis 5305 (EPFL, 2012)
[1]
Wake Potential
Impedance
E.g. vertical TCSG CFC collimator vertical dipolar impedance at GHz vs. vertical source offset
E.g. simulation of lossy pillbox cavity with CST®
Reconstructed
[2]
[2] N. Mounet. ImpedanceWake2D BE-ABP-CEI 22/04/2021

## Slide 7: How to obtain ?
From the time domain (TD)
Directly in frequency domain (FD)
Eigenmode solver (CST®):
Resistive wall impedance: (IW2D@CERN)
Wakefield solver (CST®):
Eigenvalue problem
Fundamental EM modes of 3D loss-less resonant structures without excitation + Q-factor postprocessing
[1] N. Mounet. The LHC Transverse Coupled-Bunch Instability, PhD thesis 5305 (EPFL, 2012)
3D time domain Maxwell equations (integral form)
+ wake potential and impedance computation:
(FT + deconvolution)
[1]
with beam excitation
Commercial /
not open-source codes

## Slide 8: Project objective
WAKE SOLVER WORKFLOW
Develop an open-source Wakefield Solver (i.e., 3D electromagnetic time-domain) at CERN

## Slide 9: PhD motivation
1st year
2nd year
PhD
Trainee
1st year
2nd year
3rd year
(v0.1) Developed wakis package:
[1] Progress and challenges of an in-house wake/impedance solver. ABP information meeting, 28th April 2022. https://indico.cern.ch/event/1154158/
Computation of wake potential and impedance from pre-computed fields
Longitudinal and transverse (dipolar & quadrupolar)
Benchmarked with CST® Wakefield fields

## Slide 10: PhD motivation (II)
1st year
2nd year
PhD
Trainee
1st year
2nd year
3rd year
(v0.2) Explored open-source EM solvers to couple with wakis:
WarpX was the most promissing option: PIC+FDTD, mesh refinement (AMR), PML boundaries, python API
Found very good agreement for pillbox cavity, AMReX developed importer for more complex geometries
WarpX at the time, did not include material tensors other than vacuum/PEC. Found limitations in beam injection & PML behaviour too, C++ core, complexity…
[2] Progress on in-house wake solver “wakis”. ABP-CEI meeting, 3rd August 2023. https://indico.cern.ch/event/1283485/

## Slide 11: PhD status
1st year
2nd year
PhD
Trainee
1st year
2nd year
3rd year
(v.0.3) Decided to explore CST®’s numerical method, the Finite Integration Technique (FIT) in a python mockup 
https://github.com/ImpedanCEI/FITwakis
CAD Geometry
(.stl)
Simulation
parameters
Geometry importer
Time stepping scheme
Mesh
Materials
Fields
,
Operators
Boundary conditions
100%
S
Wake solve
Visualization
& post-proc
wakis (v0.3)

## Slide 12: Outline
Slides 4 - 11
Slides 13 - 38
Slides 40 - 42
1. Introduction to Beam-Coupling Impedance simulations & Motivation
2. The Finite Integration Technique (FIT) step-by-step:
2.1. Numerical Algorithm in free-space
2.2. Geometry definition: STL importer
2.3. Adding material tensors: and
2.4. Particle beam injection & Absorbing boundaries
2.5. Adding conductivity
2.6. Low- simulations
3. Conclusions, Challenges & Future work

## Slide 13: Finite Integration Technique
, ,
, ,
Maxwell Equations (Integral form)
Maxwell Grid Equations*
Operators
Grid areas and lengths
Materials
Domain discretization
1st approximation
z
x
y
*Formulation by T. Weiland: Wakefields and Impedances , 1991

## Slide 14: Finite Integration Technique (II)
, ,
Maxwell Grid Equations
Domain discretization
With Yee grid
Time-stepping scheme (leapfrog)
2nd approximation
Evolution in timestep
2nd order convergence in time
Primal grid
Dual Grid
Gauss Laws (for and ) considered satisfied* for no charges
Can pre-compute most of the quantities  speed 🚀
No matrix inversion needed during time loop
*Raymond Rumpf, Electromagnetic and Photonic Simulation for the Beginner, Artech, 2022.

## Slide 15: FIT (III): Operators
The curl operator on primal grid and on the dual grid, with is a sparse matrix made of bands of and
By modifying the columns or rows of C, one can add boundary conditions:
Perfect Electric Conductor (PEC): columns to zero at of boundary cells
Perfect Magnetic Conductor (PMC): rows to zero at of boundary cells
primal
dual
Size:
Sparcity of C
Lexicographic
indexation
Time-stepping scheme in vacuum
Notes: PEC Tangential electric field to zero at boundary
PMC Tangential magnetic field to zero

## Slide 16: FIT (IV): Diagonal matrices
The diagonal matrices contain the grid information:
and are analogous for the dual grid. Due to the Yee staggering, some of the components are zero:
If not set to zero, but equal to and at the opposite end Periodic boundary conditions
Where (i.e. x-direction):
*generated with wakis built-in 3D plotting
Time-stepping scheme vacuum

## Slide 17: FIT (V): Fields
Lexicographic
indexation
The fields are stored in memory as 3 () 3d numpy matrices np.zeros. In the time-stepping, they must be converted to 1d arrays with lexicographic indexing:
field.py
class Field:
Class Field has custom magic methods (__getitem__, __setitem__, __mul__, …) to handle 3d to collapsed conversion, operations and built-in visualization methods (inspect(), inspect3d())
*E.g., E field in a coarse-meshed cube resonator generated with wakis built-in 3D plotting solver.E.inspect3d()
Time-stepping scheme vacuum

## Slide 18: Example: Perturbation in free-space with BC
Vacuum
Plotting
plane XY
Perturbation
Perturbation at , ,
A static field perturbation in generates a spheric wavefront that is reflected for PEC BCs or re-enters the domain for Periodic BCs
examples/script_noeb_fit.py

## Slide 19: Example: Perturbation in free-space with BC
Vacuum
Plotting
plane XY
Boundary conditions (BCs): All Periodic
Perturbation
Perturbation at , ,
A static field perturbation in generates a spheric wavefront that is reflected for PEC BCs or re-enters the domain for Periodic BCs
examples/script_noeb_fit.py

## Slide 20: Example: Perturbation in free-space with BC
Vacuum
Plotting
plane XY
Boundary conditions (BCs): All Periodic
Perturbation
Perturbation at , ,
Boundary conditions (BCs): all PEC
A static field perturbation in generates a spheric wavefront that is reflected for PEC BCs or re-enters the domain for Periodic BCs
examples/script_noeb_fit.py

## Slide 21: Outline
Slides 4 - 11
Slides 13 - 38
Slides 40 - 42
1. Introduction to Beam-Coupling Impedance simulations & Motivation
2. The Finite Integration Technique (FIT) step-by-step:
2.1. Numerical Algorithm in free-space
2.2. Geometry definition: STL importer
2.3. Adding material tensors: and
2.4. Particle beam injection & Absorbing boundaries
2.5. Adding conductivity
2.6. Low- simulations
3. Conclusions, Challenges & Future work

## Slide 22: Importing geometry with
https://github.com/pyvista/pyvista
https://docs.pyvista.org/version/stable/
Using PyVista capabilities, wakis can:
Import CAD geometry: stl= pv.read(stl_file)
Generate a grid: grid = pv.StructuredGrid(X, Y, Z)
Find the cells that are inside the geometry with advanced collision filters* mask for material properties
State-of-the-art interactive 3d plotting
Cells inside the goniometer** shown in blue
*Pyvista extract_cells_inside_surface filter
** Simplified goniometer geometry by C. Antuono
wakis interactive grid.inspect() method

## Slide 23: Example: Perturbation with imported STL
Vacuum
BCs:
all PEC
PEC
z
y
x
Perturbation moving at
Plotting
plane YZ
*STL files generated with online tool: https://text2stl.mestres.fr/
A field perturbation in moving at excites the field in the vacuum domain revealing the PEC imported geometry
examples/script_letters_fit.py

## Slide 24: Example: Perturbation with imported STL
Vacuum
BCs:
all PEC
PEC
z
y
x
Perturbation moving at
Plotting
plane YZ
*STL files generated with online tool: https://text2stl.mestres.fr/
A field perturbation in moving at excites the field in the vacuum domain revealing the PEC imported geometry
examples/script_letters_fit.py

## Slide 25: Outline
Slides 4 - 11
Slides 13 - 38
Slides 40 - 42
1. Introduction to Beam-Coupling Impedance simulations & Motivation
2. The Finite Integration Technique (FIT) step-by-step:
2.1. Numerical Algorithm in free-space
2.2. Geometry definition: STL importer
2.3. Adding material tensors: and
2.4. Particle beam injection & Absorbing boundaries
2.5. Adding conductivity
2.6. Low- simulations
3. Conclusions, Challenges & Future work

## Slide 26: Material tensors for
Time-stepping scheme with 𝜀, 𝜇
The material matrices are considered diagonal* tensors:
User can specify relative permitivity/permeability:
The matrix will be built with a background material
The material associated with each imported stl geometry will overwrite the background material in the tensor (numpy + pyvista)
User can also specify anisotropic materials by defining , , …
*This approximation is only not valid for Gyrotropic materials
examples/test/test_materials.py
A PEC sphere and a Dielectric sphere imported in a vacuum background .
User can inspect the material tensors by: solver.ieps.inspect(plane=‘YZ’)

## Slide 27: Example: Planewave interacting with sphere
Vacuum
Plane YZ
PEC
Plane
wave
port
Vacuum
Plane YZ
Dielectric
Plane
wave
port
BCs:
Periodic x-/x+
Periodic y-/y+
PEC z-/z+
BCs:
Periodic x-/x+
Periodic y-/y+
PEC z-/z+
Special thanks to Prof. M. Cotelo (UPM) for the help with the planewave port setup and validation
examples/script_planewave_fit.py

## Slide 28: Example: Planewave interacting with sphere
Vacuum
Plane YZ
PEC
Plane
wave
port
BCs:
Periodic x-/x+
Periodic y-/y+
PEC z-/z+
Special thanks to Prof. M. Cotelo (UPM) for the help with the planewave port setup and validation
*wakis built-in 2d plotting solver.plot2d(**kwargs)
examples/script_planewave_fit.py
Vacuum
Plane YZ
Dielectric
Plane
wave
port
BCs:
Periodic x-/x+
Periodic y-/y+
PEC z-/z+

## Slide 29: Example: Planewave interacting with sphere
Vacuum
Plane YZ
PEC
Plane
wave
port
Vacuum
Plane YZ
Dielectric
Plane
wave
port
BCs:
Periodic x-/x+
Periodic y-/y+
PEC z-/z+
BCs:
Periodic x-/x+
Periodic y-/y+
PEC z-/z+
Special thanks to Prof. M. Cotelo (UPM) for the help with the planewave port setup and validation
*wakis built-in 2d plotting solver.plot2d(**kwargs)
examples/script_planewave_fit.py

## Slide 30: Example: Planewave interacting with sphere
Vacuum
Plane YZ
PEC
Plane
wave
port
Vacuum
Plane YZ
Dielectric
Plane
wave
port
BCs:
Periodic x-/x+
Periodic y-/y+
PEC z-/z+
BCs:
Periodic x-/x+
Periodic y-/y+
PEC z-/z+
Generated with wakis built-in 3d plotting solver.plot3d(**kwargs)
based on pyVista
examples/script_planewave_fit.py
Special thanks to Prof. M. Cotelo (UPM) for the help with the planewave port setup and validation

## Slide 31: Outline
Slides 4 - 11
Slides 13 - 38
Slides 40 - 42
1. Introduction to Beam-Coupling Impedance simulations & Motivation
2. The Finite Integration Technique (FIT) step-by-step:
2.1. Numerical Algorithm in free-space
2.2. Geometry definition: STL importer
2.3. Adding material tensors: and
2.4. Particle beam injection & Absorbing boundaries
2.5. Adding conductivity
2.6. Low- simulations
3. Conclusions, Challenges & Future work

## Slide 32: Beam injection as current
Sources () are managed in a dedicated class inside sources.py
Each source should have a source.update(t) method that will be called every timestep in the simulation loop.
For the case of a particle beam, the source is a current in applied at with a gaussian time profile.
  is the charge in [C], typically C
  is the beam size [m]
  is the ratio of the beam speed to the speed of light

## Slide 33: Beam injection as current
Sources () are managed in a dedicated class inside sources.py
Each source should have a source.update(t) method that will be called every timestep in the simulation loop.
For the case of a particle beam, the source is a current in applied at with a gaussian time profile.
  is the charge in [C], typically C
  is the beam size [m]
  is the ratio of the beam speed to the speed of light

## Slide 34: Minimizing injection perturbation: ABC
The perturbation appears due to the violation of the continuity law
We can mitigate it with boundary conditions: 1st attempt was the FOEXTRAP* absorbing boundary condition (ABC)
*FOEXTRAP: First Order Extrapolation (backup slides)

## Slide 35: Minimizing injection perturbation: ABC
The perturbation appears due to the violation of the continuity law
We can mitigate it with boundary conditions: 1st attempt was the FOEXTRAP* absorbing boundary condition (ABC)
ABC
PEC
Thanks to Prof. M. Cotelo (UPM) for the ABC idea
*FOEXTRAP: First Order Extrapolation (backup slides)

## Slide 36: Example: PEC cubic cavity
Geometry:
= 30 mm
= 50 mm
= 50 mm
= 100 mm
= 15 mm
= 15 mm
BCs:
wakis: ABC*
WarpX: PML*
CST: CPML
Beam:
= 18.5 mm (5 GHz)
q = 1e-9 C
Mesh:
nx, ny, nz = 50, 50, 150
total: 375000 cells
Cutoff frequency: GHz
Simulation time: for 1m wakelength (8760 timesteps):
CST: 42s, 16 threads, in `abpimp60g01`
Wakis: 3m40s , single core in `abpimp60g01`
WarpX: 12m, single core, #MP 1e6, in `abpimp60g01`
Very good agreement
WarpX shows a non-vanishing injection perturbation while in wakis it disappears
Some phase error comes from the CST field monitor extraction (very close to simulation’s timestep)
benchmarks/cubcavitymm/
Remarks

## Slide 37: Example: PEC cubic cavity
Geometry:
= 30 mm
= 50 mm
= 50 mm
= 100 mm
= 15 mm
= 15 mm
BCs:
wakis: ABC*
WarpX: PML*
CST: CPML
Beam:
= 18.5 mm (5 GHz)
q = 1e-9 C
Mesh:
nx, ny, nz = 50, 50, 150
total: 375000 cells
Cutoff frequency: GHz
Simulation time: for 1m wakelength (8760 timesteps):
CST: 42s, 16 threads, in `abpimp60g01`
Wakis: 3m40s , single core in `abpimp60g01`
WarpX: 12m, single core, #MP 1e6, in `abpimp60g01`
DC component from non-vanishing injection perturbation in WarpX
Simulation wakis vs WarpX vs CST: (keeping same mesh)
*last 10 cells in z- and z+ were removed for the wake calculation to mitigate injection perturbation
benchmarks/cubcavitymm/

## Slide 38: Outline
Slides 4 - 11
Slides 13 - 38
Slides 40 - 42
1. Introduction to Beam-Coupling Impedance simulations & Motivation
2. The Finite Integration Technique (FIT) step-by-step:
2.1. Numerical Algorithm in free-space
2.2. Geometry definition: STL importer
2.3. Adding material tensors: and
2.4. Particle beam injection & Absorbing boundaries
2.5. Adding conductivity
2.6. Low- simulations
3. Conclusions, Challenges & Future work

## Slide 39: Conductivity in time domain
Relative permittivity is often a frequency-dependent, complex quantity:
The simple model for a metal with broadband conductivity is:
How to implement this in a time domain (TD) simulations?
In TD, fields are purely real all matrix elements should be real
Introducing frequency dependence involves a de-convolution… (computationally expensive 💲 💲)
Time-stepping scheme:

## Slide 40: Conductivity in time domain
Time-stepping scheme:
From the Frequency domain Maxwell equations:
Ampere’s law:
To convert to TD: *
=
+ constitutive relation for
Time-stepping scheme with :
Relative permittivity is often a frequency-dependent, complex quantity:
The simple model for a metal with broadband conductivity is:
*Raymond Rumpf, Electromagnetic and Photonic Simulation for the Beginner, Artech, 2022.

## Slide 41: Example: lossy cubic cavity
Conductivity: 10 S/m
Skin-Depth:
: 542754
Runtime: 4’, 30’’ , single core in `abpimp60g01`
: 0.5 mm > 3
Remarks:
To match CST results, we had to remove 10 cells z-/z+ and increase the mesh by 20%
Low conductivity was chosen to have a fast decaying wake
benchmarks/condcubcavitymm/

## Slide 42: Example: lossy fancy-shaped* cavity
Conductivity: 1000 S/m
Skin-Depth:
: 271600,
Wakelength: 100 m
: 1.5 mm < 3
Runtime: 20’ 40’’ single core in `abpimp60g01`
Remarks:
Staircased grid can induce the frequency shift at 800 MHz
Skin Depth** is not well modelled  difference in shunt impedance
**for , CST uses surface impedance model (Leontovich)
= 80 cm
= 12 cm
Shows the need for Surface impedance model for good conductors
Simulation is stable even for very long wakes
*CST’s Default Acc. Cavity model
benchmarks/condcylcavity/

## Slide 43: Outline
Slides 4 - 11
Slides 13 - 38
Slides 40 - 42
1. Introduction to Beam-Coupling Impedance simulations & Motivation
2. The Finite Integration Technique (FIT) step-by-step:
2.1. Numerical Algorithm in free-space
2.2. Geometry definition: STL importer
2.3. Adding material tensors: and
2.4. Particle beam injection & Absorbing boundaries
2.5. Adding conductivity
2.6. Low- simulations
3. Conclusions, Challenges & Future work

## Slide 44: Simulation script example
from wakis import GridFIT3D, SolverFIT3D, WakeSolver
import pyvista as pv
# ---------- Domain and Grid setup ---------
# Number of mesh cells
Nx = 57
Ny = 57
Nz = 109
#dt = 5.707829241e-12
# Geometry Import
stl_cavity = 'cavity.stl'
stl_pipe = 'beampipe.stl'
stl_solids = {'cavity': stl_cavity, 'pipe': stl_pipe}
# Materials
stl_materials = {'cavity': 'vacuum', 'pipe': 'vacuum'}
background = [1.0, 1.0, 100] # lossy metal [ε_r, µ_r, σ]
# Domain bounds (from stl)
surf = pv.read(stl_cavity) + pv.read(stl_pipe)
xmin, xmax, ymin, ymax, zmin, zmax = surf.bounds
# Set grid and geometry
grid = GridFIT3D(xmin, xmax, ymin, ymax, zmin, zmax, Nx, Ny, Nz,
stl_solids=stl_solids,
stl_materials=stl_materials)
#grid.inspect()
# ------------ Beam source ----------------
# Beam parameters and wake obj.
beta = 0.8 # beam relativistic beta
sigmaz = beta*6e-2 # [m] -> multiplied by beta to have f_max cte
q = 1e-9 # [C]
xs = 0. # x source position [m]
ys = 0. # y source position [m]
xt = 0. # x test position [m]
yt = 0. # y test position [m]
# tinj = 8.53*sigmaz/(beta*c) # injection time offset [s]
wake = WakeSolver(q=q, sigmaz=sigmaz, beta=beta,
xsource=xs, ysource=ys, xtest=xt, ytest=yt,
save=True, logfile=True)
# ----------- Solver & Simulation ----------
# boundary conditions and solver obj.
bc_low=['pec', 'pec', 'pec']
bc_high=['pec', 'pec', 'pec'] solver = SolverFIT3D(grid, wake,
bc_low=bc_low, bc_high=bc_high,
use_stl=True, bg=background)
# Run wakefield time-domain simulation
wakelength = 5. #[m]
add_space = 10 # no. cells to remove for the wake calculation
solver.wakesolve(wakelength=wakelength, add_space=add_space,
plot=True, plot_every=30, save_J=True,
**plotkw)

## Slide 45: Example: results for different
benchmarks/betacavity/
Simulation of a cylindrical pillbox* below cut-off for different relativistic values
*Model by Elena Macchia
Work in progress!
1st attempt shows some agreement, but mesh needs to be optimized
The behaviour with is consistent

## Slide 46: Outline
Slides 4 - 11
Slides 13 - 38
Slides 40 - 42
1. Introduction to Beam-Coupling Impedance simulations & Motivation
3. Conclusions, Challenges & Future work
2. The Finite Integration Technique (FIT) step-by-step:
2.1. Numerical Algorithm in free-space
2.2. Geometry definition: STL importer
2.3. Adding material tensors: and
2.4. Particle beam injection & Absorbing boundaries
2.5. Adding conductivity
2.6. Low- simulations

## Slide 47: Challenges: Simulations above cut-off
Cutoff frequency: GHz
benchmarks/cubcavitycm/
wakis does not show good agreement above cut-off (yet)
Perfect matching layers (PML) BCs are needed to simulate propagating modes
When the bunches are short, they excite to higher frequencies:
When of the pipe, some modes are in propagation and reach the boundaries

## Slide 48: Challenges: Simulations above cut-off
Cutoff frequency: GHz
benchmarks/taperout/
This becomes more evident in a non-resonant structure, like a transition (i.e., Step-out)
All modes should propagate, but in wakis they are reflected back. To simulate propagating modes, we need the PML boundary conditions

## Slide 49: More challenges for the near future
PML & Simulations above cutoff
Staircased grid
Numerical dispersion
GPU acceleration
Surface impedance
Wake extrapolation (genetic algorithm)
Frequency dependent (dispersive) materials
Frequency domain monitors
Staircased grid with curved geometry generates artifacts and difficulties convergence
For some optic applications, the code shows numerical dispersión
examples/script_wavepacket_fit.py
Acceleration should be possible with cupy since it supports scipy.sparse

## Slide 50: Conclusions
Developed a 3D Electromagnetic and Wake Solver in time domain, 100% in python: wakis
  Uses the Finite Integration Technique and scipy.sparse matrices, allowing for fast computations, extendable to GPU
  Different boundary conditions: PEC, PMC, Periodic, ABC
  Importing CAD geometry with pyvista
  Simulate materials with with diagonal tensors. Possibility of anisotropic properties.
  Simulate several sources: Planewave, gaussian wave packet, and the particle beam for different
  Several on the fly built-in plotting capabilities in 1d, 2d, 3d
  Interactive visualization methods to inspect the grid and the geometry
  +10 examples and benchmark simulations (⏳~2’ to 20’) already available on GitHub.
wakis solver has been benchmarked with CST Wakefield Solver® with pillbox cavities of different materials and geometries, below cut-off.
It is built also as a general-purpose 3D TD EM code, capable of simulating optical lenses, diffraction gratings and much more.
However, many challenges need to be investigated: simulations above cutoff with PML boundaries, advanced mesh generation, GPU acceleration, numerical dispersion correction, surface impedance condition… That will be addressed during the PhD!
https://github.com/ImpedanCEI/FITwakis

## Slide 51
Thank you  !!!
Elena de la Fuente García (BE–ABP–CEI)
wakis: 3D Electromagnetic Time- Domain Wake and Impedance Solver

## Slide 52: Bibliography used
Wakefields and Impedances [T. Weiland, 1991]
TE/TM FIT for accelerators [I. Zarg, 2005]
Open boundaries for FIT [MC. Balk, 2005]
2D expansion [I. Zarg, 2015]
2D freq. domain [R. SChumann, 2000]
Frequency domain FIT and FEM Uwe Niedermayer PhD thesis [2015]
Eigenmode + MPI + Gyrotropic materials Klaus Klopfer PhD thesis [2014]
EMcLAW: An unsplit Godunov method for Maxwell ’s Equations. (UPM) Moreno, José A. PhD Thesis [2020]

## Slide 53: Absorbing boundary condition (ABC)
A first attempt to reduce the perturbation of the field when the beam current enters/exits it to use absorbing boundary conditions (ABC)
Since PML formulation is complex, the simplest ABC, the FOEXTRAP, was tested first. This is a first order extrapolation that mimics a continuous field at the boundary cells
It has to be updated every timestep
Same for all 6 boundaries (low and high, x, y, z)

## Slide 54: Challenges: Simulations above cut-off
Cutoff frequency: GHz
benchmarks/taperout/
The agreement is okay when we use PEC boundaries In both wakis and CST®

## Slide 55: Optimizing results with wakis
If we remove the last 8 cells in z-/z+ with the add_space parameter
Conductivity: 10 S/m
Skin-Depth:
: 542754
Runtime: 4’, 30’’ ,
single core in `abpimp60g01`
: 0.5 mm > 3

## Slide 56: Optimizing results with wakis
Then, if we increase the mesh resolution by 15%
Conductivity: 10 S/m
Skin-Depth:
: 542754
Runtime: 4’, 30’’ ,
single core in `abpimp60g01`
: 0.5 mm > 3

## Slide 57: FITwakis GitHub overview
FDTD EM solver
by Lorenzo
FIT EM Solver
Wake Solver
Benchmarks vs CST, WarpX …
Wakis(v0.2) code is refactored into class WakeSolver
Examples & university tests:
Plane wave propagation
Gaussian wavepacket propagation
Cubic Resonator
Field class to manage matrix formulation
are instances of this class
GridFIT3D class in charge of STL importer and grid definition
SolverFIT3D class that solves Maxwell equations
Pre-defined materials library (vacuum, dielectric, PEC)

## Slide 58: SolverFIT3D development (I): memory optimization
Deletes from memory the matrices that will not be used for the timestepping routine:
Improves memory allocation by 60%
Increases speed performance by 5%

## Slide 59: SolverFIT3D development (II): 1D, 2D, 3D plotting
Plot3D example:
examples/script_planewave_fit.py
A planewave interacting with a dielectric sphere (University test)
Using PyVista (vtk based) functions.
Plots can also be interactive:
clip_volume or clip_normal flags when off_screen =True

## Slide 60: SolverFIT3D development (II): 1D, 2D, 3D plotting
Plot2D and 1D example:
examples/script_planewave_fit.py
A planewave propagating through vacuum being repflected at the PEC boundary
Matplotlib based coutourf (2D) and line plot (1D)

## Slide 61: SolverFIT3D development (IV): EM solve
Runs Electromagnetic time domain simulation given an initial condition or source
EM solve example:
examples/script_wavepacket_fit.py
A gaussian wavepacket propagating through vacuum domain (University test)

## Slide 62: SolverFIT3D development (V): Wake solve
Runs Wakefield time domain simulation given a wakelength.
Beam source injected is defined by WakeSolver object.
Computes wake potential and impedance by saving Ez field every timestep and using the routines in WakeSolver class (needs h5py)
Wake solve example:
examples/script_cubcavity_fit.py
A gaussian beam traversing a PEC cubic pillbox cavity