## Slide 1: H6 Modification – Smaller Beam Spot
Luke Weaver
Supervisors: Dr. Laurie Nevay & Dr. Fabian Metzger
15 - July - 2024

## Slide 2: A Brief Recap
R&D silicon groups testing small silicon sensors which require smaller beam size for sufficient rate (already at RP safety limit)
Investigate possible configurations of quadrupoles to minimize beam spot
Accurately predict beam size taking into account filtering of secondary beam and multiple scattering in air
Last doublet of quadrupoles
beam
Free Area for Quadrupoles

## Slide 3: Work Thus Far
Final focus study
Determine acceptance
Application of Twiss parameters and R-Matrices to model beam optics
Utilize MAD-X to evaluate different configurations of quadrupoles varying:
  Position
  Separation
  Quadrupole number
Compared focus size at different positions in user zones PPE146 and PPE156
540 (m)
Free Area for Quadrupoles
Quads
L
485 (m)
492.5 (m)
500 (m)
533 (m)
536.5 (m)
PPE146 Foci
PPE156 Foci

## Slide 4: Optimal Setup
With no Doublet
Doublet Solution – makes sense as previous focus comes from a Doublet
Quads as far downstream as possible – larger beam focuses to smaller spot size
Separation of 4.2 (m) – determined from varying separation distances in MAD-X
With Doublet
: 13.65 times smaller
: 2.56 times smaller

## Slide 5: Multiple Scattering
End of beamline has ~40 m of air
Monte Carlo simulation of multiple scattering in air from reference beam

## Slide 6: Multiple Scattering
Convolution with sigma
Monte Carlo simulation of multiple scattering in air from reference beam
Relative Frequence of X (normalized)

## Slide 7: Beamline Model BDSIM
Added vacuum begin and end statements that were missing in the previous model
Added new quadrupoles
Verified the optics
New Quadrupoles

## Slide 8: Next Steps
Simulate whole beamline start to finish in BDSIM (with physics on)
  Determine multi-species distribution of beam
Compare to measurements during first week of August
(Preliminary Results)