## Slide 1
|
0
Computing at CERN
Maite Barroso Lopez CERN IT department

## Slide 3: What do we need?
Millions of lines of code (C++,Python, …)
Large infrastructure
  Customized hardware
  PC farms
  Database and storage systems, data management systems
  Distributed analysis facilities
  The grid

## Slide 4: What happens to the data?:
Event filtering, tagging and storage
Calibration, alignment
Event reconstruction
Storage
Event simulation
Physics analysis

## Slide 5: Computing at CERN: the big picture
Data Acquisition
(trigger)
Data Recording and Archive
Data Reconstruction
and Derivation
Simulated Data
Event Generation(part. inter.) Simulation(int. w/ det.)
Digitization(simul detector resp)
Preservation: Data and Analysis
Data
Analysis
Computing at CERN - International Teachers Programme - xavier.espinal@cern.ch
HPCs
Detector Data

## Slide 6: Step by step
Each step involves some data reduction
  data are discarded (online)
  data are compressed (offline)
In each step the data get closer to be interpretable in
physical terms
Some steps are repeated many times until the output is
satisfactory (offline reprocessing)

## Slide 7: Our Data Generators
Experimental physics is about DATA!
CERN experiments transfer all data to the Computing Center
Data is stored and ready to be processed, analyzed and shared

## Slide 8: A comparison of the yearly data volumes of current and future projects:
Credits: APS/Alan Stonebraker and V. Gülzow/DESY

## Slide 9: LHC Experiments: the big 4
A computing perspective: O(10-100) Pb/year, 0.5M running jobs (continuous), fat and long-haul networks
General-purpose:Higgs boson, extra dimensions, dark matter
General-purpose:Higgs boson, extra dimensions, dark matter
CP violation in the interactions of b-hadrons: matter-antimatter asymmetry of the Universe.
heavy-ion physics, strongly interacting matter at extreme energy densities (quark-gluon plasma)

## Slide 10: Plus more experimets
Fix target (COMPASS, CLOUD, NA64, etc)
Antimatter (AEGIS, ALPHA, etc)
Non-accelerator (AMS, CAST, OSCAR)
Experimental facilities (ISOLDE, Medicis, n_TOF, Neutrino platform)

## Slide 11: Astroparticle Physics and Radio Astronomy
Knowledge transfer and expertise sharing among large ESFRIs on scientific computing
Data Recording from remote sources

## Slide 12: Computing at CERN: the big picture
Data Acquisition
(trigger)
Data Recording and Archive
Data Reconstruction
and Derivation
Simulated Data
Event Generation(part. inter.) Simulation(int. w/ det.)
Digitization(simul detector resp)
Preservation: Data and Analysis
Data
Analysis
Computing at CERN - International Teachers Programme - xavier.espinal@cern.ch
HPCs
Detector Data

## Slide 13: Online versus offline
Online
  In real time, fast!
  Decisions are irreversible
  Data cannot be recovered
Offline
  From almost real time to long delays
  Decisions can be reconsidered
  Data can be reprocessed

## Slide 14: Online processing
Data Acquisition
(trigger)
Data Recording and Archive
Data Reconstruction
and Derivation
Simulated Data
Event Generation(part. inter.) Simulation(int. w/ det.)
Digitization(simul detector resp)
Preservation: Data and Analysis
Data
Analysis
Computing at CERN - International Teachers Programme - xavier.espinal@cern.ch
HPCs
Detector Data
Overall guideline in designing trigger system: what are the essential features of interesting physics in the detectors?
Trigger: event selection
Primary (design) collision rate: 40 MHz
Recording rate: a few hundred Hz to kHz
How is this achieved?
          Multi-level trigger – chain of yes/no decisions
      Very fast first level: (Programmable) hardware
      Slower higher level(s): Software on specialized or
      commodity processors
Has to be reliable
Rejected data are lost forever
Continuous monitoring
Do not lose new physics!
Must therefore be open to many different signatures of potentially new physics in the detector system

## Slide 15: Online processing
Data Acquisition
(trigger)
Data Recording and Archive
Data Reconstruction
and Derivation
Simulated Data
Event Generation(part. inter.) Simulation(int. w/ det.)
Digitization(simul detector resp)
Preservation: Data and Analysis
Data
Analysis
Computing at CERN - International Teachers Programme - xavier.espinal@cern.ch
HPCs
Detector Data

## Slide 16: From the Hit to the Bit: DAQ
  100 million channels
  40 million pictures a second
  Synchronised signals from all detector parts

## Slide 17: From the Hit to the Bit: event filtering
L1: 40 million events per second
  Fast, simple information
  Hardware trigger in a few microseconds
L2: 100 thousand events per second
  Fast algorithms in local computer farm
  Software trigger in <1 second
EF: Few 100 per second recorded for study

## Slide 18: From the Hit to the Bit: event filtering
L1: 40 million events per second
  Fast, simple information
  Hardware trigger in a few microseconds
L2: 100 thousand events per second
  Fast algorithms in local computer farm
  Software trigger in <1 second
EF: Few 100 per second recorded for study
1PB/s: few hundred trillion euros/yr !!!
From 40 MHZ to 100kHz

## Slide 19: From the Hit to the Bit: event filtering
L1: 40 million events per second
  Fast, simple information
  Hardware trigger in a few microseconds
L2: 100 thousand events per second
  Fast algorithms in local computer farm
  Software trigger in <1 second
EF: Few 100 per second recorded for study
1PB/s: few hundred trillion euros/yr !!!
From 40 MHZ to 100kHz
We keep ~1 event in a million
From 100 kHZ to 25kHz

## Slide 20: From the Hit to the Bit: event filtering
L1: 40 million events per second
  Fast, simple information
  Hardware trigger in a few microseconds
L2: 100 thousand events per second
  Fast algorithms in local computer farm
  Software trigger in <1 second
EF: Few 100 per second recorded for study
1PB/s: few hundred trillion euros/yr !!!
From 40 MHZ to 100kHz
We keep ~1 event in a million
From 100 kHZ to 25kHz
From 25 kHZ to few kHz
Final data rates ~10 GB/s

## Slide 21: Offline computing
Data Acquisition
(trigger)
Data Recording and Archive
Data Reconstruction
and Derivation
Simulated Data
Event Generation(part. inter.) Simulation(int. w/ det.)
Digitization(simul detector resp)
Preservation: Data and Analysis
Data
Analysis
Computing at CERN - International Teachers Programme - xavier.espinal@cern.ch
HPCs
Detector Data
Tier-0 processing (CERN)
Archive raw data on mass storage
First event reconstruction without or with a small delay
Archive reconstructed data on mass storage
A few hundred kByte/event, depending on physics
Reconstructed objects (hits/clusters, tracks, vertices, jets,
electrons, muons)
Send raw and processed data to LHC Grid for analysis

## Slide 22: CERN IT Department
Data Storage
Network
DataBases
Facilities
Data Processing
Distributed Computing
Applications and devices
CERN IT Department

## Slide 23: Offline computing
Calibration: Convert raw data to physical quantities
Alignment: Find out precise detector positions
Event reconstruction:
  Reconstruct particle tracks and vertices (interaction points)
  Identify particle types and decays
Simulation:
  Generate artificial events resembling real data as closely as possible
  Needed for background studies, corrections, error estimation, …

## Slide 24: Offline: data analysis
Extract physics signals from
background
  Compute masses, cross-sections, branching ratios, discovery limits, …
Requires sophisticated multivariate techniques
Distributed: Physics analysis takes place in many labs all over the world

## Slide 25: The Worldwide LHC Computing Grid
WLCG provides global computing resources to store, distribute and analyse the LHC data

## Slide 27: The Worldwide LHC Computing Grid
Data Archive Only (tapes)
(10PB)
(1PB)

## Slide 29: The last LHC Run: data recording
LHC Experiments recorded 88 Petabytes of data in 2018 (15.8PB only in November)
The LHC data is aggregated at the CERN data centre to be stored, processed and distributed
~0.5GB/s
~3GB/s
~3GB/s
~ 4GB/s (Heavy Ion Run)
Ian Bird@WLCG-OB

## Slide 30: 2025 LHC Data Taking
Recorded data into the CERN tape archive (PB/week)
Daily average data rate from experiments to T0 (Gb/s)
The 2025 LHC data taking started
Data rates higher than in 2024 for the same period, inline with expectations
CERN and generally WLCG services running smoothly
2024 pp
2024 HI
EYETS
2025 pp

## Slide 31: LHC data processing
EYETS
2024 LHC Run
2025 LHC Run
Number of cores in use (WLCG pledge + opportunistic)
Volume of data recalled from CERN tape (PB/week)
Experiments leveraging all WLCG available cores …
… plus ~50% extra opportunistic capacity (including HLTs and HPCs)
pledge
Intense reprocessing campaigns during EYETS recalling data from tape systems

## Slide 32: HL-LHC: a computing challenge

## Slide 36: CERN Data Center
Built in the 70s on the CERN site (Meyrin,Geneva)
  3.5 MW for equipment
Hardware generally based on commodity
  10,000 servers, providing 500,000 processor cores (14.000 VMs)
  120,000 disk drives providing 0.6EB disk space (1EB=1000PB)
  40,000 tapes drives, providing 0.5EB capacity (1EB=1000PB)

## Slide 37: Green IT
Power Usage Effectiveness (PUE): Total Facility Energy / IT Facility Energy
PUE
DCiE
More efficient
Less efficient
33%
50%
100%
1.0
2.0
3.0
Achievable w/best practices
and efficient equipment

## Slide 38: Take-away (1)
Computing is instrumental for science. Detectors and sensors evolving: growing IT demands.
  LHC raw data rates are PB/s scale but lowered to GB/s after data filtering
CERN remains largest scientific repository in the world
Scientific data already at the Exabyte scale:
  1EB = 1.000PB = 1.000.000 TB = 1.000.000.000 GB
(1TB is your computer)
(100 GB is your smartphone)

## Slide 39: Take-away (2)
A bright future of HEP ahead of us: many questions to answer, discoveries made accessible thanks to the HL-LHC program
More events, more complex, at a finer granularity
  Processing and analysing them is a challenge for us
  To be faced with a constantly evolving hardware landscape
Two elements which help succeeding: parallelism and heterogeneity
Interesting times for motivated scientists-engineers!
A lot has been achieved, but a lot still needs to be done

## Slide 40: Credits
Xavier Espinal (material from previous years)
Danilo Pipparo (tCSC 2024)
Simone Campana (WLCG material)
Arnulf Quadt (CERN School of Computing 2024)