## Slide 1
Marlene Turner
AWAKE and Plasma Wakefield Acceleration
Go to vevox.app
Enter the session ID: 131-113-101
Or scan the QR code

## Slide 2: Join the Vevox session
Go to vevox.app Enter the session ID: 131-113-101 Or scan the QR code

## Slide 3: What do you think plasma wakefield acceleration is?
##/##
Question slide
Join at: vevox.app
ID: 131-113-101
A way to speed up plasma flow in natural lightning.
0%
A method of accelerating particles using waves created in plasma.
0%
A technique for heating plasma to generate energy.
0%
A way to slow down fast-moving ions in a laboratory.
0%
A method of propelling spacecrafts using solar plasma.
0%
Go to vevox.app
Enter the session ID: 131-113-101
Or scan the QR code

## Slide 4: What do you think plasma wakefield acceleration is?
##/##
Preparing Results
Join at: vevox.app
ID: 131-113-101
A way to speed up plasma flow in natural lightning.
0%
A method of accelerating particles using waves created in plasma.
0%
A technique for heating plasma to generate energy.
0%
A way to slow down fast-moving ions in a laboratory.
0%
A method of propelling spacecrafts using solar plasma.
0%
RESULTS SLIDE
✓

## Slide 5: Outline
Physics of plasma wakefields
Introduction
AWAKE Experiment
What’s next?
Summary
State of the Art

## Slide 6: Outline
Physics of plasma wakefields
Introduction
AWAKE Experiment
What’s next?
Summary
State of the Art

## Slide 7: To accelerate a charged particle, you need…
0/0
Question slide
Join at: vevox.app
ID: 131-113-101
A magnetic field only.
0%
A electric field only.
0%
A magnetic and electric field.
0%
All four fundamental forces: strong, weak, gravitational and electromagnetic.
0%

## Slide 8: To accelerate a charged particle, you need…
0/0
Preparing Results
Join at: vevox.app
ID: 131-113-101
A magnetic field only.
0%
A electric field only.
0%
A magnetic and electric field.
0%
All four fundamental forces: strong, weak, gravitational and electromagnetic.
0%
RESULTS SLIDE
✓

## Slide 9: Why Plasma Wakefield Acceleration?
Goal: Build smaller, cheaper, or more energetic particle accelerators.
 New way to accelerate charged particles
Acceleration gradient: e.g. 100 MeV/m,…
e-
100 MV/m
e-
Static field is not ideal
Better:
  Field travels together with the beam

## Slide 10: Current State-of-the-Art Acceleration Technology
Metallic cavities
Limited to ~100 MV/m due to electric breakdowns (ionization).
  Operate typically around 30 MV/m
  To overcome this limit  change the medium
Metallic radiofrequency (RF) cavities
Source: https://cerncourier.com/a/cern-thinks-bigger/

## Slide 11: Plasma Wakefield Acceleration
Plasmas are not limited by electrical breakdown.
i.e.: ~1 GeV/m for a plasma electron density of npe = 1014 cm-3
~100 GeV/m for a plasma electron density of npe = 1018 cm-3
(Cold plasma wavebreaking limit)
11
10 GeV = 100 GeV/m x 0.1 m
10 GeV = 100 MeV/m x 100 m

## Slide 12: Circular and Linear Accelerators
Image from P. Arpaia et al., NIMA 985, 164652 (2021)
Circular accelerators
Synchrotron radiation loss
r

## Slide 13: Synchrotron Radiation
Field lines
Field left behind
v < c
v = c
Synchrotron radiation is caused by leaving part of fields behind
when the beam moves along the curve.
∝ E4/(r2m4)
Particle
energy
Bending
radius
Mass of the particle
 Needs to be taken into account when accelerated charged particles are deflected in the radial direction.

## Slide 14: Circular and Linear Accelerators
Image from P. Arpaia et al., NIMA 985, 164652 (2021)
Circular accelerators
Max. energy (E) limited by synchrotron radiation (SR) losses ∝ E4/(r2m4)
r
Advantage: beam passes accelerating section many times
Disadvantage: synchrotron radiation losses
LHC tunnel:
p+p+  14 TeV  limited by magnets
e+e-  209 GeV  limited by SR
r  bending radius
m  mass of the particle
e-
e-
9.1 × 10-31 kg
1.67 × 10-27 kg

## Slide 15: Circular and Linear Accelerators
Image from P. Arpaia et al., NIMA 985, 164652 (2021)
Circular accelerators
Beam passes acceleration section multiple times.
Max. energy (E) limited by synchrotron radiation losses ∝ E4/(r2m4)
r
Linear accelerators
Beam passes acceleration section multiple times.
Negligible synchrotron radiation losses
Accelerator length and accelerating gradient define final beam energy.

## Slide 16
Plasma
Wakefield Acceleration
Plasma ?
Wakefield ?
Acceleration ?

## Slide 17: Definition of Plasma and Plasma Wakefield
Plasma
Plasma: ionised gas (4th state of matter)
  Quasi-neutrality: the overall charge of a plasma is about zero.
  Collective effects: Charged particles must be close enough together that each particle influences many nearby charged particles.
  Electrostatic interactions dominate over collisions or ordinary gas kinetics.
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 18: How much plasma is out there in the visible universe?
##/##
Question slide
Join at: vevox.app
ID: 131-113-101
About 99% of the visible universe consists of plasma
0%
Less than 10% — it’s mostly solid and liquid
0%
Around 50%, evenly mixed with gases
0%
Only in stars — so 1% or less
0%

## Slide 19: How much plasma is out there in the visible universe?
##/##
Preparing Results
Join at: vevox.app
ID: 131-113-101
About 99% of the visible universe consists of plasma
0%
Less than 10% — it’s mostly solid and liquid
0%
Around 50%, evenly mixed with gases
0%
Only in stars — so 1% or less
0%
RESULTS SLIDE
✓

## Slide 20: Definition of Plasma and Plasma Wakefield
Plasma
Plasma Wakefields
Plasma: ionised gas (4th state of matter)
  Quasi-neutrality: the overall charge of a plasma is about zero.
  Collective effects: Charged particles must be close enough together that each particle influences many nearby charged particles.
  Electrostatic interactions dominate over collisions or ordinary gas kinetics.
Plasma Wakefields:
  are the fields created/sustained by collective motion of plasma particles.
e-
Electric field
Acceleration
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 21: Let Us Repeat…
We quantify the acceleration process using the acceleration gradient
Plasma wakefields allow to accelerate charged particles with ~ 1-100 GeV/m
High gradients are important when using linear accelerators (e.g. for light particles) to minimize synchrotron radiation losses
  For linear accelerators, their length defines the final beam energy

## Slide 22: Outline
Physics of plasma wakefields
Introduction
AWAKE Experiment
What’s next?
Summary
State of the Art

## Slide 23: How to Create Plasma Wakefields?
Two ingredients
Plasma
(Medium)
Relativistic charged particle beam or
Short intense laser pulse
(Energy source)
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 24
Image from https://revbalance.com/improving-balance-for-wakesurfing/

## Slide 25: Energy Source: The Driver
e- bunch
Relativistic charged particle bunches or laser pulses
   Relativistic charged particle bunches carry almost purely transverse electric fields
What we need  longitudinal electric field to accelerate charged particles
Trick:
Use plasma to convert the transverse electric field of the proton bunch into a longitudinal electric field in the plasma.
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
v ~<c
At rest:

## Slide 26: How to Drive a Plasma Wave
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
-- - - - -
Important to understand
Rb ions are heavy and do not move significantly on the timescale of the electrons
Wakefield is moving with the particle bunch (v~c)
Plasma electron motion is mostly transverse
  Electrons do not move significantly longitudinally
e.g. ~3 mm for npe = 1014 cm-3 ~30 μm for npe = 1018 cm-3

## Slide 27: How to Drive a Plasma Wave
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
Charge separation  electric field
(longitudinal and transverse)
Where should we place an electron bunch to be accelerated?

## Slide 28: Plasma Wakefields
Accelerating for negatively charged particles
Decelerating for negatively charged particles
Focusing for negatively charged particles
Defocusing for negatively charged particles
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 29: Plasma Acts As a Transformer Driver deposits energy, witness gains energy
Depletion: The drive bunch/pulse running out of energy. Solution: couple in a new driver or use a more energetic driver
Dephasing: The witness bunch outruns the driver. Solution: couple in a new driver or shape the plasma density
Diffraction: Drive beam evolution. Solution: Guiding or use a more rigid driver
Acceleration distance typically limited by either
driver
witness
driver
witness
driver
witness

## Slide 30: Let Us Repeat…
Driving plasma wakefields requires plasma, energy source (driver)
  Place a particle beam (witness) to be accelerated
Plasma acts as a transformer
  Drive beam energy is transferred to the witness bunch
What limits the energy gain:
  Depletion: Driver runs out of energy
  Dephasing: Accelerating bunch outruns the driver
  Diffraction: Driver no longer intense enough

## Slide 31: Outline
Physics of plasma wakefields
Introduction
AWAKE Experiment
What’s next?
Summary
State of the Art

## Slide 32
Reference:

## Slide 34: State-of-the-Art Results Beam-Driven
SLAC (Stanford, California)
Blumenfeld, I., Clayton, C., Decker, FJ. et al. Energy doubling of 42 GeV electrons in a metre-scale plasma wakefield accelerator. Nature 445, 741–744 (2007).
3.2 km
42 GeV energy gain
in 85 cm of plasma
~ 50 GeV/m
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 35
20 cm
Capillary Discharge Plasma

## Slide 36
Slit Jet

## Slide 37: Why is the plasma purple/pink?
0/0
Question slide
Join at: vevox.app
ID: 131-113-101
Because it was photoshopped to look good.
0%
Because of the very high temperature.
0%
Because Hydrogen was used to create the plasma.
0%
Because plasma absorbs all colors except pink.
0%

## Slide 38: Why is the plasma purple/pink?
0/0
Preparing Results
Join at: vevox.app
ID: 131-113-101
Because it was photoshopped to look good.
0%
Because of the very high temperature.
0%
Because Hydrogen was used to create the plasma.
0%
Because plasma absorbs all colors except pink.
0%
RESULTS SLIDE
✓

## Slide 39
Laser System
BELLA PW (Berkeley, California)
40 J, 30 fs  1.2 PW
Focused to σr = 50 μm
9.2 GeV in 30 cm of plasma
 30.6 GeV/m
Phys. Rev. Lett. 133, 255001 (2024).
39
State-of-the-Art Results Laser-Driven
Wave-breaking

## Slide 40: Let Us Repeat…
Plasma wakefields acceleration has been demonstrated experimentally:
  ~10 GeV in 30 cm of plasma  ~30 GV/m
  42 GeV in 85 cm of plasma  ~50 GV/m

## Slide 41
Staging
More energetic
drivers
How to Reach Even Higher Energies?
Driver 1
Driver 2
Acc. Stage 1
Acc. Stage 2
Refocus
 AWAKE experiment
41
Goal: Keep interstage distance short

## Slide 42: Outline
Physics of plasma wakefields
Introduction
AWAKE Experiment
What’s next?
Summary
State of the Art

## Slide 43: The AWAKE Experiment @CERN

## Slide 44: What does AWAKE stand for?
0/0
Question slide
Join at: vevox.app
ID: 131-113-101
Applied Wakefield Acceleration of Kinetic Electrons
0%
Active Wakefield Acceleration via Kinetic Electrodynamics
0%
Advanced Wakefield Experiment
0%
Angry Wizards And Kryptonite Everywhere
0%

## Slide 45: What does AWAKE stand for?
0/0
Preparing Results
Join at: vevox.app
ID: 131-113-101
Applied Wakefield Acceleration of Kinetic Electrons
0%
Active Wakefield Acceleration via Kinetic Electrodynamics
0%
Advanced Wakefield Experiment
0%
Angry Wizards And Kryptonite Everywhere
0%
RESULTS SLIDE
✓

## Slide 46: AWAKE: Advanced Wakefield Experiment International Collaboration
46
Experiment @
19 Institutes Worldwide:
CERN, Geneva, Switzerland
University of Manchester, Manchester, UK
Cockcroft Institute, Daresbury, UK
Lancaster University, Lancaster, UK
Oxford University, UK
Max Planck Institute for Physics, Munich, Germany
Max Planck Institute for Plasma Physics, Greifswald, Germany
UCL, London, UK
UNIST, Ulsan, Republic of Korea
Philipps-Universität Marburg, Marburg, Germany
Heinrich-Heine-University of Düsseldorf, Düsseldorf, Germany
University of Liverpool, Liverpool, UK
ISCTE - Instituto Universitéario de Lisboa, Portugal
GoLP/Instituto de Plasmas e Fusão Nuclear, Instituto Superior Técnico, Universidade de Lisboa, Lisbon, Portugal
Technical University Munich, Munich, Germany
University of Wisconsin, Madison, US
Uppsala University, Sweden
Wigner Institute, Budapest
Swiss Plasma Center group of EPFL, Lausanne, Switzerland
46

## Slide 47: AWAKE is Unique in Using Proton Drivers
SPS Driver (19 kJ):
~ 200 GeV in ~200 m
~ 109 e-
LHC Driver (112 kJ):
~ 5 TeV in ~7 km
~ 109 e-
Highly-relativistic, highly-energetic (hundreds of kJ) bunches are available at CERN
Accelerating externally-injected electrons (e-) to GeV (SPS) or TeV (LHC) energy scale
P. Tuev, K. V. Lotov, PPFC 63, 125027 (2021)
A. Caldwell, K. V. Lotov, Phys. Plasmas 18, 13101 (2011)
47

## Slide 48: The AWAKE Plasma
Rubidium vapour cell.
The laser ionizes the outermost electron of each rubidium atom.
Desired plasma density: ~1-10x1014 electrons/cm3.

## Slide 50: AWAKE Requires Microbunching of p+ Bunch
To effectively excite wakefields:
The drive bunch length has to be on the order of the plasma wavelength
⇒ Plasma process: Self-Modulation Instability (SMI)
CERN SPS proton bunch length is ~6 cm
Wakefields driven resonantly to large amplitude
Self-modulation necessary to drive ~GV/m accelerating fields in 1014 cm-3 density plasma
For AWAKE  mm-scale bunch length
Resonant excitation
(7x1014 cm-3)

## Slide 51: Self-Modulation in Plasma Wakefields
Accelerating for negatively charged particles
Decelerating for negatively charged particles
Focusing for negatively charged particles
Defocusing for negatively charged particles
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 52: Self-Modulation Measurement Results
Plasma off:
Plasma off:
Plasma on:

## Slide 53
Shortly after we have observed the Seeded-Self Modulation for the first time!

## Slide 54: Frequency of Self-Modulation
Varied in the
experiment
Prediction:
Spacing of the microbunches  Plasma electron wavelength
Excellent agreement between prediction and measurement
Now used as a tool to measure plasma density only method at the % level
AWAKE Collaboration, Phys. Rev. Lett. 122, 054802 –2019
54

## Slide 55
Wakefield (blue)
Protons (red)
Focused micro-bunch
Defocused protons
Laser (green)
Gaussian proton beam distribution
e-

## Slide 57: First Electron Acceleration
No electrons accelerated.
Accelerated electrons.

## Slide 58
Image from: Yan Shen et alIE 11909, Tenth International Symposium on Ultrafast Phenomena and Terahertz Waves (ISUPTW 2021), 119090T (2021);

## Slide 59: Electron Acceleration Results
AWAKE Collaboration, Nature volume 561, pages 363–367 (2018)

## Slide 60
Shortly after we have observed electron acceleration for the first time!

## Slide 61: Let Us Repeat…
To realize the AWAKE experiment at CERN, we need:
  Plasma (vapor source + laser)
  Proton bunch (wakefield driver)
  Electron bunch (witness – to be accelerated)
AWAKE was able to show that:
  Proton bunches do self-modulate and drive high-amplitude wakefields
  Electrons can be accelerated in these wakefields to GeV energies

## Slide 62: Outline
Physics of plasma wakefields
Introduction
AWAKE Experiment
What’s next?
Summary
State of the Art

## Slide 63: Next: Two Plasmas
63
Expected parameter reach:
εN = (2-30) mm-mrad
Q = 100 pC, Ne-~6x109 e-
∆E/E = 5-8%
Run 2c: E ~ 4-10 GeV, 10m
Separate Self-Modulation from acceleration to accelerate bunches with quality
Experiments starting in 2029

## Slide 64: Next Next: Demonstration of Scalability Use Scalable Plasma Source for Acceleration
64
Expected parameter reach:
εN = (2-30) mm-mrad
Q = 100 pC, Ne-~6x109 e-
∆E/E = 5-8%
Run 2c: E ~ 4-10 GeV, 10m
Run 2d: E >10 GeV, 10+m, scalable
scalable
Experiments starting in 2030s

## Slide 65
Helicon source: magnetized RF discharge
Pulsed discharge
Buttenschön, PPFC 60(7), 075005 (2018)
Laser ionization does not scale to long plasma lengths (100m-1km): laser pulse energy depletion!
Plasma source development laboratory as part of AWAKE
Torrado, IEEE-TPS 51(12) (2023)
Scalable Plasma Source Development

## Slide 66: Most Recently: New Plasma Source Technology

## Slide 67
Xe
Xe
A = 131

## Slide 68
Ar
Ar
(A=40)

## Slide 69
He
He
(A=4)

## Slide 70: Motion of Ions Leads to Decoherence of Plasma Electron Motion
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
Rb+
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 71
tail

## Slide 72: Outline
Physics of plasma wakefields
Introduction
AWAKE Experiment
What’s next?
Summary
State of the Art

## Slide 73: What’s next?
Plasma wakefield acceleration is a developing concept  trying to make it a technology
  For colliders: high risk, high reward

## Slide 74: The next collider will need
Collision energy defines
what can you discover
Luminosity defines
how likely you are to discover
⇒ Cross section: probability of that a particular event occurs
Number of collisions are produced (per cm2 and per second).
E
L
Notes: A lot of opinions and a lot of discussion out there on what is the right thing to do and why,
We are accelerator physicist and we have to build a machine

## Slide 75: What’s next?
Plasma wakefield acceleration is a developing concept  trying to make it a technology
  For colliders: high risk, high reward
Next steps
  Produce also high-quality beams (with high charge)
  Start using them for first applications: medical accelerators, FELs, radiation generation,…

## Slide 76: Summary and Conclusions
Plasma wakefield acceleration is a novel technique to accelerate charged particles
  Advantage: Very high accelerating gradient, compact accelerators
  Proof of principle acceleration is demonstrated
AWAKE is an accelerator R&D experiment at CERN:
  Only proton-driven wakefield acceleration experiment worldwide
  The experiment opens a pathway towards particle physics applications
  Next step: aim for high beam quality in long plasmas first applications
Final Goal: Design high quality & high energy electron accelerator based on acquired knowledge.

## Slide 78
Leaderboard
Total participants: 0
🏆
Average Score: - / 5
Position
Participants
Score

## Slide 79: Join the Vevox session
Go to vevox.app Enter the session ID: 131-113-101 Or scan the QR code