## Slide 1: Radiation Hard embedded FPGA – Programmable Logic Array IP
Michael Karagounis
25.09.2023
2nd DRD7 Workshop CERN

## Slide 2: Motivation
State of the art chip-design methodology in HEP is based on hardwired non-programmable logic
  Advantage
    optimized hardware for specific application case
    High resource efficiency in terms of power and area consumption
  Disadvantage
    no flexibility
    bug fixes require costly design iteration
    reuse of chips in different projects and applications difficult
Embedded FPGA / Programmable Logic Array IP
  allow reprogramming/reconfiguration of logic for bugfixes and project adaption

## Slide 3: Collaboration Partners & Ressources
Imperial College London, Andrew Rose
  1 FTE, 1 MPW ASIC production
FH Dortmund, Michael Karagounis
  0.5 FTE 2024-2027, 1 Mini-Asic MPW production
    BMBF (applied, evaluation is still pending)
  0.5 FTE 2024-2025, 2 Mini-ASIC MPW production

## Slide 4: FHDO FPGA Development Background
Collaborating with Cologne Chip AG in design and characterization of the Gatemate FPGA
  Design is supported by EU (IPCEI) Important Projects of Common European Interest
  SRAM based FPGA in Globalfoundries 28 nm CMOS
radiation characterization in cooperation with CERN, Salvaore Danzeca & Rudy Ferraro
design and implementation of innovative architectures in TSMC 7 nm
Parameter | Detail
Logic Cells | 20,480 CPE correspond to * 20,480 8-Input-LUT trees or * 40,960 4-Input-LUT trees with * 40,960 FF/Latches
Block RAM | Total 1,280 Kb 20Kb blocks: 64 40Kb blocks: 32
PLLs | 4
SerDes 5 Gb/s | 1
I/Os | single-ended: 162 differential: 81 1.2V to 2.5V

## Slide 5: Plans
FHDO
  Study OpenFPGA and/or FABulous framework
  XML-to-Prototype Flow
    FPGA architecture is described in XML
    Backend flow creates “production ready” layouts
  FABulous offers partial reconfiguration
  Add radiation hardening features
    Error Detection & Correction in the Configuration Memory
    Scrubbing
    Reconfiguration
Imperial
  Support either Logic Array IP from industrial partner or develop own IP
  Develop software & infrastructure for synthesis and mapping of user-code

## Slide 6: Status
Project has been put on hold by steering committee
Call for participation of additional interested institutes