## Slide 1: Tuning studies with pyAT
Elaf Musa
Jul 23th, 2024
FCCIS – The Future Circular Collider Innovation Study. This INFRADEV Research and Innovation Action project receives funding from the European Union’s H2020 Framework Programme under grant agreement no. 951754.
1

## Slide 2
2
Table of content
Tuning simulations with SR:
- w & w/o zero crabbing
- Including:
    Dipole misalignments
    BPM misalignments
Z& tt bar lattice sensitivity to errors.
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 100 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 100 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 25 & 25 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 3
3
Nominal DA with synchrotron radiation
For V22 @ Z lattice
DA @ ca1.1
512 turns
sigma_x = 0.000452 sigma_y = 0.000018
Since last tuning meeting 28th June:
Adjusting proper RF parameters.
Iterations of Phase/RDT correction.
Constant correction of orbit and tune.
Zero crabbing :
k2sy2l=k2sy1l k2sy2r=k2sy1r
k2 of left sy is 6.291 while for right is -5.940
(AT sextupole strength notation is half the K2
values from MAD-X file)
Nominal chroma.=
[-0.01448, -0.060 , -0.0705]
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 4
4
After correction of alignment errors
elements | Hor. & Ver. displacement | Tilt θ
Arc quads and sext | 100 μm | 100 μrad
All dipoles | 150 μm | 150 μrad
20 seeds/ 1 failed seed
median εy = 0.091 pm
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 5
5
After correction of alignment errors
elements | Hor. & Ver. displacement | Tilt θ
Arc quads andsext | 100 μm | 100 μrad
All dipoles | 150 μm | 150 μrad
Zero crabbing
20 seeds/ 1 failed seed
median εy = 0.06 pm
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 6
6
Adding BPM misalignments
Appling BPM misalignments in PyAT
BPMs are attached to each quadrupole or to each sextupole.
Defining “Offset” field to BPM elements.
The values of each BPM offset are equal to the assigned offset errors to the corresponding quadrupole or sextupole
The hor. & ver. BPM offsets represent the new hor. & ver. reference orbit.
Orbit to be corrected = distorted orbit (At get optics function) – new reference orbit.
T2[0]
Ref orbit =0
New Ref orbit = T2[0]
BPM
s
x
Quad/sext
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 7
7
After correction of alignment errors
BPMs aligned to quadrupoles
elements | Hor. & Ver. displacement | Tilt θ
Arc quads and sext | 100 μm | 100 μrad
All dipoles | 150 μm | 150 μrad
BPMs | Same as quads. | -
20 seeds/ 1 failed seed
median εy = 0.029 pm
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 8
8
Z & tt lattice sensitivity to errors
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 9
9
IR
1000.07 / 1.599
99.898 / 0.7934
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 10
10
IR
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 11
11
Arc region
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 12
12
Change of optics with alignment errors (tt bar vs. z)
DX, DY misalignment errors assigned to all quadrupoles, sextupoles and dipoles.
tt bar
Z
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 13
13
tt bar
Z
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 14
14
tt bar
Z
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 15
15
tt bar
Z
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 16
16
tt bar
Z
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 17
17
Summary
Removing the crabbing from the V22 Z lattice had a marginal impact on the tuning results.
Adding BPMs and dipoles misalignments led to the failure of some seeds.
The lattice is less sensitive to errors and is therefore easier to correct compared to the Z lattice.
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 18: Thank you for your attention

## Slide 19: Backups

## Slide 20
20
After correction of alignment errors :
Elements | Hor. & Ver. displacement
Arc quads and sext | 100 μm
All dipoles | 150 μm
20 seeds
median εy = 0.159 pm
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 21
21
After correction of alignment errors
Elements | Hor. & Ver. displacement
Arc quads and sext | 100 μm
All dipoles | 150 μm
Zero crabing
20 seeds/ 1 failed seed
median εy = 0.10 pm
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 22
22
After correction of alignment errors
BPM aligned to sextupoles
Elements | Hor. & Ver. displacement
Arc quads and sext | 100 μm
All dipoles | 150 μm
BPMs | Same as sext.
20 seeds/ 2 failed seed
median εy = 0.81 pm
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}

## Slide 23
23
Z and ttbar parameters
Number of Elements | z | Tt bar
IR quads | 436 | 488
IR sext | 64 | 96
Arc quads | 1856 | 3324
Arc sext. | 632 | 2368
Dipoles | 3056 | 3056
Notes: Ttbar, 4IP lattice. These are the main results.
%$\epsilon_{x, \textrm{median}} = 1.509$ nm rad \\
%$\epsilon_{y, \textrm{median}} = 0.353$ pm rad \\
$\frac{\epsilon_{y}}{\epsilon_{x}} = 0.023$ $\%$ \\
\begin{table}[htb!]
\centering
\begin{tabular}{p{3cm}cccccc}
\hline
Type & $\Delta$X & $\Delta$Y & $\Delta$PSI & $\Delta$S & $\Delta$THETA & $\Delta$PHI \\
& ($\mu$m) & ($\mu$m) & ($\mu$rad) & ($\mu$m) & ($\mu$rad) & ($\mu$rad) \\
\vspace{.1cm} \\
\hline
Arc quadrupole* & 100 & 50 & 300 & 150 & 70 & 70 \\
Arc sextupoles* & 100 & 50 & 300 & 150 & 70 & 70 \\
\hline
Dipoles & 1000 & 1000 & 300 & 1000 & 0 & 0 \\
\hline
Girders & 200 & 200 & - & 1000 & 0 & 0 \\
\hline
IR quadrupole & 100 & 100 & 250 & 200 & 70 & 70 \\
IR sextupoles & 100 & 100 & 250 & 200 & 70 & 70 \\
%\hline
% BPM** & 40 & 40 & 100 & - \\
\hline
\end{tabular}
\end{table}