## Slide 1: Readout Software
Jüri Jõul
03.09.2024

## Slide 2: What will not be covered
Some software on FECs:
  BGIPXL FESA class (next presentation)
  FESA classes related to slow control:
    Power supplies
    Cooling
    Temperature probes
PLC software
  A complexity in its own right!
Slow control GUI
Operator GUI
Vistar
Beam loss removal / post-processing

## Slide 3: Introduction
Overview of the BGI software stack

## Slide 4: Simple overview
Three main groupings
  SoC
  FEC
  User applications (expert and OP)
Three main communication channels
  HTTP/REST
  PyJapc
  IPbus
Two languages
  C++
  Python
Data flow
OP
VM
FEC
SoC
PL-FPGA
OP GUI
BIPXL Expert API (Pybind11 + Python)
Expert GUI (Python)
BIPXL Software Driver (C++)
BIPXL API (C++)
FESA (C++)
BIPXL Internal Driver (C++)
Pybind11 Python wrapper (C++)
Custom Wishbone module (Python)
REST server (Python)
Event Processing Application (C++)
IPbus ControlHub
nginx reverse proxy
PS
HTTP
PyJapc
IPbus

## Slide 5: SoC software
A more detailed look into software components

## Slide 6: Internal Driver (C++)
Purpose
  Library to abstract register level functionality
  Provides unified interface for hardware access
Technologies
  Standard libraries
  CMake
Key features
  Quasi-object-oriented
    Organised by functionality:
      Readout, Detectors, Acquisition
Interactions
  Gateware: UIO and DMA
  REST server: via Python bindings
OP
VM
FEC
SoC
PL-FPGA
OP GUI
BIPXL Expert API (Pybind11 + Python)
Expert GUI (Python)
BIPXL Software Driver (C++)
BIPXL API (C++)
FESA (C++)
Pybind11 Python wrapper (C++)
Custom Wishbone module (Python)
REST server (Python)
Event Processing Application (C++)
IPbus ControlHub
nginx reverse proxy
PS
HTTP
PyJapc
IPbus
BIPXL Internal Driver (C++)

## Slide 7: Pybind (C++/Python) and Python
Purpose
  Wraps C++ Internal Driver for Python
  Provides direct Python access to hardware using UIO
    Legacy functionality, to be removed
Technologies
  Pybind11 library for wrapping C++ code
  NumPy for both pure-Python implementation of memory mapping, but also arrays, etc, in the wrapper
Key features
  Organised similarly to the Internal Driver
  Enables scripting on the SoC
    Still, C++ is preferable
Interactions
  Internal Driver
  REST server
OP
VM
FEC
SoC
PL-FPGA
OP GUI
BIPXL Expert API (Pybind11 + Python)
Expert GUI (Python)
BIPXL Software Driver (C++)
BIPXL API (C++)
FESA (C++)
BIPXL Internal Driver (C++)
REST server (Python)
Event Processing Application (C++)
IPbus ControlHub
nginx reverse proxy
PS
HTTP
PyJapc
IPbus
Pybind11 Python wrapper (C++)
Custom Wishbone module (Python)

## Slide 8: REST server (Python)
Purpose
  Exposes a unified interface of the readout system
    Language agnostic: different clients
  Brings complexity from client to server
    Compared to IPbus
Technologies
  Flask-RESTX as the web framework
Key features
  Organisation of resources similar to the underlying layers
  User input validation
  Error propagation
  Web UI for debugging/testing/exploration (next slide)
Interactions
  Python C++ wrappers and pure-Python implementations
  Clients via HTTP
OP
VM
FEC
SoC
PL-FPGA
OP GUI
BIPXL Expert API (Pybind11 + Python)
Expert GUI (Python)
BIPXL Software Driver (C++)
BIPXL API (C++)
FESA (C++)
BIPXL Internal Driver (C++)
Pybind11 Python wrapper (C++)
Custom Wishbone module (Python)
Event Processing Application (C++)
IPbus ControlHub
nginx reverse proxy
PS
HTTP
PyJapc
IPbus
REST server (Python)

## Slide 10: Event Processing Application (C++)
Purpose
  Processes Timepix3 data according to timing events
  Produces beam profiles
Technologies
  Standard libraries
  CMake
Key features
  Standalone application
  Minimal hardware configuration
    Might be removed
  Utilises interrupts
Interactions
  REST server via shared memory (metadata)
  REST server via DMA buffer (profiles)
  REST server via HTTP (configuration)
OP
VM
FEC
SoC
PL-FPGA
OP GUI
BIPXL Expert API (Pybind11 + Python)
Expert GUI (Python)
BIPXL Software Driver (C++)
BIPXL API (C++)
FESA (C++)
BIPXL Internal Driver (C++)
Pybind11 Python wrapper (C++)
Custom Wishbone module (Python)
REST server (Python)
IPbus ControlHub
nginx reverse proxy
PS
HTTP
PyJapc
IPbus
Event Processing Application (C++)

## Slide 11: FEC software
A more detailed look into software components

## Slide 12: BIPXL API (and the software driver)
Purpose
  Provide a simple interface for the FESA class
  Include high-level business logic that does not fit into the Internal Driver
Technologies
  IPbus (raw data)
  nlohmann::json
  httplib (communication with REST server)
  Makefile Generic
Key features
  Even higher level than previous layers
  Automated configuration and masking
  Raw data readout
Interactions
  REST server via HTTP
  FESA class
  Filesystem for saving raw data
OP
VM
FEC
SoC
PL-FPGA
OP GUI
BIPXL Expert API (Pybind11 + Python)
Expert GUI (Python)
FESA (C++)
BIPXL Internal Driver (C++)
Pybind11 Python wrapper (C++)
Custom Wishbone module (Python)
REST server (Python)
Event Processing Application (C++)
IPbus ControlHub
nginx reverse proxy
PS
HTTP
PyJapc
IPbus
BIPXL Software Driver (C++)
BIPXL API (C++)

## Slide 13: Client-side software
A more detailed look into software components

## Slide 14: Expert GUI
Purpose
  Enables expert users to set up and monitor the instrument
Technologies
  PyQt5 and related dependencies
  AccWidgets
  Qt Designer for UI design
  PyJapc
  PyCCDA
Key features
  Configuration and control of detectors, acquisition, various displays, masking, etc…
Interaction
  FESA via PyJapc
  CCDB via PyCCDA
  REST server via HTTP requests
OP
VM
FEC
SoC
PL-FPGA
OP GUI
BIPXL Software Driver (C++)
BIPXL API (C++)
FESA (C++)
BIPXL Internal Driver (C++)
Pybind11 Python wrapper (C++)
Custom Wishbone module (Python)
REST server (Python)
Event Processing Application (C++)
IPbus ControlHub
nginx reverse proxy
PS
HTTP
PyJapc
IPbus
BIPXL Expert API (Pybind11 + Python)
Expert GUI (Python)

## Slide 16: Improvements
In the past year and ongoing

## Slide 17: Stability of the readout system
Identified and fixed multiple memory leaks and memory-related issues in our software
  Avoiding manual memory management in C++
  More correct usage of shared memory
    No more leaks
  Hidden complexity: C++ and Pybind11 interplay
    E.g. double freeing of memory
Result: more stability, better understanding of our system
  In future, we know how to avoid potential dangers/gotchas

## Slide 18: Reworking error handling
Previously, problems with propagating errors between different layers
  Example: REST server  various clients (FESA, Expert API)
  In some cases, invalid states / errors were not detected
Solutions
  Using Flask-RESTX’s built-in exception handling capabilities in combination with rethrowing exceptions on the client side.
  We have also added further user input validation to different layers (at the interfaces) of the software, so that we would discover problems as early as possible, and not let them propagate through the system.
Result: more responsive and reliable system
Additionally, reduced cost of software maintenance (less duplication of custom checks / error handling)
  Also easier to understand and reason about the code

## Slide 19: Settings management (I)
Identified problem: disjointed settings files
Proposal: centralised settings management
  FESA as the single source of truth
  Including the possibility of InCA/LSA
  In line with BI-TB recommendations
Involved reworking all parts of the software stack
  Eradicating dependencies on settings files
  Settings can instead be accessed via FESA or via REST, which gets its settings directly from FESA
  Among other things, almost complete redesign of BIPXL API

## Slide 20: Settings management (II)
Related changes:
Automated pixel masking
  Easier to implement than before
  Leads to fewer expert interventions on operational instruments
Faster reconfiguring of the detectors
  Due to some redesign, we can more easily configure the detector periphery in parallel
  Can also load the pixel masks more quickly
  This leads to better effective radiation hardness and robustness

## Slide 21: Logging
Previously, no logging on SoC
With the help of the tracing team (BE-CSS-CPA), we have now implemented logging functionality in our software stack
  Including LUMENS-based configuration of the FECs
This enables us to detect and investigate problems with much more ease, leading to increasing system reliability over time
We can also monitor chosen parameters of our system (e.g. memory usage), further helping us in analysing our system’s performance

## Slide 22: Quality of life (and code) improvements
Reducing technical debt (in addition to better memory management)
  Removing code duplication
  Avoiding global state
  Increasing cohesion and modularity
  Adding tests
  Partial support for cross-compilation and testing
  All of the above improve the software and reduce maintenance cost!
Better access to software on the SoC
  GitLab access – leads to quicker development and updates
Reverse proxy
  Easier access to instruments
Revived equalization procedure
  As script
Long list of small improvements/modifications…

## Slide 23: Current problems
And complexities

## Slide 24: Internal Driver + Python + REST server
Problems:
  Non-uniform hardware access
    Via Internal Driver or Python module
  Global state
    Difficult to understand and test
Solutions:
  Remove standalone Python module
  Rework/refactor to reduce global state

## Slide 25: Event Processing Application
Problems:
  Inefficient – waits too long to start processing
  Not well-behaved
    When signals arrive out of order
    When there is no injection
  Mixed control and data readout – race conditions
  Duplication of raw data processing (REST server)
Solutions:
  Review and improve the processing logic
    Start processing as early as possible
  Create a state machine more tolerant towards missing events
    Utilise logging and status flags to notify users of issues
  Move hardware control to REST server
  Move all event processing functionality to REST server?

## Slide 26: BIPXL API
Problems:
  Legacy dependencies
    BIPXL Software Driver
  Two communication channels
    HTTP/REST
    IPbus
  Complicated and inflexible build system
  Complicated testing – meant to run on TN-trusted machines
Solutions:
  New raw data readout
  Remove one channel?
    Or FESA-on-SoC
  Use CMake instead?
  Extract platform independent functionality

## Slide 27: Expert GUI
Problems:
  Very high complexity
    Rarely used functionality also needs maintenance
    High coupling
  Non-standard components
    Mutually exclusive dependencies with new GUI initiatives
  Multiple communication channels and paradigms
    HTTP/REST – get/set
    PyJapc – get/set/subscribe
Solutions:
  Reduce complexity by
    Move supporting functionality to scripts?
    GUI design patterns (MVP)
  New implementation from ground up?
  Everything via PyJapc?

## Slide 28: Stack-wide problems
Problems:
  Non-standard solutions – more development effort
    Communication channels/protocols
    Development tools
    Linux
  Overall stack complexity
Solutions:
  FECOS and FESA-on-SoC
  Diligent refactoring/redesigning

## Slide 29: Outlook
Future of the software stack

## Slide 30: Consolidation of FEC and SoC software
BIPXL Internal Driver (C++)
FECOS and the FESA-on-SoC project
  Simplifies software stack
  Provides common standard functionality, such as logging capabilities, CI/CD, etc
  No need for custom Linux
OP
VM
FEC
SoC
PL-FPGA
OP GUI
BIPXL Expert API (Pybind11 + Python)
Expert GUI (Python)
BIPXL Software Driver (C++)
BIPXL API (C++)
FESA (C++)
BIPXL Internal Driver (C++)
Pybind11 Python wrapper (C++)
Custom Wishbone module (Python)
REST server (Python)
Event Processing Application (C++)
IPbus ControlHub
nginx reverse proxy
PS
HTTP
PyJapc
IPbus
OP
VM
SoC
PL-FPGA
OP GUI
Expert GUI (Python)
BIPXL API (C++)
FESA (C++)
Event Processing Application (C++)
PS
HTTP
PyJapc
IPbus

## Slide 31: Alternative architecture
Standalone data processing server
SoC readout for fast data transfer
  No on-board processing
Raw data available for everybody
OP
VM
FEC
SoC
PL-FPGA
OP GUI
BIPXL Expert API (Pybind11 + Python)
Expert GUI (Python)
BIPXL Software Driver (C++)
BIPXL API (C++)
FESA (C++)
BIPXL Internal Driver (C++)
Pybind11 Python wrapper (C++)
Custom Wishbone module (Python)
REST server (Python)
Event Processing Application (C++)
IPbus ControlHub
nginx reverse proxy
PS
HTTP
PyJapc
IPbus
Data processing server + NXCALS

## Slide 32: Conclusion

## Slide 33: Conclusion
Many problems already identified
Actively working on improving software
Eagerly awaiting FECOS / FESA-on-SoC
Alternative architectures possible – up for discussion