## Slide 1: Impedance modelling and equipment design
Chiara Antuono, Michela Neroni on behalf of
H. Bursali, E. De La Fuente, M. Diaz, G. Favia, L. Giacomel, I. Karpov, P. Krkotic, A. Lasheen, J. Li, N. Mounet, B. Salvant, L. Sito, C. Vollinger, M. Zampetakis, C. Zannini
and the big support of:
W. Andreazza, M. Barnes, G. Bregliozzi, S. Calatroni, J. A. Ferreira Somoza, R. Franqueira Ximenes, D. Mirarchi, C. Pasquino, A. Perillo Marcone, S. Redaelli, R. Seidenbinder, J. Sestak.
11th December 2024, JAP Workshop, Montreux

## Slide 2: Introduction

## Slide 3: Introduction
Equipment degradation or damage due to beam induced heating and/or sparking, perturbation to electronics (EMI issues)
Beam quality degradation and beam instabilities
Impedance-induced effects
When facing cross section variations of the vacuum chamber wall, as well as its finite resistivity, charged particles travelling in the accelerator, induce electromagnetic fields mainly left behind the source particle.
 Wakefield
Effect can be quantified through
Beam coupling impedance
FFT
 Accurate and up-to-date accelerator impedance model is crucial

## Slide 4: Methodology
Close collaboration between impedance team and equipment owners,
Allocation of time for impedance validation.
Impedance modelling of each component and optimization
Accelerator impedance model
Electromagnetic simulations
e.g. CST Studio Suite®
Beam dynamics simulations
Accurate prediction of accelerator performance
New equipment design
RF bench measurements
 Needed for validation of component before any installation
Ʃ
Beam dynamics observations and accelerator upgrades

## Slide 5: Methodology
Beam dynamics observations and accelerator upgrades
Complex loads installation on 630 MHz HOM-couplers - SPS 200 MHz cavity
P. Kramer, PhD Thesis
PSB horizontal instability post LIU
New region explored
SPS dark impedance
E. De La Fuente, et al., HB2023
C. Antuono, et al., IPAC24

## Slide 6: Impedance studies in the CERN complex
 | 2023 | 2024
Unshielded pumping manifold |  | 
Rotary wire scanners |  | 
Injection kicker MKI-cool |  | 
TDIS |  | 
Vacuum modules |  | 
Not limited beam operation with no hardware failure
Limited beam operation with no hardware damage
Limited beam operation with hardware damage
PS
SPS
LHC
Impedance modelling is a constant work on going and it often requires dedicated students' projects.
Here covering impedance related studies and observations in the CERN complex for 2023-24.
Many other accelerator components to be followed up…
 Complete overview for 2025 and HL-LHC in conclusions
Close to limit, requires impedance optimization

## Slide 7: Impedance-related observations in the CERN complex in 2023/24

## Slide 8
Unshielded pumping manifold (PS)
Observations in 2023 and 2024 of high frequency modulation at transition crossing for ion and proton beams (AWAKE)*.
Impedance source identified in high frequency range (1.2 GHz)  vacuum equipment: unshielded pumping manifold.
Close to longitudinal stability limit also for AWAKE beam: about 15-20% margin in longitudinal emittance.
See talk by A. Lasheen at IPP
E. Vinten, et al., IPAC23
ILHC75ns#3b
28/11/2024
Avoided through emittance blow up
However, uncaptured beam observed at flat top.
Courtesy of J. Flowerdew
Current operational conditions close to the stability limit. Further improvements in beam quality or performance requires impedance optimization.
Combined impedance and beam dynamics study necessary for a full understanding of limitations and possible future bottlenecks.
* Impact on other beams to be evaluated.
 Follow up for prototype shield is ongoing

## Slide 9
Rotary wire scanners (SPS)
  Following the failure of 4 wire scanners in April 2023, impedance mitigation was put in place with 5 ferrite tiles and RF coupler.
Impedance mitigation put in place in 2023 remains effective.
No limitations foreseen if the fork is in parking position.
Wire breakage happened with 4x72b, p/b  was predicted with accurate impedance simulations and beam induced heating calculations*.
Observations in 2024 run:
Task force impedance study 2023:
RF coupler
Fork in parking position
Fork in stuck configuration in July 2024 for one wire scanner (more info in I. Ortega Ruiz talk, “Beam instrumentation (focus up to 2026)”).
strong resonance at 380 MHz, lead to 70% power dissipated on the wire
Up to 10 kΩ
*L. Sito, ABP meeting
*E. De La Fuente, IPP

## Slide 10
LHC injection kickers - MKI-cool
MKI-cool:
2 MKI-cool already installed and successfully tested in 2023 and 2024 in Point 8 (more info in G. Favia talk, “ABT Equipment: Operational Insights and Future Perspective”).
2 more MKI-cool to be installed in Point 8 during YETS24/25.
  Full upgrade of Point 2 with 4 MKI-cool foreseen for LS3 (plus 4 additional spares)
water cooling of RF damper was necessary in view of HL-LHC beams
Reduction of beam induced heating in view of HL-LHC beams required an impedance optimization of the design* verified with simulations and benchmarked through stretched wire measurements.
* M. J. Barnes, 13th HL-LHC meeting
RF Damper
(ferrite ring)
Magnet
Beam
Screen conductors
Alumina tube
Cooling pipes
Metallization
Courtesy of G. Favia
H. Day, PhD Thesis

## Slide 11: TDIS high temperature readings
2023: Unexplained high temperature signals in the RF screen: caused interlocks and limited LHC filling
In the LHC injection beam dumps protection elements are installed, particularly two Target Dump Injection Segmented (TDIS):
  TDIS002 in point 2
  TDIS001 in point 8
Carbajo Perez, David, et al. at IPAC2021
For each TDIS module:
  6 temperature probes : 4 on jaws and 2 on the screen
Module A
Module B
Module C
5.8 m

## Slide 12: TDIS high temperature readings
Temp. decrease with opened jaws
2023: Unexplained high temperature signals in the RF screen: caused interlocks and limited LHC filling
Temp. increase with closed jaws
Reaching the interlock…
interlock
Temp. decrease with opened jaws

## Slide 13: TDIS: 2023 Vs 2024
2023:high temperature signalscaused interlocks and limited LHC filling
2024: spare TDIS were installed
2024:significantly lower temperature signals no limitations in the LHC
Which is the cause of the different behavior?
The 2023 and 2024 TDIS are supposed to be identical
2023: Hybrid filling scheme beam
2024: Standard beam with 3x36b

## Slide 14: TDIS : correlations with impedance studies
Impedance measurements on 2023 TDIS*:
  Electromagnetic (EM) coupling with probes
    Correlations with temperature readings:
      EM coupling higher with closed jaws
      EM coupling higher with screen probes (interlock)
      EM coupling significantly higher for TDIS in point 8 (interlock)
  Unexpected low frequency resonance detected
* L. Giacomel et al. at the 81st IWG, * L. Sito et al. at the 92nd IWG
Development of impedance model ongoing:
  Low frequency resonances with missing contact
  Factor 4 higher beam induced power on the probe with missing contact
Preliminary model results
The non-conformities might explain the higher temperature readings and the different behavior observed on 2023 TDIS
2023 TDIS: presence of non-conformities:
  Partially lost finger contact
  Melted spring

## Slide 15: TDIS in 2025 Run
2025 TDIS will benefit of several improvements
  Improved shielding of existing screen temperature probes
  Two additional fully shielded screen temperature probes
Impedance measurements* on 2025 TDIS:
  Contrary to 2023, no correlations with jaw aperture, probe type and
  TDIS device
  Moreover, the unexpected low frequency resonance not detected
Impedance measurements on 2024 TDIS desirable
For conforming TDIS no impedance induced issues are expected
* L. Sito et al. at the 92nd IWG meeting
The issue in 2023 seems to be correlated with the observed non-conformities
To be confirmed after inspecting the 2024 TDIS
However, the origin of the non-conformity is unknown
Impedance measurements

## Slide 16: LHC vacuum module: impedance understanding
Pipe tube
RF fingers
Tension spring
2023: Pressure spikes and impossibility to fill the LHC
Localized heating on the tension spring of ID212
1 week downtime for LHC
Big effort to build an accurate impedance model to address the issue
  impedance bench measurements
  impedance simulations
2023 JAP talk, C.Antuono & P.Krkotic
ID212
Validation of the impedance model

## Slide 17: LHC vacuum module: impedance understanding
Pipe tube
RF fingers
Tension spring
two beams
beam offset
non ideal contact fingers/tube
2023: Pressure spikes and impossibility to fill the LHC
Localized heating on the tension spring of ID212
Impedance studies revealed EM field leakage inducing localized heating on the spring compatible with the spring breakage
beam
In presence of
Intensity limitation set at 1.6 1011 p/b for 2024 (by CERN management)
1 week downtime for LHC
Big effort to build an accurate impedance model to address the issue
  impedance bench measurements
  impedance simulations
  Analytical computations using BIHC*
2023 JAP talk, C.Antuono & P.Krkotic
ID212
* https://github.com/ImpedanCEI/BIHC
3D plot generated with wakis

## Slide 18: LHC vacuum module in 2024 Run
Intensity limitation 1.6 1011 p/b
Mitigation strategy:
  1. Beam operation in 2024:
    intensity limitation at 1.6e11 p/b
    interlock for bunch length lower than 1.2 ns (never reached, more on A. Calia talk)
Deformable RF fingers (DRF)
Optimized unshielded bellows
No pressure spikes or failure detected in 2024
More at the 2023 JAP talk-C.Antuono and P.Krkotic
2358
Year | Numbers of . ID212
2023 | 71
2024 | 24
Replace/transform ID212 spring+fingers
with newly designed modules wherever it is possible

## Slide 19: LHC vacuum module in 2025 Run
Year | Numbers of . ID212
2023 | 71
2024 | 24
2025 | 4
Beam induced heating at least halved compared to the heating of the failed ID212
1 beam
Mitigation strategy:
  1. Beam operation in 2024:
    intensity limitation at 1.6e11 p/b
    interlock for bunch length lower than 1.2 ns (never reached, more on A. Calia talk)
  Replace/transform ID212 spring+fingers with newly designed modules wherever it is possible

## Slide 20: LHC vacuum module in 2025 Run
Year | Numbers of . ID212
2023 | 71
2024 | 24
2025 | 4
Beam induced heating at least halved compared to the heating of the failed ID212
1 beam
Mitigation strategy:
  1. Beam operation in 2024:
    intensity limitation at 1.6e11 p/b
    interlock for bunch length lower than 1.2 ns (never reached, more on A. Calia talk)
  Replace/transform ID212 spring+fingers with newly designed modules wherever it is possible
2700

## Slide 21: LHC vacuum module in 2025 Run
Elliptical modules
  The most dangerous (bigger aperture 128-53) already significantly less critical w.r.t circular ID212
  Failure can still be reached depending on the contact quality
1. Smaller ID expected to be less critical (C. Zannini talk at Chamonix ‘24)
The bottleneck is the circular ID212
These curves can be lifted up by removing the remained 4 ID212
What about the other modules with the critical spring+fingers design ?
Expected failure

## Slide 22: 3. LHC Impedance model update

## Slide 23
Update on LHC impedance
 | Longitudinal Increase of effective Im(Z/n) w.r.t . baseline* | Transverse Increase of octupolar current w.r.t .baseline*
Unshielded bellows | 0.35 mΩ | < 0.001
DRFs | 0.13-0.67 mΩ | < 0.01 A
TWO CRYST | < 0.02 mΩ | < 0.01 A
Rotated Roman Pots |  | 
CMS Double bellows | 0.45 mΩ | 0.03 A
MKIs-cool | TBC | -0.1 A
LHC: Impact on stability with p/b is:
  Negligible in transverse
  Acceptable in longitudinal
HL-LHC: longitudinal stability is more critical *
  Higher intensity and HOMs from crab cavities
Machine developments (MD) studies are needed to
  Test/refine the LHC impedance model
  Refine the longitudinal stability limit
MD in 2024 with p/b with ~1000 bunches at flat bottom allowed the beam to circulate for about 1 hour.
  In 2025/26 MDs with higher number of bunches will be required to assess beam stability and losses
    Particularly needed for HL-LHC
Devices to be installed during YETS 24-25
* M. Zampetakis's talk at the HiLumi annual meeting
* C. Lannoy’s talk at the HiLumi annual meeting
Vacuum module consolidation
Double crystal experiment in IR3
In only with stable beams
current to keep the beam stable
Longitudinal baseline: 75-135 mΩ *
Transverse baseline> 300 A *

## Slide 24: Conclusions
 | 2023
Unshielded pumping manifold | 
Rotary wire scanners | 
Vacuum module | 
TDIS | 
Injection kicker MKI-cool | 
Beam impedance limitations observed in the LHC and injectors during RUN 3
2023
Not limited beam operation with no hardware damage
Limited beam operation with hardware damage
2024
Limited beam operation with no hardware damage
PS
SPS
LHC

## Slide 25: Conclusions
 | 2023
Unshielded pumping manifold | 
Rotary wire scanners | 
Vacuum module | 
TDIS | 
Injection kicker MKI-cool | 
Not limited beam operation with no hardware damage
Limited beam operation with hardware damage
Beam impedance limitations observed in the LHC and injectors during RUN 3
  Most of them have been addressed, particularly thanks to the development of accurate impedance models
2024
Limited beam operation with no hardware damage
PS
SPS
LHC

## Slide 26: Conclusions
 | 2023 | 2024
Unshielded pumping manifold |  | 
Rotary wire scanners |  | 
Vacuum module |  | 
TDIS |  | 
Injection kicker MKI-cool |  | 
Not limited beam operation with no hardware damage
Limited beam operation with no hardware damage
Limited beam operation with hardware damage
To be followed up for Run 3
Not expected limitations for
p/b
MD: with bl >1.2 ns
Others… | 2023 | 2024
Extraction kicker KFA14 |  | 
MKP-S |  | 
Beam Gas Ionization (BGI) | Not yet installed | 
MKDH |  | 
Crystal goniometers |  | 
TCLD and E4R5 |  | 
To be followed up for HL
Reaching p/b is a key step to further exploit additional limitations during the remaining time of Run 3
  MDs with p/b at injection provide valuable input for refining impedance models and stability limit
Step forward the readiness of HL-LHC
Beam impedance limitations observed in the LHC and injectors during RUN 3
  Most of them have been addressed, particularly thanks to the development of accurate impedance models
2025/26
PSB
PS
SPS
SPS
LHC
LHC
- Mitigation studies
- Continuous monitoring
- Finalizing understanding
- Finalizing installations
2025/26
Further understanding for higher intensity MDs

## Slide 27: Thank you! 

## Slide 28: Backup

## Slide 29: PSB extraction kicker KFA14
PSB horizontal instability post LIU
C. Antuono, et al., IPAC24
PSB horizontal kicker instability
-Not limited 2024 Run
-However, with the aim of increasing intensity (and the energy , e.g. ISOLDE) both the instabilities at 1.6 GeV and 1.3 GeV might be a limitation
Activity already observed during measurements for the 1.3 GeV instability increasing the intensity up to 1.28e13 p/b with the TFB on.
The change of tune for the 1.3 GeV to mitigate the instability (as for 1.6 GeV) cannot be done easily since the curve of energy with tune is quite flat
  tune has to change a lot to push the instability!
Latest impedance model based on more precise kicker circuit info (including filters)
C. Zannini et al. at Zermatt 2019 MCBI proceeding
Sacherer stability criteria

## Slide 30: MKP-S kicker
The new MKP-L exhibits a beam induced heating significantly lower than the present MKP-S
Critical kicker for beam induced heating is now the MKP-S: 2023 scrubbing had to be modulated to accommodate MKP-S heating
C. Zannini at the CEI section meeting-22-02-24
MKP-S impedance mitigation option
10-20 mm beam offset towards ground conductor
  First test foreseen during 2024 scrubbing run
Power loss expected to be almost halved with 20 mm offset
Circulating
beam
Impedance mitigation successfully tested in the SPS!
Mitigation will be implemented during LS3

## Slide 31: TCLD pressure spikes in the LHC
TCLD:
  Pressure spikes observation for some fills during injection and energy ramp
  Not clear if impedance is involved
  Movement of TCLD jaws show no direct correlation with the pressure spikes and with measured temperatures on the jaws
  Higher spikes (>1e7 mbar) stopped from 16th Sept. 2024

## Slide 32: Pressure spikes in E4R5 sector of LHC
4R5:
  Pressure spikes close to interlock observation during MD at 2.3e11p/b with 1000 bunches at inj.
    They might reach interlock for future MDs with 2.3 and higher No.bunches
  Already some spikes in 2022
  Suspects:
    RF bridge close to a sector valve (possible inspection during LS3)
    Non-conformity on the BQS revealed so far (already detected during intervention in YETS 22-23)
Courtesy of E. Metral (451st LMC meeting)

## Slide 33: Vertical Scan In Between the Jaws (half Gap 6 mm)
L. Teofili at the 37th IWG meeting
Longitudinal Impedance
TDIS
Notes: Vertical Scan in between the jaws with half gap 6 mm.
When really close to the jaw, two modes at approximately 800 Mhz appears, in red in the picture.
The mode at 1.06 it is present in the figure.

## Slide 34: TDIS
hybrid
standard

## Slide 35: LHC crystal goniometers
  After years of crystal collimation in the LHC in IR7
    From 2023 channelling position of crystal was drifting during operation with strange temperature readings
      newly installed goniometers (2 devices, 1 Hor. and 1 Ver.)
    Observations demonstrated that the drift was related to the beam intensity
    Suspect on beam induced heating from Impedance on crystal and holder
      However, the expected crystal drift from was in the opposite direction of the observed one
      Suspect fell on tank movements (maybe coming from different causes) and sensor will be installed in YETS24/25
      Ongoing studies/to be followed up
    No limitation in 2024 ion RUN thanks to an implemented automatized crystal positioning correction
      HL ion intensity already surpassed the HL goal
  Crystal goniometers might be a concern for new experiments using crystal with higher proton intensity
    TWOCRYST plans low-intensity tests
    Future experiments based on double-crystal setups, like ALADDIN ,need new design compatible with nominal HL proton beam

## Slide 36
Titanium coated ceramic rod
NEG coated ceramic cathode
SPS-BGI impedance study
Courtesy of H. Bursali, J. Storey, E. De La Fuente
H. Bursali, C. Vollinger, CERN internal note
Problem
Loss of communication (synchronisation) with Timepix3 dataout signals & corruption of pixel matrix registers during:
  AWAKE cycle after bunch rotation, and
  LHC25NS cycles.
Timepix3 recovered after reloading registers (100 ms - 1 s).
Communication problem not observed on any other beams (SFTPRO, LHC3.)

## Slide 37
SPS-BGI Impedance Study
Courtesy of J. Storey , 94th IWG meeting
EMC Lab* Findings & Actions
Radiated RF from the HV cable, coupling to the signal cables, is a plausible mechanism for the SPS BGI EMI problems.
Found -45dB coupling between stretched wire & HV cable, but no direct coupling between stretched wire and Timepix3 signals.
Actions during YETS 24/25:
Add shielding to both HV & signal cables;
Fit ferrites to the HV cable.
On the new SPS BGI-Vertical install denser Faraday shield over the detectors.
High Voltage Feedthrough
Signal & Low Voltage Feedthroughs
Timepix3 inside Faraday Cage
Beam
(*) Many thanks to Daniel Valuch (SY-RF)

## Slide 38
MKDH – SPS beam dump kicker system
  Alumina tube coated on the inside with Cr2O3:
    has a low SEY
    does not produce dust in the vacuum system
    is beneficial for high voltage issues
Feasibility study ongoing for a ceramic chamber that can fit spares and operational magnets MKDH (currently 3 MKDH, 2 different types).
Ceramic chamber mainly foreseen to improve conditioning and avoid missing kicks.
Optimization of the chamber design ongoing to prevent impedance issues as well as high voltage ones.
Courtesy of Dylan Standen
More info in G. Favia talk, “ABT Equipment: Operational Insights and Future Perspective”).

## Slide 39
Instability thresholds at flat bottom for 𝑉rf = 8 MV:
HOM -
BB - ,
LHC longitudinal impedance and Loss of Landau Damping
I. Karpov, Special Joint WP2/WP4/WP7 meeting, June 2024
*LHC design report
*

## Slide 40
LHC longitudinal impedance and Loss of Landau Damping
Observation of oscillation amplitude (measurements vs. simulations) allows extraction of effective impedance ImZ/n and cut-off frequency
 Discrepancy between recent measurements and simulations was observed (M. Zampetakis, et al., HL-LHC collaboration meeting 2024)
Investigation of the validity of the longitudinal impedance model is crucial. Missing components?
Larger oscillation amplitude in measurements wrt simulations suggests that:
 Lower cut-off frequency is needed to match with simulations,
 Keeping same LLD threshold for lower cut-off means to have higher Im(Z/n).
LLD intensity threshold:
1I. Karpov, T. Argyropoulos, E. Shaposhnikova, Phys. Rev. Accel. Beams 24, 011002, 2021

## Slide 41
I.Karpov at IWG
[6] O. S. Bruning et al.,“LHC Design Report”, CERN Yellow Reports: Monographs, CERN, Geneva, Switzerland, 2004