## Slide 1: Evolution of beam quality from the injectors to the LHC
S. Kostoglou, H. Bartosik, I. Efthymiopoulos, Y. Papaphilippou, G. Sterbini on behalf of BE-ABP
With invaluable contributions from:
F. Asvesta, M. Bozatzis, X. Buffat, D. Butti, R. Bruce, A. Calia, R. De Maria, Y. Dutheil, B. Emil Karlsen-Baeck,
S. Fartoukh, J. Flowerdew, P. Hermes, M. Hostettler, G. Iadarola, E. Lamb, T. Lefevre, G. Marek,
F. Maria Velotti, I. Mases Sole, L. Mether, D. Mirarchi, C.E. Montanari, S. Morales Vigo, T. Persson,
S. Redaelli, M. Rakic, B. Salvachua, M. Solfaroli Camillocci, F. Soubelet, A. Lasheen, T. Levens, H. Timko,
R. Tomas Garcia, G. Trad, J. Uythoven, A. Valeri Radoslavova, J. Wenninger
Joint Accelerator Performance Workshop 2024

## Slide 2: Motivation
Main indicators of beam quality:
  Emittance: avoiding emittance growth
  Intensity: minimizing losses & preventing beam dumps
  Tail population: preserving tails & avoiding tail increase
  from the injectors to the LHC.
Degradation starts already in the injectors and continues throughout the LHC.
Goal is to:
  Identify where the degradation occurs.
  Understand the cause.
  Evaluate the impact on LHC performance & define priorities.
  Provide recommendations to optimize performance for next year & next runs.

## Slide 3: Overview
Beam quality in the injectors:
  Emittance growth PSB PS  SPS, standard vs BCMS beams.
  Tail population from PSB PS  SPS & “low-tail” BCMS.
  Losses from PS  SPS.
Impact on integrated luminosity:
  BCMS vs standard: model vs measurements
  Reduction of losses with ”low-tail” BCMS.
  Impact of emittance growth beyond IBS.
Lessons learned from 2024.
Beam quality in the LHC:
  Tail population SPS LHC & transfer line mismatch.
  Injection losses: 2024 vs 2023.
  Emittance with standard & BCMS beams.
  Emittance growth at injection beyond IBS & tail evolution.
  Debunched beam at injection & losses at the start of ramp.
  Power supply ripple at the end of ramp.
  Losses at the end of adjust & correlation with tails.
  Losses during leveling & DA.
  Losses beyond burn-off due to collisions in IP8
  Emittance growth during collisions.
Injection
Ramp
Collisions

## Slide 4: Overview
Beam quality in the injectors:
  Emittance growth PSB PS  SPS, standard vs BCMS beams.
  Tail population from PSB PS  SPS & “low-tail” BCMS.
  Losses from PS  SPS.
Impact on integrated luminosity:
  BCMS vs standard: model vs measurements
  Reduction of losses with ”low-tail” BCMS.
  Impact of emittance growth beyond IBS.
Lessons learned from 2024.
Beam quality in the LHC:
  Tail population SPS LHC & transfer line mismatch.
  Injection losses: 2024 vs 2023.
  Emittance with standard & BCMS beams.
  Emittance growth at injection beyond IBS & tail evolution.
  Debunched beam at injection & losses at the start of ramp.
  Power supply ripple at the end of ramp.
  Losses at the end of adjust & correlation with tails.
  Losses during leveling & DA.
  Losses beyond burn-off due to collisions in IP8
  Emittance growth during collisions.
Injection
Ramp
Collisions

## Slide 5: Emittance evolution in the injectors
Emittance measurements at PSB PS  SPS:
  Emittance blowup along the chain:
    ~5% PSB extraction PS extraction
    ~15-20% PS extraction  SPS after scraping:
      PS extraction  SPS injection: emittance growth & tail population, trends similar to observation from SPS  LHC transfer line mismatch, under investigation.
      SPS flat bottom: improved with tune optimizations IPP I. Mases Sole.
  Standard vs BCMS: ~25% reduction in emittance with BCMS at SPS after scraping.
F. Asvesta, I. Mases Sole

## Slide 6: Tail evolution & losses in the injectors
Systematic q-factor increase (~5-15%) PS extraction  SPS after scraping.
Significant improvements in tail population during 2024:
  1st ”low-tail” BCMS variant:
    Introduction of PSB scraping, achieving q=1 at extraction.
    Significant tail increase during PS γtrans transition crossing related to space charge: improved with PS tune optimizations IPP M. Bozatzis.
    No clear tail improvement at LHC injection.
  2nd ”low-tail” BCMS variant:
    Source of improvement not fully understood, traced back to PS.
    Clear tail reduction at LHC injection.
~5% losses in SPS before scraping:
  Injection losses, slow losses, losses during ramp.
  Improvement with “low-tail” BCMS.
F. Asvesta, M. Bozatzis, I. Mases Sole
Reduction also seen at LHC injection
J. Flowerdew, A. Lasheen

## Slide 7: Tail evolution & losses in the injectors
Systematic q-factor increase (~5-15%) PS extraction  SPS after scraping.
Significant improvements in tail population during 2024:
  1st ”low-tail” BCMS variant:
    Introduction of PSB scraping, achieving q=1 at extraction.
    Significant tail increase during PS γtrans transition crossing related to space charge: improved with PS tune optimizations IPP M. Bozatzis.
    No clear tail improvement at LHC injection.
  2nd ”low-tail” BCMS variant:
    Source of improvement not fully understood, traced back to PS.
    Clear tail reduction at LHC injection.
~5% losses in SPS before scraping:
  Injection losses, slow losses, losses during ramp.
  Improvement with “low-tail” BCMS.
F. Asvesta, M. Bozatzis, I. Mases Sole
Reduction also seen at LHC injection
J. Flowerdew, A. Lasheen
Further tail & emittance improvements from PS extraction  SPS extraction.
Try to understand origin of tail reduction in the PS on the 10th of September.
Need for online analysis of SPS losses & automatic profile measurements to monitor quality of injected LHC profiles & detect changes fast and efficiently.
Follow-up

## Slide 8: Overview
Beam quality in the injectors:
  Emittance growth PSB PS  SPS, standard vs BCMS beams.
  Tail population from PSB PS  SPS & “low-tail” BCMS.
  Losses from PS  SPS.
Impact on integrated luminosity:
  BCMS vs standard: model vs measurements
  Reduction of losses with ”low-tail” BCMS.
  Impact of emittance growth beyond IBS.
Lessons learned from 2024.
Beam quality in the LHC:
  Tail population SPS LHC & transfer line mismatch.
  Injection losses: 2024 vs 2023.
  Emittance with standard & BCMS beams.
  Emittance growth at injection beyond IBS & tail evolution.
  Debunched beam at injection & losses at the start of ramp.
  Power supply ripple at the end of ramp.
  Losses at the end of adjust & correlation with tails.
  Losses during leveling & DA.
  Losses beyond burn-off due to collisions in IP8
  Emittance growth during collisions.
Injection
Ramp
Collisions

## Slide 9: SPS extraction to LHC injection
Systematically observed tail population increase in B1H pointing to transfer line mismatch.
Tested new QTL transfer function prepared by ABT:
  MD with INDIVs q=1 at SPS extraction, achieved with ~18% scraping.
  q=1 maintained for B1V and B2H & V at LHC injection, while q=1.2 for B1H.
  Tail comparison at LHC injection with nominal and new QTL transfer functions clearly shows mismatch improvement.
Optimizations to be deployed in 2025.
B1H
B2H
WS in SPS
WS in LHC
B1H
New TF
F. Velotti, Y. Dutheil,
C. Bracco, M. Hostettler

## Slide 10: Injection losses
In 2023:
High and fast losses during B1 injection: BLM saturation limits in TCP-C/B (horizontal & skew) in IR7 for RS01.
Losses correspond to < 109 protons (less than 1 pilot per injection).
Correlated with losses in TL & steering. Mitigated with aggressive SPS scraping (~10%  ~20 nominal bunches per injection).
In 2024:
Significant improvement while SPS scraping at ~4% (BLM talk by S. Morales Virgo & LBOC Y. Dutheil).
Interlock moved to new BLMs on the WALL increasing margin by factor of ~2 (HL S. Morales Virgo).
Exact origin of losses remains unclear:
  2024 vs 2023: shorter trains per LHC injection (i.e. lower intensity per injection).
  Small improvement with “low-tail” BCMS.
Y. Dutheil, F. Velotti, C. Bracco,
B. Salvachua, S. Morales
BLM limit

## Slide 11: Injection losses
In 2023:
High and fast losses during B1 injection: BLM saturation limits in TCP-C/B (horizontal & skew) in IR7 for RS01.
Losses correspond to < 109 protons (~1 pilot per injection).
Correlated with losses in TL & steering. Mitigated with aggressive SPS scraping (~10%  ~20 nominal bunches per injection).
In 2024:
Significant improvement while SPS scraping at ~4% (BLM talk by S. Morales Virgo & LBOC Y. Dutheil).
Interlock moved to new BLMs on the WALL increasing margin by factor of ~10 (HL S. Morales Virgo).
Exact origin of losses remains unclear:
  2024 vs 2023: shorter trains per LHC injection (i.e. lower intensity per injection).
  Small improvement with “low-tail” BCMS.
Y. Dutheil, F. Velotti, C. Bracco,
B. Salvachua, S. Morales
BLM limit
New QTL transfer function for B1  expect to reduce B1H tails.
Improved margin with new B1 BLMs on the WALL by a factor of 2 & improved injection losses could allow for longer trains next year.
As soon as possible, prepare BLM system for higher acceptable injection losses.
Follow-up

## Slide 12: Emittance at injection: standard vs BCMS
Emittance (μm) | B1H | B1V | B2H | B2V
Standard | 1.56 | 1.58 | 1.5 | 1.5
BCMS | 1.19 | 1.27 | 1.13 | 1.17
% | -23.8 | -19.84 | -24.96 | -22.33
20-25% emittance reduction at LHC injection with BCMS w.r.t to standard, 10-15% at start of SB.
Start of injection
Standard
BCMS
Low-tail BCMS
Low-tail BCMS
BCMS
Emittance (μm) | B1H | B1V | B2H | B2V
Standard | 1.77 | 1.71 | 1.63 | 1.61
BCMS | 1.47 | 1.42 | 1.31 | 1.31
% | -16.85 | -16.77 | -19.55 | -18.97
Emittance (μm) | B1H | B1V | B2H | B2V
Standard | 1.84 | 1.67 | 2.25 | 2.3
BCMS | 1.57 | 1.54 | 1.97 | 2.02
% | -14.74 | -7.38 | -12.48 | -12.06
End of injection
Start of Stable Beams
BSRT H-plane
BSRT V-plane
Impact on integrated luminosity:
15% smaller emittance start of collisions (nominal BCMS)
  βmin≥ 36cm: 5% gain, confirmed with experimental data.
    βmin= 30cm & 1.65e11 ppb: 2-2.5% gain.

## Slide 13: Emittance growth at injection
Emittance growth mechanism at injection not fully understood.
Max. brightness
-20% brightness
-60% brightness
Measurements
  Comparison of measured emittance growth & bunch length evolution against theoretical IBS model.

## Slide 14: Emittance growth at injection
Emittance growth mechanism at injection not fully understood.
o Measured emittance growth for H & V
x IBS model emittance growth for H & V
Emittance growth in H with unknown origin after subtracting IBS contribution
Max. brightness
-20% brightness
-60% brightness
Measurements
  Comparison of measured emittance growth & bunch length evolution against theoretical IBS model.
  Horizontal plane:
    Systematically larger in B1H: ~0.6 μm/h in addition to e-cloud:
      0.4 μm/h from IBS.
      0.2 μm/h of unknown origin:
        even with single bunches.
        brightness independent.
IBS + 0.2 μm/h

## Slide 15: Emittance growth at injection
Emittance growth mechanism at injection not fully understood.
o Measured emittance growth for H & V
x IBS model emittance growth for H & V
Emittance growth in H with unknown origin after subtracting IBS contribution
Max. brightness
-20% brightness
-60% brightness
Measurements
  Comparison of measured emittance growth & bunch length evolution against theoretical IBS model.
  Horizontal plane:
    Systematically larger in B1H: ~0.6 μm/h in addition to e-cloud:
      0.4 μm/h from IBS.
      0.2 μm/h of unknown origin:
        even with single bunches.
        brightness independent.
  Vertical plane:
    ~0.1-0.3 μm/h in addition to e-cloud (B1 & B2).
      Low vertical dispersion & good coupling control  small IBS contribution.
      Measurements suggest some brightness dependence  possibly underestimating IBS or emittance exchange with horizontal in the modeling.
      Linear increase of emittance over time.
IBS + 0.2 μm/h

## Slide 16: Emittance growth at injection
Emittance growth mechanism at injection not fully understood.
o Measured emittance growth for H & V
x IBS model emittance growth for H & V
Emittance growth in H with unknown origin after subtracting IBS contribution
Max. brightness
-20% brightness
-60% brightness
Measurements
  Comparison of measured emittance growth & bunch length evolution against theoretical IBS model.
  Horizontal plane:
    Systematically larger in B1H: ~0.6 μm/h in addition to e-cloud:
      0.4 μm/h from IBS.
      0.2 μm/h of unknown origin:
        even with single bunches.
        brightness independent.
  Vertical plane:
    ~0.1-0.3 μm/h in addition to e-cloud (B1 & B2).
      Low vertical dispersion & good coupling control  small IBS contribution.
      Measurements suggest some brightness dependence  possibly underestimating IBS or emittance exchange with horizontal in the modeling.
      Linear increase of emittance over time.
Continue investigation of unexplained emittance growth.
Minimize time spent at injection.
Follow-up
IBS + 0.2 μm/h

## Slide 17: Tails at injection
Systematic profile monitoring in 2024:
  From Fill 9912 (July), full-cycle bunch-by-bunch BSRT profile logging in NXCALS thanks to D. Butti.
Profiles at injection had heavily populated tails: q~1.4 at the start of 2024.
No significant tail reduction with the 1st “low-tail” BCMS variant (July).
Tail reduction (q~1.2) at LHC injection > Fill 10100 (September), linked to injector tail improvement traced back to PS with unknown origin.
Profile evolution:
  Tend to converge to Gaussian over time, no mechanism of tail population during nominal operation.
  However, tail increase during LHC injection observed during specific MDs.
10th of September

## Slide 18: Tails at injection
Systematic profile monitoring in 2024:
  From Fill 9912 (July), full-cycle bunch-by-bunch BSRT profile logging in NXCALS thanks to D. Butti.
Profiles at injection had heavily populated tails: q~1.4 at the start of 2024.
No significant tail reduction with the 1st “low-tail” BCMS variant (July).
Tail reduction (q~1.2) at LHC injection > Fill 10100 (September), linked to injector tail improvement traced back to PS with unknown origin.
Profile evolution:
  Tend to converge to Gaussian over time, no mechanism of tail population during nominal operation.
  However, tail increase during LHC injection observed during specific MDs.
Further improvements on ”low-tail” BCMS.
Continue systematic BSRT profile logging & monitoring during whole LHC cycle to:
  Monitor quality of injected profiles & detect changes.
  Correlate with loss or gain of LHC performance.
Follow-up

## Slide 19: Debunched beam at injection & losses during ramp
H. Timko, B. Karlsen-Baeck, M. Zampetakis, HL-WP5
IR3 high losses at start of Ramp, reaching warning levels on BLMs & causing 3 dumps.
Strong correlation between IR3 losses and debunched beam (~up to 50 nominal bunches).
Correlation of debunched beam with:
  Brightness.
  Time spent at injection.
  possibly indicating IBS related mechanism.
More critical for BCMS compared to standard due to higher brightness.
Mitigations:
  Clearly demonstrated by RF that increase of RF voltage is beneficial (talk by B. Karlsen-Baeck).
  Increase of BLM thresholds (talk by S. Morales).
Debunched beam in 2024 fills
Debunched beam vs IR3 losses

## Slide 20: Debunched beam at injection & losses during ramp
Debunched beam in 2024 fills
Debunched beam vs IR3 losses
IR3 high losses at start of Ramp, reaching warning levels on BLMs & causing 3 dumps.
Strong correlation between IR3 losses and debunched beam (~up to 50 nominal bunches).
Correlation of debunched beam with:
  Brightness.
  Time spent at injection.
  possibly indicating IBS related mechanism.
More critical for BCMS compared to standard due to higher brightness.
Mitigations:
  Clearly demonstrated by RF that increase of RF voltage is beneficial (talk by B. Karlsen-Baeck).
  Increase of BLM thresholds (talk by S. Morales).
Debunched beam in 2024 fills
Investigate possibility to increase RF voltage (see talk by B. Karlsen-Baeck) & review BLM thresholds.
Minimize time spent at injection.
H. Timko, B. Karlsen-Baeck, M. Zampetakis, HL-WP5
Follow-up

## Slide 21: Power supply ripple at the end of ramp
50 Hz power supply ripple constantly present throughout LHC cycle, real dipolar beam excitation.
Origin of high-frequency 8 kHz cluster is not understood:
  Clear amplitude increase at the end of the ramp when reaching 6.8 TeV.
  Sensitivity to tune trims consistent with dipolar excitations.
  Significantly attenuated amplitude during p-p ref Run (2.68 TeV).
  Impact on performance is unclear, reproducible fill-by-fill.
Nominal fill
p-p ref
A. Valeri Radoslavova

## Slide 22: Power supply ripple at the end of ramp
50 Hz power supply ripple constantly present throughout LHC cycle, real dipolar beam excitation.
Origin of high-frequency 8 kHz cluster is not understood:
  Clear amplitude increase at the end of the ramp when reaching 6.8 TeV.
  Sensitivity to tune trims consistent with dipolar excitations.
  Significantly attenuated amplitude during p-p ref Run (2.68 TeV).
  Impact on performance is unclear, reproducible fill-by-fill.
Nominal fill
p-p ref
A. Valeri Radoslavova
Based on the successful compensation of 50Hz in the SPS, should we finally make a similar effort for the 50Hz ripple in the LHC?
Follow-up

## Slide 23: Losses at the end of adjust/start of collisions
Large beam lifetime drop (<10 h in some fills) during final seconds of Adjust.
Driving mechanism:
  DA reduction when entering head-on beam-beam dominated regime.
DA target of 6σ
Beam lifetime
DA

## Slide 24: Losses at the end of adjust/start of collisions
Large beam lifetime drop (<10 h in some fills) during final seconds of Adjust.
Driving mechanism:
  DA reduction when entering head-on beam-beam dominated regime.
  Clear correlation between tails & losses:
    First observations from MDs with groups of low-tail & large-tail bunches.
    Confirmed in nominal fills.
Burn-off limit
Large tails
Low tails
Low tails  Large tails

## Slide 25: Losses at the end of adjust/start of collisions
Large beam lifetime drop (<10 h in some fills) during final seconds of Adjust.
Driving mechanism:
  DA reduction when entering head-on beam-beam dominated regime.
  Clear correlation between tails & losses:
    First observations from MDs with groups of low-tail & large-tail bunches.
    Confirmed in nominal fills.
    Losses reduced close to burn-off limit by September with “low-tail”: strong correlation of tail reduction & loss reduction at the start of SB.
10th of September

## Slide 26: Losses during collisions
Observed beam lifetime degradation with extended stay at 1.2 m, μmax<μtarget before leveling.
Fill 10100 in September:
“Low-tail” BCMS
Short stay at 1.2 m
Fill 9864 in July:
Nominal BCMS
Extended stay at 1.2 m
Losses equivalent to ~90 nominal bunches in 1st hour of SB
Losses equivalent to ~20 nominal bunches in 1st hour of SB

## Slide 27: Losses during collisions
Observed beam lifetime degradation with extended stay at 1.2 m, μmax<μtarget before leveling.
Fill 10100 in September:
“Low-tail” BCMS
Short stay at 1.2 m
Fill 9864 in July:
Nominal BCMS
Extended stay at 1.2 m
Losses equivalent to ~90 nominal bunches in 1st hour of SB
Losses equivalent to ~20 nominal bunches in 1st hour of SB
1. DA < 6σ due to:
High brightness
High chromaticity
High octupoles
Small crossing angle
2. DA > 6σ due to:
Chromaticity reduction (major contributor).
Bunch intensity decrease (major contributor).
Crossing angle increase (minor contributor).

## Slide 28: Losses during collisions
Observed beam lifetime degradation with extended stay at 1.2 m, μmax<μtarget before leveling.
Fill 10100 in September:
“Low-tail” BCMS
Short stay at 1.2 m
Fill 9864 in July:
Nominal BCMS
Extended stay at 1.2 m
Losses equivalent to ~90 nominal bunches in 1st hour of SB
Losses equivalent to ~20 nominal bunches in 1st hour of SB
Impact on integrated luminosity:
Up to* 5.2% loss
for fills that reached optimal fill length
Impact on integrated luminosity:
Up to 1.5% loss
for fills that reached optimal fill length
*Exact contribution of tails on luminosity to be refined

## Slide 29: Losses during collisions
Observed beam lifetime degradation with extended stay at 1.2 m, μmax<μtarget before leveling.
Fill 10100 in September:
“Low-tail” BCMS
Short stay at 1.2 m
Fill 9864 in July:
Nominal BCMS
Extended stay at 1.2 m
Losses equivalent to ~90 nominal bunches in 1st hour of SB
Losses equivalent to ~20 nominal bunches in 1st hour of SB
Up to* 5.2% loss of integrated lumi for fills that reached optimal fill length
Up to 1.5% loss of integrated lumi
for fills that reached optimal fill length
Aim to inject in LHC profiles as close as possible to Gaussian from the injectors.
Reaching DA ≥ 6σ at end of adjust/start of leveling is critical to minimize losses:
  chromaticity reduction after emittance scans or as quickly as possible.
  combined with “low-tail” BCMS.
*Exact contribution of tails on luminosity to be refined
Follow-up

## Slide 30: Emittance growth at collisions
Emittance growth of unknown origin also during collisions:
  Cannot be fully explained by IBS models.
  Vertical emittance expected to be shrinking due to SR.

## Slide 31: Emittance growth at collisions
Emittance growth of unknown origin also during collisions:
  Cannot be fully explained by IBS models.
  Vertical emittance expected to be shrinking due to SR.
Luminosity model with IBS & SR

## Slide 32: Emittance growth at collisions
Emittance growth of unknown origin also during collisions:
  Cannot be fully explained by IBS models.
  Vertical emittance expected to be shrinking due to SR.
Impact on integrated luminosity:
2-3% loss for fills that reached optimal fill length & τ=2.5 h
Luminosity model with IBS & SR & extra emittance growth

## Slide 33: Lessons learned from 2024
Need to minimize time spent at LHC injection due to:
  Unexplained emittance growth at injection.
  Increase of debunched beam & eventually losses during ramp.
  Longer trains for 2025 due to faster injection time & gain in integrated luminosity (see X. Buffat):
    Injection losses: source remains unclear, increase of margin to BLM saturation for B1 w.r.t 2023.
Standard vs BCMS:
  Start of collisions with 10-15% smaller emittances.
  Depending on virtual luminosity, 2-5% gain in performance w.r.t to standard for fills that reached optimal fill length.
  Main gain comes from “low-tail” BCMS:
    Clear correlation between losses at the end of collapse/start of collisions and tail population: reduction of tails observed Fills>10100 (10th of September), starting from tail reduction in the injectors, resulted in loss improvement at start of collisions:
  Preparation from the injectors has direct impact on LHC performance: to be considered not only for nominal operation but also for special beams (VdM & BSRT calibration fills).

## Slide 34: Lessons learned from 2024
Minimize losses during collisions:
  Start LHC injection with profiles as close as possible to Gaussian from the injectors.
    Tail increase for B1 from SPS to LHC due to transfer line mismatch, expected to improve with new transfer function.
    Further improve & optimize “low-tail” BCMS in the injectors.
  Critical to maintain DA target of 6σ at end of adjust/start of leveling:
    2024 DA below target at this stage & improved during leveling  seen on beam lifetime.
    DA can be increased by reducing non-linearities (e.g. chromaticity reduction after emittance scans, switching to negative octupole polarity).
Other issues: unknown emittance growth at injection & collisions, 50 Hz ripple..
Need for more automatic tools for profile monitoring and losses in the injectors & throughout the whole LHC cycle to detect changes fast & efficiently and eventually connect with gain or loss of LHC performance.
Thank you!

## Slide 35: Backup

## Slide 36: A closer look in the SPS
Measurements from high-intensity MDs (4x48b, ~2.3e11 ppb at SPS extraction), similar observations with 2024 nominal configuration.
  Emittance and q-factor increase PS extractionSPS injection:
    Similar trends observed between SPS extractionLHC injection due to transfer line mismatch.
  Emittance blowup & tail population at SPS flat bottom:
    Emittance reduction through tune optimizations.
  SPS scraping fully correlated with tails at SPS extraction/LHC injection: In 2024, Gaussian bunch profiles and nominal intensity with ~15% scraping.
I. Mases Sole, F. Asvesta

## Slide 37: PSB scraping
F. Asvesta
PSB Transmission
Tails before/after scraping

## Slide 38: PS optimization during γtrans crossing
M. Bozatzis, F. Asvesta

## Slide 39: SPS measurements with 3x36 1.6e11 ppb
I. Mases Sole, F. Asvesta

## Slide 40: Losses during collisions: DA for 2024

## Slide 41: Statistics from 2024

## Slide 42: Leveling time

## Slide 43: Luminosity model: pure model

## Slide 44: Luminosity model: extra losses

## Slide 45: Luminosity model: extra losses & emit growth

## Slide 46: LHC injection profiles vs SPS scraping

## Slide 47: Losses during the collapse of the separation bump & start of collisions
Collisions in IP1/2/5/8
Collisions in IP1/2/5
First year where we also observe impact from LHCb: LHCb luminosity 2e33 Hz/cm2 while ATLAS/CMS 2e34 Hz/cm2

## Slide 48: Losses during the collapse of the separation bump & start of collisions
Collisions in IP1/2/5/8
Collisions in IP1/2/5
First year where we also observe impact from LHCb: LHCb luminosity 2e33 Hz/cm2 while ATLAS/CMS 2e34 Hz/cm2

## Slide 49: Losses during collapse and collisions
Good correlation between DA and beam lifetime.
Beam lifetime of ~10h indicates DA<4.5 σ

## Slide 50: Luminosity model

## Slide 51: Performance gain BCMS vs standard
Fill 9614, Standard
Fill 9667, BCMS
Considering a turn-around time of 2.5h:
        From 1.22 fb-1/day with standard to 1.32 fb-1/day with BCMS: +8.2% integrated luminosity for fills that make it to the optimal fill length (>8h), 5% from the lower emittance and 3.2% from the intensity increase.

## Slide 52: Emittance growth at injection
Emittance growth mechanism at injection not fully understood:

## Slide 53: Emittance growth at injection
Emittance growth mechanism at injection not fully understood:

## Slide 54: Impact of improved losses
Nominal
Fill 9864
Fill 10100

## Slide 55: Tails at injection
Systematic profile monitoring in 2024:
  From Fill 9912 (July), full-cycle bunch-by-bunch BSRT profile logging in NXCALS thanks to D. Butti.
Note on special beams (1/2):
    BSRT profiles must be deconvoluted.
    Deconvolution relies on specific information obtained during BSRT calibration fills.
    In 2024 preparation & effort from the injectors to provide Gaussian beams during these fills & simplify deconvolution, similar type of preparation for next year.

## Slide 56: Impact on integrated luminosity
Luminosity model provides accurate predictions for beam parameter evolution & luminosity estimates throughout a fill: can include additional effects beyond theoretical models to match the data.
Considering ideal case where fills are dumped at optimal fill length and turn-around of 2.5 h.
Standard vs nominal BCMS in 2024
Assuming -15% emittance reduction at start of SB as only difference:
  βmin≥ 36cm: 5% gain, confirmed with experimental data.
    βmin= 30cm & 1.65e11 ppb: 2-2.5% gain.
    for fills that made it to optimal fill length (10h) with τ=2.5 h
“Low-tail” BCMS:
On average, reduction of σeff from ~100 mb to ~85 mb after Fill 10100.
Exact contribution of tails on luminosity to be studied.
Maximum gain up to 4% for fills reaching optimal fill length with τ=2.5 h.