## Slide 1: Automatic Fault Analysis & Prognostics JAP Workshop 12.12.2024
A. Asko*, B. Bradu, S. Deghaye, L. Delprat, L. Felsberger, R. Garcia, A. Huschauer, I. Kozsar, A. Lasheen, K. Papastergiou, C. Roderick, F. Velotti, R. Ximenes, C. Zamantzas

## Slide 2: Introduction
For this presentation I had the chance to talk to different experts and get more details in their tools, frameworks etc. I will attempt to present the current status and high level workflows on…
Accelerator fault tracking & Equipment fault tracking
Fault diagnostics, prognostics & data analysis
Needs & Ideas for a future vision on the above
Disclaimer: I am not an equipment expert Aim to stimulate discussions on the future of fault tracking, diagnostics & prognostics
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko

## Slide 3: Accelerator Fault Tracking (AFT) - Current status
AFT is the standardized approach used to track faults in different systems, focusing on the impact on accelerator complex availability
Fault recording based on predefined accelerator specific conditions
System experts get notified for faults registered under their responsibility
Faults are reviewed by RAWG & equipment experts (documentation)
Depending on the system: sometimes long or incomplete follow-up (due to other priorities)
AFT has a high level classification of faults to accelerator systems, with limited expert follow up, requiring manual, time consuming steps
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko

## Slide 4: Accelerator Fault Tracking (AFT) - Current status
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
Operate accelerators
Log Faults (partially automated)
Review Faults
RAWG
Follow-up of Fault reviews
Follow-up of Logged Faults
AFT
Operators & Machine Coordinators
Equipment experts
Accelerator Complex
Review Faults

## Slide 5: Accelerator Fault Tracking (AFT) - Current status
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
Operate accelerators
Log Faults (partially automated)
Review Faults
RAWG
Follow-up on Fault reviews
Follow-up of Logged Faults
AFT
Operators & Machine Coordinators
Equipment experts
Accelerator Complex
Review Faults
Standardized approach to track faults impacting accelerator complex availability
High-level classification of faults to accelerator systems
Limited expert follow up, requiring manual, time consuming steps

## Slide 6: Equipment Fault Tracking - Current status
Equipment fault tracking is diverse → different workflows & tools in each system…
Directly affected by the system complexity (the more complex the system the more challenging to track faults precisely)
Automation of equipment fault reporting exists in some systems but often at a rudimentary level
EAM is used by most equipment groups for asset management, but only to varying levels for lifetime assessment
Equipment Fault Tracking is sometimes primitive & distributed with limited common workflows
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko

## Slide 7: Equipment Fault Diagnostics - Current Status
Equipment-related faults are reported by operators, then diagnosed using system specific expert tools (mainly by expert support team e.g. Piquet)
Time consuming & sometimes complicated process to correctly identify the system responsible for the fault (e.g. wrong expert called)
Automation of fault diagnostics is a challenging task for most equipment
Monitoring & alarms are not always present
Performing thorough effective diagnostics among different systems is cumbersome & time consuming
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
Notes: To be reworked a bit more

## Slide 8: Equipment Fault Diagnostics - Current status
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
Attempt to fix (limited to few systems)
Contact
(potentially wrong person)
EAM
Follow-up (diverse levels & tools)
Operators & Machine Coordinators
Equipment experts
Auto diagnose (rare & unrefined)
Attempt to fix (complicated & time consuming)
Diverse workflows
Equipment Failure
(limited self reporting)
Asset Management & Lifetime Assessment (to varying levels)
Diagnostic tools
Diagnostic tools

## Slide 9: Equipment Fault Diagnostics - Current status
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
Attempt to fix (limited to few systems)
Contact
(potentially wrong person)
EAM
Follow-up (diverse levels & tools)
Operators & Machine Coordinators
Equipment experts
Auto diagnose (rare & unrefined)
Attempt to fix (complicated & time consuming)
Diverse workflows
Equipment Failure
(limited self reporting)
Asset Management & Lifetime Assessment (to varying levels)
Diagnostic tools
Diagnostic tools
Diagnostics are often cumbersome & time consuming (see talk from K. Papastergiou)
Due to higher priorities, not always followed up extensively

## Slide 10: Fault Prognostics - Current status
A lot of data is being gathered in various systems that can be used for fault analysis and prognostics, but…
Data is distributed among different systems making analysis challenging (NXCALS, AFT, EAM, etc.)
Data analysis, when existing, sometimes primitive & diverse between teams (due to data gathering complexity, lack of time etc.)
A lot of manual effort & expertise required to make sense of available data
Currently challenging to establish a common workflow & proactively use existing data
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko

## Slide 11: Fault Prognostics - Proactive analysis
Various efforts are in place but progress is slow due to limited resources
In some cases significant effort has been invested to proactively analyse existing data to:
Generate detailed reports on system condition
Validate potential problems and prevent faults
Identify needed interventions and future consolidations (CRG, BLM)
Further research on…
Anomaly detection for prognostics is visible in multiple expert teams
Initial ML & AI attempts are slowly being developed (MSC, HSE, LHC Dipole Circuits)
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
(see talk from R. Murillo-Garcia)

## Slide 12: Fault Tracking - Future vision
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
AFT
Accelerators
Equipment Fault Tracking
EPA WP8
Beam parameters
Controls/Interlock
Equipment
WP8 APIs
Auto-diagnose
Auto-config
AFT GUI & DB
Automatic Fault Recording
APIs
Operations
Logbook
Work orders
Asset data
Logging/IoT
Physical/Operations Virtual/Analysis
Equipment Accelerator Complex
* see next slides
Ongoing effort, to be completed*
To be streamlined*
Consolidate & Extend*
Notes: Highlight what needs to be done. What’s the difference of what needs to be done. EG. WP8 under development, AFT in need of consolidation & extensions. Eq fault tracking to be standardised and streamlined

## Slide 13: Equipment Fault Diagnostics - Future vision
Automation of fault recording on equipment level will provide a lot of valuable data (hardware failures, software failures, degrading of operation, etc.)
Requires:
Creating a common language for equipment reporting
Using common tools supporting shared workflows & diagnostics as well as knowledge sharing (NXCALS, UCAP, EAM etc.)
Investing in automatic hardware diagnostics, wherever possible (crucial for fault recovery)
Supports: Automated fault recovery (in addition to a basis for prognosis)
Need to minimise human interactions & automate procedures empowering experts to focus on other things (development, system evolution, research, etc.)
EPA - WP8
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko

## Slide 14: Fault Prognostics - Future vision
Aiming at providing a Platform as a Service which will allow to…
Provide streamlined access to different data sources
Perform on-line processing of a combination of live and historical data as needed to support prognosis
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
Including support for the integration of new paradigms based on intelligent agents (Machine Learning & Artificial Intelligence)

## Slide 15: Fault Prognostics - Future vision
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
PostMortem
CCS
LAYOUT
FGC
NXCALS
CMW
LSA
EAM
AFT
Data Processing Platform
GUIs
Reset tools
Alerts
Automations
UCAP
AI
MLP
Common Data Extraction API
CTTB endorsed
Notes: Cttb supported collaborative activity (DPP) Marcin

## Slide 16: Fault Prognostics - Future vision
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
PostMortem
CCS
LAYOUT
FGC
NXCALS
CMW
LSA
EAM
AFT
Data Processing Platform
GUIs
Reset tools
Alerts
Automations
UCAP
AI
MLP
Common Data Extraction API
CTTB endorsed
A Platform As A Service which will provide common access to different online & offline data sources, allowing to make prognostics based on analysis algorithms and intelligent agents (see talk from M. Sobieszek).
Notes: Cttb supported collaborative activity (DPP) Marcin

## Slide 17: Some next steps
2025 Q1
Initial AFT & EAM integration
AFT 2.0 project definition, endorsement & resource allocation (AFT is 10 years old, requirements have evolved, & technical consolidation is needed)
On-going
Close collaboration with EPA WP8 to “Automate Equipment”
Providing framework for standardized state reporting, actor classes for communication, fault recovery design, access to accelerator context information & pre-built integrations (inc. AFT)
2025 Q3
New Data Processing Platform PoC will be in place (see talk from M. Sobieszek)
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
What other concrete steps need to be taken in the short term?
Notes: We need someone to drive all this effort on the high level

## Slide 18: Summary
Accelerator fault tracking is well established (but needs consolidation → AFT 2.0).
Equipment fault tracking is diverse & less mature & needs streamlining.
Advanced fault diagnostics can build on the above & support automated recovery (EPA WP8). Then prognostics can follow in a robust & standardised manner.
Questions?
JAPW 2024: Automatic Fault Analysis & Prognostics - Anti Asko
Key points for improvement:
Integration of existing tools is the natural next step (e.g. AFT/EAM, UCAP/DPP).
Diagnostics, recovery (EPA WP8 as a driver), & prognostic frameworks to be established on top of existing & emerging tools (DPP).
Agree on common solutions across teams to minimise duplication of efforts.
Long-term maintainability should be considered up-front.