## Slide 1: Some Remarks on the p-linac Power Consumption
43rd Joint FCCee Injector Collaboration WP1 Meeting
Jean-Yves Raguin
Paul Scherrer Institute, 23 August 2023

## Slide 2: 14 MV/m accelerating gradient case
New baseline layout: 4 AS per module, 4 bunches, 100 Hz Acc. Grad.: 14 MV/m
From Yongke:
  Capture linac: 7 AS, Linac section 1: 20 AS, Linac section 2: 20 AS, Linac section 3: 24 AS
  Total number of solenoids: 271 (Capture linac and Linac section 1)
From Riccardo: assume a power consumption of 16 kW per solenoid
Assume 18 RF modules + 1 spare
Power consumption: RF only: 3.5 MW, Solenoids only: 4.3 MW !!!, 7.8 MW
10-year operating cost: RF only: 12.9 MCHF, Solenoids only: 15.4 MCHF !!!, 28.3 MCHF

## Slide 3: 20 MV/m accelerating gradient case
Layout: 2 AS per module, 4 bunches, 100 Hz Acc. Grad.: 20 MV/m
From Yongke:
  Capture linac: 5 AS, Linac section 1: 14 AS, Linac section 2: 14 AS, Linac section 3: 16 AS
  Total number of solenoids: 141 (Capture linac and Linac section 1)
Assume 25 RF modules + 1 spare
Power consumption: RF only: 5 MW, Solenoids only: 2.3 MW, 7.3 MW
10-year operating cost: RF only: 17.7 MCHF, Solenoids only: 8 MCHF, 25.7 MCHF