## Slide 1: Cycle configuration
Cycle execution
Optics determined with:
Mad-X
Own routines
Procedures
Beam diagnostic
Optics computations
Cycle Configuration
Element cycle depends on:
Cycle code (Energy, Intensity)
Beam optics settings
(e.g. Tune, Chromaticity)
Notes: Jump right into the topic
Main diplo cylce depends on what beam you’d like to have. Beam characteristic influenced by particle type, energy and optics considerations.
E.g. tune set by Sync Quadrupoles to get beam 200 Mev, Tune 1.6 because that is ideal for extraction

## Slide 2: Agenda
Workflow
Cycle Configurator
Optics computations with Mad-X
Optics connector API draft
Modules in MACS, exchanged data
The role of RMS in the cycle configuration
Status, outlook, next steps

## Slide 3: Cycle Configurator
Normalized strengths (k1l)
computed with Mad-X
Cycle Configurator first computes main dipole cycle
Cycle Configurator de-normalizes the strengths and creates quadrupole cycle
Output
List of integrated magnetic field values
Timing

## Slide 4: Mad-X
mqzc : quadrupole;
mr02000mqf : mqzc, l = 0.36;
mbhc : sbend;
mr01000mbh : mbhc, l = 1.67;
mr: sequence;
mr01000mbh, at 1.3;
mr02000mqf, at = 3.5;
endsequence;
@ Q1 %le 1.666614532
@ Q2 %le 1.789160081
* NAME KEYWORD ANGLE K1L
$ %s %s %le %le
"MR00001MQF" "QUADRUPOLE" 0 0.106507156
"MR01000MBH" "SBEND" -0.392699081 0
"MR01000MCV" "VKICKER" 0 0
"MR01000MQD" "QUADRUPOLE" 0 -0.184823110
"MR01000PUV" "VMONITOR" 0 0
Model
Output
Input
Commands
qx = 1.7392;
qy = 1.799;
match;
vary,name = mqf1k1, step = 1E-6;
vary,name = mqdk1, step = 1E-6;
constraint, expr = table(summ, q1) = qx;
constraint, expr = table(summ, q2) = qy;
endmatch;
TWISS, save, file = "mrinj.twiss";

## Slide 5: Optics Connector API
MadDB
Covers some of the complexity of the file handling
Allows to directly read and write values

## Slide 6: Components
Mad-X
Output files
Repository Management System
Element information
Cycle Configurator
Element strengths
Cycle code
Waveforms, setpoints (integrated magnetic field)
Timing
Optics
Initial settings
Input files
Basic optics computations

## Slide 7: RMS
RMS has the following data stored in its database:
Cycle codes
Timing event definition
Timing sequence of the cycles
Optical length and position of the machine elements
Transfer functions of the magnets BL(I)
Waveforms and setpoints for the cycles in integrated magnet field values
RMS generates the control values for the power supplies:
BL(t), BL(I) -> I(t)

## Slide 8: Status
Ideas and first documents:
  Controls: Cycle Configuration Workflow, Optics Connector Design (Mad-X and API)
  Physics: Mad-X usage, Cycle Configuration, Physics Library
  Cycle Configurator design, Interface definitions (e.g. interfaces to RMs)
  Clarification of many, many details
  User interface
What do we have so far?
What is missing?

## Slide 9: Outlook
RMS
Element information
Cycle Configurator
Waveforms, setpoints, timing
Waveforms, setpoints, timing
Optic values
Element strengths
Element strengths
Orbit, Matching settings
BD measurements
Optics
Cycle code
Element strengths
Compute cycle
Timing settings
Basic optics computations
Procedure
Framework

## Slide 10: Next steps
Implement first workflow:
  Read existing Mad-X file, parse it and offer the element strength via the Optics API
  Implement code to build main dipole cycle, quadrupole cycle
Continue working on specifications, interface design, …