## Slide 1
the challenges of quantum computing
science, technology, energetics and economics
Olivier Ezratty
olivier@oezratty.net www.oezratty.net @olivez
INFIERI International Summer School, Pisa, September 2nd, 2025

## Slide 2: what is this talk about?
defining quantum technologies and their use cases.
segmenting quantum computing use cases and algorithms.
describing the basics of quantum computing and algorithms.
uncovering hardware scalability challenges.
look at vendor roadmaps, including energetic aspects.
Notes: looking forward !
- applis avec avantage : chimie, not optim et ML et gros FTQC
- pb de prepa classique et de cout non estimé
- cout de compilation et syndrome detection, fixe vs data
- cout interconnect incontournable
- vitesse portes et temps calcul
- prix machines
- energy acceptability
- qu’elles transversalités ?
- quel est le role de la qei pour regler ces pbs ?
- questions fondamentales : large scale entanglement.
- question alternative : limites de l’analog quantum computing ?
- budgets bruits des qubits , ex d’oxford
- comment impliquer les participants a la conference ? scanner les. les mettre dans les stacks.
- besoin de mieux expliquer pourquoi le nisq n’est pas intéressant. no scale. no biz value. too long computing particularly with vqe.

## Slide 3: 1st and 2nd quantum revolutions
quantum information research started hopefully before classical computing reached the peak oil of Moore’s law. scaling issues lead to many research in unconventional computing areas and QC is one of the most promising ones.
manipulating superposition and entanglement and/or individual particles
quantum computing
quantum telecommunications
quantum cryptography
quantum sensing
manipulating groups of quantum particles photons, electrons and atoms interactions
transistors, lasers, fiber optics, GPS
photovoltaic cells, atom clocks
medical imaging, digital photography and video
LEDs, LCD TV quantum dots
1982-*
1947-*
(cc) Olivier Ezratty, 2021-2024
second quantum revolution
first quantum revolution

## Slide 4: quantum sensing
lasers and frequency combs
magnetometers
gravimeters
gas detectors
chemical sensors
thermometers
clocks
spectrographs
ultra-sound mikes
microscopy medical imaging
radars
LiDARs
entangled photons
ultra-sensitive
imaging
SQUIDs
(cc) Olivier Ezratty, 2021-2024.
large range of quantum sensing applications
can mention what Thales does with NV center magnetometers
the amazing world of quantum radars
also, many medical imaging applications
RF analysis
ions
inertial sensors
gyroscopes
sonars
cold atoms or atoms vapor
NV centers
ODMR
Notes: https://www.researchgate.net/figure/Schematic-of-photonic-optical-atomic-clock_fig1_328736626

## Slide 5: quantum telecommunications
quantum technologies
classical technologies
QRA quantum resistant cryptography
classical cryptography resisting to quantum algorithms
Quantum Key Distribution (QKD)
V1 first generation, prepare-and measure based, protects public keys sent through optical links, use trusted nodes as repeaters
PQC post-quantum cryptography
new classical asymmetric keys and signatures resisting to quantum algorithms
QRNG
quantum random key generators
ensure the quality of public keys in classical and quantum cryptography
QCKA Quantum Conference Key Agreement
entangled quantum keys shared with more than 2 parties.
entanglement distribution
entangled photons distribution to multiple parties
V2 second generation, entanglement based,
protects public keys sent through optical links, use memory based repeaters
symmetric keys
classical cryptography already resistant to quantum algorithms (AES-256, …)
quantum repeaters
with quantum memory, enable entanglement sharing over long distances
quantum Internet
(cc) Olivier Ezratty, 2023
distributed quantum computing
connection between quantum computers and sensors, blind quantum computing
QSDC Quantum Secure Direct Communication
quantum data transfer without encryption keys
quantum computing cryptography
generated by a quantum computer
quantum teleportation
teleporting one qubit state to another qubit using entanglement distribution
Unsafe cryptography classical cryptography based on RSA

## Slide 6: quantum random number generators
photons counting
photons arrival time
vacuum fluctations
phase noise
qubit Bell-state measurement
other
self-certified SDI QRNG
radioactive decay

## Slide 7: potential quantum computing benefits
energy advantage (NISQ).
energy acceptability (FTQC).
computing faster than classical systems.
solving problems inaccessible to classical computers.
improving results quality: chemical accuracy, better heuristics, etc.
reducing required training data, particularly for machine learning tasks.
usefulness: which depends on the stakeholder (fundamental research, governments, industry).
or
or

## Slide 8: typical difficult problems
iℏ =
solving Schrodinger’s wave equation to simulate quantum systems
combinatorial optimizations
machine learning and deep learning
solving partial differential equations
breaking asymmetric cryptography keys
Notes: https://pypi.org/project/cvt-tensorflow/

## Slide 9: from science to industry applications
fundamental research
business operations
régalien
condensed matter physics
high-energy particle physics
transportation
logistics and retail
telecoms
financial services
manufacturing
energy utilities
astrophysics
applied research
drugs
batteries
fertilizer production
material design
semiconductors
climate modeling
Notes: Source of High-Energy Particle physics illustration : Quantum Computing for Data Analysis in High-Energy Physics by Andrea Delgado et al, March 2022 (22 pages)
Source of condensed matter physics illustration : Quantum computing enables simulations to unravel mysteries of magnetic materials by Elizabeth Rosenthal, Oak Ridge National Laboratory, February 2021, using a 2000Q D-Wave annealer.
Marketing: https://www.dwavesys.com/media/i2fjhzy2/recruit_case_story_v5.pdf

## Slide 10: what is a qubit?
two-level state controllable quantum object
basic unit of quantum information
vector in a 2-dimension complex numbers Hilbert space
mathematically
physically
1
complex numbers
amplitudes
probabilities and Born normalization constraint
e-
separable atom energy level
electron or nucleus spin orientation
photon mode (polarization, number, frequency)
(cc) Olivier Ezratty, 2023-2024
Bloch sphere representation with amplitude and phase

## Slide 11: qubits mathematical operations
N qubits handle the equivalent of 2N+1 -1 floating point numbers
combinations of 0s and 1s
complex amplitudes
two-level quantum object, handling the equivalent of two floating point numbers
entanglement creates links between qubits and brings computing power under certain circumstances
.
CNOT gate
Bloch sphere

## Slide 12: what is a quantum algorithm?
N qubits
circuit depth D
two-qubit gate
temps
three-qubit gate
single qubit gate
initialization
readout
quantum algorithm: decomposes a solution to solve some mathematical problem into a quantum circuit.
quantum circuit: series of operations (gates) acting on a quantum memory, on individual qubits (superposition) or with connecting them (entanglement in most cases).
matrix computing: operating on a memory space of dimension 2N+1 real numbers.
mecanism: exploit various techniques to yield a value of interest in a series of classical bits.
classical computing: used to prepare the circuit, encore data, and extract useful result from multiple circuit runs.

## Slide 13: key differences
uncopiable data, but transferable
need to (re-)learn linear algebra
probabilistic results, and repeated computing to generate a deterministic outcome
visual or Python scripted « circuits » programming
qubit 1 state
qubit 2 state
qubit 1 state
qubit 2 state
entangle
copy
qubit 1 state
qubit 2 state
teleport

## Slide 14: main quantum computing paradigms
gates-based quantum computers
quantum annealers
analog quantum simulators
(cc) Olivier Ezratty, 2022-2025
problem solved with an algorithm containing a series of quantum gates, implementing any unitary transformation
problem embedded in a BQM model to solve Ising or QUBO problems, using static qubit connectivity and local control
problem embedded in a graph to solve Ising or QUBO problems, using dynamic qubit positioning but no or poor local qubit control

## Slide 15: typical target Hamiltonians per paradigm
gates-based quantum computing
quantum annealing
analog quantum simulation
(cc) Olivier Ezratty, 2025
Heisenberg model (VQE)
spin dynamics, quantum magnetism, superconductivity.
electronic structure model (VQE, QPE) encoded into qubit gates using Jordan–Wigner and Bravyi–Kitaev transforms, also applicable with HEP.
Ising Hamiltonian
spin–spin interactions, quantum magnetism, and lattice models.
XX Ising models
quantum transport, superfluid-Mott insulator transitions, topological phases…
XY Ising models
non-trivial topological effects, real-time quench dynamics…
XXZ Ising models
ferromagnetic, antiferromagnetic, spin-liquid states, U(1) LGT simulations…
Fermi-Hubbard model (VQE, QPE)
strongly correlated systems in condensed matter physics, magnetism, Mott insulators, high Tc superc.
QUBO formulation
optimization problems, graph partitioning, route planning
MaxCut problems
solving various graph problems.
create unitary based on so that (error rate), and find eigenvalue or eigenstate of of interest
find minimizing a cost function that is the minimum eigenvalue of
find and/or minimizing a cost function that is the minimum eigenvalue of
QAOA (NISQ)
combinatorial optimization (MaxCut, traveling salesman problem, etc.).
Notes: Fermi Hubbard : For the Fermi–Hubbard model, one typically applies a fermion-to-qubit mapping first—Jordan–Wigner being the most direct example—so the on-site interaction Un^i,↑n^i,↓U \hat{n}_{i,\uparrow} \hat{n}_{i,\downarrow}Un^i,↑​n^i,↓​ and hopping terms t (ai,σ†aj,σ+h.c.)t\,(a_{i,\sigma}^\dagger a_{j,\sigma} + \text{h.c.})t(ai,σ†​aj,σ​+h.c.) become strings of Pauli operators that preserve fermion statistics.
Cold atoms and gauge theory: https://www.nature.com/articles/s41567-024-02721-8
A 2+1D U(1) model is a quantum field theory with two spatial dimensions and one time dimension whose local symmetry group is the abelian U(1) group. In practical terms, it can be viewed as a lower-dimensional analogue of electromagnetism (or other abelian gauge fields) where the gauge field is still governed by Maxwell-like equations, but the reduced dimensionality profoundly alters the nature of confinement, screening, and possible topological effects.
A cold atom analog quantum simulation of an XY Ising model involves preparing ultracold atoms in a specifically arranged lattice or tweezer array, then engineering interactions that mimic the XY Hamiltonian. The XY part of the Hamiltonian typically involves spin-exchange terms σixσjx+σiyσjy\sigma_i^x \sigma_j^x + \sigma_i^y \sigma_j^yσix​σjx​+σiy​σjy​ among neighboring sites, and the Ising label often highlights the possibility of including an external field or longitudinal coupling (though, strictly speaking, “XY” is already an anisotropic spin-1/2 model). In a cold atom setting, each site corresponds to a spatial position in the lattice occupied by an atom whose internal (usually hyperfine) states represent the spin degree of freedom. Laser-induced tunneling and controlled interatomic interactions (via Feshbach resonances in neutral atoms, or Rydberg excitations with van der Waals or dipole–dipole couplings) can be tuned to achieve the pairwise exchange required for the XY interaction. The “input data” in such a simulation are primarily the physical parameters specifying the Hamiltonian to be realized: these include the lattice geometry (one-dimensional chain, two-dimensional square lattice, etc.), the coupling strengths JxJ_xJx​ and JyJ_yJy​, the external fields (if present), and any boundary conditions. Experimentalists translate these Hamiltonian parameters into laser intensities, detunings, magnetic field gradients, and lattice depths that define how strongly atoms tunnel or interact on each bond. Once the system is prepared in a particular initial state—often the ground state of a simpler Hamiltonian or a fully polarized state—and allowed to evolve under the engineered XY Hamiltonian, the resulting “output data” are typically the measured spin configurations, correlation functions, or global observables such as magnetization. Modern quantum gas microscopes permit single-site resolved fluorescence imaging, so one can measure site-by-site spin orientations after a quantum quench or adiabatic ramp. This real-time measurement of local observables and correlation spreads allows direct insight into out-of-equilibrium phenomena, critical dynamics, and entanglement growth that would be challenging to compute via classical methods. Studies of the XY model with cold atoms have demonstrated intriguing effects such as dynamical phase transitions, spin-charge separation (when mapped to fermionic modes), and exotic quantum states of matter.

## Slide 16: from Hamiltonian to… values of interest
ground state.
eigenvalues.
eigenstates.
unitary approximation.
circuit synthesis.
embedding.
analog QPU
gate based QPU

## Slide 17: quantum algorithms interdependency clusters
A typology of quantum algorithms by Pablo Arnault, Pablo Arrighi, Steven Herbert, Evi Kasnetsi, and Tianyi Li, Inria, Quantinuum, arXiv, July 2024 (60 pages).
FTQC QPE & QFT based
analog QUBO
NISQ
VQE
QPE
HHL
QFT
QAE
QAOA
Grover
Notes: https://www.oezratty.net/Files/Conferences/A%20new%20agenda%20proposal%20for%20the%20Quantum%20Energy%20Initiative.pdf

## Slide 18: potential quantum speedups
superpolynomial
polynomial
exponential
weakly superpolynomial
NISQ or limited quantum advantage
for FTQC QPUs
quadratic
unknown
(heuristics)
simulations | VQE | amplitude estimation |  | QPE (quantum phase estimate) | 
searches and combinatorial optimizations | QUBO QAOA | quantum walks | Grover search |  | Deutsche-Jozsa Simon, Bernstein-Vazirani
machine learning | variational QML variants |  | reinforcement learning recommendation supervised clustering ensemble methods Bayesian networks |  | PCA SVM k-means convolutional networks
other | QSVD | Quantum Monte Carlo primality proofs | linear regressions | HHL based linear solvers PDEs QSLA | QFT QSVT, QSP Shor factoring & d-log Gauss sums, Jones polynomials
speedups
classical reference n = problem size
Understanding Quantum Technologies by Olivier Ezratty, as of November 2024.
Ising model and QUBO formulation on analog quantum computers

## Slide 19: theoretical vs practical speedups
total computing time, linear scale
problem size (N)
classical computing
quantum computing
exponential or polynomial
theoretical speedup
the typical and naive way to illustrate quantum computing theoretical speedups.
inspired by Opening the Black Box inside Grover's Algorithm by E. Miles Stoudenmire and Xavier Waintal, PRX, November 2024.
(*) for a fair comparison, the classical computer can be as expensive and/or energy hungry as the QPU.
number of qubits
classical computing (*)
quantum computing
exponential speedup
total computing time, log scale
polynomial speedup
are Te and Tp
compatible with the use case constraints?
Te
Tp
“prefactors”
intractable (exponential) problem
Tq
Tc

## Slide 20: how variational algorithms work
1
0
0
0
classical initialization with having energy
classical optimizer used to compute a new to minimize cost function
inject new
exit when is stabilized
post-processing computing expectation value
error mitigation post-processing
(cc) Olivier Ezratty, 2023-2025
number of L layers
depending on the algorithm
number of Pauli strings
)
M=4 for electronic structure
M=1 for Heisenberg model
M=1 for QAOA
number of shots per Pauli strings?
)
1 million for VQE and chemical ground state computing
unknown number of ansatz iterations
n qubits
VQE
QAOA
QML

## Slide 21: how oracle based algorithms work
U quantum oracle function flips the sign/phase of found computational state x
Grover diffusion operator series of gates amplifying x and attenuating other states
index response readout: solution index x with n bits
oracle sign inversion on one computational base value, x
creates a superposition of N=2n computational states
repeated times
classical preparation of a quantum circuit
qRAM accessing classical data
or
example with the Grover algorithm
Grover
Simon
Bernstein-Vazirani

## Slide 22: how Quantum Phase Estimation works
results post-processing
inspired by Quantum chemistry, classical heuristics, and quantum advantage by Garnet Kin-Lic Chan, arXiv, July 2024 & On the feasibility of performing quantum chemistry calculations on quantum computers by Thibaud Louvet, Thomas Ayral, and Xavier Waintal, arXiv, June 2023-October 2024.
state vector encoding circuit
problem Hamiltonian encoding
modular exponentiation
repeated times
decreasing exponentially with molecule size
classical pre-processing (HF, FCI, DFT, …) for N orbitals
as close as possible to target ground state
Block-encoding.
Trotter-Suzuki decomposition.
QSVT.
Linear Combination of Unitaries (LCU).
n qubits in phase register
n exponentiations of U
find U using
= system Hamiltonian
= unitary encoding it
classical computing time scale
to
to
N = number of orbitals
n ≈ phase output precision
m ≈ Hamiltonian complexity.
Notes: LCU cost : O(N4) for N orbitals. Matrix recomputation scales as O(N4) to O(N5).

## Slide 23: key FTQC quantum algorithms food chain
integer factoring
& dlog
Shor algos
HHL
solving linear equations
QPE quantum phase estimation
quantum Fourier transform
modular exponentiation
quantum machine learning (FTQC)
quantum chemistry
cryptanalysis
computational fluid dynamics
partial differential equations (PDEs)
QSVT
Why Haven’t More Quantum Algorithms Been Found? by Peter Shor, 2003 (4 pages).
Quantum algorithms: A survey of applications and end-to-end complexities by Alexander M. Dalzell, Fernando G. S. L. Brandão et al, AWS, RWTH Aachen University, Imperial College London, Caltech, October 2023 (337 pages).
QAE
quantum amplitude estimation
Quantum Monte Carlo methods
oracle and amplitude amplification

## Slide 24: hybrid software architecture
this chart describes not an hybrid classical-quantum algorithm but an hybrid classical-quantum whole architecture, to simulate digitally how niobium-rich refractory alloys could reduce corrosion. Source: Quantum computing for corrosion-resistant materials and anti-corrosive coatings design by Nam Nguyen et al, arXiv, June 2024 (52 pages).

## Slide 25: HEP quantum algorithms
Quantum Computing for High-Energy Physics: State of the Art and Challenges by Alberto Di Meglio et al., PRX Quantum, July 2023-August 2024 (49 pages) focuses on utility-scale NISQ algorithms.
typical problems:
low-dimensional lattice gauge theory (LGT).
anomaly detection in collider experiments.
detector operation algorithms.
identification and reconstruction algorithms.
simulation and inference tools.
mix of analog, NISQ and FTQC algorithms.
theoretical physical models
experimental challenges

## Slide 26: NISQ cases
120
112
A comparison of HPC-based quantum computing simulators using Quantum Volume by Lourens van Niekerk, Christian Boehme et al, arXiv, December 2024.
log times in seconds
for simulating a single quantum volume of the given qubit number for tested emulator on a single classical cluster node
5/2024
https://www.worldscientific.com/doi/full/10.1142/S0217751X24500076
1 s
11/2024
https://www.arxiv.org/abs/2411.02486
6
30
12/2024
https://arxiv.org/abs/2412.21177
https://arxiv.org/abs/2401.08044
GPU-based emulations are faster
6/2024
https://arxiv.org/abs/2411.13520
11/2024

## Slide 27
NISQ
FTQC
100-128
4,728
logical qubits
physical qubits
10-200
error rate in (power of 10)
-1
-2
-3
-4
-6
-7
-8
-9
-10
-11
-12
-13
-14
-15
-16
-17
-18
-19
-20
-21
-22
# qubits
928
7,925
catalysts for nitrogen fixation
corrosion-resistant materials
8,763
725K
incompressible CFD
“1000s to 100Ks”
-23
-24
vendors roadmaps 2028 - 2033
10
100
1,000
10,000
100,000
1M
Shor on RSA-2048
pricing derivatives
11K
amyloid beta binding
15K
4K
VQE, QAOA, QML, QUBO
with potential quantum advantage
VQE, QAOA, QML, experiment
100
Stage 1
NISQ
Stage 2
early stage FTQC
Stage 3
utility-scale FTQC
Notes: compilation of some resource estimates for key algorithms which have some industry relevance. The top part contains some typical algorithms and their resource estimated ranges in gates, T gates or Toffoli gates. These resource estimates correspond to an error rate for the qubits (physical in NISQ and logical in FTQC) in the purple scale crossed by the dotted lines. Below in orange and red are the related resource estimates in physical (NISQ) and logical (FTQC) qubits, regardless of the implementation. Source: DARPA benchmarks mentioned in the text. Physical qubits and logical qubits are on a similar log scale. What determines the characteristics of logical qubits like the physical per logical qubit count is their target error rate itself dependent on the number of algorithms gates. What the chart shows is that the key vendor’s roadmaps with goals of reaching 100 to 128 logical qubits before 2033 are far off the practical needs of impactful algorithms for the industry related to financial, chemical applications, nitrogen capture and pharmaceutical applications. (cc) Olivier Ezratty, July 2024. Sources: TDA: Towards Quantum Advantage on Noisy Quantum Computers by Ismail Yunus Akhalwaya et al, September 2022, Feasibility of accelerating homogeneous catalyst discovery with fault-tolerant quantum computers by Nicole Bellonzi et al, June 2024, A threshold for quantum advantage in derivative pricing by Shouvanik Chakrabarti et al, Goldman Sachs, IBM and University of Maryland, May 2021 (41 pages). Real Option Pricing using Quantum Computers by Alberto Manzano et al, March 2023, How to factor 2048 bit RSA integers in 8 hours using 20 million noisy qubits by Craig Gidney and Martin Ekerå, 2019, Quantum Resources Required for Binding Affinity Calculations of Amyloid beta by Matthew Otten et al, June 2024, Quantum computing for corrosion-resistant materials and anti-corrosive coatings design by Nam Nguyen et al, June 2024, Feasibility of accelerating homogeneous catalyst discovery with fault-tolerant quantum computers by Nicole Bellonzi et al, June 2024, Feasibility of accelerating incompressible computational fluid dynamics simulations with fault-tolerant quantum computers by John Penuel et al, June 2024.

## Slide 28: >90 QPUs industry vendors!
superconducting
topological
vacancies
annealing
silicon
trapped ions
photons
cold atoms
electrons controlled spin and microwave cavities
atoms
photons
Z-Axis Quantum
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Notes: Map of the 90+ industry vendors in quantum computing hardware per qubit type. Some qubit categories are organized in subclasses as follows: (1) for laser driven ions, (2) for microwave driven ions, (3) for ions in Rydberg states, (4) for regular cold atoms, (5) for cold atoms with nuclear spin manifold, (6) for a variant of cold atoms with ionization preparation, (7) for transmon superconducting qubits, (8) for other superconducting qubits like bosonic qubits, dual rail qubits and fluxonium qubits, (9) for silicon spin qubits, (10) for silicon-germanium qubits, (11) for other spin variant qubits like nanosphere and nanotubes, spin on helium and donor spin, (12) for NV centers qubits, (13) for silicon vacancies qubits, (14) for direct variable photon qubits, (15 for continuous variable photon qubits and (15) for coherent Ising model photonics systems.

## Slide 29
Notes: https://globalventuring.com/university/asia/8-quantum-spinouts-breaking-new-ground/

## Slide 30: inside a typical quantum computer
qubits control electronics
microwave generators, readout systems and various electronics
computing
servers, network,
software, data
cryogenic installation
helium 3 & 4 gas pumps and compressor
quantum chipset
« chandelier » in cryostat
where quantum stuff happens!
QC in a cryostat but a lot of other components are outside, and always a classical computer driving the QC.
15mK
(cc) Olivier Ezratty, 2023
for superconducting or electron spin qubits
helium 4
water
vacuum pump
4K
compressor
pumps
filters
external compressor
helium 3
liquid nitrogen
gas filter

## Slide 31: rough qubit modalities comparison
 | cold atoms | trapped ions | superconducting | silicon | NV centers | photons
operations fidelities |  |  |  |  |  | 
gate times | with no shuttling |  |  |  |  | 
qubit connectivity | with shuttling |  |  |  |  | 
cooling needed | 4K | 4K | 15 mK | ≈500 mK | TBD | 1.8 to 4K
qubit size |  |  |  |  |  | 
scalability |  | with tiled chips |  |  |  | 
electrons controlled spin and microwave cavities
photons
atoms
Notes: Data sources:
Cold atoms: https://arxiv.org/pdf/2006.12326.pdf
In situ equalization of single-atom loading in large-scale optical tweezer arrays by Kai-Niklas Schymik, Florence Nogrette, Antoine Browaeys, Thierry Lahaye et al, PRA, August 2022 and Ultrafast energy exchange between two single Rydberg atoms on a nanosecond timescale by Y. Chew et al, Nature Photonics, 2022 (7 pages).
Trapped ions : https://arxiv.org/pdf/1904.04178.pdf, https://arxiv.org/pdf/2009.00568.pdf, https://www.infineon.com/cms/en/product/promopages/trapped-ions/
Silicon: https://iopscience.iop.org/article/10.1088/1361-6528/abb333/pdf
Superconducting: Google Sycamore and IBM papers
NV centers: https://aip.scitation.org/doi/pdf/10.1063/5.0007444

## Slide 32: raw algorithm fidelities requirements
N qubits
desired error rate
computing depth D
two-qubit gate
time
three-qubit gate
single-qubit gate
initialization
readout
qubit operations accumulated errors quickly kills algorithms accuracy
possible solutions:
use shallow circuits on a few qubits (NISQ).
quantum error mitigation (NISQ).
quantum error correction (FTQC).

## Slide 33: the qubit fidelities challenge
viable NISQ zone in a quantum advantage regime without QEM
(hard to obtain)
quantum error mitigation NISQ utility window
good
bad
route to FTQC, requiring a large number of quality qubits

## Slide 34: logical qubits and FTQC
physical qubit
logical qubits
error rates ≈0.1%
error rate ≈10-4 to ≈10-18
fault tolerance (FTQC)
implement logical gate correction.
avoid error propagation and amplification.
implement a universal gate set.
fault-tolerant results readout.
correct correlated errors.
tens to thousands physical qubits per logical qubits
error correction code
threshold, physical qubits overhead, connectivity requirements, syndrome decoding and scale
Notes: Source : arxiv 1202.2639

## Slide 35: beyond the first breakeven logical qubits
10-6 logical error rates would require 1,457 physical qubits per logical qubits and a distance-27 surface code with existing qubit fidelities.
Google Willow = 105 qubit chip with a distance-7 single logical qubit
error rate (two-qubit gates)
surface code distance
Quantum error correction below the surface code threshold by Rajeev Acharya, Frank Arute, Michel Devoret, Edward Farhi, Craig Gidney, William D. Oliver, Pedram Roushan et al, Google, arXiv, August 2024.
plan for 10K qubits chips
+
QPU interconnect
physical error rate
logical error rates
number of physical qubits per logical qubit
factor slope that may improve over time

## Slide 36: multiple QPUs interconnect options
approximate physical qubits # required to reach 100 logical qubits and 10-6 error rate, the lower being the better.
photonic coupling with transduction
single monolithic chip or QPU
direct photonic coupling
short range or mid-range microwave couplers
interconnect using same qubit modality
single chip
short range microwave couplers
mid-range microwave couplers
photonic coupling and transduction
transmon
cat-qubits
trapped ions
cold atoms
trapped ions
QD spins
single chip
microwave couplers
photonic coupling and transduction
single chip
ions shuttling between ion traps chips
photonic coupling
single chip
photonic coupling
single QPU
photonic coupling
single QPU
photonic with transduction or shuttling electrons coupling
photons
single photonic integrated circuit
photonic coupling
transmons
single chip
photonic…
growing complexity with rough estimates thresholds requiring these techniques
multi 10K

## Slide 37
2025
2026
2027
2028
2029
2030
2031
2032
2033
2034
2035
200
100M
156x7 PQ
2000
1B
15K
5K
10K
7.5K
150
300
4-36
60-180
240-720
600-1800
2400-7200
1K
5K
40K
100K
1M
96
192
1000s
~ 50
~100
~100s
30
3K
100
>10K
>10
8K
>100
40K
2
1.6K
1M
~100s
1M
50s
50K
10
15
1K
100
2K
25-45
4K
50-100
20K
180-360
120K
1,400
1M
5
250
4
48
(cc) Olivier Ezratty, August 2025.
1M
100K
1M
≈1G
≈1T
≈100T
256
64
2-10
64
10K
800
256
12
10M
200
10K
2
20
200+
100
140
16
200
5,000
50K
1K
1M
1G
1T
logical qubits
gates / QOPS
physical qubits
box color codes
QEC overhead
circuit depth
logical qubits fidelities
100
50
1,000
12,000
40,000
>1M
500
1,000s
10,000s
20,000
1,600
200K
8,000
2M
80,000
1T
1T
superconductors & spins
cold atoms
tapped ions
photons
100
1000

## Slide 38: QPU vs HPC power scale guesstimates
acceptability threshold hypothesis
largest WW supercomputers
4K logical qubit QPU estimates
estimate base power for various QPUs and actual for existing largest HPCs WW. HPC source: https://www.top500.org/lists/top500/2024/06/.
circuit shots parallelization
peak power consumption (log scale)
(cc) Olivier Ezratty, 2025.
IEEE P3329 Quantum Energy Initiative (QEI) Working Group
https://www.youtube.com/watch?v=rUcPLZeZxG0&t=3048s

## Slide 39: quantum technologies in astrophysics
dark matter search quantum sensors

## Slide 40: industry vendors country + creation year
source : Olivier Ezratty compilation, September 2024
quantum computing
telecommunications and security
quantum sensing
enabling technologies
number of industry vendors
creation year
France, #4 in number of ccmpanies (but not in $ raised).

## Slide 41
trapped ion qubits
trapped ion qubits
computers
simulators
telecoms
sensing
superconducting qubits
cold atoms and trapped ions
cold atoms
photons
trapped ions (simulation and universal QC)
QRNG, CMOS SPADs
repeater network, interface with qubits
system on chip
QKD on photonics, telcos
NV centers
optical clock
IRM & NV centers
cold atoms
photons
photonic
photonic
IPC micro-waves
the role of the EU quantum flagship
QLSI lead by Grenoble
Pasqal et Atos in PASQuans
PSL pilote PhoQuS
Thales in Asteriqs, coordonné par Onera
QLSI 2
silicon qubits
software applications
software
NV centers / SiC qubits

## Slide 43
get these slides
(free) 1,554 pages ebook, 7th edition
Notes: https://www.oezratty.net/Files/Conferences/Olivier%20Ezratty%20Pisa%20Quantum%20Computing%20Sept2025.pdf