## Slide 1
Hybrid Pixel Single Photon Detector for Quantum Applications
Innovative Solutions for Quantum Imaging and Real-Time Feedback
Shazia Farooq 25th January 2025
Notes: I’ll be talking about the advancements we’ve made at ASI with hybrid pixel single-photon detectors, and how they are opening up new possibilities for quantum imaging and real-time feedback systems I’ll give you an overview of our technological advancements, discuss some of the challenges we’ve encountered, highlight the current gaps in the field, but before that I will share my perspective as someone working in the industry.

## Slide 2: Outline
Perspectives from Academia to Industry
Technological Advancements
Challenges
Current Gaps in the Field

## Slide 3: From Lab Coat to Business Suit 

## Slide 4
2011
ASI was found as spin-off from NIKHEF and AMOLF in Amsterdam
2013
First deliveries of TPX-1 detectors to synchrotron customers
2017
Commercial Restructuring under new leadership
2018
Release of TPX3CAM
2020
Release of CheeTah M3 and T3 Retractables
2022
Release of CheeTah 1MP
2021
Release of LumaCam
2023
Release of 4D-STEM solutions
2024
Release of Hyperion
Release of Phoebe

## Slide 5: TPX3CAM: Hybrid Pixel Photon Detector
Prof. Andrei Nomerotski
(StonyBrook & BNL)
Single-Photon-Sensitive Event-Driven , Tim-Resolved 2D Detector
Detection of optical photons (VIS to UV range) making use of optical photon sensors:
Conventional silicon sensor adapted to optical photons sensing
Electron multipliers (MCP)
Image Intensifiers

## Slide 6: Hybrid Pixel Detectors
Sensor material is separate from electronics this makes Timepix3 very robust.
Noise Free (counting mode, thresholding)​
Ultra-sensitive (high intrinsic amplification)

## Slide 7
Hybrid Pixel Detector
Semiconductor
Sensor
(Si, GaAs, CdTe)
ASIC Chip
Pixel Size: 55 µm
256 x 256 pixels
Amplifier
Comparator
Threshold
level
+
Digital Counter
Read-out
N+
P+
Bump
Bonds
+ 1 count
Working principle

## Slide 8
Data-driven – direct readout of the hit
Time of Arrival (ToA) of each electron with 1.56 ns time resolution
Very high effective frame rates – 640 MHz
3D information (x,y and time)
Measuring energy deposited (~10 -20% resolution)
Time over Threshold (ToT) of each event with 25 ns resolution
Measuring pile-up (multi hit)
What does Timepix3 offer/enable: ToA & ToT
V
Chip
Si-Sensor
Photon
Bias
Electron hole pairs
Time over Threshold: Energy / Double Hits
Signal
Time
Threshold
Data[X, Y, ToA, ToT]
Time of Arrival: 1.56 nanoseconds precision

## Slide 9: Event-based detection can also create images!
Event-based
T = 1 ns
T = 2 ns
T = 4 ns
T = 6 ns
Event List
Timepix 3
Sum of Events

## Slide 10: Modes of Operation
Chip
Si-Sensor
Timepix 3
Timepix 3
Frame-based
Event-based

## Slide 11: TDC (Time to Digital conversion) input
Low voltage TTL input on TDC
Source examples:
Pulsed laser sync
Photon counter (e.g.SPAD)
ASI Timepix3 Detectors has two external TDC inputs with 260 ps time resolution
These allow synchronization with arbitrary external signals
The inputs are clock synchronized with the Timepix3
They appear as events in the event list output
 | Time-of-Arrival (s) | X | Y
TPX3 | 0.00405912969 | 56 | 239
TPX3 | 0.00405912969 | 0 | 214
TPX3 | 0.00405912969 | 121 | 163
TPX3 | 0.00405912656 | 68 | 145
TDC | 0.00405912655 | - | -
TPX3 | 0.00405920938 | 133 | 197
TPX3 | 0.00405912500 | 32 | 98
TXP3 | 0.00405956094 | 12 | 228
TDC | 0.00405956096 | - | -
List of events
Electron
Timepix3 Detectors
TDC Specifications | 
Time resolution | 260 ps
Number of inputs | 2
Trigger | Rising or falling edge or both
Maximum rate | 10 MHz

## Slide 12: Clock synchronization
Clock reference 40 MHZ
Source examples:
Function generator
Scan generator
Raspberry Pi
An alternative is to synchronize the clock of the Timepix3 detectors with an external reference
Timepix3 Detectors has a 40MHz input and output
It is even possible to daisy-chain Timepix3 Detectors
Electron
Timepix3 Detectors
Timepix3
Detectors

## Slide 13: Chronos: The Optical TPX3CAM

## Slide 14
Application Specific Chronos Series
Quantum Science:
Phoebe & Rhea
Ion Detecton:
Hyperion
Neutron Detection:
Telesto
TPX3CAM (legacy)
Notes: Tpx3cam is adapted for different application and modified for according to its need

## Slide 15
159 publications in past 5 years using TPX3CAM and Chronos
MassSpec
Quantum
VMI
Neutrons

## Slide 16: Chronos Series: Quantum Imaging
Phoebe is an intensified hybrid pixel detector based on TPX3CAM especially designed for Quantum Science applications.
Phoebe
the single-photon TPX3CAM

## Slide 17
https://doi.org/10.48550/arXiv.2005.07982
Hong-Ou-Mandel effect

## Slide 18
Notes: ​

## Slide 19: Crystal clear insights on the quantum states of hundreds of trapped-ion qubits with Phoebe: the single-photon TPX3CAM!

## Slide 21
https://doi.org/10.1103/PhysRevA.103.023105
Simultaneous time & position information allows to monitor ion micro-motions
Notes: FIG. 1. (a) Diagram of the experimental setup with ions in a linear RF trap formed by four rods and two needle end-cap electrodes. dc bias voltages may be applied to any of the four rods to compensate the micromotion. The cooling laser (red arrow) is applied at 45◦ to the trap axis and the ion string is imaged from above. (b) Image of eight Ba+ ions taken with the Tpx3Cam camera over a 20-s integration period. The ion brightness variation is due to the Doppler cooling beam profile. The distance between the middle ions is approximately 5 μm.

## Slide 22: Ongoing Projects: 2025-2026
256 x 256 pixels
C-Mount
1.56 ns
80 Mhits/s
TDC: 260 ps
256 x 256 pixels
c-Mount
Latency optimized
TDC: 260 ps
512 x 448 pixels
M-Mount
200 ps
1.2 Ghits/s
512 x 448 pixels
M-Mount
200 ps
1.2 Ghits/s
Chronos Phoebe
Chronos Rhea
Chronos Phoebe T4 +SPAD
Chronos Phoebe T4
STANDARD
In Progress
In Progress
Conceptual

## Slide 23: Chronos Series: Real-Time Feedback
Rhea is an intensified hybrid pixel detector based on TPX3CAM especially designed for real-time feedback control applications. Our development team is currently working on a prototype.
Rhea
the real-time feedback control TPX3CAM

## Slide 24: Quantum Computing with Atoms
Quantum computing leverages particles as qubits, and in our case, we focus on atoms.
Atoms function as qubits because they exhibit two distinct states—"dark" (logical 0) and "bright" (logical 1).
  When exposed to light at a specific wavelength, atoms either reflect or do not reflect light, making their state visible in imaging.
  This property allows us to determine whether they represent a 0 or a 1 by taking pictures and analyzing their brightness.
Application Context
Atoms are held in optical tweezers, and their states (light or dark) are measured using imaging detectors.
The key requirement in this process:
  Capture an image of the array of atoms.
  Identify the states (light or dark) as quickly as possible to ensure precise feedback.
Typical fluorescence Imaging of single atoms:
Need to collect tens of photons to clear camera noise
Need to have a deep enough trap to tolerate heating
or cool simultaneously
Image durations (exposures): 10-100 ms
  record is 500 us
Notes:   Rhea is a fast real time feedback camera for quantum computing

## Slide 25: Why Speed Matters
Fast Feedback is Critical in Quantum Systems
Atoms' states are unstable and decay rapidly (e.g., within ~100 ms).
Delays in feedback, even as little as 10 ms, can result in a 10% loss of quantum states.
Speed is essential to maintain coherence and correct errors in real-time.
Current Workflow Challenges
Standard systems involve these steps:
  Take exposure (open/close shutter).
  Read out data from the detector.
  Transfer data to the control system.
Typical readout involves transferring data from the detector chip to an FPGA, then to a PC for processing. This can introduce critical latency.

## Slide 26: The Innovation of Rhea
What Rhea Does
Rhea accelerates the feedback loop by enabling ultrafast readout and processing of the quantum system states.
The detector computes the region of interest (ROI) directly on the FPGA:
  Determines whether each region represents a light or dark state.
  Immediately transfers this information to the quantum control system.
Key Innovation
Eliminates the need for data transfer to a PC for processing.
Reduces latency by performing computations directly on the FPGA, ensuring near-instantaneous feedback.
Readout chip
PC
FPGA
High latency
Hit/pixel data
Correction setup (external)
Interaction site information
Light or dark state for atoms in array
Computation happens on FPGA and is fast
Interface to setup needs to be defined

## Slide 27: Challenges and Uncertain Elements
Standardization Challenges
There is no universal standard for transferring data from detectors to quantum control setups.
Different quantum systems (e.g., ion traps, neutral atom processors) require unique configurations.
Latency and Data Rate
Achieving low latency is challenging due to:
  High photon rates overwhelming the system during exposure.
  Balancing data-driven mode and frame-based mode to ensure optimal performance.
Developing physical electronic connections that meet the speed and reliability requirements.
Technical Barriers
The system must manage high data rates while maintaining precision.
Integration with diverse quantum computing setups requires adaptable solutions.

## Slide 28: Why Rhea is Needed
Problem Rhea Solves
Traditional systems face delays in transferring and processing data, which slows down real-time feedback.
These delays lead to errors in quantum computations due to state decay.
Rhea's Solution
Implements low-latency processing directly at the detector level.
Provides immediate feedback to the quantum control system, enhancing error correction and system reliability.

## Slide 29: A little Sneak Peek at our current project

## Slide 30: Optical TPX4...(in progress)
The max rate is 1.2 Ghits/s.
195ps time bin
For experiments where High hit rate and large area detection system and much faster time-resolution is required
First optical TPX4 signals
70 ps pulsed laser (thanks to Andrei Nomerotski)
TPX4 Full rate Data Pipeline
16 GWT links from TPX4 chip (2.56 Gb/s for now, 5.12 Gb/s later)
2 x FireFly → 16 fibers on MPO → 4 x QSFP → BittWare card
16 receivers → packet builders → Wupper interface → memory
Serval: merge streams → sort → split
Notes: Gigabit Wireline Transmitter. It's the interface Timepix4 uses to offload data which is much faster than Timepix3, maximally at 10.24Gbps (giga bit per second) per link. Currently, it is proven to work reliably at half that rate (5.12 Gbps) using wirebonds. Using TSVs it might be able to work at 10.24Gbps.

## Slide 31: Technical Challenges in Development
Fast phosphors
Large Area Intensifier
Processing Data
Readout Rate
Single Photon Sensitive Sensor
Higher QE of Intensifiers
Notes: Better sensor Single Photon Sensitive Sensor

## Slide 32: Non-Technical Challenges in Development
Securing long-term R&D funding.
Aligning R&D expenses with scalability.
Managing academic collaborations alongside industrial schedules. (UvA)
Bridging the talent gap in quantum expertise.
Ensuring access to specialized materials and manufacturing techniques.
Identify companies for integration into the quantum industry sector.
Transitioning from academia-focused sales to targeting the broader industry in the quantum domain.
Identifying what appeals to a larger market in the quantum sector.
Developing strategies for effective networking within the industry.

## Slide 33: ASI Effort’s in Quantum Domain
Rhea Project Collaboration Partnering with the University of Amsterdam (UvA) to advance quantum research.
Quantum Delta NL Grant Proud recipients of this prestigious grant to support groundbreaking quantum initiatives.
Active Collaborations with QBN Strengthening ties with the Quantum Business Network to drive innovation and ecosystem development.
Upcoming QBN Event Hosting the next Quantum Business Network event in Q4 2025.

## Slide 34
Let’s collaborate to push the boundaries of quantum technology!