## Slide 1: Transition Edge Sensors: From First Principles to Applications in Particle Detection and Quantum Technologies
José Alejandro Rubiera Gimeno
Postdoctoral researcher at Helmut-Schmidt-Universität (HSU)

## Slide 2: Outline
Beginning of Transition Edge Sensors (TES)
TES physics
High energy photon detection
Visible to IR photon detection
Applications in Quantum technologies

## Slide 3: Transition Edge Sensor (TES)
Normal
Conduction
Super-
Conduction
region
Working
point
K. Irwin, G. Hilton, Transition-edge sensors, in: Cryogenic Particle Detection, Springer Berlin Heidelberg, Berlin, Heidelberg, 2005, pp. 63–150, http://dx.doi.org/10.1007/10933596_3.
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
*Courtesy of Katharina-Sophie Isleif

## Slide 4: Transition Edge Sensor (TES)
K. Irwin, G. Hilton, Transition-edge sensors, in: Cryogenic Particle Detection, Springer Berlin Heidelberg, Berlin, Heidelberg, 2005, pp. 63–150, http://dx.doi.org/10.1007/10933596_3.
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
Change in resistance produced by energy deposition
Very good energy resolution
*Courtesy of Katharina-Sophie Isleif

## Slide 5: First TESs (‘40s – ‘90s)
Normal
Conduction
Super-
Conduction
region
K. Irwin, G. Hilton, Transition-edge sensors, in: Cryogenic Particle Detection, Springer Berlin Heidelberg, Berlin, Heidelberg, 2005, pp. 63–150, http://dx.doi.org/10.1007/10933596_3.
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Controlling bath temperature
*Courtesy of Katharina-Sophie Isleif
Working
point

## Slide 6: First TESs (‘40s – ‘90s)
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Controlling bath temperature
Thermal circuit

## Slide 7: First TESs (‘40s – ‘90s)
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Controlling bath temperature
Thermal circuit
Electrical circuit

## Slide 8: First TESs (‘40s – ‘90s)
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Controlling bath temperature
Thermal circuit
Electrical circuit
Readout with FET and other solutions
Very noisy ...

## Slide 9: First TESs (‘40s – ‘90s)
Normal
Conduction
Super-
Conduction
region
K. Irwin, G. Hilton, Transition-edge sensors, in: Cryogenic Particle Detection, Springer Berlin Heidelberg, Berlin, Heidelberg, 2005, pp. 63–150, http://dx.doi.org/10.1007/10933596_3.
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Controlling bath temperature
*Courtesy of Katharina-Sophie Isleif
Working
point

## Slide 10: Nowadays TES physics
Normal
Conduction
Super-
Conduction
region
K. Irwin, G. Hilton, Transition-edge sensors, in: Cryogenic Particle Detection, Springer Berlin Heidelberg, Berlin, Heidelberg, 2005, pp. 63–150, http://dx.doi.org/10.1007/10933596_3.
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Voltage-biased TES
*Courtesy of Katharina-Sophie Isleif
Working
point

## Slide 11: Nowadays TES physics
Normal
Conduction
Super-
Conduction
region
K. Irwin, G. Hilton, Transition-edge sensors, in: Cryogenic Particle Detection, Springer Berlin Heidelberg, Berlin, Heidelberg, 2005, pp. 63–150, http://dx.doi.org/10.1007/10933596_3.
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Voltage-biased TES
Superconducting Quantum Interference Device (SQUID) readout
*Courtesy of Katharina-Sophie Isleif
Working
point

## Slide 12: Nowadays TES physics
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Voltage-biased TES
Thermal circuit
TES can be at different temperature than bath

## Slide 13: Nowadays TES physics
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Voltage-biased TES
Thermal circuit
Electrical circuit

## Slide 14: Nowadays TES physics
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Voltage-biased TES
Thermal circuit
Electrical circuit
Non-linear system

## Slide 15: TES Small Signal Theory
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Voltage-biased TES
Thermal circuit
Electrical circuit
Linearize with respect to working point for small variations of and
Normal
Conduction
Super-
Conduction
region

## Slide 16: TES Small Signal Theory
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Voltage-biased TES
Normal
Conduction
Super-
Conduction
region
If L is small, so :

## Slide 17: TES Small Signal Theory
Cryogenic detector operated at transition region
Connected to a colder thermal bath
Possible definition of the point in the transition
  Voltage-biased TES
Normal
Conduction
Super-
Conduction
region
Slower rise time
Faster decay time
If L is small, so :

## Slide 18: TES Strong ETF
If L is small, so :
Strong electrothermal feedback (ETF) if

## Slide 19: TES Strong ETF
If L is small, so :
Strong electrothermal feedback (ETF) if
TES as bolometer:
TES as calorimeter:
K. Irwin, G. Hilton, Transition-edge sensors, in: Cryogenic Particle Detection, Springer Berlin Heidelberg, Berlin, Heidelberg, 2005, pp. 63–150, http://dx.doi.org/10.1007/10933596_3.

## Slide 20: TES noise and energy resolution
Thermal fluctuation noise (TFN)
Johnson or Nyquist noise
Thermal noise
Electronic noise
K. Irwin, G. Hilton, Transition-edge sensors, in: Cryogenic Particle Detection, Springer Berlin Heidelberg, Berlin, Heidelberg, 2005, pp. 63–150, http://dx.doi.org/10.1007/10933596_3.

## Slide 21: TES noise and energy resolution
K. Irwin, G. Hilton, Transition-edge sensors, in: Cryogenic Particle Detection, Springer Berlin Heidelberg, Berlin, Heidelberg, 2005, pp. 63–150, http://dx.doi.org/10.1007/10933596_3.
Thermal fluctuation noise (TFN)
Johnson or Nyquist noise
Thermal noise
Electronic noise
Excess noise

## Slide 22: TES physics summary
*Courtesy of Katharina-Sophie Isleif
Rise time
Decay time
Measured power with TES as bolometer
TES in strong ETF
Measured energy of photon with TES as calorimeter
Theoretical limit for TES energy resolution

## Slide 23: TES physics summary
*Courtesy of Katharina-Sophie Isleif
Rise time
Decay time
Measured power with TES as bolometer
TES in strong ETF
Measured energy of photon with TES as calorimeter
Theoretical limit for TES energy resolution

## Slide 24: High energy photon detection

## Slide 25: X-ray and gamma TES detectors
Decay time
Theoretical limit for TES energy resolution
C increases due to the absorber
worsens and increases
Absorber big enough to increase probability of X-ray and gamma interaction

## Slide 26: X-ray and gamma TES detectors
C increases due to the absorber
worsens and increases
Very high S-to-N ratio
Excellent energy resolution of ~0.01%
A Review of X-ray Microcalorimeters Based on Superconducting Transition Edge Sensors for Astrophysics and Particle Physics. Applied Sciences, 11(9), 3793. https://doi.org/10.3390/app11093793

## Slide 27: Extending the range to ~100 keV
Rev. Sci. Instrum.. 2012;83(9). doi:10.1063/1.4754630
High purity Germanium detector
TES
Absorber Sn: 1.45 x 1.45 x 0.38
High efficiency for gamma and low C

## Slide 28: Extending the range to ~100 keV
Rev. Sci. Instrum.. 2012;83(9). doi:10.1063/1.4754630
High purity Germanium detector
TES
Absorber Sn: 1.45 x 1.45 x 0.38
High efficiency for gamma and low C
SQUID multiplexing

## Slide 29: X-ray astrophysics
X-rays emitted by ionized atoms and energetic electrons near active objects
Energies of discrete X-ray lines reveal elements
Doppler shift of lines indicate dynamic conditions of elements
Presence of several ionization lines
Requires excellent energy resolution

## Slide 30: X-ray astrophysics
X-rays emitted by ionized atoms and energetic electrons near active objects
Energies of discrete X-ray lines reveal elements
Doppler shift of lines indicate dynamic conditions of elements
Presence of several ionization lines
Requires excellent energy resolution
Athena/X-IFU to be launched with more than 3000 pixels
doi:10.1007/s10686-022-09880-7

## Slide 31: Visible to IR photon detection

## Slide 32: Visible to IR photon TES detectors
Decay time
Theoretical limit for TES energy resolution
The TES is the absorber C lower
is lower and also lower

## Slide 33: Visible to IR photon TES detectors
The TES is the absorber C lower
is lower and also lower
and much faster
1064nm pulse
doi:10.3204/PUBDB-2024-07357

## Slide 34: Propagating photons to the detector
Use of an optical fiber to transmit photons to the TES
Optimized for photon with an optical stack
A tungsten microchip () provided by NIST and SQUID and packaging PTB stabilized in the transition region (~ 140 mK)
* TES setup at DESY

## Slide 35: Propagating photons to the detector
Use of an optical fiber to transmit photons to the TES
Optimized for photon with an optical stack
A tungsten microchip () provided by NIST and SQUID and packaging PTB stabilized in the transition region (~ 140 mK)
TES at DESY for the ALPS II experiment
doi:10.22323/1.449.0567
* TES setup at DESY

## Slide 36: Background in the TES
Schematic adapted from Katharina-Sophie Isleif.
Fiber disconnected from the TES.
The recorded rate of events in the order is usually below (depends on the trigger)
Origin associated to radioactivity and cosmic rays.
TES response different than photon pulses. Allows pulse shape discrimination and machine learning
e.g. [1]
[1] doi:10.22323/1.398.0801
[2] doi:10.3204/PUBDB-2024-07357

## Slide 37: Background in the TES
Schematic adapted from Katharina-Sophie Isleif.
Fiber disconnected from the TES.
The recorded rate of events in the order is usually below (depends on the trigger)
Origin associated to radioactivity and cosmic rays.
TES response different than photon pulses. Allows pulse shape discrimination and machine learning
e.g. [1]
[1] doi:10.22323/1.398.0801
[2] doi:10.3204/PUBDB-2024-07357
Fiber connected from the TES and other end in the dark.
The recorded rate of events in the order can be up to (depends on the trigger)
Mainly Black Body Radiation coupling to the optical fiber.
TES energy resolution allows background discrimination [2]
Very low background requires other strategies.

## Slide 38: Multicolor measurement with TES
doi:10.3204/PUBDB-2024-07357
Use in energy dispersive spectroscopy for bioanalysis research and industry.
Sensitive to different wavelengths
doi:10.1038/srep45660
CMOS
TES
Conditions:
100x brightness
10x exposure
Exposure 8 min

## Slide 39: Photon Number resolution
Near unity quantum efficiency
Very good photon number resolution
  Number of photons of same wavelength arriving at a given time.
Maximum repetition rate depending on decay time of TES pulses
doi:10.1117/12.852221

## Slide 40: Quantum Metrology with TESs
TES allow direct access to photon statistics from light sources.
Possibility to study entangled and squeezed states.
Analysis and exploration of solid-state-based quantum light sources for applications in quantum information, quantum-enhanced sensing and quantum metrology
doi:10.1103/PhysRevA.82.031802

## Slide 41: TES in quantum computing
Combining TES with a superconducting qubit on a shared silicon substrate.
Idea of detecting correlated disturbances induced by the radiation.
TES as a veto to reject the calculations that could be potentially incorrect due to an environmental disturbance.
Monitoring with a TES has been demonstrated.
doi:10.1103/PhysRevApplied.16.024025

## Slide 42: Towards future TESs
High detection efficiency > 95%, up to 99.8% @ 1550nm
Faster TESs
Better energy resolution
Improve in readout complexity
Lower background level
doi:10.1117/12.852221

## Slide 43: Towards future TESs
ER = 0.062 eV
High detection efficiency > 95%
Faster TESs
Better energy resolution
Improve in readout complexity
Lower background level
doi:10.1117/12.852221

## Slide 44: Thank you!

## Slide 45: References
Transition-edge sensors, in: Cryogenic Particle Detection. http://dx.doi.org/10.1007/10933596_3
A Review of X-ray Microcalorimeters Based on Superconducting Transition Edge Sensors for Astrophysics and Particle Physics. https://doi.org/10.3390/app11093793
A high-resolution gamma-ray spectrometer based on superconducting microcalorimeters. https://doi.org/10.1063/1.4754630
The Athena X-ray Integral Field Unit: a consolidated design for the system requirement review of the preliminary definition phase. https://doi.org/10.1007/s10686-022-09880-7
Optimizing a Transition Edge Sensor detector system for low flux infrared photon measurements at the ALPS II experiment. https://doi.org/10.3204/PUBDB-2024-07357
A TES system for ALPS II - Status and Prospects. https://doi.org/10.22323/1.449.0567
Superconducting transition-edge sensors optimized for high-efficiency photon-number resolving detectors. https://doi.org/10.1117/12.852221
Generation of optical coherent-state superpositions by number-resolved photon subtraction from the squeezed vacuum. https://doi.org/10.1103/PhysRevA.82.031802
Sensor-Assisted Fault Mitigation in Quantum Computation. https://doi.org/10.1103/PhysRevApplied.16.024025
Fast transition-edge sensors suitable for photonic quantum computing. https://doi.org/10.1063/5.0149478
An optical transition-edge sensor with high energy resolution. https://doi.org/10.1088/1361-6668/ac7e7b
Kinetic inductance current sensor for visible to near-infrared wavelength transition-edge sensor readout. https://doi.org/10.1038/s44172-024-00308-y

## Slide 46: Backup

## Slide 47: SQUID multiplexing
Also, microwave KID
And microwave SQUID

## Slide 48: Any Light Particle Search II (ALPS II)
Schematic adapted from Todd Kozlowski
Motivated by astrophysics
Enhancement by optical cavities

## Slide 49: Transition Edge Sensor in ALPS II
Requirements for ALPS II:
Sensitivity to very low rates (1-2 photons a day)
Low energy photon detection (1064nm equivalent to 1.16eV)
Long term stability ( days)
High system detection efficiency [1]
Low background rate: 1 photon (1064nm−like) every 2 days
  Intrinsics [2]
  Extrinsics
  Good energy resolution (for background rejection) [1]
[1] J. A. Rubiera Gimeno, F. Januschek, K.-S. Isleif, A. Lindner, M. Meyer, G. Othman, C. Schwemmbauer, R. Shah, “A TES system for ALPS II - Status and Prospects”, PoS EPS-HEP2023 (2023) 567. https://doi.org/10.22323/1.449.0567
[2] Rikhav Shah, Katharina-Sophie Isleif, Friederike Januschek, Axel Lindner and Matthias Schott, “TES Detector for ALPS II”, Proceedings of The European Physical Society Conference on High Energy Physics, Volume 398, Page 801, (2022); https://doi.org/10.22323/1.398.0801

## Slide 50: Extrinsics background
Additional curling uncertainty
Good agreement with data in region not dependent on curling
Remnant intrinsic background
in simulation
doi:10.3204/PUBDB-2024-07357