## Slide 1: UQDS – a versatile quench detection and measurement system for the HiLumi era
Jens Steckert, Reiner Denz, Tomasz Podzorny, Jelena Spasic David Bailey, Daniel Blasco Serrano, Magnus Christensen, Adam Hollos, Josef Kopal, Surbhi Mundra, Guzman Martin, Andrzej Skoczen, Dragos Gabriel Vancea & MPE-EP Colleagues
Thanks to SM18 & Test bench crews for their support !

## Slide 2: Introduction
Motivation
HiLumi comprises of many different new and complex magnets:  Big variety but small numbers per item (compared to LHC)
Design one generic system with enough resources to perform quench detection and monitoring of all HiLumi circuit elements
MQXFA
MCBXFA
MQSXF
MCBXFB
MCBRDHA
MBRD
SC Link
MQXFB
MBXF
MCBRDVA
Implementation
Base new design on programmable Logic (FPGA) in combination with a number of galvanically isolated front-end channels
Quench detection algorithm defined in Gateware of FPGA
Design is a quench detection AND measurement system

## Slide 3: System overview (UQDSv2)
Insulated font-end channel
Insulated font-end channel
Insulated font-end channel
.
.
.
Processing Element
(FPGA)
Interlocks &
Active
triggers
Up to 16 channels galvanic insulation
Digital platform
Communication interface
Power Supply (monitored) 230V AC
Power Supply (monitored) 230V AC
Passive mid-plane
Voltage taps

## Slide 4: System performance
Real time digital signal processing on FPGA (filters, gain/offset correction)
Quench detection algorithms or other user code in FPGA
Various interlocking options and standards (modular design)
Post Mortem event recording
Absolute time synchronization on microsecond level
Fast logging up to 10kHz via EDAQ
Parameter | Value
Resolution (20-bit ADC) | 105 nV/LSB .. 48 uV/LSB
ADC speed | Up to 909 kS/s
Analogue bandwidth | 120 kHz @ G=1
Active input voltage range | +/-50 mV (G=450) .. +/-22.5 V (G=1) (1.2kV with divider)
Max differential input voltage | 1 kV/1 s
Galvanic insulation | 2.5 kV/1h, 5kV/1min
Total Harmonic distortion
<-110dBfs @ 1kHz
Linearity (calibrated): < 5ppm
(uncalibrated ~0.1%)
Common mode rejection vs frequency
> 100dB
Noise: 2.3ppm standard deviation
Excellent analogue performance both in AC and DC measurements

## Slide 5: Gateware structure – One platform multi-purpose
Hardware abstraction Layer Hardware specific interfaces Static for each hardware
Interfaces to payload code “config block”
Superconducting Link protection
Inner triplet protection
Swiss Knife
Common UQDS services (interfaces, communication & control)
Payload code
“config block”

## Slide 6: Multi-purpose Gateware on multiple Hardware
HAL
Hardware abstraction Layer
Hardware abstraction Layer
Common Logic & communication interface
Config blocks
Hardware abstraction Layer
Gateware compiled from common code base
Common Repository
Application specific parts defined in HDL and Spreadsheet
Automatic VHDL code generation for register map and interfaces
Toolchain heavily scripted (Python & tcl)
Hardware-in-the loop verification techniques
Common Codebase
Spreadsheet (config block specific)
Configuration files & HAL
Toolchain
 Toolchain allows selection of target hardware and config block

## Slide 7: Gateware structure – “config block” examples
Swiss Knife
Q3 protection
IT corrector Prot.

## Slide 8: UQDS ecosystem (produced devices)
Bus-bar and current lead monitor
2 config blocks
120 boards produced Pilot installation in LHC
UQDSv2 16 isolated channels
27 configurations … and counting
Protection Devices Supervision Unit for HiLumi
~120 systems produced and in use (usage: see next slides)
Versatile quench detector board for
LHC CONS
3 config blocks planned
60 boards produced production of 630 boards pending
10 systems produced for IT STRING
3 configurations planned
Image Description Configuration Status

## Slide 9: UQDS ecosystem (in development/prototyping)
UQDS v3 Up to 32 isolated channels,
Faster acquisition speed
Optimized mechanics
Evolutionary upgrade of UQDSv2 Baseline for the HiLumi quench detection system
First prototype in final implementation stage
Upgrade of LHC dipole quench detection
 Evolutionary upgrades and extensions of the ecosystem
Big production of 2500 pieces to be installed at the end of LS3. Variable threshold & radiation tolerant

## Slide 10: EDAQ – timing and communication for UQDS
Ethernet based solution with ~ 1000x the throughput compared to field bus used in LHC (~10Mbit per client)
Timing precision > 1000x better than previous solution using ethernet precision timing protocol  absolute precision better than 1us
Fully integrated in CERN controls infrastructure
Connects to services such as logging and post mortem
Q2 quench in cluster F1

## Slide 11: Applications at CERN
FAIR magnet test stand in B180
18 x UQDSv2
FRESCA facility B163
6 x UQDSv2
C3
C7
C20
SM18 cluster F1 & F2 (HiLumi Q2 & SC Link testing)
30 x UQDSv2
SM18 HiLumi STRING
35 x UQDSv2
LHC tunnel
C22
C23
C19
C3
C24
8 x Busbar Monitor (more in TS#2)
SM18 clusters A, B, C, D
10 x UQDSv2
6 configurations
C6
 Full exploitation of flexible Gateware to follow the rich test program in SM18

## Slide 12: Applications outside CERN
FREIA test facility Uppsala Sweden
2x UQDSv2
For test of HiLumi magnets
IFJ PAN Krakow Poland
2 x UQDSv2
C3
PSI Villingen Switzerland
2x UQDSv2 for SC Magnet Lab
7x UQDSv2 quench detection of SLS2.0 2x super bend magnet
C8
C16
 INFN LASA (Milano) showed interest in UQDS for their test lab
300 uV
50Hz moving average filter
Data: M. Duda PSI

## Slide 13: Summary
Established platform with full system integration in CERN controls services
Inhouse solution with full control about all elements  We can cope with obsolescence etc…
Quite unique feature set
  High performance measurement channels with galvanic insulation of ~5kV peak
  FPGA for real time processing of data & hardware interlocks
Flexible adaptable design which can serve many purposes
Focus now in completion of units for IT STRING
 We’re open for new applications