## Slide 1: Mini-Chamonix Introduction
Where do we stand?
What are the possibilities?
Mike Lamont

## Slide 2: 2011 parameters
Energy [TeV] | 3.5
beta* [m] | 1.5, 10, 1.5, 3.0 m
Emittance [microns] | 2.5 – 3.1 start of fill
Bunch intensity | 1.1 - 1.2e11
Number of bunches | 1380 1318 collisions/IP1&5
Bunch spacing | 50 ns – good choice
Stored energy [MJ] | ~90
Peak luminosity [cm-2s-1] | 1.27e33
Beam-beam tune shift | ~0.015 – 0.017

## Slide 3: Recent bunch intensity/emittance

## Slide 4: Performance
Integrated Luminosity to date (IR1-5/IR8) | 1.3 fb-1/0.44 fb-1
Peak Stable Luminosity Delivered | 1.28 x 1033 cm-2s-1
Maximum number of bunches | 1380
Maximum number of colliding bunches/experiment | 1318
Maximum intensity in collision | 1.64 x 1014 p/beam
Maximum Luminosity Delivered in one day | 63 pb-1
Maximum Luminosity Delivered in 7 days | 242 pb-1

## Slide 5: Luminosity
26 pb-1/day

## Slide 6: Ramp-up
Intermediate energy, TS, scrubbing
MD, technical stop
15 weeks

## Slide 7: Ramp-up: not all plain sailing
UFOs
  In particular MKIs
SEUs
  QPS et al
RF
  Couplers
  RF wave-guide arc detectors
Beam induced heating
  injection kickers, cryogenics, collimators..
Vacuum activity
From 3 to 1380 with a previous maximum of 368 in 15 weeks elapsed (via MD, TS, scrubbing, intermediate energy) has to be regarded as impressive, however…
All to be discussed today

## Slide 8: Increasing intensity – machine protection
Collimation loss of hierarchy at 450 GeV
  Orbit stability. Regular loss maps performed – inefficiency has increased
72 (108/144) bunches from SPS
  Beam quality from injector very important
  144 bunches per injection from SPS > 1 MJ down the lines
High temperature superconducting current lead quenched (7th April)
  Invoked quench of 11 magnets
Injection Kicker Flashover (18th April)
  Not pretty, heavy beam loss

## Slide 9: Wrestling with a mixed bag

## Slide 10: Dumps from Stable beams 1/2

## Slide 11: Dumps 2/2
Clear number of these related to the increase in intensity
Some problems revealed and solved or in the process of being solved

## Slide 12: Summary 1/2
Ramp & squeeze essentially without loss
Excellent performance of Machine Protection related systems
  No quenches with beam above 450 GeV
Optics close to model (and well corrected)
Excellent reproducibility and stability
  Magnetic machine, orbit, collimation…
Aperture as expected
Better than nominal emittance and intensity from injectors
How has the observed performance been possible?

## Slide 13: Summary 2/2
Beam-beam – no problem (head-on/long range)
Excellent single beam lifetime
Healthy luminosity lifetime
Emittance growth
  Minimal through the cycle
  Acceptable in collisions
Excellent machine availability via performance:
  Cryogenics, QPS, BIS, LBDS, injection, power converters, ADT, RF, collimators, controls, instrumentation, vacuum, access, EL, CV…

## Slide 14: Next few months

## Slide 15: Schedule

## Slide 16: What are days for?
Ah, solving that question Brings the priest and the doctor In their long coats Running over the fields.
 | Days
Calendar | 107
Special runs | 3 (say, see Anders..)
Technical stop | 5
TS recovery | 1
Ramp-up | 1+3
Machine development | 5
Floating MD | 2
Physics | ~87
15th July to 29th October inclusive
+25 ns studies to come during MDs (to sort out injection and beam stability issues) and possibly an operational development period to validate scrubbing and future operation

## Slide 17: Maximize peak luminosity
N | Number of particles per bunch
Kb | Number of bunches
f | Revolution frequency
 | Beam size at interaction point
F | Reduction factor due to crossing angle
 | Emittance
 | Normalized emittance
 | Beta function at IP

## Slide 18: Maximize integrated luminosity
Possible turnaround time is ~2.5 hours
Effective turn around time is long:
  Problem resolution, accesses etc…
Message that long fills are good has got through
Exposed to the intersecting failure space of a number of complex systems with huge number of components.
This failure space is inflated by high intensity
Holding is sometimes more effective than raising although “conditioning” and mitigation (UFOS, vacuum, RF, QPS, SEUs) is clear…
1380 * 1.5e11 = 2e14 protons per beam is over 60% nominal intensity… machine protection is, as always, the priority