## Slide 1
Bernd Stechauner1,2, Rebecca Taylor2, Rudolf Frühwirth1,4, Andrea Latina2, Chris Rogers3, Daniel Schulte2, & Jochen Schieck1,4
1University of Technology, Vienna
2CERN, Geneva
3STFC Rutherford Appleton Laboratory, Didcot
4Institute of High Energy Physics (HEHPY), Vienna
RF-Track
Software Mini-Workshop, online, 17.10.2024

## Slide 2: Overview
Focus on RF-Track [1] as a novel simulation tool for final cooling
Overview of implemented particle-matter interaction models
Compare RF-Track with ICOOL[2] and G4BL[3]
To-Dos
Conclusion

## Slide 3: About the RF-Track software
C++ code for accelerator physics simulations.
Utilizes GNU Scientific Library (GSL) and the FFTW library .
Software supports parallel processing for increased computational efficiency in complex particle tracking within field maps.
Users have the option to interface with RF-Track using Python or Octave.
Collective Effects:
  Space charge forces
  Short- and long-range wakefields
  Beam loading phenomena
Single-Particle Effects:
  Incoherent synchrotron radiation
  Magnetic multipole kicks
  Multiple Coulomb scattering
Many RF-Track contributions [4-8]

## Slide 4: Particle-material interactions that are relevant for ionization cooling
Energy loss/ loss fluctuation
Multiple Coulomb scattering
Implementation into the RF-Track code

## Slide 5: Reference materials for benchmarkings studies
Performed benchmarkings:
  Absorbers
    Liquid hydrogen
    Lithium hydride
    Beryllium
  Solenoid
  Single final cooling cell

## Slide 6: Energy loss liquid hydrogen
Energy loss of muons depends on:
Energy of the particle
Material properties
Path length
Compare RF-Track energy loss of liquid hydrogen with ICOOL
Error is less than 0.3%
Results show good agreement.
Error increase in case of particle losses (see lower right plot).
Bethe-Bloch equation

## Slide 7: Energy loss lithium hydride (LiH)
The ICOOL manual presents LiH with a different density and a varying composition of Li6 and Li7 compared to the LiH sample form MICE.
Mixing a specific material with ICOOL might require some additional clarification, as the process isn't immediately intuitive.
Therefore, RF-Track energy loss benchmarking of LiH with G4Bl.
How to mix material in RF-Tack and G4BL – code example:
Special thanks to D. Kaplan
frac_Li = 0.86
frac_H = 0.14
A_Li_Mice, A_H = 6.05, 1.0079 #atomic numbers
Li = RF_Track.Absorber(abs_len, X0_Li, Z=3., A=A_Li_Mice, rho_LiH * frac_Li, I=40.)
H = RF_Track.Absorber(abs_len, X0_H, Z=1., A=A_H , rho_LiH * frac_H, I=21.)
V.add(Li, 0, 0, 0, 'entrance')
V.add(H, 0, 0, 0, 'entrance')
material Li6 Z=3 A=6 density=0.539
material Li7 Z=3 A=7 density=0.534
material LiH Li6,0.814 Li7,0.043 H,0.143 density=0.69
RF-Track
G4Bl

## Slide 8: Energy loss lithium hydride (LiH)
Error slightly higher, than compared to LH
Might come from different mixing techniques

## Slide 9: Semi-Gaussian distribution as scattering model in RF-Track [9,10]
The tail weight factor indicates the probability of a particle to be long ranged scattered
The first term represents the core Gaussian of the distribution
Term 2 shows a non-Gaussian single scattering distribution (tails)
ICOOL and G4Bl use the Moliér algorithm from the Gant4 library.

## Slide 10: First try: ICOOL vs RF-track: Beryllium
1E6 muons for each simulation
Start: 1 GeV mono energetic pencil beam
Absorber length: 1% of radiation length
The shape of the distribution changes minimally with the number of integration steps.
The Moliér model lacks on the convolution property, indicating potential for further improvement.

## Slide 11: ICOOL vs RF-Track: Liquid hydrogen
1E6 muons for each simulation.
Example with 1, 10, 100 and 1000 steps.
Excellent agreement is observed with ICOOL.
Exception: the ICOOL model overestimates the tails slightly .

## Slide 12: Std. scatter angle benchmarks
LiH Examples
Liquid hydrogen Examples
Error are in the range of 5%.
Exception: low energy example, due to high losses.

## Slide 13: Solenoid model
RF-Track uses the current sheet model for solenoids.
The model is based on elliptical integral functions.
These functions come from GSL but require more computational time to evaluate field strength for all particle positions.
Solution: RF-Track creates a meshgrid of the 3D solenoid field and uses an interpolation function to provide field strengths during particle tracking.

## Slide 14: Solenoid field benchmarking
Comparison RT-Track with G4BL.
Sheet number: 200
We find slightly differences in the off-axis and coil regions.
difference
Analysis from R. Taylor

## Slide 15: Solenoid field: particle tracking benchmarking
Analysis from R. Taylor

## Slide 16: Final cooling cell example
Initial emittances taken form [11]
No absorber
With absorber
Slightly higher cooling with RF-Track, which must be investigated.
Computation time
Computation time

## Slide 17: To-do list for RF-Track
RF-Track assumes the energy fluctuation as normal distributed.
It must be Vavilov/Landau distributed.
The Gauss approximation is valid for very thick materials.
Comparison of tracking in cavities.
RF-Track uses TM011 mode; G4BL uses TM010 mode.
TM011 is the better option, since we consider window less cavites in final cooling.

## Slide 18: Summary & outlook
Energy loss model in RF-Track show high agreement with ICOOL and G4BL
A multiple Coulomb scattering model based on a semi-Gaussian mixture model was added in RF-Track and compared with ICOOL.
Results were compared with ICOOL, showing excellent benchmarking results.
This new tool enables an optimized design of ionization cooling channels for a future muon collider.
Next step: Focus on longitudinal beam distributions

## Slide 19
Thank you for your attention

## Slide 20: Reference list
[1] A.Latina,RF-TRACK, https://gitlab.cern.ch/rf-track.
[2] R. Fernow, "COOL: a simulation code for ionization cool- ing of muon beams", Proc. of the 1999 Particle Accelerator Conference, New York, NY, USA, 1999, pp. 3020-3022 vol.5, doi:10.1109/PAC.1999.792132.
[3] T.J. Roberts, "G4beamline simulation program for matter- dominated beamline", IEEE Particle Accelerator Conference (PAC), Albuquerque, NM, USA, 2007, pp. 3468-3470, 2007, doi: 10.1109/PAC.2007.4440461.
[4] S. Benedetti et al., “High gradient linac for proton therapy”
[5] C. Rossi et al., “The deep electron flash therapy facility”
[6] Y. Han et al., “Optimization of the clic positron source using a start-to-end simulation approach involving multiple simulation codes”.
[7] Y. Zhao et al., “Comparison of Different Matching Device Field Profiles for the FCC-ee Positron Source,”
[8] V. Musat et al., “A high-energy and high-intensity inverse Compton scattering source based on compact light technology,”

## Slide 21: Reference list
[9] R. Frühwirth, M. Liendel: Mixture models of multiple scattering: computation and simulation.
[10] R. Frühwirth, M. Regler: On the quantitative modelling of core and tails of multiple scattering by Gaussian mixtures .
[11] B. Palmer: Muon final cooling in 30-50T solenoids.