## Slide 1: Modelling resonant depolarisation for FCC-ee
C. Kiel, J. Keintzel, F. Zimmermann

## Slide 2: Overview
Theory
Model
Results
Summary and outlook

## Slide 3: Motivation
Precise and accurate measurement of beam energy using resonant depolarisation

## Slide 4: Theory
Spin variations follow BMT- equation
Spin reacts to magnetic and electric fields
Spin precession in accelerator (spin tune)
Beam depolarisation by applying an electric field on the beam
Spin
Magnetic field
Electric field
BMT-equation
Field strength
Start of scan
step
Number of turns

## Slide 5: Theory
Goal of the depolarisation: precise measurement of beam energy
Resonant behaviour of the spin when the electric field frequency corresponds to the spin tune
Resonance
Gyromagnetic anomaly of the electron
Lorentz energy factor
Spin tune

## Slide 6: Model
Self-developed simplified python code
Storage ring with only dipoles (only vertical magnetic field)
Vertical initial spin
Spin tune Q=103.257
Depolariser modelled as an oscillating external driver (radial electric field)
Single or multiple particles
Synchrotron oscillations
Energy spread
Goal : finding dependence of depolarisation to the
  Strength of the depolarising field
  Step size of the scan
  Direction of the scan

## Slide 7: Results – strength of the depolarising field
105 turns, = 10-3, =10-6
105 turns, = 10-2, =10-6
Stronger field leads to a stronger depolarisation
1 particle, no synchrotron oscillations

## Slide 8: Scan precision
106 turns, = 10-3, =10-7
Smaller steps lead to stronger depolarisation
1 particle, no synchrotron oscillations
105 turns, = 10-3, =10-6

## Slide 9: Changing scan direction
1 particle, no synchrotron oscillations, 105 turns, = 10-2, =10-6
Depolarisation does not seem to change with scan direction

## Slide 10
Adding synchrotron oscillations
Depolarisation also at synchrotron tune sideband
1 particle, with synchrotron oscillations, 105 turns, = 10-3, =10-6
Qs
Qs

## Slide 11: Resonance for different energies
δ1=0
δ2=10-4
δ3=2x10-4
δ4=3x10-4
105 turns, = 10-2, =10-6
Resonance linked to energy as Q
4 distinct particles, no synchrotron oscillations

## Slide 12: Average spin with energy spread
δ1=0
δ2=10-4
δ3=2x10-4
δ4=3x10-4
δ5 = -10-4
δ6 = -2x10-4
δ7 = -3x10-4
Each particle’s resonance clearly visible
7-particle bunch with different momenta, no synchrotron oscillations

## Slide 13: Considering synchrotron oscillations
δ1=0
δ2=10-4
δ3=2x10-4
δ4=3x10-4
δ5 = -10-4
δ6 = -2x10-4
δ7 = -3x10-4
How can we distinguish resonance from sidebands in experiments?
7-particle bunch with different momenta, synchrotron oscillations

## Slide 14: What does theory say ?
Final polarisation
Initial polarisation
Spin tune
Spin kick
Scan precision
M. Froissart and R. Stora, Nucl. Instrum. Meth. 7, 297 (1960)
M. Bai, Overcoming Intrinsic Spin Resonances by using an RF Dipole, PhD thesis, Indiana U. (1999)
1 particle, no synchrotron oscillations, 4x105 turns, = 10-2, =10-6
Simulation: 0.880
Theory: 0.877

## Slide 15
Simulated results agree well with theoretical predictions

## Slide 16: Accuracy of found depolarisation frequency
Error increases with , very little difference between scan directions
Difference between and simulation for 1 particle, both scan directions
logarithmic scale, = 10-2
Onward scan
Backward scan
1 particle, no synchrotron oscillations, =10-6 , = 10-2
depolarising field tune

## Slide 17: Accuracy of found depolarisation frequency
Absolute error one order of magnitude higher for Gauss energy distribution
spin turns less than with 1 particle
Difference between and the simulation for 100 particles with synchrotron oscillations
both scan directions, logarithmic scale, = 10-2
Onward scan
Backward scan

## Slide 18: Improving precision
Method :
Frequency at intersection of both scan directions
Mean of both frequencies
Ideal model without energy drift
Advantages :
Works even if the spin does not reach 0
Returns the exact value, independently from
Vertical spin component
100 particles and synchrotron oscillations, =2x10-6 = 10-2
Vertical spin component
depolarising field tune
depolarising field tune

## Slide 19: Summary
Successful creation of simplified model to simulate resonant depolarisation in storage rings
Field strength and step size influence depolarisation
Without synchrotron oscillation, energy spread in a particle bunch smooths out the depolarisation curve
With synchrotron oscillation, visible synchrotron side bands
High precision measurements by using both scan directions in a simple model
Include energy drift
Include synchrotron radiation
Develop measurement procedure to distinguish synchrotron sidebands from beam energy
Outlook