## Slide 1: EN-MME contribution to the ET project: the vacuum system
Anité Pérez – EN-MME-MM
2024-12-06

## Slide 2: Outline
Einstein Telescope (ET)
ET Vacuum System
EN-MME contribution
Summary and perspectives

## Slide 3: Einstein Telescope (ET)
Next generation of GW detectors
Underground Infrastructure: 200 – 300 meter
Probably largest UHV system ever built: 120 km!
Triangle
≥ 10 km each arm
Triangular (or L-Shaped) Underground
ET concept
Current detectors observe about one signal per week.
Next generation 100.000 to 1.000.000 binary black holes mergers per year! And many other new sources!

## Slide 4: Einstein Telescope (ET)
2L misaligned of 45°
Two locations presented their candidature (NL & IT)
Saxony (DE) is very present in ET and ETpathfinders
Triangle
≥ 10 km each arm
Triangular (or L-Shaped) Underground
Limburg (NL)
Sardinia (IT)
Next generation of GW detectors
ET concept
15 km

## Slide 5
ET vacuum system
If VIRGO vacuum system costs are scaled to ET dimensions
ET total
budget
Civil engineering & services (54%)
Vacuum system* (33%)
Optics and lasers (7%)
Suspension system (3%)
Cryogenics (3%)
Installation (1%)
*including towers
(~<10% of the vacuum system budget2)
~ 440 M€
(estimated) [3, 4]
Conceptual Design?
Cost estimation?
Objectives:
  To design and test technical solutions that fulfil the ET requirements and cost effective
  To manufacture, assemble and test a pilot sector (in TT4)
  To write the TDR, including cost estimations
MoU in 2022 between CERN, INFN, Nikhef and since 2023 also IFAE
Pilot sector at CERN
Are there cost-effective alternatives (material, design, manufacturing, post-processing treatments) to achieve the needed vacuum performance?

## Slide 6
Objectives:
  To design and test technical solutions that fulfil the ET requirements and cost effective
  To manufacture, assemble and test a pilot sector (in TT4)
  To write the TDR, including cost estimations
ET vacuum system
Baseline based on VIRGO vacuum pipes [5]:
AISI-304L
4-mm-thick
Ø1.2 m x 15-meter-long
Pipes reinforced with stiffeners & air-fired

## Slide 7
Objectives:
  To design and test technical solutions that fulfil the ET requirements and cost effective
  To manufacture, assemble and test a pilot sector (in TT4)
  To write the TDR, including cost estimations
Main requirements in ET:
  Beampipes of Ø1 m x 120 km
  UHV (H2 partial pressure 10-10 mbar)
  Fast production and easy to handle in an underground facility
  Supports capable of holding, aligning and dumping the pipes
  Lifetime 50 years
ET vacuum system
AISI-304L
4-mm-thick
Ø1.2 m x 15-meter-long
Pipes reinforced with stiffeners & air-fired
Baseline based on VIRGO vacuum pipes [5]:

## Slide 8
ET vacuum system
Interdepartmental collaboration
Project leader: Paolo Chiggiato (TE-VSC)
Deputy: Anité Pérez (EN-MME)
Objectives:
  To design and test technical solutions that fulfil the ET requirements and cost effective
  To manufacture, assemble and test a pilot sector (in TT4)
  To write the TDR, including cost estimations
Main requirements in ET:
  Beampipes of Ø1 m x 120 km
  UHV (H2 partial pressure 10-10 mbar)
  Fast production and easy to handle in an underground facility
  Supports capable of holding, aligning and dumping the pipes
  Lifetime 50 years
ET vacuum team @ CERN
Monthly updates on activities:
ETC: Aniello Grado, Nick Van Remortel
ETO: Patrick Werneke, Fernando Ferroni (Giovanni Bisoffi), Andreas Freise, Mario Martinez

## Slide 9
ET vacuum system
Objectives:
  To design and test technical solutions that fulfil the ET requirements and cost effective
  To manufacture, assemble and test a pilot sector (in TT4)
  To write the TDR, including cost estimations
EN-MME activity:
  Design office
  Materials, metrology and NDT
  Mechanical workshop
  Assembly and metal forming
  Technical subcontracting service

## Slide 10
    In ET, the space required for the supporting structure shall be minimized allowing welding and future inspections
    Vacuum chamber position is adjustable within +/- 20 mm in both directions
EN-MME contribution:
Light supports based on standard beams with additional leg
Vacuum chambers suspended by cables (high strength synthetic ropes)
The insulated vacuum chambers lies on the cradle
Conceptual design of dampers
1.7 m
Design and manufacturing drawings for beampipes and supports of pilot sector  Applicable for ET

## Slide 11
EN-MME contribution:
Stresses
Eigenbuckling
Finite element studies to optimize the supports dimensions and their positioning

## Slide 12
EN-MME contribution:
Design of complementary parts, prototypes and supports
Finite element analysis for end caps end supports
Von Mises stresses
Buckling mode
Plastic strain

## Slide 13
Ferritic StSt
Mild steel
Austenitic StSt
Measurement error: ±40%; Detection limit: 50% of background
Courtesy of C. Scarcia
EN-MME contribution:
Select alternative materials with low H2 content/outgassing rate
Vacuum properties
+
Availability and lower cost
+
Formability and weldability
+
Corrosion resistance
Ferritic StSt AISI 441
Low C, iron-chromium alloy
With addition of Ti and Nb
The native H2 content of ferritic grades is comparable to that of vacuum-fired austenitic StSt​

## Slide 14
Mechanical testing
Tensile testing with DIC
Non-destructive testing
110°
180°
Radiography testing
Dye penetrant testing after flexural test
Metallurgical analysis
Optical microscopy on weld’s cross sections
TIG welding
Laser welding
Flexural testing
EN-MME contribution:
Welding testing and qualification for UHV applications

## Slide 15
EN-MME contribution:
Annular corrugation performed at CERN
Two technical solutions:
Define fabrication and welding procedures applicable to the pilot sector and ET beampipes
Corrugated pipes
Thin walls (≤ 2 mm)
Longitudinal welding
Corrugation after welding
Prototypes
Courtesy of C. Garion
Smooth pipes
4 mm thick
Longitudinal welding
Reinforced by stiffeners
Pilot Sector

## Slide 16
EN-MME contribution:
Sleeves testing for pilot sector sections connection
Mock-up manufacturing
and assembly
End caps and pumping modules for pilot sector
Manufacture of prototypes, pilot sector components
Propose and test innovative solutions for pipe’s connection (also applicable for ET)

## Slide 17
EN-MME contribution:
Sub-contracting the manufacturing of main support system, beampipes and complementary structures
Corrugated pipes
Thin walls (≤ 2 mm)
Spiral welding + helicoidal corrugation simultaneously
Pilot Sector
(externalized)
Development needed!
Innovative solution:
Primary solution:
Smooth pipes
4 mm thick
Longitudinal welding
Reinforced by stiffeners
Pilot Sector
(externalized)

## Slide 18
EN-MME contribution:
Redaction of technical specifications for the price enquiries and market survey processes
Close follow-up of the production
Sub-contracting the manufacturing of main support system, beampipes and complementary structures
Corrugated pipes
Thin walls (≤ 2 mm)
Spiral welding + helicoidal corrugation simultaneously
Pilot Sector
(externalized)
Development needed!
Innovative solution:
Primary solution:
Smooth pipes
4 mm thick
Longitudinal welding
Reinforced by stiffeners
Pilot Sector
(externalized)

## Slide 19: Summary and perspectives
Sub-contracting pilot sector structural support and 1st beamline in ferritic StSt
Design, simulations and manufacturing drawings for supports and components
Selection and testing of alternative material (ferritic StSt AISI 441)
Manufacturing parts, welding procedures compatible with UHV
Corrosion studies
2nd beamline
Dust control studies
2025:
Finalize the installation and testing of the pilot sector at CERN + TDR

## Slide 20: Thanks for your attention!

## Slide 21: References
[1] Video | Ripples in Spacetime Pond | LIGO Lab | Caltech
[2] What is an Interferometer? | LIGO Lab | Caltech
[3] ET collaboration, Einstein Telescope preliminary cost book, 2020
[4] ET Science Team, Einstein gravitational wave Telescope conceptual design study, 2011
[5] Ultra high vacuum beam pipe of the Einstein Telescope project: Challenges and perspectives. A. Grado et al. Journal of Vacuum Science & Technology (2023)
[6] Outgassing properties of vacuum materials for particle accelerators. P. Chiggiato
[7] Vacuum for Accelerators: Introduction to Materials and Properties. S. Sgobba
[8] Study of selected mild steels for application in vacuum systems of future gravitational wave detectors. C. Scarcia et al. Journal of Vacuum Science & Technology (2024)

## Slide 22
EN-MME contribution:
Air bake-out 410°C
on finished tubes (15 m long)
5 days cycle in electrical furnace
Production Bottleneck!
Austenitic StSt, specifically AISI 304L, are a standard material for UHV applications in scientific equipment. To reduce H2 outgassing at RT to acceptable levels high-temperature treatments (firing) are needed [6, 7]
The methods applied to reduce the H2 outgassing in current GWD include ex-situ heating at high temperatures in a vacuum or air furnace (vacuum or air firing) and in-situ bakeout at medium temperatures [5]
(used in Virgo [5], LIGO and ET baseline)
Select alternative materials with low H2 content/outgassing rate

## Slide 23
EN-MME contribution:
Select alternative materials with low H2 content/outgassing rate
Austenitic StSt, specifically AISI 304L, are a standard material for UHV applications in scientific equipment. To reduce H2 outgassing at RT to acceptable levels high-temperature treatments (firing) are needed [6, 7]
The methods applied to reduce the H2 outgassing in current GWD include ex-situ heating at high temperatures in a vacuum or air furnace (vacuum or air firing) and in-situ bakeout at medium temperatures [5]
Ferritic - bcc - structures present lower residual H2 and higher diffusivity compared to the close-packed fcc resulting in a faster degassing at lower temperatures (≤ 150°C) [8]

## Slide 24: Broader CERN involvement
Beampipes for Gravitational Wave Telescopes Workshop (CERN, March 2023)
ET Civil Engineering Workshop
(CERN, April 2024)
Vacuum system: MoU in 2022 between CERN, INFN, Nikhef and IFAE  Dedicated activity ongoing and sharing the knowledge with Cosmic Explorer
Civil engineering: MoU in 2023. CERN will provide consultancy and technical support towards the creation of the TDR for the civil engineering and technical infrastructure for 2026

## Slide 25: Broader CERN involvement
Vacuum system: MoU in 2022 between CERN, INFN, Nikhef and IFAE  Dedicated activity ongoing and sharing the knowledge with Cosmic Explorer
Civil engineering: MoU in 2023. CERN will provide consultancy and technical support towards the creation of the TDR for the civil engineering and technical infrastructure for 2026
Document management: Project management required specific tools (i. e. EDMS) and CERN is providing support for a pilot study
Engineering support: Discussions are ongoing for a dedicated support for the design of the technical infrastructure
Other subjects related to occupational health and safety, integration, planning, support for costing, cryogenic infrastructure, survey…
Dimensions comparison

## Slide 26: What’s the Einstein Telescope?
Next generation of GW detectors
≥ 10 km each arm
Triangular (or L-Shaped) Underground
L – 40km and 20 km
L-shaped surface observatory
Current detectors observe about one signal per week.
Next generation 100.000 to 1.000.000 binary black holes mergers per year! And many other new sources!

## Slide 27: Let’s push the Universe exploration!
Einstein Telescope
Current observatories
Courtesy of P. Werneke

## Slide 29
From current detectors to …
LIGO, Hanford, WA
LIGO, Livingston, LA
Virgo, Cascina, Italy

## Slide 30
Courtesy: A. Pasqualetti
Virgo Pipes