## Slide 1: Modelling Activities in TE-MPE-PE: FE Models, Transients in SC Magnets, and Quench Protection
Julien Dular, on behalf of the TE-MPE-PE section members
CERN, Switzerland
6th December 2024

## Slide 2: Contents
Context and STEAM framework
New methods and models
Tools and selected results
Summary and perspectives

## Slide 3: Contents
Context and STEAM framework
New methods and models
Tools and selected results
Summary and perspectives

## Slide 4: Quench of Superconducting Magnets
Quench: Loss of superconductivity leading to a thermal runaway.
  Violent process: high voltage, temperature, thermal and mechanical stress.
  Dissipation of stored magnetic energy in the coolant (rapid boil-off).
Complex phenomenon:
  Multi-physics, -rate, and -scale problem.
  Highly nonlinear process.
  Local phenomenon  need for 3D models or clever 2D reduced order models.
Accurate and robust modelling tools are essential for magnet protection.
Ph. Lebrun, et al., “Report of the task force on the incident of 19th September 2008 at the LHC” . Technical report, CERN (2009), https://cds.cern.ch/record/1168025.
  Stored energy in each main dipole circuit of the LHC:
  ~ 1 GJ = 250 kg of TNT.
Quench in coil due to interturn short

## Slide 5: Modelling Challenges
Intertape coupling currents [G. Vernassa]
Magnets are multi-scale structures.
The macroscopic response depends on currents at small scales, which must be resolved accurately:
  Interfilament coupling in LTS strands.
  Interstrand coupling in LTS cables.
  Current sharing in multilayer HTS tapes.
  Intertape coupling in HTS coils.
Detailed magnet models are too computationally expensive.
Need for efficient and reliable techniques:
  Homogenization, reduced order modelling, parallelization, thin-shell approximations…
Interstrand coupling currents
Interfilament coupling currents
Multilayer HTS tapes [E. Schnaubelt]

## Slide 6: Simulation of Transient Effects in Accelerator superconducting Magnet circuits - STEAM
TRANSIENTS
Energy extraction and quench-back
Quench heater induced quench
Fast current discharges (CLIQ)
Electro-Magneto-Thermal(-Mechanical)
Sensitivity studies
Fault analysis
Short circuit
Electrical arc
Frequency transfer measurement
MAGNET TYPES
Cos-theta, Block-coil, Common coil
Canted Cos-Theta (CCT), Curved CCT
Solenoid, Pancake coils (Insulated, No-, Metallic-)
CONDUCTOR TYPES
Nb-Ti
Nb3Sn
Bi-2212
YBCO
CIRCUIT TYPES
Stand-alone magnets
Nested circuits
Series-connected magnets
… for LHC, HiLumi, and future projects
LEVEL OF DETAIL
Circuit → Magnet → Cable → Wire → Filament
No single tool can do it all. Therefore, we have many tools connected by the framework.
Courtesy of Mariusz Wozniak, Emmanuele Ravaioli

## Slide 7: Contents
Context and STEAM framework
New methods and models
  LTS magnets
  HTS magnets
Tools and selected results
Summary and perspectives

## Slide 8: LTS Conductors – 2D FE Models
Phase 1 – Detailed 2D-based models:
  Transients in superconducting strands and Rutherford cables.
  Coupled Axial and Transverse currents (CATI) method, 2D Finite Element (FE)
Courtesy of Fredrik Magnus, Alexander Glock and Mariusz Wozniak
Geometry from TE-MSC
Rutherford cable model
Multifilamentary strand
Phase 2 – Homogenized model:
  Reduced Order Hysteretic Magnetization (ROHM) model:
    Describes AC loss and magnetization.
    Includes rate-dependent effects.
J. Dular et al. 2024 https://arxiv.org/abs/2409.13653
J. Dular et al. 2024 https://arxiv.org/abs/2411.13347
J. Dular et al. 2024 DOI: 10.1088/1361-6668/ad650d
Next steps:
Transport current effect, HTS Conductors.

## Slide 9: LTS Magnet – 2D FE Model
Courtesy of Erik Schnaubelt, Andrea Vitrano and Mariusz Wozniak
MQXA
TSA
Coupled 2D FE magnetostatic and transient thermal models of LTS multipole magnets:
Automated computation of geometry, mesh, and solution from ROXIE and text-based versioned files.
Thin shell approximations (TSA) to model thermal gradients across insulation layers:
Enables correct modelling of Quench Heaters (computationally prohibitive for classical FE).
E. Schnaubelt et al., SUST 2023, DOI 10.1088/1361-6668/acbeea
Next steps:
Incorporate ROHM method for accurate AC loss modelling.
Implement active quench detection and protection circuits for QH, EE, CLIQ, and ESC.
Validate this model against experimental data.

## Slide 10: No Insulation HTS Coil – 3D FE Model
Courtesy of Erik Schnaubelt, Sina Atalay and Mariusz Wozniak
E. Schnaubelt et al., "Magneto-Thermal Thin Shell Approximation for 3D Finite Element Analysis of No-Insulation Coils," IEEE TAS (2024)
3D magneto-thermal model in FiQuS/GetDP.
Homogenization of the HTS coated conductor (CC):
  Power law with angle dependency for HTS.
  Anisotropic homogenization.
Thin-Shell Approximation (TSA) for the turn-to-turn contact layer (T2TCL): both thermal and magnetic.
HPC and parallelization efforts with benefits for all FiQuS models (parallelization in time, MPI with PETSc).
E. Schnaubelt et al., “Parallel-in-Time Integration of Transient Phenomena in No-Insulation Superconducting Coils Using Parareal”, SCEE’24 proceedings

## Slide 11: No Insulation HTS Coil – 3D+2D FE Model
J4
J3
J2
J1
Jz12
Jz23
Jz34
Modelling of the 40 T Final Cooling Solenoid of the Muon Collider.
Iterative scheme: 3D FE magnetic coupled with 1D+2D FD electric.
Courtesy of Davide Rinaldoni and Bernardo Bordini
Bordini et al. (2024)
US Muon Accelerator Program
1D/2D: Longitudinal, turn-to-turn and screening currents
3D: Computes m.v.p. based on current density
Model in Comsol Multiphysics.
Work in progress with the T-A homogeneous formulation.

## Slide 12: No Insulation HTS Coil – 2D/3D Network Model
Courtesy of Tim Mulder and Leon Teichrob
3D version is under development
NICQS is being used as one of the design tools for a 40 T final cooling solenoid for a muon collider
NICQS: No Insulation Coil Quench Simulator
  Network model (PEEC): finite difference solved with ODE solver.
  Smart homogenization → ideal for solenoids with many turns.
Supports:
Screening currents and eddy currents in coupled cylindrical normal conducting elements.
Axisymmetric events (ramp, heating, protection techniques, quench).
Various quench detection and protection techniques.
Critical current of HTS tape .
Ramp optimization.

## Slide 13: Contents
Context and STEAM framework
New methods and models
Tools and selected results
Summary and perspectives

## Slide 14: Finite element Quench Simulator
Multipole models (2D)
Curved CCT magnet (3D)
No-insulation HTS coil (3D)
CATI method on strands and cables (2D)
HTS and LTS Racetrack coils (3D)
Developed in TE-MPE-PE
In STEAM framework
Coded in Python
Based on Gmsh and GetDP

## Slide 15: Lumped-Element Dynamic Electro-Thermal - LEDET
Courtesy of Emmanuele Ravaioli
Simulate electro-magnetic and thermal transients in superconducting magnets in 2D and 3D geometry using the Finite Difference (FD) method.

## Slide 16: FiQuS – LEDET Co-Simulation
Co-simulation for Canted-Cos-Theta (CCT) magnets:
  FiQuS: 3D FE magneto-thermal model with homogenized conductors, for eddy currents in formers and shell.
    Thin-shell insulations between windings, formers and shell for efficient simulations and simplified meshing.
  LEDET: finite difference for currents, loss, and temperature in windings.
Courtesy of Mariusz Wozniak, Emmanuele Ravaioli and Erik Schnaubelt
Temperature of former
Magnet designs by A. Haziot and the Fusillo team
M. Wozniak et al., "Quench Co-Simulation of Canted Cos-Theta Magnets," IEEE TAS (2023)
More details:
https://doi.org/10.1109/TASC.2023.3338142
https://doi.org/10.1109/TASC.2024.3355358
16

## Slide 17: Dipole Magnets Impedance Model
Courtesy of Marvin Janitschke, Emmanuele Ravaioli and Valentina Reynaud
Transfer Function Measurements (TFM) on all 1232 dipole magnets of the LHC.
Model to reproduce impedances based on FE, analytical models, and circuit equations.
Average error below 5 % up to 10 kHz.
Identification of outlier magnets.
Frequency (Hz)

## Slide 18
Conductor
Magnet
Circuit
Co-operative simulation
Consecutive analysis
Parametric analysis
Dakota
Materials properties
COSIM
STEAM SDK
STEAM SDK
Component library
STEAM SDK
Conductor
Input files
Magnet
Circuit
Analysis
Parametric
Meas. config
Co-sim.
Meas. data
STEAM SDK
PyBBQ
LEDET
LEDET
ProteCCT
SIGMA
FiQuS
PSPICE
BBQ
XYCE
CHALLENGES
Commercial software is not easily available to all users and expensive
Comparison to
measurements
STEAM SDK
Conductor
Magnet
Circuit
Co-operative simulation
Consecutive analysis
Parametric analysis
Comparison to
measurements
Dakota***
STEAM SDK
Materials properties
COSIM
STEAM SDK
STEAM SDK
Component library
STEAM SDK
Conductor
Input files
Magnet
Circuit
Analysis
Parametric
Meas. config
Co-sim.
Meas. data
STEAM SDK
PyBBQ
LEDET
LEDET
ProteCCT
SIGMA*
FiQuS
PSPICE**
BBQ*
XYCE***
Software in green boxes is free to use
*COMSOL license needed. **Commercial circuit solver from Cadence Design Systems. ***Free tools from Sandia Labs.
FiQuS
NICQS
The framework
Courtesy of Mariusz Wozniak, Emmanuele Ravaioli

## Slide 19: Contents
Context and STEAM framework
New methods and models
Tools and selected results
Summary and perspectives

## Slide 20: Summary and Perspectives
Superconducting Conductors and Magnets Modelling.
  For LTS: efforts for development of FE and FD models.
  For HTS: efforts for development in four directions (FiQuS, NICQS, LEDET, and Comsol).
  Homogenization and reduced order modelling are necessary to obtain affordable computing time.
  HPC, parallelization in space/time are a must-have for 3D modelling.
  → Need for novel methods and cutting-edge modelling tools.
Perspectives for collaborations with modelling experts at the University of Liège.
  Research on formulations, homogenization techniques, coupling between machine learning techniques and reduced order modelling approaches.
  Synergies for the use and development of open-source software and modelling tools.
  Co-simulation with mechanical and/or cryogenic models.