## Slide 1: Exercise 34
List the 3 conditions for a sustained fusion and explain why these conditions are satisfied in the sun.
  High temperature of the plasma for the plasma ions to have the speed needed to over the Coulomb barrier
  High plasma density for frequent collisions between ions
  Confinement. The plasma of the reacting nuclei must remain together for a sufficiently long time
  These conditions are satisfied in the sun. Extremely high temperature, a large source of hydrogen as fuel and the gravitational confinement
List 2 fusion cycles that generate energy in the sun
  p-p cylce and CNO cycle
Explain why fusion is not possible a room temperature
  Not high speed of the plasma ions to overcome the Coulomb barrier of the ion repulsions
Explain how the high temperature helps overcome the Coulomb barrier in fusion. Use your knowledge of statistical mechanics.
  The Boltzman factor. The velocity distribution of ions as function of temperature ~ exp(-E/KT)
Explain why fusion has not being used successfully as a source of energy on Earth
What are breakeven and ignition in fusion reactors?
  Breakeven when energy input equals energy output, no loss no gain
  Ignition when fusion is self-sustained

## Slide 2: Exercise 34
Describe the motivation and the objectives of ITER. Explain how ITER plans to achieve the 3 conditions for sustained fusion
  Motivation : to provide electrical energy from man-made self-sustained fusion
  Thru magnetic and laser confinement, laser hearting and D-D and D-T fusions
What are the possible fusion reactions that can be used to generate fusion energy on Earth?
  D-T might be the first to be used due to high Q-value. The T will requirement Li to be produced since we have light source of natural T on Earth.
Explain the different methods of confinement fusion. What is responsible for confinement in the sun?
  Generally 3 methods. Gravitational such as in the sun. For fusion reactors on Earth, use magnetic confinement (toroidal and poloidal fields) and inertial confinement
Are there any disadvantages for fusion reactors? Explain.
  Yes. Large release of neutrons and helium waste
Why would we be interested in fusion reactors when we have already mastered fission reactors? Explain.
  Fusion reactors relatively non-polluting, safe and the oceans supplying the source of fuel, D. Furthermore, fusion can release more energy than fission per kilogram of starting materials
References
Concepts of Modern Physics, 5th edition, Arthur Beiser, 1995, McGraw-Hill, Chapter 12
Introductory Nuclear Physics, Kenneth S. Krane, 1988, John Wiley & Sons, Inc. Chapter 20