## Slide 1: Development and Preliminary Results of a Large-Volume Time Projection Chamber for X-ray Polarimetry
Davide Fiorinaa,b, Elisabetta Baracchinia,b, Giorgio Dhoc, Paolo Soffittad, Samuele Torellia,b, David J. G. Marquesa,b, Enrico Costad, Sergio Fabianid, Fabio Mulerid , Giovanni Mazzitelli c
aGran Sasso Science Institute
bINFN Laboratori Nazionali del Gran Sasso
cINFN Laboratori Nazionali di Frascati
dIAPS - INAF Istituto di Astrofisica e Planetologia Spaziali

## Slide 2: Polarization in Astrophysics
The polarization of a photon refers to the orientation of the oscillating electric field vector perpendicular to its propagation direction.
Polarization of photons has always been an important dimension to study astronomical sources
In around 50 years of Xray astronomy, only one positive detection of X-ray Polarization: the Crab nebula Novick et al. 1972, Weisskopf et al.1976, Weisskopf et al. 1978

## Slide 3: Polarization in Astrophysics
The polarization of a photon refers to the orientation of the oscillating electric field vector perpendicular to its propagation direction.
Polarization of photons has always been an important dimension to study astronomical sources
In around 50 years of Xray astronomy, only one positive detection of X-ray Polarization: the Crab nebula Novick et al. 1972, Weisskopf et al.1976, Weisskopf et al. 1978
Then IXPE arrived equipped with 3x Gas Pixel Detector
10x15x15mm DME 800 mbar
Single GEM – Pad readout
Energy range 2-8 keV
Angular resolution: better than 30 arcsec, field of view larger than 9 arcmin
Energy resolution: better than 25%
Launched 9 Dec 2021  164 papers

## Slide 4: Physics and polarimetry
XIPE: the x-ray imaging polarimetry explorer (unipa.it)
Develop a Detector capable of Measure Polarization through photoelectric effect for energies >10keV

## Slide 5: Detector overview
Gas volume filled with He/CF4 60/40
1atm
CMOS
Hamamatsu ORCA Quest (2)
High-granularity
X+Y+Energy measurement

## Slide 6: Detector overview
Gas volume filled with He/CF4 60/40
1atm
Collimator
Large FoV up to 25°

## Slide 7: Photographing particle tracks
Notes: Some photo

## Slide 8: Detectors Timeline
PMT
Integrated
Z + Energy measurement
Straight track:
Drift
direction
Tilted track:
Drift
direction
pixels 2304 x 2304 pixels - Imaging 36 x 36 cm2 area Effective - pixel granularity 155 x 155 um2
D.Fiorina
The CYGNO experiment, a Gaseous TPC for directional Dark Matter searches

## Slide 9: From Underground to Space
From Nuclear Recoils
Dark Matter on nuclei
He++ recoil
To Electron Recoils
X-rays on atoms

## Slide 10: From Underground to Space
He++ recoil

## Slide 11: Introduction
Measure the Angular Resolution of our detector to electron
  Collimated 90Sr shooting perpendicularly to the GEM surface (and readout plane)
  2D tracking (possibility to have 3D in future) and energy measurement
Measure the performance of a triple-GEM TPC optically readout for polarimetry in the range [10,60] keV
  Infer the expected modulation factor µ  detector response to a fully polarized source
  Deduce the expected figure-of-merit µ√ε  modulation factor weighted for the efficiency. Related to Minimum Detectable Polarization
N=Flux×efficiency
Source Position
The modulation factor is the ‘efficiency’ of detecting fully polarized photons
The MDP is the maximum polarization that we
expect to measure with a probability of 99% when the true polarization is zero

## Slide 12: Conceptual Map
55Fe and 109Cd calibration Runs
(5.9 and 8 keV peaks)
90Sr Runs
Reconstruction
90Sr Geant4 Simulation
Reconstruction
Calibrated Data
Directionality Code
(full containment)
Photon response Geant4 Simualtion
Intrinsic Angular Resolution for fully contained e-
Efficiency of a 10cm side detector to photons (Photoelectric only)
Measured Angular Resolution for fully contained e-
Deconvolution to get the Detector Response
Cos2 convolution
Modulation Factor
Angular Resolution
Figure-of-merit
Test @ INAF
µ√ε

## Slide 13: Reconstruction and Direction
5.9keV photons
e- track
8keV photons
8keV photons
Compton/photoelectric form 22keV/80keV
The directionality algorithm is inspired from IXPE:
Optimized for our energy range
New strategies under evaluation
Tracks reconstructed with the actual reconstruction code used by the CYGNO collaboration
Low energy electrons <10keV dominated by diffusion in the GEM, limited directionality
Source Position
Source Direction
-Journal of Instrumentation 15, T12003
-Measurement Science and Technology 34, 125024
Astroparticle Physics 133, 102628 (2021)

## Slide 14: Measurement Results
Source Position
Calibrated 90Sr Spectrum
Fully contained tracks

## Slide 15: Measurement Results
Source Position
Calibrated 90Sr Spectrum
Fully contained tracks
Frequency
Measured RMS 32.3°
Simulated RMS 23.6°
Deconvolution
RMS of deconvolved RMS is the angular resolution of the detector

## Slide 16: Angular Resolution & Modulation Curve
Using the deconvolved RMS as sigma of a Gaussian, then convolve with a cos2
Distributions are nearly-gaussian

## Slide 17: Angular Resolution & Modulation Curve
Using the deconvolved RMS as sigma of a Gaussian, then convolve with a cos2
Expected modulation curves for a fully polarized photon beam if the measured performance is conserved!
Distributions are nearly-gaussian

## Slide 18: Modulation Factor

## Slide 19: Modulation Factor
A good modulation factor is expected!
In particular for energies above 20 keV >0.8
IXPE modulation factor (not to be compared)

## Slide 20: Figure-of-merit
N=Flux×efficiency
The probability for a photon to interact photoelectrically and be fully contained in the detector

## Slide 21: Figure-of-merit
N=Flux×efficiency
The probability for a photon to interact photoelectrically and be fully contained in the detector
He/CF4 is a very good mixture for Dark Matter searches, but it may not be the perfect one for X-ray imaging!

## Slide 22: Other Gases
More CF4 helps because of larger density, but photoelectric interaction probability scales linearly with density but scales with Z5!!!
While Angular resolution is almost the same (depending on the sCMOS and software), the figure-of-merit can be increased by more than a factor 3-4 in Ar-based mixtures!
He/CF4 60/40 - He/CF4 40/60 - Ar/CF4 60/40 – Ar/CF4 80/20
Other Gases tested!

## Slide 23: Conclusions
We proudly operate a triple-GEM with optical Readout for Dark Matter Search, and we want to apply our detector concept to X-ray polarimetry.
Polarimetry with our concept appears very promising in the range [10,60] keV
From preliminary measurement, we may infer for X-ray energy above 20 keV
(IXPE <0.8 not to compare)
ε : [1E-4, 5E-2] (IXPE [2E-1,1E-2] not to compare)
Future tests:
Hamamatsu ORCA Quest qCMOS
  With 3D implementation
Different gas mixtures, pressures and ratios

## Slide 24: Conclusions
We proudly operate a triple-GEM with optical Readout for Dark Matter Search, and we want to apply our detector concept to X-ray polarimetry.
Polarimetry with our concept appears very promising in the range [10,60] keV
From preliminary measurement, we may infer for X-ray energy above 20 keV
(IXPE <0.8 not to compare)
ε : [1E-4, 5E-2] (IXPE [2E-1,1E-2] not to compare)
Future tests:
Hamamatsu ORCA Quest qCMOS
  With 3D implementation
Different gas mixtures, pressures and ratios
Polarized X-ray Beam test @ INAF TorVergata
  Validate Simulation
  Provide full simulation on an astronomical physics case

## Slide 25: BACKUP

## Slide 26: High-precision 3D TPC with optical readout via PMT + sCMOS
JINST 13 (2018) no.05, P05001

## Slide 27: High-precision 3D TPC with optical readout via PMT + sCMOS
JINST 13 (2018) no.05, P05001
PMT
Integrated
Z + Energy measurement
Straight track:
Drift
direction
Tilted track:
Drift
direction

## Slide 28: High-precision 3D TPC with optical readout via PMT + sCMOS
JINST 13 (2018) no.05, P05001
PMT
Integrated
Z + Energy measurement
Straight track:
Drift
direction
Tilted track:
Drift
direction
sCMOS
High-granularity
X+Y+Energy measurement

## Slide 29: High-precision 3D TPC with optical readout via PMT + sCMOS
JINST 13 (2018) no.05, P05001
PMT
Integrated
Z + Energy measurement
Straight track:
Drift
direction
Tilted track:
Drift
direction
sCMOS
High-granularity
X+Y+Energy measurement

## Slide 30: sCMOS characteristics & He/Ar:CF4 emission spectra
Hammamatsu | # of pixels | Pixel size [um] | Sensor area [cm2] | Dynamic range | Readout noise (enc) | Mix exposure | 
Orca Flash | 2048 x 2048 | 6.5 x 6.5 | 1.33 x 1.33 | 37000:1 | 1.4 (1.6) rms | 33 (10) us | 
Orca Fusion | 2304 x 2304 | 6.5 x 6.5 | 1.498 x 1.498 | 21400:1 | 0.7 (1.4) rms | 280 (17) us | Used for the reasult shown
Orca Quest | 4096 x 2304 | 4.6 x 4.6 | 1.884 x 1.060 | 25900:1 | 0.27 (0.43) rms | 200 (7.2) us | Tested
Orca Quest2 | 4096 x 2304 | 4.6 x 4.6 | 1.884 x 1.060 | 25900:1 | 0.27 (0.43) rms | 200 (7.2) us | Under Procurament
NIM A 504 (2003) 88-92
improving performances
Notes: Optical spectrum and cameras

## Slide 31: detectors and timeline

## Slide 32: detectors and timeline
LIME
- The first large-size prototype
- Currently taking data
CYGNO04
The first detector for physics runs
Currently under design

## Slide 33: Long Imaging ModulE
1 sCMOS + 4 PMT + 3 GEMs 33 x 33 cm2 readout area 50 cm drift length
1.498 x 1.498 cm2 sensor 6.5 x 6.5 um2
pixels 2304 x 2304 pixels
Imaging 36 x 36 cm2 area Effective
pixel granularity 155 x 155 um2
Sensor geometrical acceptance Ω =1.1 x 10-4
Successfully Running since 2022 at the underground laboratory of Gran Sasso, Italy
PMT
Integrated
Z + Energy measurement
Straight track:
Drift
direction
Tilted track:
Drift
direction

## Slide 34: CYGNO04
Common Cathode TPC
2x 3 sCMOS + 8 PMT + 3 GEMs 80 x 50 cm2 readout area 50 cm drift length
0.4m3 Volume
Last generation sCMOS
  Better granularity
  Lower noise
More radiopure materials

## Slide 35: Reconstruction and Direction
5.9keV photons
e- track
8keV photons
8keV photons
Compton/photoelectric form 22keV/80keV
The directionality algorithm is entirely derived from IXPE:
Optimal for short, almost straight track (IXPE energy range)
May fail in case of long zigzaggy tracks
New strategies under evaluation
Tracks reconstructed with the actual reconstruction code used by the CYGNO collaboration
Low energy electrons <10keV dominated by diffusion, limited directionality
From LIME (underground detector) Simulation

## Slide 36: Introduction
Measure the performance of a triple-GEM TPC optically readout for polarimetry in the range [10,50] keV
  Measure the expected modulation factor µ  detector response to a fully polarized source (if 1 is perfect if 0 is non sensible)
  Measure the expected figure-of-merit µ√ε  modulation factor weighted for the efficiency. Related to Minimum Detectable Polarization
Measure the Angular Resolution of our detector to electron
  Source is 90Sr shooting perpendicularly to the GEM surface (and readout plane)
  Ionization tracks are multiplied by a triple-GEM structure, and the scintillation light from the CF4 gas is read by a CMOS camera
    2D tracking (possibility to have 3D in future) and energy measurement
I will elaborate on the measurement with the standard gas mixture He/CF4 60/40 1atm, but other gases have been tested
N=Flux×efficiency

## Slide 37: Conceptual Map
55Fe and 109Cd calibration Runs
(5.9 and 8 keV peaks)
90Sr Runs
Reconstruction
90Sr Geant4 Simulation
Reconstruction
Calibrated Data
Directionality Code
(full containment)
Photon response Geant4 Simualtion
Intrinsic Angular Resolution for fully contained e-
Efficiency of a 10cm side detector to photons (Photoelectric only)
Measured Angular Resolution for fully contained e-
Deconvolution to get the Detector Response
Cos2 convolution
Modulation Factor
Angular Resolution
Figure-of-merit
Test @ INAF

## Slide 38: Measurements
55Fe and 109Cd calibration Runs
(5.9 and 8 keV peaks)
90Sr Runs
Reconstruction
Reconstruction
Test @ INAF
Example of e- track from 90Sr
DBSCAN is used to find clusters of pixels over the threshold
Directional DBSCAN is used to aggregate clusters that came from the same track
Source Position
Source Direction
Calibrated Data
Directionality Code
(full containment)
Measured Angular Resolution for fully contained e-
CYGNUS-RD/reconstruction: Camera and scope analysis tools (github.com)

## Slide 39: Measurements
55Fe and 109Cd calibration Runs
(5.9 and 8 keV peaks)
90Sr Runs
Reconstruction
Reconstruction
Test @ INAF
5.9keV photons
e- track
Calibrated Data
Directionality Code
(full containment)
Measured Angular Resolution for fully contained e-
8keV photons
8keV photons
Compton/photoelectric form 22keV/80keV

## Slide 40: Measurements
55Fe and 109Cd calibration Runs
(5.9 and 8 keV peaks)
90Sr Runs
Reconstruction
Reconstruction
Test @ INAF
Calibrated Data
Directionality Code
(full containment)
Measured Angular Resolution for fully contained e-
The directionality algorithm is entirely derived from IXPE (main developer S.Torelli)
IPmoving circularly where skewness is positive far away from Barycenter
DIRmaximizes RMS of selected points around IP with exponentially scaled intensity
fiorotto8/CygnoAnal (github.com)

## Slide 41: Measurements
55Fe and 109Cd calibration Runs
(5.9 and 8 keV peaks)
90Sr Runs
Reconstruction
Reconstruction
Test @ INAF
Calibrated Data
Directionality Code
(full containment)
Measured Angular Resolution for fully contained e-
Full containment is defined as:
IP region
  'X_ImpactPoint' > 1700 &
  'X_ImpactPoint' < 1800 &
  'Y_ImpactPoint' > 850 &
  'Y_ImpactPoint' < 1450 &
Camera containment:
  'Ymin' >500 &
  'Ymax' <2304-500 &
  “Xmin">500
IP after cut
IP with direction line
Calibrated 90Sr Spectrum
Fully contained tracks
Angular resolution
fiorotto8/Directionality (github.com)

## Slide 42: Intrinsic Angular spread simualtion
90Sr Geant4 Simulation
Intrinsic Angular Resolution for fully contained e-
Deconvolution to get the Detector Response
Angular Resolution
Simulation with a simple geometry:
Cylindrical gas volume h=5cm, r=3.7cm
Field cage rings, 1cm with SS ring 0.1cm radius
90Sr Source with r=1mm tungsten collimator
90Sr decay, electrons tracked only in the gas volume!
  Deposited energy measurement in sensitive volume
Full containment:
Track without hits in 5mm from the border or the circle
But allowed if the hit is in the +/- 30° region of the entering angle
No containment in cylinder height (we are only 2D for now)
z
x
90Sr source
fiorotto8/MANGO_RadioactiveSource: Simulation of Cd-109 Radioactive source in MANGO (github.com)

## Slide 43: Intrinsic Angular spread simualtion
90Sr Geant4 Simulation
Intrinsic Angular Resolution for fully contained e-
Deconvolution to get the Detector Response
Angular Resolution
Fully contained Simulated Tracks!
fiorotto8/Directionality (github.com)

## Slide 44: Detector Resolution
90Sr Geant4 Simulation
Intrinsic Angular Resolution for fully contained e-
Deconvolution to get the Detector Response
Angular Resolution
Richardson-Lucy deconvolution to get the Detector Angular resolution:
Deconvolution and Subtraction in quadrature give very similar results
Errors are calculated by bootstrapping the measured and intrinsic distributions and deconvolving many times
With these bins:
np.linspace(-100, 100, 151)
Deconvolved distribution
Detector Angular resolution

## Slide 45: Modulation factor and figure-of-merit
Photon response Geant4 Simualtion
Efficiency of a 10cm side detector to photons (Photoelectric only)
Cos2 convolution
Modulation Factor
Angular Resolution
Figure-of-merit
Using the deconvolved RMS as sigma of a Gaussian, then convolve with a cos2

## Slide 46: Modulation factor and figure-of-merit
Photon response Geant4 Simualtion
Efficiency of a 10cm side detector to photons (Photoelectric only)
Cos2 convolution
Modulation Factor
Angular Resolution
Figure-of-merit
fiorotto8/Directionality (github.com)

## Slide 47: Modulation factor and figure-of-merit
Photon response Geant4 Simualtion
Efficiency of a 10cm side detector to photons (Photoelectric only)
Cos2 convolution
Modulation Factor
Angular Resolution
Figure-of-merit
Geant4 simulation of a gas cube of 10cm side with 2cm of Al shielding
Hole of 10.6mm to put an eventual MCP plate
Shooting photons [10,70]keV through the hole
Photon is considered detected if:
  The total energy deposited is its primary energy (with 200eV clearance)
  It did only one interaction (photoelectric selection) in the gas
fiorotto8/MANGOspaceG4 (github.com)

## Slide 48: Modulation factor and figure-of-merit
Photon response Geant4 Simualtion
Efficiency of a 10cm side detector to photons (Photoelectric only)
Cos2 convolution
Modulation Factor
Angular Resolution
Figure-of-merit
N=Flux×efficiency
Huge quenching of the good modulation factor is caused by very low efficiency!
This is the best possible condition! We are not considering the reconstruction efficiency and possible background!!

## Slide 49: Other results
He/CF4 at atmospheric pressure is great for DM searches. However, it mayshould be optimized for polarimetry
Argon ensures up to an order of magnitude of efficiency
More CF4 helps because larger density, but photoelectric
Iteraction probability scales linearly with density but scale with Z5!!!

## Slide 50: Modulation Factors and figure-of-merits