## Slide 1: Technical challenges for the new T2K High Angle TPCs 17 October 2024 Stefano Levorato on behalf of the T2K ND280 upgrade group
The 8th International Conference on Micro-Pattern Gaseous Detectors | Oct.14th - Oct.18th 2024 USTC·Hefei, China | S. Levorato

## Slide 2: Outlook
The T2K ND280 experiment
The ND280 upgrade project
  The motivations
  The upgrade
The High Angle Time Projection Chambers (HATPC)
  A short detector description
The Encapsulated Resistive Anode Micromegas (ERAM)
  Construction
  Quality assessment
  Performance
Conclusions

## Slide 3: The T2K experiment and the role of ND280
High intensity, 0.6 – 2.2 GeV 𝜈μ beam produced at J-PARC (Tokai) → 𝜈 or 𝜈̅ mode by changing the horn polarity
Neutrinos detected at the Near Detector (ND280) and at the Far Detector (Super-Kamiokande)
  𝜈e and 𝜈̅e appearance → determine θ13 and δCP
  Precise measurement of 𝜈μ disappearance → θ23 and |Δm232|
Near Detector complex at
280 meters from the target
Several detectors installed to monitor the beam reduce systematic uncertainties in oscillation analyses, and measure 𝜈 and 𝜈̅ cross-sections
ND to measure un-oscillated beam flux and n cross sections

## Slide 4: The ND280 experiment: the upgrade
Reduced angular acceptance 𝜈 events, mostly reconstruct forward going tracks entering the TPCs
Low eﬃciency to reconstruct low momenta protons
New detectors to extend acceptance for tracks at high angles
Detector installed inside
UA1/NOMAD magnet (0.2 T)

## Slide 5: ND280: the upgrade detectors

## Slide 6: ND280: upgrade completed! Top-HATPC installed in the end of April 2024
Top HATPC
SFGD
Bottom HATPC
TOF
TOF

## Slide 7: ND280: upgrade completed! Top-HATPC installed in the end of April 2024
Top HATPC
SFGD
Bottom HATPC
TOF
TOF
Installation of the Detectors of the ND280 upgrade
successfully completed in May 2024!

## Slide 8: The ND280 experiment: High Angle TPC highlights
The HATPC detector
  A short introduction
Encapsulated Resistive Anode Micromegas (ERAMs)
    The realization of the 50 ERAM sensors
    The ERAM characterization
  Detector response, signal
HATPC performance

## Slide 9: The ND280 experiment: HATPC requirements
Momentum resolution sp/p < 9% at 1GeV/c
(neutrino energy)
Energy resolution sdE/dx< 10%
(PID muons and electrons)
Space resolution O(500 mm)
(3D tracking & pattern recognition)
Low material budget walls ~ 3% X0
(matching tracks from neutrino active target)
High Angle TPC
  Atmospheric pressure TPC
    Gas: T2K mixture (Ar-CF4-isoC4H10 = 95-3-2)
    Gas contaminants better than O(10 ppm) level
    Drift length 1m
    Central Cathode @ -27kV
    E field unif. < 10-3 @1cm from walls
    Low material budget, thin walls
    Active volume ~ O(3m3)
  Resistive MicroMegas sensors (ERAMs)
    Overall anode active surface ~ O(3m2)
    Sampling length ~ 80-160 cm
    pads ~ 1x1cm2
    10k+10k channels / TPC @ End Plates (Anodes)

## Slide 10: HATPC, an overview on the main elements
HATPC in two half FCs
Central cathode
Special cathode flanges w/ HV ft
Two End Plates (Al)
8 Readout Modules each
1 2 3 4
5 6 7 8
Two voltage dividers In parallel ~400 5.1MΩ resistors each: Overall R ~ 1GΩ
Produced at CERN EP-DT LAB

## Slide 11: The ND280 experiment: High Angle TPC highlights
The HATPC detector
  A short introduction
Encapsulated Resistive Anode Micromegas (ERAMs)
    The realization of the 50 ERAM sensors
    The ERAM characterization
  Detector response, signal
HATPC performance

## Slide 12: ERAM: MicroMegas with DLC resistive foil
Resistive layer enables charge spreading
→ space resolution below 500mm with larger pads
→ less FEE channels (lower cost)
→ improved resolution at small drift distance
(where transverse diffusion cannot help)
Resistive layer prevents charge build-up and quench sparks
→ enables operation at higher gain
→ no need for spark protection circuits for ASICs
→ compact FEE → max active volume
Resistive layer encapsulated and properly insulated from GND
→ Mesh at ground and Resistive layer at +HV
→ improved field homogeneity → reduced track distortions
→ better shielding from mesh and DLC → potentially better S/N

## Slide 13: ERAM Module breakout
 Very compact Electronics parallel to the detector
8 + 8 ERAMs per HATPC

## Slide 14: Charge spread on low resistivity foil
Charge Spreading 2D telegraph eqn. solution
time scale is driven by RC
Gaussian spread
Final ERAM layout choice for series production:
Considering pads of 11x10 mm2 parameters
400 kΩ/□ DLC resistivity – low resistivity
150 mm thickness glue – Cdlc-pad/gnd ~ O(20pF)
 RC ~ O(100ns/mm2)
Trade-off optimal charge spread VS spark protection
Gain not affected by resistivity
(transparency to induced signals is guaranteed)

## Slide 15: ERAM production ~ 50 detectors
Crucial steps in production
(CERN EP-DT MPGD workshop)
Selecting DLC foil resistivity
Large variations from DLC provider
Value stable after annealing
Gluing steps by Pressing
DLC to PCB
Stiffener to DLC-PCB

## Slide 16: DLC layer: foil selection, QC

## Slide 17: ERAM Series production experience: X-ray scan
X-rays Test Bench at CERN
fundamental to
1) Qualify, characterize and calibrate
all prototypes and series ERAMs
2) Support the development of
detailed ERAM response model
A) Mesh Pulsing: before and after stiffener gluing
Aim: detector geom defects (i.e. pillar detach),
stiffener gluing issues, electronic noise
X-ray scan
Mesh pulsing
B) X-ray scan of finalized detectors with final electronic modules. Remote controlled station for scanning with mm step fine steps
Aim: QC and fine calibration in terms of gain, resolution and RC

## Slide 18: ERAM Series production experience: X-ray scan
Production steps: tough!
(needed long tuning)
Selecting DLC foil resistivity
Large variations from DLC provider
Stable values only after annealing
Gluing steps by Pressing
DLC to PCB
Stiffener to DLC-PCB
RC map of ERAMS on bottom HATPC EP1
ns/mm2
ERAM with DLC-PCB gluing issue
Gain map of ERAM OK
1mm mesh-DLC gap variation => 10% variation in gain
up 20% RC variation
over same ERAM

## Slide 19: ERAM Series production experience: X-ray scan the importance of the (fast) QA
Gain maps of eight ERAMs tested together in a field cage prototype
A map of gain non-uniformity within a pad.
relative shift of the mean amplitude reconstructed in the top, bottom, left or right region of each pad under study w.r.t mean amplitude of the pad
DLC pressing on the PCB during detector assembly resulting in the non-uniformities observed on the 2D gain and energy resolution maps
 The solder mask is removed and replaced by the copper mesh.

## Slide 20: ERAM Series production: a summary table
Energy resolution
RC distribution
Gain distribution @350V

## Slide 21: ERAM Assembly and Operation experience
Low resistivity DLC O(~500kΩ/□) [after annealing] features
Optimal charge spread → uniform response across pad
(combined with C ~ O(20pF/cm2)
Fast Q removal and Effective Protection against sparks
included at moderate rates ~ O(1kHz) tracks crossing pads
Leakage currents at level of few nA in normal conditions
(no beam)
Challenging installation conditions
→ high sensitivity to dust
→ low H2O level (100ppm) before HV on
0.8 ÷ 2 sparks/day
→ Confirmed by the detector operation at T2K

## Slide 22: Noise: stability of the installed detector
Noise in module 0 has been stable between September 23 and June 24
All the Erams are quasi-identical but one, Eram 27, due its higher capacitance
 the excellent uniformity of the electronics and of the mechanical definition of the glue layer driving the detector capacitance

## Slide 23
ERAM detector response – Noise model
Previous conclusions supported by the noise detailed model included in the MC for Simulation of charge deposition in events

## Slide 24: The ND280 experiment: High Angle TPC highlights
The HATPC detector
  A short introduction
Encapsulated Resistive Anode Micromegas (ERAMs)
    The realization of the 50 ERAM sensors
    The ERAM characterization
  Detector response, signal
HATPC performance

## Slide 25: The ND280 experiment: High Angle TPC highlights
How does the signal look ? Point deposition for example
ADC signal : max 4096 counts
Time window of 511 time bins
Time bin (typ.): 40 ns (25 MHz sampling)
Peaking time (typ.) : 412 ns
Leading pad: highest and earliest signal
⇒ current induced on pads from by avalanche, ie ions signal (as electrons’ signal is too fast)
Adjacent pads: lower and later signals
⇒ current induced by potential field adjustments after electrons are collected by on DLC
(current induction by “charge spread on resistive layer”)

## Slide 26: Reconstruction of charge deposition 1/2
Within our electronics shaping time scale
in primary pads, the signal of ions is diluted by the signal of charge spreading
=> Need to combine information of all pads (primary and secondary)
Recovering information about deposited Q is not trivial

## Slide 27: Reconstruction of charge deposition 2/2
Charge on DLC spreads along any direction including track direction
«longitudinal correlation» across primary pads within our electronics shaping time scale
requires a dedicated signal formation model

## Slide 28: ERAM response – Signal formation model
Main ingredients
Avalanche signal
measured
with fast electronics
on bulk micromegas
Electron signal
(too fast for our shaping times)
Ions signal (slow)
FEE Response Function
In the time scale of our shaping time O(100ns)
Charge spread is properly described by
Electrical model of the sensor
2
1
3
4
Note: Of course, gas transport properties
(L, T diffusion) have to be accounted for
Solutions of 2D diffusion eqn.

## Slide 29: ERAM response – Signal formation model
Main ingredients
Avalanche signal
measured
with fast electronics
on bulk micromegas
Electron signal
(too fast for our shaping times)
Ions signal (slow)
FEE Response Function
In the time scale of our shaping time O(100ns)
Charge spread is properly described by
Electrical model of the sensor
2
1
3
4
Note: Of course, gas transport properties
(L, T diffusion) have to be accounted for
Solutions of 2D diffusion eqn.
Daniele D’Ago’s talk on Monday

## Slide 30: The ND280 experiment: High Angle TPC highlights
The HATPC detector
  A short introduction
Encapsulated Resistive Anode Micromegas (ERAMs)
    The realization of the 50 ERAM sensors
    The ERAM characterization
  Detector response, signal
HATPC performance

## Slide 31: ERAM detector response: impact on reconstruction
Use of the model for Reconstructing the charge deposition
Due to square shape of ERAM pads, the classical method (PRF+clustering) works OK
only for tracks with horizontal or vertical direction (wrt pads coordinates)
Better methods use solutions of telegraph equation in order to
compute the pattern templates for charge diffusion on DLC
calculate the overall expected signal waveform per each pad
find the best matching with the recorded waveforms
Its computationally heavy  different approximations are used for different analysis
X-rays analysis – ERAM characterization
Measurement of dE/dx – Particle Identification
Track reconstruction – momentum measurement

## Slide 32: Reconstructing X-rays charge deposition
Qpad(t) = Solution of 2D Teq. for diffusion of initial Q deposited charge (point-like, delta-pulse initial conditions)

## Slide 33: Reconstructing X-rays charge deposition
Current induced on a pad dQpad(t) / dt
to be convoluted with
electronics transfer function R(t)
dQ/dt R(t) = Q(t)  dR(t)/dt
Q(t)  dR(t)/dt is more practical
Simultaneous fit of waveforms of
Leading pad + Neighboring pads
to get the best 5 parameters
WF templates
Results about Gain and RC
WF fit against templates

## Slide 34: Extraction of RC and Gain maps from X-rays
Converted X-ray impact point position is also fitted
accurate maps of Gain and RC
Use of the method for the extraction of ERAM GAIN and RC
Use for detailed studies of charge diffusion and ERAM response at fine PAD position level
Indications are that the lower resistivity
the better the performance (eg space resolution)

## Slide 35: Reconstructing Q along tracks
For the reconstruction of the charge along the tracks two methods
- Waveform Sum (WS) - Crossed Pad (XP)
Compare the performance of the two methods for dE/dx extraction

## Slide 36: Reconstructing Q along tracks: Waveform Sum
OK for almost H & V tracks
Q missing for inclined tracks
Simple method based on
Sum of waveforms(t) (WS)
over pads in a cluster

## Slide 37: Reconstructing Q along tracks: Crossed Pad (XP)
Reconstruct tracks and consider only pads crossed (XP) by the track (primary pads)
Reconstruct original (ion induced) charge (Q) for each XP (given the track parameters there)
by Q = A x (Q/A) – where A is recorded amplitude on XP and rescaling ratio (Q/A) from Look Up tables (LUT)
LUTs build from model: original Q is distributed linearly over the segment for each XP so that solutions of diffusion equations can be used
Model
No clustering => potentially more accurate method because reconstructing full induced charge on primary pads
«dilution of ion signal» on a XP pad, due to charge spread over the pad is correctly taken into account
«longitudinal correlation» among adjacent XP pads, due to charge spread along track direction is accounted for
Fast method though based on model templates (long time is to generate LUTs …)

## Slide 38: Reconstructing Q along tracks: Crossed Pad (XP)
Building the rescaling ratio Q/A ratio 4D LUTs via model

## Slide 39: dE/dx preliminary results: (WS) and (XP) methods
dE/dx (4GeV electrons) – comparison of WF and XP methods on Test Beam data (DESY)

## Slide 40: dE/dx preliminary results: (XP) method
dE/dx via XP method on Test Beam data (CERN PS T10)

## Slide 41: PID preliminary results (XP) vs (WS)
e/m separation @ 1.5 GeV – Test Beam data (CERN PS T10)
Long tracks (~160cm)
Short tracks (~40cm)

## Slide 42: Reconstructing tracks
For the reconstruction of the tracks
Log(Q) methods
Full Waveform fit Method

## Slide 43: Reconstructing tracks, trajectory fitting: an example
LogQ Method based on clustering & Log[Qprimary /Qsecondary]
logQ method to reconstruct position in each cluster
Helix fit performed on those reconstructed positions
Full Waveform fit Method – based on model & no clustering
1) Use all the pads associated to a track (Qmax values) to define a (v,u) local frame
2) Distribute “arbitrary” point charges along v axis separated by Dv (5mm)
the Q per each point is a free parameter
3) Diffusion model to predict the waveform generated by point charges in surrounding pads
4) Move all points along the u axis to minimize the chi-square difference between measured waveforms and templates  extract the coordinates

## Slide 44: Spatial resolution: the importance of the QA
Top HAT was equipped with ERAMs with larger RC variation w.r.t. Bottom
High RC → less charge spreading “flatter curve”
Low RC → more charge spreading “steeper curve”
Non negligible RC variation among the same Endplate of the TPC
Need to tune the log(Q) parametrization  ERAM dependent….
dX: distance from the center of the cluster and the real position

## Slide 45: Spatial resolution after reparameterization
With the new parametrization all modules have similar performances in terms of spatial resolution
s ≈ 0.45 mm
Work in progress, preliminary

## Slide 46: Reconstructing tracks: momentum resolution
ϕ = 45°
ϕ = 5.7°
ϕ = 84.3°
sp/p momentum resolution as a function of track drift distance: simulated 700 MeV/c muons

## Slide 47: Event display, full ND280 detector!

## Slide 48: Conclusions
Two new TPCs have been just installed in ND280 at JPARC
Very stable operations in commissioning and technical runs
Firs Neutrino Data taking just completed, restarting now !
Resistive MM with encapsulated anode ERAM
- First time use of an encapsulated resistive Micromegas in a High Energy running experiment
Low resistivity & optimal charge spread & no sparks effects
Series production allowed several detailed studies
The ERAM technology is complex and delicate to produce as are all the resistive MPGDs. The expertise and excellent partnership with the CERN/PCB workshop enabled a high yield (~80%) of high-quality production
New algorithms for square pads exploiting detailed response model under development
Detector performance, still preliminary but very promising!

## Slide 49: Conclusions
Two new TPCs have been just installed in ND280 at JPARC
Very stable operations in commissioning and technical runs
Firs Neutrino Data taking just completed, restarting now !
Resistive MM with encapsulated anode ERAM
- First time use of an encapsulated resistive Micromegas in in a High Energy running experiment
Low resistivity & optimal charge spread & no sparks effects
Series production allowed several detailed studies
The ERAM technology is complex and delicate to produce as are all the resistive MPGDs. The expertise and excellent partnership with the CERN/PCB workshop enabled a high yield (~80%) of high-quality production
New algorithms for square pads exploiting detailed response model under development
Detector performance, still preliminary but very promising!
Thanks!

## Slide 50: Spare
Just in Case

## Slide 52: Reconstructing tracks: trajectory fitting
LogQ Method based on clustering & Log[Qprimary /Qsecondary]
logQ method to reconstruct position in each cluster
Helix fit performed on those reconstructed positions
Full Waveform fit Method – based on model & no clustering
1) Use all the pads associated to a track (Qmax values) to define a (v,u) local frame
2) Distribute “arbitrary” point charges along v axis separated by Dv (5mm)
the Q per each point is a free parameter
3) Diffusion model to predict the waveform generated by point charges in surrounding pads
4) Move all points along the u axis to minimize the chi-square difference between measured waveforms and templates
RungeKutta method to fit (u0, du/dv, q/p, t0, dv/dt)

## Slide 53: GAIN, RC

## Slide 54: Detailed R measurement (dedicated probe)
R inhomogeneities in the sputtering are clearly visible in the direction perpendicular to the drum rotation axis.
A dedicated probe has been built to perform a fine measurement of the surface resistivity.
Will be soon complemented with the comparison with the data extracted from X-ray analysis

## Slide 56: Conclusions
Two new TPCs have been just installed in ND280 at JPARC
Very stable operations in commissioning and technical runs
Firs Neutrino Data taking just completed, restarting in October 2024
Field cages
High ratio active/passive volume
Highly effective insulation & E field uniformity
Composite material technology exploited at the limit of the technology
Resistive MM with encapsulated anode
Low resistivity & optimal charge spread & no sparks effects
Series production allowed several detailed studies
The ERAM technology is complex and delicate to produce as are all the resistive MPGDs. The expertise and excellent partnership with the CERN/PCB workshop enabled a high yield (~80%) of high-quality production
New algorithms for square pads exploiting detailed response model under development

## Slide 57: HATPC: features, challenges, constrains and solutions
Mechanics and Electric Field uniformity
Min dead space & max active volume in the dipole magnet
Rectangular shape & thinnest walls & field shaping electrodes incorporated into the walls
Electric field uniformity better than 10-3 @1cm from walls
 Mechanical accuracy: inner surfaces planarity & parallelism ~ O(0.2mm/m)
 Shaping Electrode design: Field and Mirror copper strip layers on two sides of a Kapton foil
Low material budget walls
   lightweight & lowest Z & robust (self supporting)
Electrical insulation Constrains
  HV insulation mantle R > 1TOhm and volume resistivity, HV
geometry: several cm paths for charge from -HV strips to GND shielding (cathode flanges)
insulating materials: very high resistivity & dielectric strength

## Slide 58: HATPC: features, challenges, constrains and solutions
Building process: hand lay-up of composite materials on a Mould & polymerization in autoclave at high Pressure
  Autoclave dimensions
     Field Cage comprising two halves (symmetrical flanges at central cathode position)
  Hand layup & large dimensions
     several hours per process step  very long pot life for epoxy resin
  Mechanical accuracy of geometry  resin curing at low T < O(40ºC)
Materials of choice
  lamination materials: Aramid polymers for peels (Twaron) and for honeycomb (Nomex paper)
  epoxy resin limited choice: Resoltech 1054 combined with quality control against contaminants (moisture, …)
  high insulation layers: Kapton
  box skeleton material: high quality laminated G10

## Slide 59: The ND280 experiment: High Angle TPC highlights
Field Cage (FC)
  Assembly and layout
  Production
  Characterization and Quality Assessment
    Mechanical
    Electrical
Encapsulated Resistive Anode Micromegas (ERAMS)
    Production of 50 sensors
    Characterization
  Detector response, signal and impact on reconstruction
Impact on HATPC performance

## Slide 60: Field Cage: walls stack up layout
Wall cross-section
Inner surface
Outer surface
Wall thickness
~ 40 mm
~ 2% radiation length
Alu (shielding)

## Slide 61: Field cage mechanical details

## Slide 62: Field cage mechanical details: charge path to gnd
Flange thickness (5cm) too small for
degrading -30kV to GND over a flat surface
Three deep grooves
for extending the path from HV to GND
for charge moving on surface and with gas
flanges
~ 7cm thick labirinth
~14 cm path lenght
→ voltage drop / path length < 3kV/cm

## Slide 63: The ND280 experiment: High Angle TPC highlights
Field Cage (FC)
  Assembly and layout
  Production
  Characterization and Quality Assessment
    Mechanical
    Electrical
Encapsulated Resistive Anode Micromegas (ERAMS)
    Production of 50 sensors
    Characterization
  Detector response, signal and impact on reconstruction
Impact on HATPC performance

## Slide 64: Field Cage building, assembling and characterization
Production at NEXUS company (Barcelona) ~ 10 weeks
Validation, QC, electrical and mechanical assembly at CERN ~ 4 weeks
Mould building (INFN)
Mold features
1cm thick Alu walls
Anodyzd. Surfaces
Waviness compl.
iso1302 N8
Surfaces ┴ and ║
better than 80mm/m
Mount / unmount
geom. reproducibility
with high precision

## Slide 65: Field Cage building, assembling & characterization at NEXUS Kapton Layer
Production at NEXUS company (Barcelona) ~ 10 weeks
Validation, QC, electrical and mechanical assembly at CERN ~ 4 weeks
Mold preparation
Inner Vacuum bag
Strip Foil positioning
Thick corners w/ Kapton tape
Electrical tests on surfaces
Resin samples electrical Tests
Kapton lamination
Curing at 40C (fast)
Electrical tests on surfaces and resin samples after curing
5 m perimeter x 1m height (drift length)
Strip foil (by CERN) alignment and
lamination of 3 Kapton layers

## Slide 66: Field Cage building, assembling & characterization at NEXUS Kapton Layer and inner Twaron
First Twaron layer lamination
Curing at 40C (fast) in autoclave
Inner Twaron peel lamination
Electrical tests
- Resin sample
- Inner Twaron layer

## Slide 67: Field Cage building, assembling & characterization at NEXUS Kapton Layer + inner Twaron + G10 Skeleton
Gluing G10 structural skeleton and casting resin on flanges for ensuring gas tightness
G10 skeleton gluing
Curing 40C in clean room
Casting low viscosity resin on top flange
sealing flange to laminated layers
Autoclave curing at 40C
Flanges & Bars
by ORVIM company
(TV, Italy)

## Slide 68: Field Cage building, assembling & characterization at NEXUS Kapton Layer + inner Twaron + G10 Skeleton + HC + Ext Twaron
Flipping the box top-bottom
Resin casting on second flange
Curing at 40C in autoclave
Second Twaron peel lamination
Curing at 40C in autoclave
Gluing Nomex Honeycomb
Curing at 40C in oven
Post-curing at 40C in oven (lasting as long as possible)
Outer Twaron peel lamination

## Slide 69: Field Cage machining and final QC at Nexus
Precision machining
of cathode and anode
flanges and surfaces finishing
Back to NEXUS company for
Mould removal
Very fine polishing of flanges
Correction of defects (eg bubbles)
Shipment to CERN
Vallmoll – Spain

## Slide 70: The ND280 experiment: High Angle TPC highlights
Field Cage (FC)
  Assembly and layout
  Production
  Characterization and Quality Assessment
    Mechanical
    Electrical
Encapsulated Resistive Anode Micromegas (ERAMS)
    Production of 50 sensors
    Characterization
  Detector response, signal and impact on reconstruction
Impact on HATPC performance

## Slide 71: Field Cage assembling, characterization at CERN
Vertical assembly of
two Field Cages into HATPC

## Slide 72: Field Cage assembling, characterization at CERN
He leak tested
  sniffer (air + 30mbar of He)
2) Tested against gas density changes
He Over-pressure (+20mbar)
Air Under-pressure (-20mbar)
Gas density corrected
for Volume variation (due to Pin - Pout)
=
Several T,P,RH sensors
Inside FC
=> Overall Leak < 10-3 mbar L / s
Gas leakages qualification

## Slide 73: Field Cage assembling, characterization at CERN
Mechanical qualification
Comparison with FEM models
in fair agreement with
load tests
deformation vs pressure

## Slide 74: Field Cage assembling, characterization at CERN
Mechanical qualification
Comparison with FEM models
in fair agreement with
load tests
deformation vs pressure

## Slide 75: Field Cage assembling, metrology at Nexus
Tolerances and specifications at a level better than 300mm/m for planes parallelism and orthogonality and better than ISO1302-N8 for waviness are respected with few localized acceptable exceptions
Reached limits of composite material technique
Large dimensions and hand lay-up

## Slide 76: Field Cage assembling, metrology at CERN
Measured internal geometry after assembly agrees with nominal CAD with pull better than 300mm with few localized, acceptable exceptions

## Slide 77: Field Cage assembling, ERAM installation
Assembly the 16 ERAMs in Clean room for each TPC
ERAMs: avoid dust

## Slide 78: Field Cage assembling, commissioning with cosmics

## Slide 79: Field Cage assembling, commissioning: gas contamination at CERN
Large amount of water uptake by Kapton: 2% in mass, with respect to dry Kapton, ~ about 70 g  purging time ~ a couple of months
δ water desorption from walls  0.06 g/day water removal / desorption (long)
Water and Oxygen contamination evolution
Different dragging coefficient ?
Under investigation

## Slide 80: Field Cage assembling, commissioning: gas contamination at J-PARC
Gas contamination from Field Cage O2 and H2O
Excellent Performance of the new gas system
Typical operational values

## Slide 81: Field Cage assembling, commissioning: drift velocity measurement
Gas contamination from Field Cage – O2 and H2O included
500 ppm H2O @ CERN Bottom TPC
Perfect agreement
with expectations (Magboltz)
Gas contamination H2O ~ 10 ppm H2O @ J-PARC All TPCs
1.45ms

## Slide 82: Thanks to CERN
We would like to express our gratitude for the continuous and extremely valuable support from CERN
Burkard Schmidt, Roberto Guida, Frederic Merlet and colleagues  Gas system EP-DT/ED-DT-FS
Davide Tommasini, Roland Piccin, Sebastien Clement, Cedric Urscheler  Polymer lab/TE-MSC
Rui de Olivera, Olivier Pizzirusso EP-DT-EF
Eraldo Oliveri, Djunes Janssen EP-DT-DD
Francesco Lanni, Lluis Secundino Miralles Verge Albert DE ROECK, Filippo Resnati  Neutrino Platform
Ahmed Cherif, Jean Philipphe Rigaudt  Metrology/TE-MSC-SMT
Antje BEHRENS, Jean Christophe Gayde  BE-GM-ESA
Mauro Taborelli, Colette Charvet, Marcel Himmerlich  TE-VSC-SCC
Paolo Chiggiato  TE-VSC
Patrick Muffat, Loredana ZENI Toberer, Laurence Planque, Stephanie Krattinger, Elsa Clerc SCE-SSC-LS

## Slide 83: Thanks to CERN
We would like to express our gratitude for the continuous and extremely valuable support from CERN
Burkard Schmidt, Roberto Guida, Frederic Merlet and colleagues  Gas system EP-DT/ED-DT-FS
Davide Tommasini, Roland Piccin, Sebastien Clement, Cedric Urscheler  Polymer lab/TE-MSC
Rui de Olivera, Olivier Pizzirusso EP-DT-EF
Eraldo Oliveri, Djunes Janssen EP-DT-DD
Francesco Lanni, Lluis Secundino Miralles Verge Albert DE ROECK, Filippo Resnati  Neutrino Platform
Ahmed Cherif, Jean Philipphe Rigaudt  Metrology/TE-MSC-SMT
Antje BEHRENS, Jean Christophe Gayde  BE-GM-ESA
Mauro Taborelli, Colette Charvet, Marcel Himmerlich  TE-VSC-SCC
Paolo Chiggiato  TE-VSC
Patrick Muffat, Loredana ZENI Toberer, Laurence Planque, Stephanie Krattinger, Elsa Clerc SCE-SSC-LS
Thanks to INFN support at CERN and the CEA ANTENNA colleagues

## Slide 85
Near Detector impact on Oscillation Analysis

## Slide 86
ND280 limitations

## Slide 87
ND280 Upgrade improvements

## Slide 88
Mantle resistance

## Slide 89
ERAM Production - about 50 detectors
Crucial steps in production (needed tuning)
Selecting DLC foil resistivity
Large variations from DLC provider
Value stable after annealing
Gluing steps by Pressing
DLC to PCB
Stiffener to DLC-PCB
X-rays Test Bench at CERN
was fundamental to
1) Qualify, characterize and calibrate
all prototypes and series ERAMs
2) support the development of
detailed ERAM response model

## Slide 90
Field Cage assembling, characterization at CERN
Gas contamination from Field Cage – other contaminants

## Slide 91
ERAM Series Production experience
Effect of gas density on (gas) GAIN
Effect of humidity on (gas) GAIN
Fine grain scan
GAIN as a function
of Pad position

## Slide 93
Reconstructing tracks dE/dx
dE/dx – comparison of SWF and XP methods on Test Beam data (4GeV electrons, DESY)

## Slide 94
Reconstructing tracks – pattern recognition
Time and charge definition for each hit
Waveform multipeak search in order to differentiate vertices and crossing trajectories
Merging between different ERAMs and End Plates

## Slide 95
Reconstructing tracks – trajectory fitting

## Slide 96
T2K gas properties

## Slide 97: RC MAP DERIVED FROM X-RAY SCANS
ERAM-16
ERAM-15
ERAM-10
ERAM-12
ERAM-01
ERAM-23
ERAM-02
ERAM-07
ERAM-01 R (k) after DLC pressing
ERAM-01 R (k) finished
Seen from Electronics side
RC is derived from the fit of the pad signal waveforms datas (leading and neighbours) with the complete modelization of the detector response
Ref: S. Joshi (Irfu/PhD)
~1/2 RC as expected
~ RC as expected
16/20
RC is quite well correlated to the measured DLC resistivity

## Slide 98: Spare
Just in Case

## Slide 99: GAIN MAPS OF THE 8 ERAMs used on the ½ mockup TPC @ CERN/T10
X-ray gain scans
Seen from electronics side
ERAM-16
ERAM-15
ERAM-10
ERAM-12
ERAM-01
ERAM-23 (New PCB)
ERAM-02
ERAM-07
Ref: S. Joshi (Irfu/PhD)
PCB backside modification
« solved » the observed gain pattern (ERAM S/N < 23)
Comments & to better understand
All ERAMs PCB but 23, >26
~35 m copper mesh
~35 m plain copper
+ ~50 m soldermask
New PCB for ERAM>26
16/20
ERAM-23

## Slide 100
x0,y0 extracted by baricentrum
Fit independent

## Slide 103
Although a-C:H and ta-C belong to the same material family, they are not produced by the same coating process.
a-C:H is achieved by PECVD (Plasma Enhanced Chemical Vapor deposition) in a gaseous environment.
Whereas ta-C is produced by PVD-arc (Physical Vapor deposition arc) from a solid carbon target.
PVD-arc technology enables the production of a ta-C coating with a higher percentage of sp3 hybridization without hydrogen and providing a higher hardness.

## Slide 105
Both experiments individually prefer normal ordering and δCP~-π/2, T2K prefers upper octant, SK prefer lower octant
We performed Bayesian and Frequentist analyses → frequentist analyses shown today
The CP-conserving value of the Jarlskog invariant is excluded with a significance between 1.9 and 2 σ

## Slide 106
R inhomogeneities in the sputtering are clearly visible in the direction perpendicular to the drum rotation axis.

## Slide 107
And this matches the resistivity direct measurement (C is very well constrained by the thickness of insulator)
R inhomogeneities in the sputtering are clearly visible in the direction perpendicular to the drum rotation axis.

## Slide 108: The ND280 experiment: High Angle TPC highlights
Field Cage (FC)
  Assembly and layout
  Production
  Characterization and Quality Assessment
    Mechanical
    Electrical
Encapsulated Resistive Anode Micromegas (ERAMS)
    Production of 50 sensors
    Characterization
  Detector response, signal and impact on reconstruction
Impact on HATPC performance
An outsider: Field Cage 0 ?
Electrical Issues, what we understood…
and learnt

## Slide 109: Insulation issue in full scale FC0 prototype

## Slide 110: Insulation issue in full scale FC0 prototype
Strip to strip V drop disuniformity

## Slide 111: Buried resistive layer: a possible explanation
All observed features could be explained by the combination of two factors:
Presence of a resistive layer buried underneath the Kapton coverlay layer protecting the mirror Mirror strip
Low resistivity of the coverlay Kapton layer

## Slide 112: Buried resistive layer: phenomenology
After applying HV after applying HV (eg -10kV) to the cathode, two phases:
Transient state: in time scale depending on the contaminated layers resistivity (in our case very short O(10s) time scale) the buried resistive layer become ~ equipotential (setting at intermediate potential -5kV) by drawing charge from the strips
2) Steady state: Mirror strips on the Anode, first half convey current to the buried layer, while mirror strips on the Cathode side draw currents from the buried layer
Glue
prepreg.
Resin
impregnated
Twaron layer
Cathode
-10kV
Kapton 50mm
Kapton 25mm
Anode
0V
Center FC
Field
strips
Mirror
strips
Buried resistive
layer
-5 kV
-5 kV

## Slide 113: Buried resistive layer: phenomenology
After applying HV after applying HV (eg -10kV) to the cathode, two phases:
Transient state: in time scale depending on the contaminated layers resistivity (in our case very short O(10s) time scale) the buried resistive layer become ~ equipotential (setting at intermediate potential -5kV) by drawing charge from the strips
2) Steady state: Mirror strips on the Anode, first half convey current to the buried layer, while mirror strips on the Cathode side draw currents from the buried layer
Glue
prepreg.
Resin
impregnated
Twaron layer
Cathode
-10kV
Kapton 50mm
Kapton 25mm
Anode
0V
Center FC
Field
strips
Mirror
strips
Buried resistive
layer

## Slide 114: Buried resistive layer: verification
In fact we verified the following
Coverlay Kapton volume resistivity ~ 1GΩcm much lower than datasheet)
Twaron layer facing the coverlay featured surface resistivity ~ 1G/□
Resin
impregnated
Twaron layer
coverlay
Kapton 25mm
Both features could on turn be explained by the accidental use of antistatic spray (resistive) on the back of the strip foil (ie on the coverlay) after the strip foil was fixed on the Mould, in order to keep the huge foil surface (5m2) clean from dust and other possible contaminants. The spray contaminated both the Kapton coverlay (being very easily adsorbed) and the innermost layer of the Twaron (being mixed with the resin which impregnates the fiber fabric, during the Twaron lamination phase)
We could not exclude alternative sources of contamination affecting the resin and making it resistive (eg presence of water if epoxy not treated in vacuum after mixing)

## Slide 115: Buried resistive layer: electrical model
R
K
V(x)
Glue
prepreg.
Resin
impregnated
Twaron layer
Cathode
-10kV
Kapton 50mm
Kapton 25mm
Anode
0V
Center FC
Field
strips
Mirror
strips
Buried resistive
layer
I1(0)+I3(0)=I1(L) –I3(L)
I2(0)=I3(0) I2(L)=-I3(L)
Symmetry =0
(middle of the cage)
Kirchhoff law
Transmission line model
I1(x)
T
I2(x)
I3(x)
Constraints
]=Ωm, [T]=Ω/□,[R]= Ω

## Slide 116: Buried resistive layer: electrical model results
Glue
prepreg.
Resin
impregnated
Twaron layer
Cathode
-10kV
Kapton 50mm
Kapton 25mm
Anode
0V
Center FC
Field
strips
Mirror
strips
Buried resistive
layer
- 5kV
- 5kV
- 5kV
- 1kV
- 3kV
- 4kV
- 6kV
- 7kV
- 9kV
R
K
V(x)
Kirchhoff law
Transmission line model
I1(x)
T
I2(x)
I3(x)
Constraints
The electric field in the active volume is non uniform
Due to the spurious voltage divider formed in parallel to the regular one

## Slide 117: Buried resistive layer: electrical model results
m
m
uA
uA
Anode
kV
kV

## Slide 118: Buried resistive layer: fit to the data
25mm Kapton
Breakdown observed at values much lower than datasheet

## Slide 119: Buried resistive layer: electrical model results
m
m
uA
uA
Anode
kV
kV
Early Stage
Later Stage

## Slide 120: Final layout, materials and procedures fixed for the series production
Key points to avoid failures
- no resin contamination !!! Note: usually glues and resins are the weakest points
- Interpose between strips and Twaron layers a “thick” layer of insulator featuring
  High resistivity rv > 1015 Ωcm
  Dielectric strength > 150kV/mm
Final layout of the stack: minimal changes to design
new strip foil w/ thicker Kapton coverlay 50mm + 25mm glue
(produced at CERN, gluing in vacuum with press)
3 layers of Kapton: 125mm + 50mm resin each
(to be laminated on the back of strip foil on the mold)
thickness Kapton+Resin ~0.5mm → “vertical R” below 1 strip O(10TΩ) @ 10kV
Materials: Same insulating materials (Kapton + Aramid) and same resin (Resoltech)
Production procedure and enhanced countermeasures and QC
Minimize moisture trapped in wall layers: drying in oven Kapton & Twaron just before use
QC epoxy contamination -> proper control of mixing and de-gassing process (new mixing / degassing tools and QC) and … avoid antistatic spray…
QC electrical resistivity measurements after each early step in the production

## Slide 121: ND280: installations at J-PARC

## Slide 122: N280: commissioning at JPARC with cosmics
Detector commissioning with and without magnetic field
Alignment runs
New software deployment
New T2K gas system commissioning for both vertical and horizontal TPCs

## Slide 123: N280: n technical runs in December 2023 and February 2024 physics run

## Slide 124: The T2K run schedule: beam upgrade
n beam @ J-PARC: dedicated upgrade of the MR facility to reach the 1.3 MW beam power
Steady improvements to reach 1.3 MW by 2027 with an increase T2K statistics ~ a factor of 3 by 2027
December 2023 → Beam power increased from 500 to 760 kW stable mode
800 kW reached in 2024 for the first run with the fully upgraded ND280
Expect to select 20k 𝜈μ CC0pi interactions in the super-FGD for 0.2e21 POT (1 month)