## Slide 1: High Energy Accelerators: recent progress and future directions
EPS-HEP Conference,
ECFA-EPS session,
Grenoble, France
SATURDAY 23rd July 2011
Steve Myers with help (slides) from
O. Bruning, R. Calaga, J-P. Delahaye, I. Efthmiopoulos, R. Garoby, M. Klein, R. Palmer, T.Roser, L. Rossi, S. Stapnes, V. Schiltsev, D. Schulte, M. Zisman,

## Slide 2: High Energy Frontier (Colliders)
Recent Progress
    Tevatron
    RHIC
    LHC
Future Directions
    Future Ion Colliders
    HL-LHC
    ILC/CLIC
    electron-hadron colliders
    HE-LHC
    Neutrinos (Intensity Frontier)
    Muon collider
Operating
Approved, funded?
Not yet approved
11 topics in 25 minutes!!
About 1 to 2 billion $ per minute!!

## Slide 3: TeVatron

## Slide 4: Tevatron

## Slide 7
Collider Run 2; Weekly/Total Integrated Luminosity

## Slide 9: Summary

## Slide 10: RHIC

## Slide 11: RHIC – a High Luminosity (Polarized) Hadron Collider
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
6:00 o’clock
PHENIX
8:00 o’clock
10:00 o’clock
Polarized Jet Target
12:00 o’clock
4:00 o’clock
2:00 o’clock
Operated modes (beam energies):
Au–Au 3.8/4.6/5.8/10/14/32/65/100 GeV/n
d–Au* 100 GeV/n
Cu–Cu 11/31/100 GeV/n
p–p 11/31/100/205/250 GeV
Planned or possible future modes:
Au – Au 2.5 GeV/n (~ SPS cm energy)
U – U 100 GeV/n
p – Au* 100 GeV/n
Cu – Au* 100 GeV/n (*asymmetric rigidity)
Achieved average store luminosities:
Au–Au (100 GeV/n) 301026 cm-2 s -1
p–p (250 GeV) (<P> = 46%) 901030 cm-2 s -1
Goal with additional luminosity upgrades:
Au–Au (100 GeV/n) 401026 cm-2 s -1
p–p (250 GeV) (<P> = 70%) 3001030 cm-2 s -1
EBIS

## Slide 12: Delivered Integrated Luminosity and Polarization
Nucleon-pair luminosity: luminosity calculated with nucleons of nuclei treated independently; allows comparison of luminosities of different species; appropriate quantity for comparing runs with different species.
Heavy ion runs
Integrated luminosity L [pb-1]
Integrated nucleon-pair luminosity LNN [pb-1]
Polarized proton runs
Notes: updated

## Slide 13: RHIC Luminosity Upgrades Under Way
3-D high-energy bunched-beam stochastic cooling (three planes in each ring) to overcome beam blow-up from intra-beam scattering
56 MHz SRF quarter wave 2 MV storage cavity to reduce vertex length
Head-on beam-beam compensation: Electron beam lenses to partially compensate head-on p-p interactions
horizontal kicker (open)

## Slide 14: LHC

## Slide 15: Peak Luminosity (22/7)

## Slide 16: Daily Integrated Luminosity (22/7)
Average 26pb-1 per physics day

## Slide 17: Weekly Integrated Luminosity (22/7)

## Slide 18: Best Fill as of 22/7

## Slide 19: Integrated Luminosity (22/7)

## Slide 20: Expected integrated luminosity for LHCb in 2011
Luminosity of LHCb levelled continuously
GPD luminosity falls-off exponentially
LHCb design luminosity
Introduced luminosity leveling for LHCb  can run at optimal μ and Lmax
 Since end of May running at constant L ~ 3∙1032 cm-2s-1 with μ ~ 1.5

## Slide 21: LHC precision front
VdM scan
IP1 H
IP1 V
absolute luminosity normalization
low, well understood backgrounds
precision optics for ATLAS-ALFA and TOTEM
precise measurement of the luminous region +
beam intensity --> absolute luminosity and
cross section calibration
currently ~ 5 % level, already better than Tevatron

## Slide 22: Evolution of Peak Performances to date

## Slide 23: Records (up to 22nd July 2011)

## Slide 24: Future Ion Colliders

## Slide 28: HL-LHC

## Slide 29: HL-LHC Performance Goals
Integrated luminosity: 200 fb-1 to 300 fb-1 per year
(assume 250 fb-1 per year in the following)
Leveled peak luminosity: L = 5 1034 cm-2 sec-1
Total integrated luminosity: ca. 3000 fb-1
Virtual peak luminosity: L = 10 1034 cm-2 sec-1

## Slide 30: Performance optimization for the LHC
Luminosity (round beams):
1) maximize bunch brightness [Nbunch/en]
beam-beam limit and injector complex performance
2) minimize beam size [b*] (constant beam power)
3) maximize number of bunches (beam power limit)
4) compensate for ‘R’
30
Event pileup & e-cloud

## Slide 31: LHC Challenges: R
geometric luminosity
reduction factor:
large crossing angle:
 reduction of long range beam-beam interactions
 reduction of head-on beam-beam parameter
 reduction of the mechanical aperture
 synchro-betatron resonances
 reduction of instantaneous luminosity
 inefficient use of beam current
 option for L leveling!
effective cross section
Piwinski angle
qc

## Slide 32: HL-LHC Performance Goals
Preferred leveling mechanism: Crab Cavities
Reservations: technology & field quality
 Supplementary tools for leveling:
# crossing angle and long-range and
beam-beam wire compensators
# transverse offsets at IP
# dynamic b* squeeze
Operation at performance limit
choose parameters that allow higher than design performance
leveling mechanisms for controlling performance during run

## Slide 33
2022
LS3
Installation of the HL-LHC hardware
Not yet approved!

## Slide 34: HL-LHC Performance Estimates
34
Parameter | nominal | 25ns | 50ns
N | 1.15E+11 | 2.0E+11 | 3.3E+11
nb | 2808 | 2808 | 1404
beam current [A] | 0.58 | 1.02 | 0.84
x-ing angle [mrad] | 300 | 475 | 580
beam separation [s] | 10 | 10 | 10
b* [m] | 0.55 | 0.15 | 0.15
en [mm] | 3.75 | 2.5 | 3.75
eL [eVs] | 2.51 | 2.5 | 2.5
energy spread | 1.00E-04 | 1.00E-04 | 1.00E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02
IBS horizontal [h] | 80 -> 106 | 25 | 37
IBS longitudinal [h] | 61 -> 60 | 21 | 21
Piwinski parameter | 0.68 | 2.5 | 2.5
geom. reduction | 0.83 | 0.37 | 0.37
beam-beam / IP | 3.10E-03 | 3.9E-03 | 3.9E-03
Peak Luminosity | 1 1034 | 7.4 1034 | 6.8 1034
minimum b*
(Leveled to 5 1034 cm-2 s-1)
nominal bunch length and minimum b*: Chamonix’11 &
‘HL-LHC Kickoff’
Events / crossing | 19 | 141 | 257 | 95 | 190
OK for HL goals, if
CRAB cavities are a viable option
5.6 1014 and 4.6 1014
p/beam
Notes: 50ns beam option provides HL-LHC performance levels at ultimate total beam currents; only the ‘large beta*’ option reaches beam-beam limit; IBS growth rates are a concern!; low beta option has 50% higher performance potential

## Slide 35: ILC/CLIC

## Slide 36
Multi-TeV Linear Colliders challenges
Luminosity
Beam acceleration: MW of beam power with high gradient and high efficiency
Generation of ultra-low emittances: micron rad-m in H, nano rad-m in V
Preservation of low emittances in strong wake field environment
Alignment (micron range)
Stability (nano-meter range)
Small beam sizes at Interaction Point: Focusing to nm beam sizes
Stability to sub nano-meter
Energy reach
e+
e-
source
damping ring
main linac
beam delivery
Accelerating structures: large accelerating fields with low breakdown rate
RF power source: high peak power with high efficiency

## Slide 38: ILC/CLIC Parameters
4.1%
5.0%

## Slide 39: ILC

## Slide 40: Proposed Design changes for TDR
RDR
SB2009
Single Tunnel for main linac
Move positron source to end of linac ***
Reduce number of bunches factor of two (lower power) **
Reduce size of damping rings (3.2km)
Integrate central region
Single stage bunch compressor ????

## Slide 42: The ILC SCRF Cavity
Achieve high gradient (35MV/m); develop multiple
vendors; make cost effective, etc
Focus is on high gradient; production yields; cryogenic
losses; radiation; system performance

## Slide 43: Global Plan for SCRF R&D
Year | 07 | 2008 |  | 2009 |  | 2010 |  | 2011 | 2012
Phase | TDP-1 |  |  |  |  |  | TDP-2 |  | 
Cavity Gradient in v. test to reach 35 MV/m |  Yield 50% |  |  |  |  |  |  Yield 90% |  | 
Cavity-string to reach 31.5 MV/m, with one-cryomodule |  | Global effort for string assembly and test (DESY, FNAL, INFN, KEK) |  |  |  |  |  |  | 
System Test with beam acceleration |  |  | FLASH (DESY) , NML (FNAL) STF2 (KEK, test start in 2013) |  |  |  |  |  | 
Preparation for Industrialization |  |  |  |  | Production Technology R&D |  |  |  | 
Communication with industry: | 2009: 1st step: Visit Venders (2009) 2010: 2nd step: Organize Workshop (2010) 2011: 3rd step: Send specification & receive response |  |  |  |  |  |  |  | 

## Slide 44: Global ILC Cavity Gradient Yield Updated at ALCPG2011
Plot courtesy
Camille Ginsburg of FNAL
TDP-2 Goal
TDP-1 Goal
Achieved

## Slide 45: Cryomodule Development & Test
DESY: PXFEL-1
  <32 MV/m> in CM operation as ACC7, FLASH (~30MV/m)
FNAL: CM-1
  In progress
KEK: S1-Global
  <26 MV/m> in CM operation

## Slide 46: CLIC

## Slide 47: The CLIC Layout

## Slide 48: Feasibility studies and the CDR
Feasibility issues:
Drive beam generation
Beam driven RF power generation
Accelerating Structures
Two Beam Acceleration
Ultra low emittances and beam sizes
Alignment
Vertical stabilization
Operation and Machine Protection System
CDRs:
Vol 1: The CLIC accelerator and site facilities (H.Schmickler)
  CLIC concept with exploration over multi-TeV energy range up to 3 TeV
  Feasibility study of CLIC parameters optimized at 3 TeV (most demanding)
  Consider also 500 GeV, and intermediate energy ranges
Vol 2: The CLIC physics and detectors (L.Linssen)
Vol 3: CLIC study summary (S.Stapnes)
  Summary and input to the European Strategy process, including possible implementation stages for a CLIC machine as well as costing and cost-drives
  Proposing objectives and work plan of post CDR phase (2012-16)
Timescales:
  By end 2011: Vol 1 and 2 completed
  Spring/mid 2012: Vol 3 ready for the European Strategy Open Meeting
Notes: Picture of CTF3 because it remains a key testing ground for the two beam concept
For information: Two options for the costing, 500 GeV and 1000 GeV (to be in line with ILC), or 500 GeV and discuss cost-drivers for the next stages. The value of 500 GeV is chosen to provide comparison to ILC

## Slide 49: CLIC energy scans (for a single stage)
Requirement from physics : vary the c.m. energy for a given CLIC machine. Main options :
Early extraction lines : expensive, large hardware modifications needed
Reduce gradient : disadvantage: need to scale down bunch charge linearly with gradient for stability, leading to a significant luminosity loss (green)
CLIC drive beam scheme: gradient can be reduced while increasing pulse length. A large fraction of the luminosity loss is recovered (black). Modifications to drive beam generation are minimal.
Lower gradient can be achieved by switching of phase of incoming drive beam bunches :
Drive beam energy after extraction

## Slide 50: CLIC energy staging
3 TeV Stage
Linac 1
Linac 2
Injector
Complex
I.P.
3 km
20.8 km
20.8 km
3 km
48.2 km
Linac 1
Linac 2
Injector
Complex
I.P.
7.0 km
7.0 km
1 TeV Stage
0.5 TeV Stage
Linac 1
Linac 2
Injector
Complex
I.P.
4 km
~14 km
4 km
~20 km
CLIC two-beam scheme with
energy staging to provide the optimal machine for large energy range
Lower energy machine can run most of the time during the construction of the next stage.
Physics results will determine the energies of the stages.
Optimization need to take into many account many others parameters: performance and luminosities (inst. and integr.) at various energies, costs, construction and commissioning times, manufacturing/re-use/move of components, etc
The drive beam can deal with various stages of the machine

## Slide 52: CLIC Tentative Schedule
Final CLIC CDR and
proposal next phase
@ European Strategy
European Strategy
for Particle Physics
@ CERN Council
Project Implementation Plan (PIP) and
proposal for next phase

## Slide 54: Electron Hadron Colliders eRHIC, LHeC

## Slide 55: eRHIC: 5 – 30 GeV pol. e- on 100 GeV/n Au or 250 GeV pol. protons High-Resolution, Ultra-Fast Imaging of Gluon-Dominated Matter
High-intensity energy recovery linacs (ERL) and six recirculation passes to accelerate and decelerate the electron beam
Single pass allows for large collision disruption of electron bunch and high luminosity
Major eRHIC R&D items:
  High current (50 mA) polarized electron gun
  Multi-pass high average current ERLs
  Small gap magnets and vacuum chambers
  Coherent electron cooling
eSTAR
ePHENIX
Coherent e-cooler
New detector
0.6 GeV
27.55 GeV
22.65 GeV
17.75 GeV
12.85 GeV
3.05 GeV
7.95 GeV
2.45 GeV Energy Recovery Linac
2.45 GeV Energy Recovery Linac
100 m
25.1 GeV
20.2 GeV
15.3 GeV
10.4 GeV
30.0 GeV
5.50 GeV
Beam
dump
Polarized
e-gun
0.6 GeV
L > 1034 cm-2 s-1

## Slide 56: Coherent electron cooling
Idea proposed by Y. Derbenev in 1980, novel scheme with full evaluation developed by V. Litvinenko
Fast cooling of high energy hadron beams
Made possible by high brightness electron beams and FEL technology
~ 20 minutes cooling time for 250 GeV protons  reduced proton emittance gives high eRHIC luminosity at much reduced electron current
Proof-of-principle demonstration planned with 40 GeV/n Au beam in RHIC.
Amplifier: Free Electron Laser (FEL) with gain of 100 -1000 amplifies density variations of electron beam, energy dependent delay of hadron beam
Pick-up: electrostatic imprint of hadron charge distribution onto co-moving electron beam
Kicker: electron beam corrects energy error of co-moving hadron beam through electrostatic interaction
Modulator
Kicker
Dispersion section
Electrons
Hadrons
High gain FEL
Eh
E < Eh
E > Eh

## Slide 57: EIC/eRHIC Realization Imagined
Activity Name | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
12 Gev Upgrade |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FRIB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EIC Physics Case |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NSAC LRP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CD0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Machine Design/R&D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CD1/D’nselect |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CD2/CD3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Potential Electron-Ion Collider Timeline Shown by Hugh Montgomery at INT Workshop, Sept. 2010
Notes: 57

## Slide 58: LHeC options: RR and LR
RR LHeC:
new ring in
LHC tunnel,
with bypasses
around
experiments
RR LHeC
e-/e+ injector
10 GeV,
10 min. filling time
LR LHeC:
recirculating
linac with
energy
recovery,
or straight
linac
Frank Zimmermann, UPHUK4 Bodrum 2010

## Slide 59: Design Parameters
electron beam | RR | LR | LR*
e- energy at IP[GeV] | 60 | 60 | 140
luminosity [1032 cm-2s-1] | 17 | 10 | 0.44
polarization [%] | 40 | 90 | 90
bunch population [109] | 26 | 2.0 | 1.6
e- bunch length [mm] | 10 | 0.3 | 0.3
bunch interval [ns] | 25 | 50 | 50
transv. emit. gex,y [mm] | 0.58, 0.29 | 0.05 | 0.1
rms IP beam size sx,y [mm] | 30, 16 | 7 | 7
e- IP beta funct. b*x,y [m] | 0.18, 0.10 | 0.12 | 0.14
full crossing angle [mrad] | 0.93 | 0 | 0
geometric reduction Hhg | 0.77 | 0.91 | 0.94
repetition rate [Hz] | N/A | N/A | 10
beam pulse length [ms] | N/A | N/A | 5
ER efficiency | N/A | 94% | N/A
average current [mA] | 131 | 6.6 | 5.4
tot. wall plug power[MW] | 100 | 100 | 100
proton beam | RR | LR
bunch pop. [1011] | 1.7 | 1.7
tr.emit.gex,y [mm] | 3.75 | 3.75
spot size sx,y [mm] | 30, 16 | 7
b*x,y [m] | 1.8,0.5 | 0.1
bunch spacing [ns] | 25 | 25
RR= Ring – Ring
LR =Linac –Ring
Ring uses 1o as baseline : L/2
Linac: clearing gap: L*2/3
“ultimate p beam”
1.7 probably conservative
Design also for deuterons
(new) and lead (exists)
*) pulsed, but high energy ERL not impossible
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble

## Slide 60
LS3 --- HL LHC
LHeC Tentative Time Schedule
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble

## Slide 62: Main accelerator challenges

## Slide 63: HE-LHC

## Slide 64: HE-LHC – LHC modifications
2-GeV Booster
Linac4
SPS+,
1.3 TeV, 2030-33
HE-LHC
2030-33

## Slide 65: Preliminary HE-LHC - parameters
Very Long Term Objectives: Higher Energy LHC
Very preliminary with large error bars

## Slide 66: HE-LHC – main issues and R&D
high-field 20-T dipole magnets based on Nb3Sn, Nb3Al, and HTS
high-gradient quadrupole magnets for arc and IR
fast cycling SC magnets for 1-TeV injector
emittance control in regime of strong SR damping and IBS
cryogenic handling of SR heat load (first analysis; looks manageable)
dynamic vacuum

## Slide 67
CERN working group since April 2010
EuCARD AccNet workshop HE-LHC’10 ,
14-16 October 2010, Proc. CERN-2011-003
key topics
beam energy 16.5 TeV; 20-T magnets
cryogenics: synchrotron-radiation heat
radiation damping & emittance control
vacuum system: synchrotron radiation
new injector: energy > 1 TeV
parameters
High Energy-LHC (HE-LHC)
 | LHC | HE-LHC
beam energy [TeV] | 7 | 16.5
dipole field [T] | 8.33 | 20
dipole coil aperture [mm] | 56 | 40
#bunches | 2808 | 1404
IP beta function [m] | 0.55 | 1 (x), 0.43 (y)
number of IPs | 3 | 2
beam current [A] | 0.584 | 0.328
SR power per ring [kW] | 3.6 | 65.7
arc SR heat load dW/ds [W/m/ap] | 0.21 | 2.8
peak luminosity [1034 cm-2s-1] | 1.0 | 2.0
events per crossing | 19 | 76
E. Todesco
hybrid magnet

## Slide 68: Neutrinos

## Slide 69: ν-Accelerators : Future possibilities
Long, Very-long baselines
Technical challenges for accelerators:
  high-power proton drivers, targets, collection systems
R&D Studies with strong EU participation and International Collaboration
  EUROnu[Super Beam, β-beam, Neutrino Factory], LAGUNA[detectors] – LAGUNA_LBNO
ν-source | Beam | [km] | Proton beam |  | Accelerators
 |  |  | [GeV] | [kW] | 
CERN | CNGS | 730 | 400 | 510 | SPS
 | Pyhasalmi | 2’300 | 400 30-50 | 510 - 750 2’000 | SPS + upgrade LP-SPL + HPPS
 | Frejus | 130 | 8 | 4’000 | HP-SPL + accumulator
FNAL | MINOS | 735 | 120 | 300 - 700 | Main Injector + upgrade
 | NOνA | 830 |  |  | 
 | LBNE | 1’600 | 120 | 700 - 2’300 | MI + upgrade, Project-X
J-PARC | T2K | 250 | 30 | 70 – 1’600 | Main Ring + upgrade
 | Okinoshima | 658 | 30 | 3’800 | Main Ring + upgrade

## Slide 70: ν-Accelerators : Future possibilities
From the (very)long ⟶(very)short baselines to search for anomalous ν oscillations – sterile ν’s ??
FNAL: Booster beam (8 GeV) to MiniBooNE and upgrades, MicroBooNE
CERN : PS Neutrino Beam
Beam line originally operated in early 80’s for PS169, PS181, PS180(BEBC)
Near (150t) + Far(600t) detector with ICARUS LArgon technology
Expect : 6.13 1019 ÷ 2.1 1020 pot/y @ 20 GeV, depending on beam sharing

## Slide 71: ν-Accelerators : Future possibilities
Intensity upgrades – Long(Very-Long)-baseline beams
Facilities for precision measurements
Super-beam (Frejus)
Neutrino Factory
Present generation
Beta-beams
NOνA – LBNE
T2K (1.6MW)
CN2PY (Pyhasalmi-FI)
θ13 measurement
θ13 measurement, CP violation, mass hierarchy
R&D Studies with strong EU participation and International Collaboration
  EUROnu
  LAGUNA – LAGUNA_LBNO
  International Design Study for a Neutrino Factory (IDS-NF)
300-400 kW
700kW – 1(2) MW
2-4 MW

## Slide 72: Muon Collider

## Slide 74: Engaging the Community
http://conferences.fnal.gov/muon11/
“…To review the physics case for a Muon Collider, accelerator R&D progress, the outstanding challenges, future plans, and opportunities for new and existing groups to participate in the R&D. “

## Slide 75: Muon Collider Challenges
Need Multi-MW proton target with long lifetime
  Liquid Hg jet MERIT experiment demo up to 8 MW
Need a technology for capture and cooling
  Gas-filled RF cavities operating inside magnetic fields offer a possible solution
  R&D program at Fermilab’s MuCool Test Area
Need demonstration of 6D cooling by a factor of 106
  4D MICE experiment in progress (demonstrate O(10%) by ~2014)
  6D cooling experiment sometime after 2015
Need development of very high field solenoids
  >30T for last stages of cooling, with luminosity proportional to field
  Program started at several labs FNAL, BNL, LBNL

## Slide 76: Muon Collider Challenges
Need substantial acceleration length (few km)
  Ideally would use ILC technology
  Major wall plug power consumer (out of perhaps 160 MW total)
Need end-to-end system simulation to understand beam dynamics, ultimate losses, and emittances
  Recent substantial progress with collider ring, optimized cooling channels and proton beam compression ring designs
Need demonstration of LC precision physics capability with realistic detector, MDI, and backgrounds simulation
  Will require detailed simulation and physics performance studies
  Upcoming workshop at Telluride, CO June 27-July 1

## Slide 77: High Energy Frontier (Colliders)
Recent Progress
    Tevatron
    RHIC
    LHC
Future Directions
    Future Ion Colliders
    HL-LHC
    ILC/CLIC
    electron-hadron colliders
    HE-LHC
    Neutrinos (Intensity Frontier)
    Muon collider
Operating
Approved, funded?
Not yet approved
Degree of feasibility, matureness,
(Likelihood)

## Slide 78: Ad personam Issues (1)
The physics output from the LHC will be decisive
If 500GeV cm is sufficient:
  ILC500; almost ready to go with construction (>200MW of electrical power, capital cost)
  CLIC500; staged version, several years technical development needed (>200MW of electrical power, capital cost)
If 1000GeV is needed and sufficient
  ILC1000; at the upper energy limit of this technology (~400MW Electrical power, serious issue, capital cost, 50km)
  CLIC1000; staged version, several years technical development needed (~400MW Electrical power is a serious issue)
If 3000GeV is needed and sufficient
  CLIC3000; maximum energy imaginable, still some major feasibility issues (560MW of electrical power would make this highly undesirable for the ecologists + operational costs)
If even higher energies are needed
  HE-LHC; aggressive R&D for high field sc magnets needed, SPS upgrade, injection/extraction systems, synchrotron radiation…
  Muon collider; many as yet unsolved technical issues (list too long to record), but very interesting accelerator physics… very long term
Aggressive R&D needed to increase the efficiency wall-plug to beam

## Slide 79: Summary (2)
If e-p is interesting as a complimentary project:
    LHeC (RR): certainly technically do-able. Integration presents major challenges, impact on the LHC operation is a major concern. By-passes are not trivial
    LHeC (LR): luminosity (1033)may be difficult to achieve, ERL a major challenge but is very interesting due to synergy with many other projects.
All these projects need continuing accelerator R&D so that the right decision can be made when the time comes to identify the next energy frontier accelerator (collider). We need to keep our choices open.

## Slide 80: Thank you
Acknowledgement
Sincere thanks to all the people from whom I have begged, borrowed or stolen slides

## Slide 81: SPARES

## Slide 82: Summary of LHC Intensity Limits (7 TeV)
Chamonix 2011
Beam Current Limit of ca. 1 A / beam!

## Slide 83: Luminosity
26 pb-1/day

## Slide 84: TeVatron

## Slide 85: RHIC

## Slide 86: LHC

## Slide 87: RHIC “Ions”

## Slide 88: LIU

## Slide 89: LIU

## Slide 90: Future directions for the LHC Injectors
R. Garoby
15/07/2011

## Slide 91: Beam specifications (Work in progress...)
 | Nominal LHC | HL-LHC | HE-LHC | 
Beam energy [GeV] | 450 | 450 | > 1000 | 
Distance between bunches [ns] | 25 | 25 (resp. 50) | 50 | 
Bunch population* [1011 p/b] | 1.2 | ~2 (resp. 3.3) | ~1.4 | 
Transverse normalized emittance [mm] | 3.5 | <2.5 (resp.3) | 3.75 (H) 1.84 (V) | 2.59 (H & V)
Longitudinal emittance [eVs] | 1 | 1? | ? | 
HL-LHC / LIU Brainstorming – June 2011 https://indico.cern.ch/conferenceDisplay.py?confId=138437
CERN-ATS-2010-177
[First thoughts on a higher energy LHC]

## Slide 92: HL-LHC (1/2)
Challenges for the injectors:
Higher brightness:
  Increased injection energy in the PSB from 50 to 160 MeV [Linac4 replacing Linac2]
2011:
Infrastructure installation
2012/13:
Accelerator installation
2013/14:
Commissioning
July 2014:
Linac4 ready

## Slide 93: HL-LHC (2/2)
Challenges for the injectors:
Higher brightness:
  Increased injection energy in the PS from 1.4 to 2 GeV [increased PSB energy or new RCS]
  Upgrades in PSB, PS and SPS for handling higher brightness beams (feedbacks, cures against electron clouds, hardware modifications to reduce impedance…)
Reliability during the period 2018-2030:
  Upgrade/replacement of ageing equipment (power supplies, magnets, RF…)
  Procurement of spares
  Improvement of radioprotection measures (shielding, ventilation…)

## Slide 94: HE-LHC
Challenges for the injectors:
1.2 TeV beam energy:
  new 1.2 TeV synchrotron either in the LHC tunnel or in the SPS tunnel,
  or use of the LHC itself, if it is economically interesting to locate the HE-LHC in a new and longer tunnel.
Operation during 2030-2050:
  replacement of all or part of the existing synchrotrons (to improve reliability, reduce the cost of maintenance and decrease the environmental impact). The specifications of these new accelerators could also be influenced by the needs of other users (e.g. for neutrinos and/or nuclear physics). Typical example:
Energy range | Machine | Other application
100 GeV – 1.2 TeV | HE-SPS | RIB acceleration?
~8 - 100 GeV | HE-PS | RIB acceleration ?
Up to ~8 GeV | SC linac | (+ 2 fixed energy rings) m production for n factory
Bmax~5 T
Bdotmax~2T/s
Bmax~4 T
Bdotmax~3T/s

## Slide 95: Potential Proton Drivers at CERN
R. Garoby
15/07/2011

## Slide 96: PS-based Proton Driver
[EDMS Document No.1108369 rev 1.1]
Draft layout
Proton beam characteristics
Short baseline experiment

## Slide 97: SPS-based Proton Driver
From LAGUNA-LBNO proposal (EU-FP7)
1.3 x nominal CNGS performance
Long baseline experiment (2300 km)
CERN-Pyhasalmi (Finland)
CERN-AB-2007-013 PAF

## Slide 98: High Power PS-based Proton Driver
New High Power PS (30-50 GeV, 2MW beam power) using the Low Power SPL (LP-SPL) as injector. Future Feasibility Study based on the work for LP-SPL and PS2 to be supported within the LAGUNA-LBNO DS (EU-FP7)
Near detector
Target
0.75-2MW
HPPS
CN2PY
(LP)-SPL
Long baseline experiment (2300 km)
CERN-Pyhasalmi (Finland)

## Slide 99: Linac (SPL)-based Proton Driver (1/4)
High Power SPL and fixed energy accumulator (5 GeV, 4MW beam power). Based on Linac4 and the HP-SPL R § D, to be complemented within the LAGUNA-LBNO DS (EU-FP7)
 | Option 1 | Option 2
Energy (GeV) | 2.5 or 5 | 2.5 and 5
Beam power (MW) | 2.25 MW (2.5 GeV) or 4.5 MW (5 GeV) | 5 MW (2.5 GeV) and 4 MW (5 GeV)
Protons/pulse (x 1014) | 1.1 | 2 (2.5 GeV) + 1 (5 GeV)
Av. Pulse current (mA) | 20 | 40
Pulse duration (ms) | 0.9 | 1 (2.5 GeV) + 0.4 (5 GeV)
2 ´ beam current Þ 2 ´ nb. of klystrons etc .
Ion species H−
Output Energy 5 GeV
Bunch Frequency 352.2 MHz
Repetition Rate 50 Hz
High speed chopper < 2 ns
(rise & fall times)
Required for muon production
Required for flexibility and low loss in accumulator
Required for low loss in accumulator
Main characteristics
Medium baseline experiment (150 km)
CERN-Frejus (France)

## Slide 100: Linac (SPL)-based Proton Driver (2/4)
Medium b cryomodule
High b cryomodules
Ejection
9 x 6
b=0.65 cavities
11 x 8
b=1 cavities
13 x 8
b=1 cavities
to
EURISOL
Debunchers
To HP-PS and/or Accumulator
High b cryomodules
From Linac4
0 m
0.16 GeV
110 m
0.73 GeV
291 m
2.5 GeV
500 m
5 GeV
HP-SPL block diagram
Segmented cryogenics / separate cryo-line / room temperature quadrupoles:
Medium b (0.65) – 3 cavities / cryomodule
High b (1) – 8 cavities / cryomodule
Low energy
Intermediate energy
High energy

## Slide 101: Linac (SPL)-based Proton Driver (3/4)
Objective of HP-SPL R § D:
String of 4 “equipped b=1 cavities” with main couplers § tuners to be installed into a short cryo-module by 2013 and tested in 2014.
Cryomodule
(CERN – CNRS)

## Slide 102: Linac (SPL)-based Proton Driver (4/4)
SPL b = 1 cavity + helium tank + tuner + main coupler
Bulk niobium cavities (CERN)
Main coupler
(CERN)
HOM coupler
(CERN – Uni Rostock)
Tuner (CEA)
Helium tank
(CERN – CEA)

## Slide 103: HL-LHC

## Slide 104: Operation Experience in 2010/2011: Pros
ability to re-optimize beam parameters for higher performance
  smaller beam emittance and larger beam-beam parameter
Leveling:  successful for LHCb by separation
beam-beam:  able to collide beams with larger than nominal
beam-beam parameters
Aperture  better than expected (b-beat, dispersion, tolerances)
Emittance  able to operate the LHC with 50% smaller than
nominal beam emittances (aperture & brightness)
Collimation  better than expected beam lifetimes

## Slide 105: Operation Experience in 2010/2011: Cons
105
UFOs:  origin not yet understood
 proportional to number of bunches (total beam current)
e-cloud  confirmed to be an issue for the LHC
beam scrubbing is effective
R2E:  first events observed, but not as bad as expected at >1033
 will increase with luminosity and beam intensity

## Slide 106: HL-LHC paves the way for the future
  SCRF (Crab Cavity), SC link 1 GW rate, HF SC magnets

## Slide 107: The goal
The main objective of HL-LHC is to implement a hardware configuration and a set of beam parameters that will allow the LHC to reach the following targets:
A peak luminosity of 5×1034 cm-2s-1 with levelling, allowing:
An integrated luminosity of 250 fb-1 per year, enabling the goal of 3000 fb-1 twelve years after the upgrade. This luminosity is more than ten times the luminosity reach of the first 10 years of the LHC lifetime.

## Slide 108: Goal – cont.
Levelled lumi of LLp =51034 s-1 cm-2 (not Hz cm-2)
Annual integrated luminosty: IL =250 fb-1
  More than 1 fb-1 a day
Which is more important? I guess IL . We take Lp as guideline, not a barrier, however it is understood that this is the nominal limit.
These goals are already questioning parameter space of Linear Collider: we need to be correct, optimist but not overoptimist

## Slide 109
We need to have potential for Lp =10-151034 (before levelling)
  Today the preferred baseline is to reach 5 1034 and then « crabbing ». But may be we put crab at max immediately and then use another parameters.
  We cannot rely only on one scheme: we need to have scheme with very low  and not small , we need to explore very high beam current and moderate beam current, and having more than on leveling methods.
  Many actions will be needed in addition to the most visible being discussed today to reach integrated :
    Turn around time: will allow « releasing » beam current (protection)
    Stops, Shutdowns, etc…
      Advanced robotics and monitoring?
      Remove on surface of sensible equipments.
    To be worked out with experiments
    The upgrade is « ultimate consolidation », too. I see these actions as a « continuum » with some spike activities , the biggest being the final installation around 2021-22

## Slide 110
Cold powering system: electrical transfer of the current from the room temperature terminal of the current leads to the magnet bus (LHe). It is an active mechanical, electrical and cryogenic system that incorporates superconducting parts - in the LHC High Temperature Superconductor (Bi-2223) in the current leads and Low Temperature Superconductor (Nb-Ti) in the bus.
Cold Powering
LHC: DFBs in line
with the magnets
in most of the cases.
Power converters are in the
tunnel in dedicated alcoves
-as near as possible to the
the DFBs.
Current Leads
SC bus bar
DFB
From A. Ballarino - CERN

## Slide 111
Link
SC bus bar
DFB
Powering via remote power converters
requires the use superconducting links
Current Leads
Electrical transfer at cryogenic temperature
across long lengths
From A. Ballarino - CERN

## Slide 112
Advantages of remote powering:
Safer long-term operation of powering equipment (power converters, current leads
and associate auxiliary devices) located in a radiation-free environment;
Safer access of personnel to equipment for maintenance, repair, diagnostic and
routine tests interventions;
Reduced time of interventions on power converters, current leads and DFBs if the
powering equipment is located outside of the tunnel areas – gain in machine
availability ;
- Free space in the beam areas which becomes available for other equipment.
Cold Powering via Superconducting Links
From A. Ballarino - CERN

## Slide 113: example HL-LHC parameters, b*=15 cm
parameter | symbol | nom. | nom.* | HL crab | HL sb + lrc | HL 50+lrc
protons per bunch | Nb [1011] | 1.15 | 1.7 | 1.78 | 2.16 | 3.77
bunch spacing | Dt [ns] | 25 | 50 | 25 | 25 | 50
beam current | I [A] | 0.58 | 0.43 | 0.91 | 1.09 | 0.95
longitudinal profile |  | Gauss | Gauss | Gauss | Gauss | Gauss
rms bunch length | sz [cm] | 7.55 | 7.55 | 7.55 | 5.0 | 7.55
beta* at IP1&5 | b* [m] | 0.55 | 0.55 | 0.15 | 0.15 | 0.15
full crossing angle | qc [mrad] | 285 | 285 | (508-622) | 508 | 508
Piwinski parameter | f=qcsz/(2*sx*) | 0.65 | 0.65 | 0.0 | 1.42 | 2.14
tune shift | DQtot | 0.009 | 0.0136 | 0.011 | 0.008 | 0.010
potential pk luminosity | L [1034 cm-2s-1] | 1 | 1.1 | 10.6 | 9.0 | 10.1
events per #ing |  | 19 | 40 | 95 | 95 | 189
effective lifetime | teff [h] | 44.9 | 30 | 13.9 | 16.8 | 14.7
run or level time | trun,level [h] | 15.2 | 12.2 | 4.35 | 4.29 | 4.34
e-c heat SEY=1.2 | P [W/m] | 0.2 | 0.1 | 0.4 | 0.6 | 0.3
SR+IC heat 4.6-20 K | PSR+IC [W/m] | 0.32 | 0.30 | 0.62 | 1.30 | 1.08
IBS e rise time (z, x) | tIBS,z/x [h] | 59, 102 | 40, 69 | 38, 66 | 8, 33 | 18, 31
annual luminosity | Lint[fb-1] | 57 | 58 | 300 | 300 | 300

## Slide 114: ILC/CLIC Steinar

## Slide 115: ILC yamamoto

## Slide 116: Major R&D Goals for Technical Design
Global Design Effort
  SCRF
    High Gradient R&D - globally coordinated program to demonstrate gradient by 2010 with 50%yield; improve yield to 90% by TDR (end 2012)
    Manufacturing: plug compatible design; industrialization, etc
    Future systems tests: NML (FNAL), STF2 (KEK)
  Test Facilities
    ATF2 - Fast Kicker tests and Final Focus design/performance
    CesrTA - Electron Cloud tests to establish damping ring parameters/design and electron cloud mitigation strategy
    FLASH – Study performance using ILC-like beam and cryomodule
Notes: 116

## Slide 117: Single Tunnel Options (HLRF)
Distributed RF Sources (DRFS)
  800 kW MAK
  Everything in tunnel
Klystron Cluster Scheme (KCS)
  Surface clusters of klystrons (2×32 MBK)
  RF power distributed via over-moded waveguide (350 MW)
    ±1 km
RDR HLRF Technology
  e.g. XFEL-like solution (pulsed cables)
  Back-up (risk-mitigation)

## Slide 118: Creation of a Global Database for Better Understanding of “Production Yield” in TDP
Global Data Base Team formed by:
  Camille Ginsburg (Fermilab)
  Rongli Geng (JLab)
  Zack Conway (Cornell University)
  Sebastian Aderhold (DESY)
  Yasuchika Yamamoto (KEK)
Activity
  July 2009:
  - Determine DESY-DB to be viable option,
  Sept., 2009: (ALCPG/GDE)
  - Dataset, web-based, support by FNAL/DESY,
  Dec., 2009: (SB2009) : 1st update
  March, 2010 (IW-ILC) : 2nd update
  June, 2010 (End TDP-1) : 3rd update
  March, 2011 (ILC-ALCPG): 4th update

## Slide 119: Cryomodule Gradient Spread Observed at DESY and KEK, as of Nov. 2010
FLASH:
  3 PXFEL cryomodules
ILC-TDP:
  S1-Global cryomodule
PXFEL-1 PXFEL-2 PFEL-3
S1-Global
D. Kostin & E. Kako

## Slide 120: RDR Design Parameters
Max. Center-of-mass energy | 500 | GeV
Peak Luminosity | ~2x1034 | 1/cm2s
Beam Current | 9.0 | mA
Repetition rate | 5 | Hz
Average accelerating gradient | 31.5 | MV/m
Beam pulse length | 0.95 | ms
Total Site Length | 31 | km
Total AC Power Consumption | ~230 | MW

## Slide 121
Cavity Gradient Milestone Achieved
2010
Milestone
TDR
Goal

## Slide 124: Integrated Systems Tests
Full systems integration testing
FLASH (DESY)
NML (FNAL)
STF (KEK)
TDP focus
Under construction
Up to 6 cryomodules
Operation: end 2012
“Quantum Beam” experiment 2011
1 CM with beam 2013
7 CM → 1.2 GeV beam
photon user facility
(2 CM 2015)
(3 CM)
“9mA experiment”
achieved ~1800 bunches at 9mA in 09.2009
DE/ERMS ~0.5% (@ 0.8 GeV)
~0.1% within pulse

## Slide 125: New Configuration for FLASH@DESY
ACC7 cavity quench limits and gradient spread are approaching ILC spec
Opportunity to study:
Gradient overhead and RF power overhead near ILC gradients
RF distribution setup schemes with cavity powers close to ILC spec
Lorentz-force detuning + piezo compensation near ILC gradients
Two 9mA runs planned for 2011
  January
  Late Autumn (TBC)
ACC6
ACC7
31.5 MV/m
40.0
35.0
30.0
25.0
20.0
15.0
Significant improvements in operability during 2010 (LLRF)

## Slide 126: FLASH: Stability
15 consecutive studies shifts (120hrs), and with no downtime
Time to restore 400us bunch-trains after beam-off studies: ~10mins
Energy stability with beam loading over periods of hours: ~0.02%
Individual cavity “tilts” equally stable
Energy stability over 3hrs with 4.5mA
~0.02% pk-pk
9 Feb 2011

## Slide 127: Beam Test Facilities (non SCRF)
Two Large Scale Test Facilities for R&D:
  Damping Ring (ATF, CesrTA)
  Beam Delivery System (Final Focus) (ATF2)
● ATF/ATF-2 (KEK)
● CesrTA (Cornell)
strong ILC-CLIC synergy

## Slide 128
Mitigating Electron Cloud
Simulations – electrodes; coating and/or grooving vacuum pipe
Demonstration at CESR critical tests
eCloud R&D

## Slide 129: Mitigation - Simulation Studies

## Slide 130
Field Region | Baseline Mitigation Recommendation |  | Alternatives for Further Investigation
Drift* | TiN Coating | Solenoid Windings | NEG Coating
Dipole | Grooves with TiN Coating | Antechambers for power loads and photoelectron control | R&D into the use of clearing electrodes.
Quadrupole* | TiN Coating |  | R&D into the use of clearing electrodes or grooves with TiN coating
Wiggler | Clearing Electrodes | Antechambers for power loads and photoelectron control | Grooves with TiN Coating
Proposed ILC Mitigation Scheme

## Slide 131: CesrTA Programme (Collaboration)
Major Reconfiguration of CESR ring
2 Year Programme
  Ending 2010 (i.e. now)
Principal goals
  Measure EC build-up in wigglers / arcs
  Evaluate experimentally mitigating techniques
  Develop (benchmark)models for EC-driven instabilities

## Slide 132: ATF2 – Beam size/stability and kicker tests
IP
Shintake Monitor
Final Doublet

## Slide 133: ATF / ATF2 After Earthquake?
See first reports in ILC Newsline 17-March-11
Articles by Toshiaki Tauchi and Rika Takahashi

## Slide 134: CLIC Steinar

## Slide 135: CLIC Power Source Concept
140 ms train length - 24  24 sub-pulses
4.2 A - 2.4 GeV – 60 cm between bunches
240 ns
24 pulses – 101 A – 2.5 cm between bunches
240 ns
5.8 ms
Drive beam time structure - initial
Drive beam time structure - final
CLIC RF POWER SOURCE LAYOUT
Drive Beam Accelerator
efficient acceleration in fully loaded linac
Power Extraction
Drive Beam Decelerator Section (2  24 in total)
Combiner Ring  3
Combiner Ring  4
pulse compression &
frequency multiplication
pulse compression &
frequency multiplication
Delay Loop  2
gap creation, pulse compression & frequency multiplication
RF Transverse Deflectors

## Slide 136: Tentative CLIC Post-CDR phase(s)
2011-2016 – Project Preparation phase
Goal: preparation of a (staged) Project Implementation Plan (PIP) at reviewed energy and luminosity (taking into account results of CDR and based on Physics requests as soon as available…) :
  - technical developments & test of critical component prototypes in upgraded facilities
  - Machine/Detector interface and Detector developments -
  - Site studies , Organisation and Governance
After 2016 – Project Implementation phase
Goal: Lay the grounds for full approval and preparation of the technical documentation needed for moving into (staged) construction following Physics requests (should be known by the time….)
    - Industrialisation & pre-series production of large series components with validation facilities
  - Detector&physics studies with emphasis on technical coordination issues&integ.
    - Project Implementation Plan (PIP) update, following staging strategy and detailed resource discussion with all partners

## Slide 137: ILC/CLIC Parameters
4.1%
5.0%

## Slide 138
CLIC Main Parameters http://cdsweb.cern.ch/record/1132079?ln=fr http://clic-meeting.web.cern.ch/clic-meeting/clictable2007.html
High gradient to reduce cost
Break down of structures at high fields and long pulses
  Pushes to short pulses
  and small iris radii (high wakefields)
High luminosity
Improve wall plug to RF efficiency
Push RF to beam efficiency
  Push single bunch charge to beam dynamics limit
  Reduce bunch distance to beam dynamics limit
Push specific luminosity -> High beam quality
  Beam-based alignment and tuning
  Excellent pre-alignment
  Component stabilisation

## Slide 141
CLIC main parameters
Centre-of-mass energy | 500 GeV | 3 TeV
Total (Peak 1%) luminosity | 2.3(1.4)·1034 | 5.9(2.0)·1034
Total site length (km) | 13.0 | 48.3
Loaded accel. gradient (MV/m) | 80 | 100
Main linac RF frequency (GHz) | 12 | 
Beam power/beam (MW) | 4.9 | 14
Bunch charge (109 e+/-) | 6.8 | 3.72
Bunch separation (ns) | 0.5 | 
Beam pulse duration (ns) | 177 | 156
Repetition rate (Hz) | 50 | 
Hor./vert. norm. emitt (10-6/10-9) | 4.8/25 | 0.66/20
Hor./vert. IP beam size (nm) | 202 / 2.3 | 40 / 1
Hadronic events/crossing at IP | 0.19 | 2.7
Coherent pairs at IP | 100 | 3.8 108
Wall plug to beam transfer eff | 4.1% | 5.0%
Total power consumption (MW) | 240 | 560
Notes: Spare slide ?

## Slide 142: CLIC Feasibility status

## Slide 143: CLIC – layout for 500 GeV
Main Beam Generation Complex
Drive beam
Main beam
Drive Beam Generation Complex
only one DB complex
shorter main linac
2.5 km
797 klystrons
15 MW, 2x29µs

## Slide 144
Helsinki Institute of Physics (Finland)
IAP (Russia)
IAP NASU (Ukraine)
IHEP (China)
INFN / LNF (Italy)
Instituto de Fisica Corpuscular (Spain)
IRFU / Saclay (France)
Jefferson Lab (USA)
John Adams Institute/Oxford (UK)
Polytech. University of Catalonia (Spain)
PSI (Switzerland)
RAL (UK)
RRCAT / Indore (India)
SLAC (USA)
Thrace University (Greece)
Tsinghua University (China)
University of Oslo (Norway)
Uppsala University (Sweden)
UCSC SCIPP (USA)
ACAS (Australia)
Aarhus University (Denmark)
Ankara University (Turkey)
Argonne National Laboratory (USA)
Athens University (Greece)
BINP (Russia)
CERN
CIEMAT (Spain)
Cockcroft Institute (UK)
ETHZurich (Switzerland)
FNAL (USA)
Gazi Universities (Turkey)
John Adams Institute/RHUL (UK)
JINR (Russia)
Karlsruhe University (Germany)
KEK (Japan)
LAL / Orsay (France)
LAPP / ESIA (France)
NIKHEF/Amsterdam (Netherland)
NCP (Pakistan)
North-West. Univ. Illinois (USA)
Patras University (Greece)
The CLIC collaboration
CLIC multi-lateral collaboration
41 Institutes from 21 countries
Notes: 144

## Slide 145
Key CTF3 feasibility milestones: drive beam generation
Fully loaded acceleration RF to beam transfer: 95.3 % measured.
No issues found with transverse wakes in structures. Operation is routinely with full loading
Full commissioning of x 4 combiner ring
Drive beam current stability at the end of the fully loaded linac : better than CLIC specification: 0.75 10-3
1.2 us drive beam pulse

## Slide 146
Chart: 
 | -2 | -7.8276 | -4.4086 | -5.8339 | -4.6515 | -5.0914 | -5.8462 | -7.077 | -6.9443
log(BDR/m)
T18 – strong tapering
T18 – strong tapering
T18 – strong tapering
T18 (CERN) – strong tapering
TD18 – waveguide damping
TD18 – waveguide damping
T24 – Higher efficiency
T24 – Higher efficiency
TD24
CLIC BDR specification
New
in CTF3
Interrupted by earthquake in Japan – last estimate available
Accelerating structures:
Achieved < nominal Break down
Scaled @ 100 MV/m (unloaded ) Accelerating Gradient and 180 ns pulse length)
Notes: The combination of high gradient, low break-down rate and the correct pulselenght
Maybe next is better

## Slide 147
Chart: 
 | 121.2667 | 85.2688 | 87.0505 | 83.2393 | 90.0189 | 95.5788 | 105.3354 | 104.2869
Unloaded gradient at CLIC 4*10-7 BDR and 180 ns pulse length
T18 – strong tapering
T18 – strong tapering
T18 – strong tapering (now with recirculation)
T18 – strong tapering (CERN built)
TD18 – waveguide damping
T24 – high efficiency
TD18 – waveguide damping
T24 – high efficiency
MV/m
1400
3900
550
1300
3200
280
600
conditioning
time [hr]
Interrupted by earthquake in Japan
1570
Notes: Maybe this one is better

## Slide 149
December 14, 2010:
Probe beam accelerated by 23 MV in a TD24 accelerating structure, corresponding to 106 MV/m, in a reproducible way.
Meas. PETS power input to structure ~ 80 MW (~200 MW in the resonant loop)
Drive beam: 12.5 A, 113 MV, 12 GHz in CLEX (1.5 GHz beam combined factor 8), 140 ns pulse length
Probe beam: 0.08 A, 173 MV, 1.5 GHz, 8 ns pulse length
2010: Two-beam acceleration with a gradient of 106 MV/m

## Slide 150: Two-beam Test Stand results 2011
2011 : CTF3 TBTS running for full after winter shut-down. Gradients of 110 – 120 GV/m are routinely reached (20% above CLIC target).
Rf power in PETS routinely reaches 300 MW (two times the CLIC target)
Notes: Expect better slide

## Slide 151: DR: comparison to other projects
CLIC requirements close to new generation synchrotron light sources (Operation- Projects)
CLIC 500 GeV similar as ILC and demonstrated in ATF/KEK (normalized emittance)
CLIC 3 TeV similar as PEPX/SLAC project.
Close collaboration with ATF/KEK (small emittances) and CESRTA/Cornell (electron clouds)
Emittance conservation a challenges:
For example, CLIC main linac design fulfills emittance requirements. Tight, but feasible component specification.
Notes: Need to be cleaned up but has to info needed to discuss initial emittance and conservation

## Slide 152: DR technology and experimental program
Super-conducting wigglers
  Demanding magnet technology combined with cryogenics and high heat load from synchrotron radiation (absorption)
High frequency RF system
  1 or 2 GHz RF system in combination with respect to power and transient beam
Coatings, chamber design and ultra-low vacuum
Electron cloud mitigation, low-impedance, fast-ion instability
Kicker technology
  Extracted beam stability
Diagnostics for low emittance
Experimental program set-up for measurements in storage rings and test facilities:
    ALBA (Spain), ANKA (Germany),
    ATF (Japan), CESRTA (USA),
    Synchrotron (Australia),
    SOLEIL (France)..
Parameters | BINP | CERN/Karlsruhe
Bpeak [T] | 2.5 | 2.8
λW [mm] | 50 | 40
Beam aperture full gap [mm] | 13 | 13
Conductor type | NbTi | NbSn3
Operating temperature [K] | 4.2 | 4.2
Notes: Spare ?

## Slide 153
Tunnel implementations (laser straight)
Central Injector complex
Central MDI & Interaction Region
Notes: To illustrate siting

## Slide 154: Work-plan for the coming years
Before 2011 - CDR (2011-12), CLIC feasibility established
2011(12)-2016 – Project Preparation phase
Goal for 2016: Develop a project implementation plan for a Linear Collider (at CERN):
  addressing the key physics goals as emerging from the LHC data
  with a well-defined scope (i.e. technical implementation and operation model, energy and luminosity), cost and schedule
  with a solid technical basis for the key elements of the machine and detector
  including the necessary preparation for siting the machine at CERN
  within a project governance structure as defined with international partners
After 2016 – Project Implementation phase, possibly including an initial period to lay the grounds for full approval (CLIC 0 – a significant part of the drive beam facility)
Notes: Pictures illustrate various parts of the activities in this period: rebasellning and staging taking into account physics results, ctf3 and other system tests of key parts of the machine, further site studies, further work on RF components, complete modules and start of industralization of components, a significant build up of testing capacity of RF components (at CERN and with collaborators)

## Slide 155
Circular Collider many magnets, few cavities, stored beam
higher energy → stronger magnetic field
→ higher synchrotron radiation losses (E4/m4R)
Linear Collider few magnets, many cavities, single pass beam, no synchrotron losses
higher energy → higher accelerating gradient
higher luminosity → higher beam power (high bunch repetition)
source
main linac
N
S
N
S
accelerating cavities
Linear versus Circular Collider

## Slide 156
Cost Linear versus Circular Collider
Circular Collider
ΔE ~ (E4/m4R)
cost ~ aR + b ΔE
optimization: R~E2 → cost ~ cE2
Linear Collider
E ~ L
cost ~ aL
cost
energy
Circular
Collider
Linear
Collider
200 GeV e-

## Slide 157: LHeC

## Slide 159: Physics and Range
New Physics
High precision
partons in plateau
of the LHC
Nuclear
Structure
& dynamics
High Density Matter
Large x
eQ states
GUT (δαs=0.1%)
Excited fermions
Hot/cold spots
Single top
Higgs
PDFs
Multi-Jets
DVCS
Unintegrated
partons
Saturation
Vector Mesons
IP - graviton
Odderons
NC couplings
sin2Θ
Beauty
Charm
Partons in nuclei
Shadowing
….
Q2 = 4momentum transfer2 x = Bjorken x: fraction of p’s momentum
Physics

## Slide 160
TOBB ETU
KEK
LHeC - Participating Institutes

## Slide 161: LHeC Design Considerations
LHC hadron beams: Ep=7 TeV EA=EeZ/A
Luminosity O (1033) cm-2s-1 with Beam Power 100 MW (wall plug)
Integrated e±p : O(100) fb-1 ≈ 100 * L(HERA)  synchronous ep and pp operation
Two solutions
e Ring in the LHC tunnel (Ring-Ring - RR) Superconducting ERL (Linac-Ring -LR)

## Slide 162
Bypassing ATLAS
For the CDR the bypass concepts
were decided to be confined to
ATLAS and CMS

## Slide 163: LINAC - Ring
Baseline Parameters [Designs, Real photon option, ERL]
Sources [Positrons, Polarisation]
Rf Design
Injection and Dump
Beam-beam effects
Lattice/Optics and Impedance
Vacuum, Beam Pipe
Integration and Layout
Interaction Region
Magnets
Cryogenics
Workpackages as formulated in 2008, now in the draft CDR
1056 cavities
66 cryo modules per linac
721 MHz, 19 MV/m CW
Similar to SPL, ESS, XFEL, ILC, eRHIC, Jlab
21 MW rf
Cryo 29 MW for 37W/m heat load
Magnets in the 2 * 3 arcs:
600 - 4m long dipoles per arc
240 - 1.2m long quadrupoles per arc
IP2
Linac (racetrack)
inside the LHC for
access at CERN
Territory
U=U(LHC)/3=9km

## Slide 164: LHeC: Ring-Ring Option
164
Challenge 1: Bypassing the main LHC detectors
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble

## Slide 165: LHeC: Ring-Ring Option
165
Challenge 2: Integration in the LHC tunnel
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble

## Slide 166: LHeC: Ring-Ring Option
166
Challenge 3: Installation with LHC circumference:
requires:
support
structure
with
efficient
montage
and
compact
magnets
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble

## Slide 167
1.67 km
0.34 km
30-GeV linac
LHC p
LHC p
1.0 km
2.0 km
10-GeV linac
10-GeV linac
p-60
erl
LHC p
70-GeV linac
3.9 km
2.0 km
p-140
injector
dump
injector
dump
dump
injector
IP
IP
IP
140-GeV linac
p-140’
injector
dump
IP
7.8 km
high
luminosity
high
energy
“least expensive"
LHeC: Linac-Ring Option 
Considdered Various Layout
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble

## Slide 168: LHeC Options: Executive Summary
168
Linac-Ring option:
-Installation decoupled from LHC operation and shutdown planning
-Infrastructure investment with potential exploitation beyond LHeC
-Challenging new technology: high current SC ERL
Ring-Ring option:
-We know we can do it:  LEP 1.5
-Challenge 1: integration in the LHC tunnel and co-existence with
LHC hardware
-Challenge 2: installation within shutdowns of LHC schedule
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble
CDR will be reviewed by Expert Panel
The goal is to identify the best option for the LHeC by the end of the year

## Slide 169: LHeC Planning and Timeline
169
LHeC operation:
-Luminosity goal based on ca. 10 year exploitation time (100fb-1)
-LHeC operation beyond or after HL-LHC operation will imply significant operational cost overhead for LHC consolidation
We assume the LHC will reach end of its lifetime with the end of the HL-LHC project:
-Goal of integrated luminosity of 3000 fb-1 with 200fb-1 to 300fb-1 production per year  ca. 10 years of HL-LHC operation
-Current planning based on HL-LHC start in 2022
 end of LHC lifetime by 2032 to 2035
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble

## Slide 170
2022
LS3
Installation of the HL-LHC hardware
Not yet approved!
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble

## Slide 171: LHeC Planning and Timeline
171
LHeC planning:
-Need to start R&D work as soon as possible
-Need to develop detailed TDR after feedback from review panel
 concentrate future effort on only one option
CERN Medium Term Plan:
-Only 2 long shutdowns planned before 2022
-Only 10 years for the LHeC from CDR to project start (other smaller projects like ESS and PSI XFEL plan for 8 to 9 years [TDR to project start] and the EU XFEL plans for 5 years from construction to operation start)
Oliver Brüning CERN
EPS-HEP, 23 July 2011, Grenoble

## Slide 172: 60 GeV Energy Recovery Linac
CERN 1
CERN 2
Jlab
BNL
Two 10 GeV energy recovery Linacs, 3 returns, 720 MHz cavities

## Slide 173
CDR draft
LINAC 60 GeV ERL

## Slide 174
CDR draft

## Slide 175
Novosibirsk dipole prototype
measured field reproducible
to the required 2 10-4
CERN prototype under test
3080 dipoles
336+148 F+D
Injector to Ring – similar to Linac design [R+D]
Magnets

## Slide 176
Bypassing CMS
RF

## Slide 177: Accelerator: Ring - Ring
Baseline Parameters and Installation Scenarios
Lattice Design [Optics, Magnets, Bypasses]
IR for high Luminosity and large Acceptance
rf Design [Installation in bypasses, Crabs?]
Injector Complex [Sources, Injector]
Injection and Dump
Cryogenics – work in progress
Beam-beam effects
Impedance and Collective Effects
Vacuum and Beam Pipe
Integration into LHC
e Beam Polarization
Deuteron and Ion Beams
5.3m long
(35 cm)2
slim + light(er)
3080 magnets
Prototypes:
BINP-CERN
LHeC Ring Dipole Magnet
.12-.8T
1.3kA
0.8MW
Workpackages as formulated in 2008, now in the draft CDR

## Slide 178: Ring: Dipole + Quadrupole Magnets
5m long
(35 cm)2
slim + light
for installation
BINP &
CERN
prototypes
736 magnets
1.2 m long

## Slide 179: HE-LHC

## Slide 180: Neutrinos

## Slide 181: ν-Accelerators : Future Possibilities
R&D Experiments
MERIT
  High-Power Target test
  Liquid Mercury inside a 20T capture solenoid
MICE
  Mon front-end ionization cooling experiment
  RF in B-fields
EMMA
  Fast acceleration of muons
  Re-circulating linacs, ns-FFAGs
Neutrino Factory
  Neutrinos from accelerated and stored μ+ and μ-

## Slide 182: ν-Accelerators : Future Possibilities
Beta-beam
  Neutrinos from accelerated and stored radioactive ions, pure νe or anti-νe beams
  Two pairs under study: 6He/18Ne and 8Li/8B
Technology challenges
  ion production
  ion collection and bunching
  ion acceleration
    collective effects
    ion decays

## Slide 183: ν-Accelerators : Present landscape
Conventional Neutrino Beams
CNGS @ CERN
  design: 500kW(beam), 750kW(infra.)
  OPERA/ICARUS experiments
    ντ appearance
T2K @ J-PARC
  design : up to 1.6MW(beam), 4MW (infra.)
  Near Detector + Super-K
    indication for θ13 non-zero and large
MINOS @ FNAL
  design: 400kW(beam), upgrade
  Near Detector + MINOS
    supports θ13 non-zero hypothesis
    differences in ν anti-ν oscillations
p + C(target) → π+, K+ → (decay) → μ+ + νμ
423 kW
Duty factor:
42s (CNGS)/49.2s (total) = 85%
362 kW average power at SPS
Design and operation of high-intensity facilities is always very challenging

## Slide 184: ν-Accelerators : Future Possibilities
NOνA Off-Axis Experiment @ FNAL
NuMI beam upgrade: 320 700kW
  120 GeV beam from Main Injector, cycle time from 2.2s to 1.5s
  More RF power (1.5s 1.33s)
  High-power target
  New extraction/injection lines
  Expect : ~6×1020 pot/yr, starting 2014
Long baseline beams @ CERN (LAGUNA-LBNO)
  Build on CNGS, and extend LAGUNA & EUROnu work
Courtesy : Ryan Patterson - CALTECH
810 km
CN2PY (Pyhasalmi)
Initial: beam from SPS (500kW-750kW)
Long term: LP-SPL + HPPS - 2MW
2300 km
CNGS - Umbria
Beam from SPS (500kW)
730 km
CN2FR (Frejus)
HP-SPL + accumulator (5 GeV – 4 MW)
130km
CERN
Synergy with β-beam for (γ=100)

## Slide 185: ν-Accelerators : Future possibilities
Intensity upgrades
Facilities for precision measurements
Super-beam (Frejus)
Neutrino Factory
Present generation
Beta-beams
NOνA – LBNE
T2K (1.6MW)
CN2PY (Pyhasalmi-FI)
R&D Studies with strong EU participation and International Collaboration
  EUROnu
  LAGUNA – LAGUNA_LBNO
  International Design Study for a Neutrino Factory (IDS-NF)
Technology challenges for accelerators
  (M)MW proton drivers
  High-power targets and ion production (β-beams)
  Muon cooling and (fast) acceleration
300-400 kW
700kW – 1(2) MW
2-4 MW

## Slide 186: ν-Accelerators : Future Possibilities - FermiLab
NOνA Off-Axis Experiment @ FNAL
  120 GeV beam from main injector like NUMI
NuMI beam upgrade: 320 700kW
  convert recycler to p-ring
  Reduce MI cycle time from 2.2s to 1.33s
  High-power target
  New extraction/injection lines
  Expect : ~6×1020 pot/yr, starting 2014
LBNE Very-Long baseline beam to DUSEL
  Initial phase : same beam line as NUMI-NOνA – 120 GeV form MI, 700 kW
  Upgrade to 2.3 MW – Project-X
Courtesy : Ryan Patterson - CALTECH
810 km
2300 km
730 km
130km
1300 km
Courtesy : G. Rameika - FNAL

## Slide 187: ν-Accelerators : Future Possibilities - Japan
T2K Beam to Super Kamiokande
  30 GeV beam from main ring
Reached 70kW [1.43e20 pot] before earthquake
Repairs ongoing, hope to restart in 2012, aim to reach ~0.5MW in 2013 [1e21 pot]
Continue approved program: reach ~1 MW in few years, extend to 3.8MW later
  Major upgrades to the accelerators would be required - Target station designed for 4 MW of beam power
Plans for longer baseline (658 km) to Okinoshima island with off-axis detector
Courtesy : T. Kobayashi - KEK

## Slide 188: ν-Accelerators : Future Possibilities - CERN
Long-Baseline Options – LAGUNA-LBNO study
    Build on CNGS experience
    Extend LAGUNA (underground detectors) & EUROnu work
    The beam to Frejus offers good synergy for enhanced physics reach with β-beam at γ=100
CN2PY (Pyhasalmi)
Initial : beam from SPS (500kW - 750kW)
Long term: LP-SPL + HPPS - 2MW
2300 km
CNGS - Umbria
Beam from SPS (500kW)
No near detector possibility
730 km
CN2FR (Frejus)
HP-SPL + accumulator (5 GeV – 4 MW)
130km
CERN

## Slide 189: ν-Accelerators : Future Possibilities – Neutrino Factory
R&D Experiments
EMMA – FFAG demonstration
MICE – Muon Cooling
MERIT – High-power target

## Slide 190
EUROnu – Super-Beam
Design of CERN to Frejus SB based on HP-SPL
Use MEMPHYS as far detector
Neutrinos created from high power proton beam on low Z target.
Pions produced focussed towards detector using magnetic horn.

## Slide 191
EUROnu – Super-Beam
Ti pebble bed target.
3mm spheres
4 target + horn system

## Slide 192
EUROnu – Beta-Beams, Isotope Production
Present estimations of isotope production

## Slide 193
EUROnu – Beta Beams, Some Technological Challenges …
28 GHz
waveguide
High voltage
ring
Plasma
chamber
Plasma
electrode
Extraction
insulator
Puller
electrode
Measurements of X-sections, energies and angles, 8Li and 8B
60 GHz pulsed ion source
Collection of produced ions in an accelerator (production ring)
Also important: accelerator and impedance challenges, RF …

## Slide 194: Muon Collider

## Slide 197: Muon Accelerator Program (MAP) R&D Plan
Fermilab-led collaboration to deliver a Design Study by ~FY2012, evaluating the feasibility of a multi-TeV Muon Collider:
  An end-to-end simulation of a MC complex based on technologies in-hand or that can be developed with a specified R&D program.
  Hardware R&D and experimental tests to guide & validate the design work.
  Rough cost range.
  R&D plan for longer term activities (e.g. 6D cooling expt)
Deliver on commitments to making MICE and the IDS-NF studies a success.
Annual cost ~10M$ now  ~15 M$ requested after FY11

## Slide 200: Muon Collider Concept: Fermilab

## Slide 202: Possible Muon Collider advantages
Compact: fits on FNAL site
Multipass acceleration: cost effective
Multipass collisions in a ring (~1000 turns): relaxed emittance requirements & hence relaxed tolerances
Narrow energy spread: precision scans, kinematic constraints
Potentially two detectors (2 IPs): lots of time for readout (DTbunch ~ 10 ms) & minimal pile up
Higgs possibly visible as s-channel resonance
Cost
Physics
Benefits very narrow resonances (Z too wide)

## Slide 203: Targeting, capturing and cooling