## Slide 1: MINERVA - Accelerator Machine Protection
Daneels Ruben - 26/09/2024
CERN ZHAW & SCK CEN Workshop

## Slide 2
MPS definition
Top level requirements
MPS protection functions
Beam interlock requirements
Beam interlock functional architecture Commissioning & validation plan

## Slide 3: MPS definition
Machine Protection Strategy System
  Scope
    Protect the equipment from getting damaged (reduce financial losses and downtime)
  How?
    Describe what other systems need to implement to fulfil the protection need
  Out of scope
    Protection of environment and people (safety)

## Slide 4: MPS top level requirements
Functional requirements
  Equipment protection (beam & non-beam related)
    For all operating conditions, the MPS shall protect the equipment from damage, which would lead to financial losses and/or downtime.
  Minimize Beam downtime
    The MPS shall not reduce beam availability more than needed.
      Modular architecture
      Reset strategy
      Redundancy
  Enable Beam availability improvement
    The MPS shall ensure systems have requirements on status signals and interfaces relevant to guarantee the reliability of the MPS features and feed info to beam availability improvement tools.

## Slide 5: MPS protection functions
Requirements in place to reduce identified unacceptable risks
  Functional
    Describe what is needed
    When <Trigger> , then <Action>
  Performance
    Describe how “well” the protection function needs to work
      Reliability (PFD/PFH) PIL
      Response time
      Proof test interval
  Implementation decision
      Which system implements which part ? Sensor / logic / actuator
      Distribute performance requirements over sub-parts

## Slide 6: Beam interlock protection functions
  Functional
    Describe what is needed
      Example: When MYR-1464 - DUMP-I temperature exceeds TBD °C, MYR-1454 – ACC PS shall stop the proton beam
  Performance
    Describe how “well” the protection function needs to work
      Reliability (PFD/PFH) PIL MAX PIL 2
      Response time fastest loops require ≤ 10 µs
      Proof test interval ≥ 1 year
  Implementation decision
      Which system implements which part ?
        Sensor BLMs, BCMs, VAC valves, PCOs, local protection systems (e.g. RFCELL), DUMP temp switch, …
        Logic Always DIS (part of MIS that is dedicated to MPS)
        Actuator Chopper + Ion source

## Slide 7: Beam interlock functional architecture

## Slide 8: Commissioning & Validation plan
Support staged commissioning
Integrate MPS tests with ‘normal’ functional tests in commissioning plans
Commissioning & Validation Template drafted on system level

## Slide 9
Copyright © SCK CEN
PLEASE NOTE!
This presentation contains data, information and formats for dedicated use only and may not be communicated, copied, reproduced, distributed or cited without the explicit written permission of SCK CEN. If this explicit written permission has been obtained, please reference the author, followed by ‘by courtesy of SCK CEN’.
Any infringement to this rule is illegal and entitles to claim damages from the infringer, without prejudice to any other right in case of granting a patent or registration in the field of intellectual property.
SCK CEN
Belgian Nuclear Research Centre
Foundation of Public Utility
Registered Office: Avenue Herrmann-Debrouxlaan 40 – BE-1160 BRUSSELS
Operational Office: Boeretang 200 – BE-2400 MOL