Preliminary design of RLA2 for the Muon Collider
Beam Dynamics for RLA2 for the Muon Collider
Avni Aksoy

---
Collider Concept
Collider Concept
Short, intense proton bunch
Ionisation cooling of muon in matter
Collision
Acceleration to collision energy
Protons produce pions which decay into muons, muons are captured
Fully driven by muon lifetime
Acceleration
from 5 GeV to 63 GeV

---
High efficient low cost acceleration for low energy Muons
Accelerator Typologies
‘Racetrack’ vs ‘Dogbone’ RLA
Racetrack
Dogbone
%mu^{"-"}
{ %DELTA E /2}
%mu^{"-"}
{ %DELTA E }
%mu^{"+"}
%mu^{"+"}
Any lattice due to symmetric acceleration
Compact short arcs that fits same tunnel
Identical beam loading
Low efficiency- more number of passes
Complex spreader
...
High efficiency-less number of passes
Better separation of spreaders
Beam loading due to following bunches
Requires symmetric optics due to charge symmetry
Long arcs

---
Initial beam parameters
Initial beam parameters
Parameter	Unit	Value
Initial beam energy	GeV	5
Final beam energy	GeV	64
Bunch charge	nC	~400
Transverse emittance	μm.rad	20
Longitudinal emittance	eVs	0.0225
RMS bunch length	mm	30
Very large energy spread and long bunch length
Low frequency acceleration, chromatic aberrations and dispersive effects
Both longitudinal and transverse emittance needs to be preserved
One needs to control higher order terms of lattice
Rapid acceleration
...

---
Choice of RF frequency
Choice of RF frequency
- We have RMS ~ 30 mm bunch  200 mm full length
- Typically the total bunch length should be < 10% of λRF
- To preserve longitudinal emittance lower frequency is preferable
  - …
- Reasonable frequency would be 350 MHz which is SC RF cavities of LEP
200MHz
350MHz
650MHz

---
Accelerating module
Accelerating module
FODO type lattice with fixed gradient SC quadrupole is proposed
  - Two quads are spaced by one SRF module (housing 3 SRF cavities) , short FODO due to weak quadrupoles at high energy
- The expected gradient for the LEP cavity is 15 MV/m (Alexej Grudiev)
- We used same dimensions for wakefield calculation.
  - For short range wake Karl Bane’s approximation is used

---
Beam Dynamics in Linac
Beam Dynamics in Linac
- Fixed optics due to opposite acceleration on other linac..
- Large initial energy spread causes emittance growth due to chromatic effects by quadrupoles, we use weak quadrupoles
  - Drawback: very weak lattice at high energy
100 CM (300 cavity per linac)
Longitudinal emittance growth with low frequency cavity

---
Beam Dynamics in Linac-2
Beam Dynamics in Linac-2
To minimize uncorrelated energy spread we propose to use harmonic cavity (1050 MHz) at the middle of linac (56 Cavity)
8 CM (40 linearizer cavity per linac)
6.6-7 GeV/linac

---
Arc Considerations
- As compact as possible !
  - SC magnets (max 10 T)
- Higher order terms needs to controlled due to high energy spread
  - Second order achromat
- High energy spread for first passes
  - Small momentum compaction factor and chromaticity
- Fitting same tunnel if possible
- . ..
- Usually sextupoles are needed to correct second-order dispersion in the bending plane but one can create second order achromat by adjusting the space between magnets..
  - In order to not to use any sextupole magnets we propose to use same principle
Y. Sun, PRSTAB, 14, 060703 (2011)

---
ARC 1-2 (12 identical cell for 90o bending)

---
ARC 1-2
Same principle is repeated for other arcs
The bending angle increased with energy
Arc1: 12 cell, arc2:10 cell, arc3:8 cell arc4:6 cell
Large energy acceptance (> 2.5%)
Very compact (~85 m)

---
Last ARC (6 identical cell for 90o bending)

---
Injection / Extraction
- The matching to the linac/arcs are performed by spreaders..
  - Fixed optics
- Smooth bending due to large energy spread
  - Normal conducting magnets (max 2T)
- Large aperture at low energy , small aperture at high energy, long matching section
Bending: green
Quadrupole: blue
Sextupole: orange

---
Injection / Extraction matching to linac/arc

---
By-pass section
The phase of beam respect to RF is defined by the arc length.
  - 1 degree RF phase (@350 MHz) is 2.4 mm (0.85 mm for 1 GHz)
- If the beam is injected off-energy to the arc it is impossible to adjust path length within ± several mm
- It is also useful to avoid meeting the opposite propagating bunches
µ-
µ+
Electrostatic deflector
Bending magnet

---
Beam dynamics in arcs
Beam dynamics in arcs
Start to end simulation in first arc (tracking)
Extraction/matching
µ+
By-pass section
90o bending
µ-

---
Beam dynamics in arcs (2)
Beam dynamics in arcs
Start to end simulation in first arc (tracking)

---
Beam dynamics in last arc

---
Start to end of all machine
Start to end of all machine
1st pass
2nd pass
….
1st arc

---
Start to end simulation of entire machine
Start to end simulation of entire machine

---
Footprint
Footprint

---
Conclusion
Conclusion
Racetrack acceleration scheme has been proposed for the RLA
  - For dogbone matching co-propagating bunches was impossible for non symmetric lattice
- FODO type 2nd order achromat lattice without sextupoles is suitable for recirculating beam
- One can improve longitudinal emittance and transverse emittance meets the target value
  - I need to improve last arc
- The Muon survival meets target value
  - We have 93 %
- The number of structures are increased about 80 but total length of machine is more less the same..
  - Machine fits into one tunnel..
- 3.5 pass instead of 4.5 would make spreader design simpler
  - Better separation and shorter beamline

---
Thanks for your attention
Thanks for your attention