## Slide 1: LHeC synergies with FCCee and Accelerator Technologies
Oliver Brüning and Yannis Papaphilippou,
CERN
15th November 2024
ESPP white paper preparation meeting for LHeC

## Slide 2: Synergies with FCCee
Synergy with FCCee injector design option with recirculating LINAC (RLI) based on LHeC ERL (even with a 1st stage @ 20 GeV as presented today by Krzysztof)
Could even be extended to cover full FCCee energy range (i.e. replacing FCCee booster)
Synergy with SRF pre-series production (including High-Temperature SRF @ 4.5 K) while building CERN SRF expertise (project/team) and industrial validation
Synergy with high-efficiency klystrons development
Cryogenic system towards reduced power and cost
CE optimization based on CO2 emission (J. Osborne)
Cost to be updated based on 2018 LHeC estimate document (consistent with Oliver’s cost and resource estimates)
  Do we need some comparison with FCCee injector cost?
Schedule to fit HL-LHC era and towards FCCee (2035-…)
Risk mitigation for certain FCCee accelerator technologies by prototyping and testing
Training opportunities for building ERL expertise (collaboration with Orsay PERLE and bERLinPRO, operational experience)

## Slide 3: RLI for FCCee
Need to update parameters for RLI to replace LINAC pre-injectors + Booster, including positron production
Accelerator | FCCee-Z |  | FCCee-W |  | FCCee-H |  | FCCee-tt | 
Energy [GeV] | 45.6 |  | 80 |  | 120 |  | 182.5 | 
Type of filling | Full | Top-up | Full | Top-up | Full | Top-up | Full | Top-up
RLI # bunches (800 GHz RF) | 832 |  | 1000 |  | 328 |  | 48 | 
RLI bunch population [109] | 3.0 | 0.15 | 1.3 | 0.04 | 1.9 | 0.06 | 2.8 | 0.08
RLI injections | 1400 |  | 140 |  | 100 |  | 100 | 
#of BR cycles | - | 1 | 1 | 2 | 1 | 1 | 1 | 1
# of injections/collider bucket | 70 | 70 | 1 | 2 | 1 | 1 | 1 | 1
Total number of bunches | 16640 |  | 2000 |  | 328 |  | 48 | 
Filling time (both species) [sec] | 0.3 | 0.3 | 5.8 | 5.8 | 4.9 | 4.9 | 8.0 | 8.0
  Tentative injector parameters with RLI @ 50 GeV (FCC week 2021)

## Slide 4: LHeC Accelerator technologies
ERL Design options and optimization (K.Andre et al.)
  Separate FFAG arc design and impact on emittance preservation
  Lattice and robustness studies (imperfections) with improved simulation framework (X-suite)
  Impact of Coherent Synchrotron Radiation and micro-bunching instability handling
IR optics design (B. Holzer et al.)
  Asymmetric magnets using HL-LHC short model coils
Machine-detector interface (L. Forthomme et al.)
  SR radiation handling/shielding in IR for machine and detector protection
Super-conducting RF development including (including High-Temperature SRF @ 4.5 K)
Fast Reactive Tuner (FRT) for microphonics mitigation
High-efficiency klystrons development
Cryogenic system for reduced power and cost
PERLE as stepping stone for proving several accelerator physics concepts and prototyping/testing technologies