## Slide 1
“Green radiators”: Controlling refractive index & reducing Cherenkov gas radiator GWP: a challenge in an era of diminishing fluorocarbon availability
Related paper: https://link.springer.com/article/10.1140/epjp/s13360-023-04703-w
See also: https://indico.cern.ch/event/1263731/contributions/5398511/attachments/2648319/4584649/G_Hallewell_DRD4%20Rad%20Gas%20GWP%20with%20annexes%20May%2016%202023.pdf
https://indico.cern.ch/event/1371158/contributions/5773321/attachments/2788215/4861759/G_Hallewell_ATLAS_sustainability_forum_Jan_26_2024_v2.pptx
ICHEP2024 (July 2024): https://indico.cern.ch/event/1291157/contributions/5900402/
G. Hallewell
Aix Marseille Université,
CNRS/IN2P3, CPPM, Marseille, France
1
.
DRD4 Collaboration Meeting,
WG-2: CERN Oct 21-25 2024
Notes: 1

## Slide 2: Abstract
COMPASS and LHCb use C4F10 and CF4 Cherenkov gas radiators.
These Saturated FuoroCarbons (CnF(2n+2)) have high GWPs, however
(5000-9000*CO2) so there is impetus to reduce their consumption.
Sound velocity monitoring was used for controlling real-time blending C5F12 with N2 in the SLD CRID. The technique could be valuable in the future operation to meet optical & low GWP constraints of future blended Cherenkov gas radiators.
Oxygenated fluorocarbons (fluoro-ketones: CnF2nO) can offer similar optical performance, with GWPs equivalent to CO2 (or zero). Their GWPs are geometry-specific however: closed molecular rings with an oxygen atom link have GWPs as high as SFCs. Reactivity & toxicity also likely to be geometry dependent.
Legislation & market forces will limit SFC & FK (PFAS) availability, maybe leaving “holes” in the CnFx FK “spectrum”, unfilled by CnF2nO equivalents.
Blending low molar concentrations of heritage-stock higher-order SFCs
or 3M NOVEC®5110: C5F10O (GWPzero) with light gases, N2, Ar, CO2… would
reduce radiator volume GWP “load”.
Examples are explored.
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 3: Molecular shapes, GWP & toxicity
Cherenkov
Radiator
(hist.) + Cooling (Liq.)
Si cooling
(Evap.)
COOLING (Liq.)
Ih.T H331,
reactive
Ih.T H330, reactive
Ih.T H331,
reactive
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Cherenkov
Radiator
Cherenkov
Radiator
Cherenkov
Radiator
(hist.)
Cherenkov
Radiator
(hist.)
Upper: molecular shapes of SFCs, including common gaseous Cherenkov radiators.
Lower: shapes of some non-cyclic CnF2nO analogues (20-year GWPs & GHS inhalation toxicities (source www.synquest.com

## Slide 4: GHS Classification Criteria for Inhalation & skin Toxicity
H330 | Fatal if inhaled
H331 | Toxic if inhaled
H332 | Harmful if inhaled
H333 | May be harmful if inhaled
H334 | May cause allergy or asthma symptoms or breathing difficulties if inhaled
H335 | May cause respiratory irritation
H336 | May cause drowsiness or dizziness
H310 | Fatal in contact with skin
H311 | Toxic in contact with skin
H312 | Harmful in contact with skin
H313 | May be harmful in contact with skin
H314 | Causes severe skin burns and eye damage
H315 | Causes skin irritation
Global Harmonized System of Classification and Labelling of Chemicals (GHS). 10th revision, United Nations (2023}
About the GHS | UNECE https://unece.org/about-ghs
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 5
C4F8O Linear with Oxygen atom as
internal link and double carbon
bonded link
C4F8O
Cyclic
Perfluorotetrahydrofuran,
Octofluorotetrahydrofuran
(GWP20 = 8975) [ref EPJP]
[H335]
C4F8O Linear & iso, with
Oxygen atom on external spur
Octafloro-1-methoxyprop-1-ene
(GWP20 = ?) [H332, 335, 336]
Octafluoro-2-butanone
(GWP20 = ?) [H335]
Heptafluorobutyryl fluoride
(GWP20 = ?) [H331]
Heptafluoroisobutyryl fluoride
(GWP20 = ?) [H335]
Pentafyoroethyltrifluorovinyl ether
(GWP20 = ?) [H332, 335]
Molecular shape is important for GWP and toxicity
Cyclic, non-cyclic & non-cyclic double c-bonded C4F8O isomers
Optical performance similar
to C4F10: (BTeV & ALICE VHMPID)
High GWP!!
GWP ?

GWP ?
GWP ?
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 6: So why are some of these spurred fluoro-ketones CnF2nO potential low GWP substitutes for saturated fluorocarbons? CnF(2n+2)
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 7: Q: What gives a spurred-Oxygen fluoro-ketone molecule (like 3M NOVEC 649/1230®) its low GWP?
A: Structure!: a double-bonded oxygen atom on a peripheral spur of the molecule
This fluoro-ketone configuration is:
CF3CF2C(O)CF(CF3)2
7
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 8: Q: What gives NOVEC 649/1230 its low GWP?
Scission by UV photons of l around 300 nm
In the atmosphere (low pressure, high UV): the fragments do not reassociate* into saturated fluorocarbons of the type CnF(2n+2) (which would have high GWP)
*The Environmental Impact of CFC Replacements HFCs and HCFCs
T. WALLINGTON et al Environ.Sci.Technol.1994(28)7 320A https://doi.org/10.1021/es00056a714
https://www.nist.gov/system/files/documents/el/fire_research/R0301570.pdf
8
[15]
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 9: Q: What gives NOVEC 649/1230 its low GWP?
Scission by UV photons of l around 300 nm
In the atmosphere (low pressure, high UV): the fragments do not reassociate* into saturated fluorocarbons of the type CnF(2n+2) (which would have high GWP)
*The Environmental Impact of CFC Replacements HFCs and HCFCs
T. WALLINGTON et al Environ.Sci.Technol.1994(28)7 320A https://doi.org/10.1021/es00056a714
https://www.nist.gov/system/files/documents/el/fire_research/R0301570.pdf
9
[15]
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 10
This latest CERN environmental report https://doi.org/10.25325/CERN-Environment-2023-003
R449: (CFH blend) GWP=1397
R1234 (HFO): GWP = 7
NOVEC 649 (C6F12O): GWP=0
CF4 LHCb RICH2: GWP20 = ¬ 4880_CO2* [16]
C2F6 ATLAS evap cooling (potential use): GWP20 = ¬ 8210_CO2* [16]
C3F8 F2 Chemicals , Astor, ATLAS evap cooling: GWP20 = ¬ 6640_CO2*[16]
C4F10 LHCb RICH1, COMPASS RICH: GWP20 = ¬ 6870_CO2* [16]
C5F12 PP50: GWP20 = ¬ 6350_CO2* [16] (ex-DELPHI, no longer used at CERN)
C6F14 PP1, F2 Chemicals: Liquid cooling, many expts:
GWP20 = ¬ 5890_CO2*[16]
For some perspective: SF6 GWP ~ 23000 * CO2
See also:
https://www.ghgprotocol.org/sites/default/files/ghgp/Global-Warming-Potential-Values%20%28Feb%2016%202016%29_1.pdf
For 100 yr (average of 2nd, 4th & 5th assessment reports; AR2,4,5)
Collective loss of SFCs only around 10 tonnes (whole of LHC + expts)
(compare that to mass-loss at a ‘grande surface’ supermarket!)
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 11
But no mention at all of the ATLAS ultrasonic fluorocarbon leak monitor system !
https://doi.org/10.25325/CERN-Environment-2023-003
G. Hallewell: Seminaire CPPM: 16 sep 2024

## Slide 12
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 13
EU strategy to reduce Fluronated (PFAS) compound production and use
(includes also fluorinated plastics not shown here: see back-up material)
ICHEP2024
Projected Usage
Dynamic price hiking :
like imposing demand-dependent customs duty…?
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 14: Cherenkovgreenicity…
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 15
Refractive index & GWP ’load’ in a Cherenkov Gas Radiator
3 large RICH detectors currently in operation at CERN:
using saturated fluorocarbon gas volumes:
C4F10 (COMPASS: 100m3, LHCb RICH 1: 4m3): GWP20 = 4880,
CF4 (LHCb RICH 2: 100m3): GWP20 = 6870
A Cherenkov radiator vessel of volume V(m3) filled with
a blend of gases of densities ri (kgm-3),
fractional concentrations wi and individual GWPi (tonnes CO2 eq.)
has a GWP environmental “load” (& release potential) L given by:
) (tonnes CO2 eq.) [Eq. (1)]
The corresponding radiator gas mixture refractivity is given by :
) [Eq. (2)]
For just two gases we can blend small conc. wx of (heavier) SFC or Fluoro-Ketone
vapour of high refractivity (n-1)x with wy of light transparent gas, refractivity (n-1)y
to replicate refractivity (n-1)z of a lighter SFC at high conc. – for a lower GWP load.
wx = [Eq. (3)]
V,r
With j contaminant gases of known molar concentrations wj present we can still
add a small concentration wx of (heavier) SFC or Lin-FK vapour of high refractivity
(n-1)x with wy of light transparent gas to substitute the refractivity (n-1)z(target)
of a lighter SFC at high concentration – to achieve a lower overall GWP load.
+
[Eq. (2) Eq. (2b)]
wx = [Eq. (3)  Eq. (3b)]
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 16
Refractive index & GWP ’load’ in a Cherenkov Gas Radiator
3 large RICH detectors currently in operation at CERN:
using saturated fluorocarbon gas volumes:
C4F10 (COMPASS: 100m3, LHCb RICH 1: 4m3): GWP20 = 4880,
CF4 (LHCb RICH 2: 100m3): GWP20 = 6870
A Cherenkov radiator vessel of volume V(m3) filled with
a blend of gases of densities ri (kgm-3),
fractional concentrations wi and individual GWPi (tonnes CO2 eq.)
has a GWP environmental “load” (& release potential) L given by:
) (tonnes CO2 eq.) [Eq. (1)]
The corresponding radiator gas mixture refractivity is given by :
) [Eq. (2)]
For just two gases we can blend small conc. wx of (heavier) SFC or Fluoro-Ketone
vapour of high refractivity (n-1)x with wy of light transparent gas, refractivity (n-1)y
to replicate refractivity (n-1)z of a lighter SFC at high conc. – for a lower GWP load.
wx = [Eq. (3)]
V,r
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 17
Use real-time speed of sound to get component molar concentrations,wi
(SoS traditionally also called “c” by acousticians to confuse things)
Then use standard refractivity formula to get from calculated w1,2
to refractive index of the radiator gas in real-time, along with standard relativistic expressions to get from n to Cherenkov g thresholds for different particle species and b = 1 angle
Real-time measurement of speed of sound c takes us via the relative concentrations of the components to the speed of light b and beyond!! in the radiator gas
17
Eyes on the prize…(focus here on LHCb RICH2 (n-1)…)
(488.10-6)CF4 = (~1750.10-6)C5F10O*0.12+(300.10-6)N2*0.88
)
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 18: Targeting the refractivity of CF4 (100 m3: example: LCHb RICH 2) at 1 barabs with gases of differing molecular weight in varying fractional concentrations (conc. > 100% indicate need for overpressure): includes hypothetical fluoro-ketones
CF4
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 19
Chart: 
| 361.57150866452997 | 256.66370132773199 | 207.76041110631601 | 177.74100163378299 | 156.771959339836 | 140.96541864529999 | 128.432486611158 | 118.12923971441801 | 109.42497216462201 | 101.912772216321 | 95.316482075286103
e thresh | 0.20021 | 0.16566 | 0.14445 | 0.12974 | 0.11878 | 0.11019 | 0.10324 | 0.09746 | 0.092555 | 0.088324 | 0.084626
mu thresh | 4.2043 | 3.4788 | 3.0335 | 2.7246 | 2.4943 | 2.3141 | 2.1681 | 2.0467 | 1.9436 | 1.8548 | 1.7772
pi thresh | 5.4857 | 4.5391 | 3.9579 | 3.555 | 3.2545 | 3.0193 | 2.8288 | 2.6704 | 2.536 | 2.4201 | 2.3188
kthresh | 19.9006 | 16.4666 | 14.3584 | 12.8965 | 11.8065 | 10.9534 | 10.2622 | 9.6876 | 9.1999 | 8.7794 | 8.4119
pthresh | 37.4788 | 31.0115 | 27.0412 | 24.288 | 22.2351 | 20.6285 | 19.3269 | 18.2446 | 17.3262 | 16.5342 | 15.842
% C5F12 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
C5F12 or C5F10O concentration (%)
LHCb RICH 2 with C5F10O/N2
GWP load = (0.13 molar*1*V.r)
LHCb RICH 2: CF4 thresholds
GWP load = (0.95 molar*4880*V.r)
Cherenkov threshold: C5F10O/N2 & (heritage) C5F12/N2 blend and GWP load comparison for LHCb RICH2 (100m3 CF4)
C5F12 SFC/N2 and NOVEC5110 (C5F10O) /N2 will be very similar (MW 266 vs. 288)
~ 14% molar C5F10O
gives a GWP load reduction of 1737 tonnes:
Even substituting CF4 with ~ 13% molar heritage stock C5F12 reduces GWP load by ~800 tonnes
19
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 20
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024
Targeting the refractivity of C4F10 (100 m3: example: COMPASS RICH) at 1 barabs
with gases of differing molecular weight in varying fractional concentrations
(conc. > 100% indicate need for overpressure): includes hypothetical fluoro-ketones
C4F10

## Slide 21
Chart: 
| 361.57150866452997 | 256.66370132773199 | 207.76041110631601 | 177.74100163378299 | 156.771959339836 | 140.96541864529999 | 128.432486611158 | 118.12923971441801 | 109.42497216462201 | 101.912772216321 | 95.316482075286103
e thresh | 0.20021 | 0.16566 | 0.14445 | 0.12974 | 0.11878 | 0.11019 | 0.10324 | 0.09746 | 0.092555 | 0.088324 | 0.084626
mu thresh | 4.2043 | 3.4788 | 3.0335 | 2.7246 | 2.4943 | 2.3141 | 2.1681 | 2.0467 | 1.9436 | 1.8548 | 1.7772
pi thresh | 5.4857 | 4.5391 | 3.9579 | 3.555 | 3.2545 | 3.0193 | 2.8288 | 2.6704 | 2.536 | 2.4201 | 2.3188
kthresh | 19.9006 | 16.4666 | 14.3584 | 12.8965 | 11.8065 | 10.9534 | 10.2622 | 9.6876 | 9.1999 | 8.7794 | 8.4119
pthresh | 37.4788 | 31.0115 | 27.0412 | 24.288 | 22.2351 | 20.6285 | 19.3269 | 18.2446 | 17.3262 | 16.5342 | 15.842
% C5F12 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
C5F10O concentration (%)
COMPASS (& LHCb RICH 1): C4F10 thresholds
COMPASS RICH GWP load = (6849 tonnes)
Cherenkov threshold in C5F10O/N2 mixtures and GWP load comparison with COMPASS RICH (100m3)
N2-NOVEC5110 (C5F10O) very similar to C5F12 (MW 266 vs. 288)
85% Novec 5110 gives a huge GWP load reduction of 6849 tonnes
21
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 22
    Legacy C4F10 replacing CF4 in the context of LHCb RICH-2
    Legacy C5F12 replacing C4F10 for COMPASS and LHCb RICH-1.
Sound velocity in C5F12 and C4F10 is based on extensive thermodynamic data:
corresponding required concentrations for C5F10O and C4F8O
will be slightly higher due to their lower densities.
Other (heritage/legacy) options (in N2)
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024
C5F12

## Slide 23
Historical: The SLD barrel CRID gas radiators (SLAC: 1990s)
87% C5F12/13%N2
gas radiator
Sonar transducer
6 transducer pairs
@ 3 different heights
(hydrostatics)
23
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 24
Maintaining C5F12/N2 refractive index
through sonar-based active mixture control
(In this paper submitted to IEEE TNS)
Flowmeter
analyzer in supply line
to tune the blend by
hardwired 4-20mA
links to mass flow controllers
24
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 25
Chart: C5F12-N2 40 ⁰C
| 361.57150866452997 | 256.66370132773199 | 207.76041110631601 | 177.74100163378299 | 156.771959339836 | 140.96541864529999 | 128.432486611158 | 118.12923971441801 | 109.42497216462201 | 101.912772216321 | 95.316482075286103
e thresh | 0.20021 | 0.16566 | 0.14445 | 0.12974 | 0.11878 | 0.11019 | 0.10324 | 0.09746 | 0.092555 | 0.088324 | 0.084626
mu thresh | 4.2043 | 3.4788 | 3.0335 | 2.7246 | 2.4943 | 2.3141 | 2.1681 | 2.0467 | 1.9436 | 1.8548 | 1.7772
pi thresh | 5.4857 | 4.5391 | 3.9579 | 3.555 | 3.2545 | 3.0193 | 2.8288 | 2.6704 | 2.536 | 2.4201 | 2.3188
kthresh | 19.9006 | 16.4666 | 14.3584 | 12.8965 | 11.8065 | 10.9534 | 10.2622 | 9.6876 | 9.1999 | 8.7794 | 8.4119
pthresh | 37.4788 | 31.0115 | 27.0412 | 24.288 | 22.2351 | 20.6285 | 19.3269 | 18.2446 | 17.3262 | 16.5342 | 15.842
% C5F12 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
SLD-CRID: Cherenkov threshold in C5F12/N2 mixtures vs. measured speed of sound in radiator gas mixture (1)
Typical mix 87%C5F12,13%N2
C5F12 concentration (%)
25
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 26
Chart: C5F12-N2 40 ⁰C: (N2-C5F10O should be very similar
| 361.57150866452997 | 256.66370132773199 | 207.76041110631601 | 177.74100163378299 | 156.771959339836 | 140.96541864529999 | 128.432486611158 | 118.12923971441801 | 109.42497216462201 | 101.912772216321 | 95.316482075286103
e thresh | 0.20021 | 0.16566 | 0.14445 | 0.12974 | 0.11878 | 0.11019 | 0.10324 | 0.09746 | 0.092555 | 0.088324 | 0.084626
mu thresh | 4.2043 | 3.4788 | 3.0335 | 2.7246 | 2.4943 | 2.3141 | 2.1681 | 2.0467 | 1.9436 | 1.8548 | 1.7772
pi thresh | 5.4857 | 4.5391 | 3.9579 | 3.555 | 3.2545 | 3.0193 | 2.8288 | 2.6704 | 2.536 | 2.4201 | 2.3188
kthresh | 19.9006 | 16.4666 | 14.3584 | 12.8965 | 11.8065 | 10.9534 | 10.2622 | 9.6876 | 9.1999 | 8.7794 | 8.4119
pthresh | 37.4788 | 31.0115 | 27.0412 | 24.288 | 22.2351 | 20.6285 | 19.3269 | 18.2446 | 17.3262 | 16.5342 | 15.842
Thresh/c | 0.99969 | 0.99954 | 0.9994 | 0.99926 | 0.99911 | 0.99897 | 0.99883 | 0.99868 | 0.99854 | 0.9984 | 0.99825
SLD-CRID: Cherenkov threshold in C5F12/N2 mixtures
vs. measured speed of sound in radiator gas mixture (2)
Cherenkov Threshold (GeV/c)
b = 1/n
Measured Sound Velocity (m/s)
So.. from (“acoustic”) c to b…
26
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 27
27
But what if a gas radiator contains more than 2 gas species like this?
(This is old: from RICH2013)
Stable N2
content
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024
O2 conc. (wO2) can be measured by electrochemical fuel cell
CO2 conc (wCO2) can be measured by Non-Dispersive Infra Red
leaving a pair of gases of “primary interest” to be measured
acoustically (CF4/N2 or a CF4 replacement gas /N2 )

## Slide 28
Refractive index & GWP ’load’ in a Cherenkov Gas Radiator
3 large RICH detectors currently in operation at CERN:
using saturated fluorocarbon gas volumes:
C4F10 (COMPASS: 100m3, LHCb RICH 1: 4m3): GWP20 = 4880,
CF4 (LHCb RICH 2: 100m3): GWP20 = 6870
A Cherenkov radiator vessel of volume V(m3) filled with
a blend of gases of densities ri (kgm-3),
fractional concentrations wi and individual GWPi (tonnes CO2 eq.)
has a GWP environmental “load” (& release potential) L given by:
) (tonnes CO2 eq.) [Eq. (1)]
The corresponding radiator gas mixture refractivity is given by :
) [Eq. (2)]
For just two gases we can blend small conc. wx of (heavier) SFC or Fluoro-Ketone
vapour of high refractivity (n-1)x with wy of light transparent gas, refractivity (n-1)y
to replicate refractivity (n-1)z of a lighter SFC at high conc. – for a lower GWP load.
wx = [Eq. (3)]
V,r
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024
With j contaminant gases of known molar concentrations wj present we can still
add a small concentration wx of (heavier) SFC or Lin-FK vapour of high refractivity
(n-1)x with wy of light transparent gas to substitute the refractivity (n-1)z(target)
of a lighter SFC at high concentration – to achieve a lower overall GWP load.
+
[Eq. (2) Eq. (2b)]
wx = [Eq. (3)  Eq. (3b)]

## Slide 29
29
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024
See back up slides for
more details
Sophisticated algorithms developed for ultrasonic analysis of a gas pair of primary interest on varying conc. of known background gases
(https://www.mdpi.com/2410-390X/5/1/6)

## Slide 30: Example: Look-up tables of SoS. vs. composition for C3F8/N2 (+ CO2) (ATLAS silicon tracker cooling leak analysis)
30
CAN UTILITY DB expanded
from 2-D to 3-D:
C3F8/N2 fit coeffs
stored @{T, P, CO2} grid
Extra interpolation step,
starting from grid cub(oid) of uncertainty
to Tmeas, Pmeas,CO2 meas
Calculate sound vel vs. conc. eqns from
C3F8 & N2 AND KNOWN CONTAMINANT GAS
Cp & Cv over expected T,P, %CO2 range.
Demonstration:
1st acoustic measurement of concentrations of binary gas pair
of interest (C3F8/N2)
in known varying conc. of 3rd gas (CO2) :
(4 envelopes cycling every 4 hours)
Algorithm: industrial & anaesthesia applications
https://www.mdpi.com/2410-390X/5/1/6
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 31
From 1st DRD4 Meeting: 17-20 June 2024
Real? Repeatable?
very crude device,
lacking details
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 32
UV transparency, refractivity, cmhemical stability & compatibility studies needed
for different CnF2nO molecular shapes. RICH detector community very competent & equipped for detailed UVT & (n-1) - much ex-DELPHI RICH diagnostic equipment at CERN for example
Minuteman Model 302 VM.
Most probable PC spectral range
in new build gas RICH detectors
A
ALICE VHMPID: transparancy
measurements in c-C4F8O
Octafluorotetrahydrofuran
CAS: 773-14-8
Synquest Inc. FL, USA
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 33: CnF2nO fluid selection search criteria
Start(ed)
Non-toxic
(MSDS)
?
N
Y
Non-
Flammable
(MSDS)
?
N
Y
Non-
Oxone-
depleting
?
N
Y
Next CnF2nO fluid
(order & isomer)
to evaluate
Materials/
purifier
Compatible
?
N
Y
N
Y
Rad.
Tolerant
(more for
cooling)
?
N
Y
Dielectric
?
Acid
formation
with H2O
?
N
Y
N
Y
N
Recirc.
Thermo-
dynamics
OK
?
Y
Y
Y
UV-Vis
transparency
OK
?
(n-1) &
Chrom. Disp.
OK
?
N
N
Accept
fluid
Optotests
Materials tests
Bibliographic
Low GWP!
?
N
Y
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 34: Thermodynamics of circulation of heavy Cherenkov radiator vapour and allowed escape of light component (N2, Ar, CO2 etc…)
Similarities with systems for the C3F8 evaporative fluorocarbon cooling of the ATLAS Silicon tracker
(CERN EN-CV responsibility)
But with enhanced monitoring, including (n-1), UV transparency
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 35
Low temperature (-80°C)
N2 gas-induced condensation (B):
of C5F12 fromC5F12/N2 radiator gas (flow~1m3/hr, negligible C5F12 loss)
followed by (C) electric re-evaporation
(1-1.5m below condenser liq. level)
Cold N2 gas (‘conditioned’ by
counter-flow with boil-off LN2
from liquid argon calorimeter: (A))
Ultrasonic (speed of sound) – aided
“on-the fly” mixing of typical
17%N2 /83%C5F12 (molar) radiator gas mixture (D)
SLD Barrel CRID C5F12/N2 gas radiator: continuous thermodynamic recirculation
A
B
C
D
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 36
(A) C5F12 Condenser
(cooled with GN2)
LN2 conditioner
(Chills GN2 in counterflow with LN2
from liquid argon calorimeter source)
(B) C5F12 storage tank
and N2 separator
(C) C5F12 Evaporator
SLD Barrel CRID C5F12/N2 gas thermodynamic recirculator
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 37: SLD CRID C5F12 circulation
Electric evaporation of C5F12
(dh ~ 1.3m)
Condensation in tank (B) @ varying temperature 
down to “keep-cold” temp of -80°C (PC5F12 ~ mbar),
drastically reduces C5F12 loss by evaporation
(D) N2 addition (C5F12 p.p. reduction)
& flow through CRID Radiator vessel
Collapsing C5F12 partial pressure
& some condensation in precooler (A)
Pure C5F12@ -80C from
bottom of tank
(C) Electric heating
of liquid C5F12
SLD CRID C5F12 Thermodynamic circulation: Pressure-Enthalpy
1barabs condenser
Headspace (& CRID
radiator vessel)
pressure maintained
by N2 in return radiator gas & condenser N2
vent to atmosphere
rgh of 1.5m C5F12 !
Vapour
Liquid
Changing Phase
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 38: C4F10 (C4F8O thermodynamics will be similar)
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024
Condensation

## Slide 39
Conclusion & avenues of study needed
High GWP SFCs (CnF(2n+2)) have ideal optical properties as Cherenkov radiators: can we secure “heritage” C4F10 & CF4 stocks to continue (deferred destruction)?
Future PFAS Availability issues, but total PFAS ban unrealistic, due to demands of electronics industry which we mightprofit from. (Other companies (Dehon (Fr), Synquest (US), various (Ch)) stepping in to fill void left by 3M departure...
While not industrialised over a wide CnF2nO range fluoro-ketones could offer similar performance at very low, or 0 GWP:
 Toxicity, materials compatibility & sophisticated optical studies needed ;
Radiation tolerance & thermal performance of 3M NOVEC 649 (lin-C6F12O) & NOVEC 7110 (C4F9OCH3) sufficiently promising for consideration to replace C6F14 (cooling); 649 acid formation via residual H2O @ low temp issue to be resolved
By analogy, lin-C4F8O might replace C4F10 , while lin-C4F8O or lin-C5F10O (or even C4F10 or heritage C5F12) blended with N2 & real-time monitored by sound velocity gas analysis - could replace CF4 in RICH radiators;
Molecular shape is everything?: lower order CnF2nO toxicity vs. shape needs study (F electron clouds shielding O atom?) : Need to work with chemical experts
Thermodynamics of circulation : usually a neglected area: Involve EN-CV from start –considerable experience at CERN from evaporative fluorocarbon cooling
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 40: CnF2nO fluid selection search criteria
Start(ed)
Non-toxic
(MSDS)
?
N
Y
Non-
Flammable
(MSDS)
?
N
Y
Non-
Oxone-
depleting
?
N
Y
Next CnF2nO fluid
(order & isomer)
to evaluate
Materials/
purifier
Compatible
?
N
Y
N
Y
Rad.
Tolerant
(more for
cooling)
?
N
Y
Dielectric
?
Acid
formation
with H2O
?
N
Y
N
Y
N
Recirc.
Thermo-
dynamics
OK
?
Y
Y
Y
UV-Vis
transparency
OK
?
(n-1) &
Chrom. Disp.
OK
?
N
N
Accept
fluid
Optotests
Materials tests
Bibliographic
Low GWP!
?
N
Y
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 41
Back up material
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 42: Ultrasonic gas analysis in a process environment with multiple background gases
42
https://www.mdpi.com/2410-390X/5/1/6
Precision: 10-5 C3F8 into N2 at 1 bar
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 43: Ultrasonic gas analysis in a process environment with multiple background gases
https://www.mdpi.com/2410-390X/5/1/6
Gas aspirated through
150m tubes from
silicon tracker
N2 environmental
volumes to
‘sonar’ devices
to look for C3F8
leak rates
(C3F8 in N2 )
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 44
Chart: CO2 concentration (ppm)
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 45
Polaroid Capacitative transducer components
Capacitative 350V activation/ bias  rapid response
37mm diameter determines 50 kHz dominant frequency: can operate over wide pressure range (50mbar >35 bar…)
45
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 46
46
Ultrasonic algorithm to find component molar concentrations wi=1,2… of a pair of gases of primary interest in multi-gas blends
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 47
(1) Calculate data base of individual CVi..n CPi..n
over expected T, P. range:
Example here: C4F10: (mol. wt.) = 238 in N2 (mol. wt. = 28)
47
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 48
(2) Calculate c‘theo’ as a function of concentration from component
Cp, Cv’s over the expected sonar temperature, pressure range to
make database of c‘theo’ vs. conc. fit equations to store in ‘cans’
Example here 0- 1% C3F8 (m.w.= 188) in N2 (m.w.= 28): only one pressure shown here for clarity)
48
Polynomial
Fit
Parameters
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 49
(3) CAN UTILITY: Store these c‘theo’ vs. molar conc. polyfit coeffs covering expected temperature & pressure range in “cans” at P,T grid intersections
T 
P 
Tmin
Tmax
Pmax
Pmin
Tstep
Pstep
Tmeas
Pmeas
(4) Calculate component concentrations wi from measured sound velocity cmeas & stored fit coeffs. interpolated to correspond to the measured T, P
!! This grid can become 3-D or higher-D with known contaminant gas(es) 
49
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 50: Aah…what if 3 gases are present? Acoustic Ambiguity ? 2 combinations of 3 gases  same c… so must find w3 from a different (non-acoustic) technology source… Examples inc. clinical…): CO2 from ND infra-red, H2O from hygrometry, O2 from EC cell… etc.
50
G. Hallewell: Seminaire CPPM: 16 sep 2024

## Slide 51: Example: Look-up tables of SoS. vs. composition for C3F8/N2 (+ CO2) (ATLAS silicon tracker cooling leak analysis)
51
CAN UTILITY DB expanded
from 2-D to 3-D:
C3F8/N2 fit coeffs
stored @{T, P, CO2} grid
Extra interpolation step,
starting from grid cub(oid) of uncertainty
to Tmeas, Pmeas,CO2 meas
Calculate sound vel vs. conc. eqns from
C3F8 & N2 AND KNOWN CONTAMINANT GAS
Cp & Cv over expected T,P, %CO2 range.
Demonstration:
1st acoustic measurement of concentrations of binary gas pair
of interest (C3F8/N2)
in known varying conc. of 3rd gas (CO2) :
(4 envelopes cycling every 4 hours)
Algorithm: industrial & anaesthesia applications
https://www.mdpi.com/2410-390X/5/1/6
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 52
52
LHCb RICH 2 change in refractivity with varying CO2 radiator addition
Acoustic ‘pair’ would be CF4 & N2 : O2 by e-chemical cell, CO2 from NDIR)
G. Hallewell: GasRad GWP: ECFA TF-4 Meeting May16-17th 2023
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 53
T
P
CO2
P
T
P
P
P
P
P
P
T
T
T
T
T
T
CO2
CO2
CO2
CO2
CO2
CO2
H2O
Example with a second known contaminant gas: here H2O but could be another measurable gas like O2 : 4-D {T,P, CO2, H2O} Process dataspace example ‘Cans’ of c vs. conc1,2 fit coefficients now at corners of tesseract. (Here in Coxeter B4 projection)
8 cube faces:
2 x {T,P,CO2} exc. H2O
2 x {T,P, H2O} exc. CO2
2 x {T, CO2, H2O} exc. P
2 x {P, CO2, H2O} exc. T
Opposite cubic faces explored in the following slides
H2O
H2O
H2O
H2O
H2O
H2O
H2O
53
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 54
Tessar-Can-Action
Canterpolation (Extractio-reduction)
https://www.mdpi.com/2410-390X/5/1/6
54
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 55
Analyseur a ultrasons de mélanges de gaz Xe-O2
Pour mesurer la concentration de Xe avec une
précision de 0.1% il faut mesurer la vitesse de son
avec une précision de 0.2 m/s
(instrument @ CERN: typ. 0.05 m/s)
In practice, work in the 100%RH regime:
 H2O molar concentration given by svp:
Xe/O2 anesthetic gas mixture can contain CO2 if soda-lime absorber cannister ineffective.
implement Xe/O2 gas concentration measurement algorithm in T, P, CO2 space
Maybe go to 4D (tessaract) if need to monitor on top of varying H2O conc..
Masse moléculaire Xe: 131
Masse moléculaire di-oxygène: 32
Polyfit parms
in « cans »
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 56
SoS CALC: Of course, CP & CV for all gases (primary & background)
must be calculated for all T, P points on the n-D grid;
CAN FILLING: Calculate & fit c in gas pair of primary interest from CP & CV over their conc. range AND @T, P, known background gas conc. Grid points.
Database size (3-D example)
DB size = No. primary fit coeffs * **…
RoI_n = range of interest_n: d_n = stepsize_n  Database explosion ?!?
Increasing stepsize ( longer interpolation distance) can reduce No. of cans (“cubes” become “cuboids”)…
Some dimensions can be suppressed altogether using physical law (rather than empirical changes):
example for temperature dimension:
Database growth control
(important in instruments using embedded m-controllers)
56
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 57: References; mainly on fluorocarbon fluids and GWP Related paper: https://link.springer.com/article/10.1140/epjp/s13360-023-04703-w
57
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 58
References
[1] CERN Environment Report 2017–2018 https://doi.org/10.25325/CERN-Environment-2020-001
[2] Eco-gas mixtures and mitigation procedures for Green-house Gases (GHGs);
B. Mandelli ECFA Detector R&D Road-map Symposium: T.F. 1 Gaseous Detectors, 29/4/2021
https://indico.cern.ch/event/999799/contributions/4204191
/attachments/2236047/3789965/BMandelli_ECFA.pdf,
[3] R&D for the optimization of the use of greenhouse gases in particle detector systems; B. Mandelli;
Mini workshop on gas transport parameters for present and future generation of experiments:
CERN April 22, 2021
https://indico.cern.ch/event/1022051/contributions/4325947/
[4] Studies to reduce greenhouse gas emissions from detectors at the LHC;
G. Rigoletti; EP-DT Seminar May 4, 2022.pdf (cern.ch)
[5] Long term experience with C4F10 in COMPASS RICH-1;
S. Dalla Torre et al; Presentation 11th Intl. Workshop on Ring Imaging Cherenkov detectors,
Edinburgh, Scotland, Sept 12-16 2022.
https://indico.cern.ch/event/1094055/contributions/4932286/attachments/2508724/4311387/
RICH2022_C4F10_dallatorre.pdf
[6] 3M PFG-3480: c-octofluorotetrahydrofuran (C4F8O).
Note: fluid out of production : product reference now used for a non-fluidic product.
For historic product data sheet mentioning its high GWP see (for example):
http://static6.arrow.com/aropdfconversion/a7116f41dfdd5b79d2eb7b40afd687f8af23d8ef/
mediawebserver(563).pdf
[7] M. Artuso et al; Nucl. Instr & Meth. A Volume 558, (2006), 373-387
[8] Product #2H07-2-08 Synonyms: 2,2,3,3,4,4,5,5-octafluorotetrahydrofuran,
Perfluorotetrahydrofuran; CAS No: 773-14-8, MDL No. MFCD00465561:
SynQuest Labs Inc., 13201 Rachael Boulevard, Alachua, FL 32615, USA
https://www.synquestlabs.com/Home/ProductDetail?SearchText=Octafluorotetrahydrofuran
[9] T. Acconcia et al ; Nucl. Instr & Meth A 767 (2014) 50–60

## Slide 59
References (cont. 1)
[10] Abundances, emissions, and loss processes of the long-lived and potent greenhouse gas
octafluorooxolane (octafluorotetrahydrofuran, c-C4F8O) in the atmosphere;
M. Vollmer et al ; Atmos. Chem. Phys., 19, 3481–3492, 2019
[11] 3M Novec® range of fluorinated fluids; https://www.3m.com/3M/en_US/p/c/b/novec/?Ntt=novec
[12] 3M Novec 649/1230 fluid (C6F12O);
https://multimedia.3m.com/mws/media/569865O/3m-novec-engineered-fluid-649.pdf,
https://multimedia.3m.com/mws/media/124688O/3m-novec-1230-fire-protection-fluid.pdf]
[13] 3M Novec 5110 fluid (C5F10O);
https://multimedia.3m.com/mws/media/1132123O/3m-novec-5110-insulating-gas.pdf
[14] CERN report EN-CV 22/12/2017, EDMS 1751219 2017-334 rev 1.0: T
echnical Note NOVEC Fluids Qualification Report: Report on the study executed for the qualification
of the NOVEC Fluid for Detector Cooling applications.
[15] Understanding the stability and environmental characteristics of a sustainable Halon alternative.
J. Owens, 3M Performance Materials 3M Center, St. Paul, MN 55144
[16] CERN Mini-workshop on gas transport parameters for present and future generation of
experiments 20/04/2021;S. Easo; LHCb-RICH detectors and their gas radiators
https://indico.cern.ch/event/1022051/contributions/4333562/attachments/2231064/3780374/
LHCb-RICH-Current-GasRadiators-April-2021.pdf,
Options for alternate radiators in LHCb-RICH system (including calculations by O. Ullaland); S. Easo,
https://indico.cern.ch/event/1022051/contributions/4319538/attachments/2231436/3781060/
LHCb-RICH-Future-Radiators.pdf
[17] S.Easo; Nucl.Inst.& Meth. A 876 (2017) 168-173
[18] E. Lemmon, M. Huber, & M. McLinden; REFPROP Standard reference database 23, version 9.0 (2010)
U.S. National Institute of Standards & Technology.
[19] E. Nappi & J. Seguinot Rivista del Nuovo Cimento Vol. 28, N. 8-9 2005 DOI 10.1393/ncr/i2006-10004-6
[20] K. Abe et al. ; IEEE Trans. Nucl. Sci. 45 (1998) 648 SLAC-PUB-7705 DOI: 10.1109/23.6826 [21] G. Hallewell et al; Nucl. Instr. & Meth A264 (1988) 219-234
[22] G. Hallewell; Nucl. Instr & Meth A 876, (2017) 50-53

## Slide 60
References (cont. 2)
[23] G. Hallewell et al; MDPI Instruments (2021) 5(1), 6;
[24] P. Stassi et al; Ultrasonic Gas mixture analysis system in the Forward RICH of DELPHI,
DELPHI Internal Note 95-124 RICH73, 25 July 1995
[25] M.Sannino; Nucl. Instr. and Methods in Physics Research A 595 (2008) 208–211
[26] Monitoring, Alignment and Control of the RICH Detectors; C. D'Ambrosio et al; LHCb-Memo-2000-80 RICH 6 September 2000.
[27] P. Fauland, PhD thesis; (COMPASS experiment) University of Bielefeld March 2004.
[28] Now marketed as SensComp model 600 transducer, http://www.senscomp.com/ultrasonic-sensors/
[29] T. Blake et al; Nucl. Instr. Meth A791 (2015) 27-31
[30] A. Papanestis; Nucl. Instr. Meth. A766 (2014) 14–18
[31] R. Calabrese et al; 2022 JINST 17 P07013
[32] R. Bates et al; 2013 JINST 8 P02006
[33] ECHA/NR/23/04; https://echa.europa.eu/-/echa-publishes-pfas-restriction-proposal]
[34] ECHA Candidate List of substances of very high concern for Authorisation;
https://echa.europa.eu/candidate-list-table
[35] Annex to the Annex XV restriction report proposal for restriction:
Per- & polyfluoroalkyl substances (PFASs);
ECHA; 22/03/2023 https://echa.europa.eu/documents/10162/d2f7fce1-b089-c4fd-1101-2601f53a07d1
[36] Per- and polyfluoroalkyl substances (PFAS); ECHA
https://echa.europa.eu/hot-topics/perfluoroalkyl-chemicals-pfas

## Slide 61
The uncertain ECHA path to prohibition
(a path paved with impracticalities?)
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 62
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 63
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 64
G. Hallewell: Seminaire CPPM: 16 sep 2024

## Slide 65
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 66
Positive and Negative exeriences with C4F8O as a substitute for C4F10
Cherenkov radiator gas
66
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 67
octafluorotetrahydrofuran
MW = 216: GWP=12000
a.k.a.
c-octafluoro-oxolane
C – F
C – F
l
F
F – C
F – C
l
F
F O F
67
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 68: Shapes of CnF2nO molecules and GWP:
c-octafluorooxolane (C4F8O),
MW = 216: GWP = 12000 BTEV stuff?
3M Specialty Gas PFG-3480 is a high-performance chamber cleaning gas that has environmental advantages and can help reduce operating costs. PFG-3480 reduces emissions of global warming compounds by 90 percent when compared to the traditional plasma enhanced chemical vapor deposition(PECVD) cleaning gas, C2F6. The replacement does not require changes to existing processes
Perfluortetrahydrofuran – the probable BTeV choice
From June 2000 3M datasheet
https://repository.library.noaa.gov/
044ed5ad-93ae-40e3-9420-d78
a4729ff0f
68
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 69: Shapes of CnF2nO molecules and GWP:
Octafluortetrahydrofuran – the probable ALICE VHPID config
C4F8O acquired from Synquest : reported by Antonello di Mauro:
C – F
C – F
l
F
F – C
F – C
l
F
F O F
69
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 70: SynQuest Labs Inc., 13201 Rachael Boulevard Rt 2054, Alachua, FL 32615, USA
70
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 71: SynQuest Labs, Inc. Can manufacture different C4F8O configurations
The cyclic molecule seems to be cheaper for SynQuest to manufacture:
whereas 3M make NOVEC 649, which is non-cyclic
71
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024

## Slide 72: Another exciting example: Novec 5110: C5F10O MW = 266: GWP <1
Mixing potential here with currently-available
low GWP « Fluoro-oxygenate » (CnF2nO) :
Blend with N2 to match C4F10 - or even CF4 - refractivity?
72
DRD4 Collaboration Meeting, WG-2: CERN Oct 21-25 2024